Source	MARKET NEWS
Date	07/05/2017
Time	06:15:42 AM

Company	 Mirasol Resources Ltd.
Title	Upgrades 
and Expands Aurora Prospect with High g





    CDNX Symbol: MRZ











Press Release





MIRASOL RESOURCES LTD ("MRZ-V;MRZLF-0")
- Upgrades and Expands Aurora Prospect with High-grade Gold
- and Silver Assays from Rock Chip

Mirasol Resources Ltd. ("Mirasol") is pleased to announce
high-grade gold and silver rock chip assays, that extend and infill
vein-breccia trends at the new Aurora prospect, part of Mirasol's 100%
owned Nico project Santa Cruz, province Argentina (Fig. 1).

This phase of mapping and sampling has increased the strike extent
of the principal north-south oriented mineralized trend to by 30% to
approximately 4 km.  A total of 1,113 rock-chip samples have been
collected to-date and with assays ranging up to 35.09 g/t Au (1.128
oz/t) and up to 2095 g/t Ag (67.4 oz/t).  This phase has upgraded the
results for the prospect (table 1) with the sample database now
including:

Gold

//st

* 178 samples greater than 1 g/t Au (0.032 oz/t)
* 34 samples greater than 5 g/t Au (0.161 oz/t)
* 6 samples greater than 15 g/t Au (0.482 oz/t)

//et

Silver

//st
* 155 sample greater than 60 g/t Ag (1.9 oz/t)
* 41 samples greater than 300 g/t Ag (9.6 oz/t)
* 5 samples greater than 900 g/t Ag (28.9 oz/t)

//et

Field observations and assays distribution suggest the presence of
multiple mineralised vein-breccia zones (potential shoots) that are
expressed as a linear alignment of intermittently outcrop, subcrop and
float of blocks, defining vein-breccia trends over a 4 x 2.1 km area at
the prospect (Fig.2).  This trend extends to the edge of post-mineral
basalt cover to the north and south, suggesting the system may continue
under cover and have a longer strike length than currently defined.  As
well, outcrop and sub-crop distribution of samples suggests the
potential for adjacent parallel vein breccia trends in some areas of
the prospect. Sample widths at surface show individual vein - breccias
typically range between 0.2 to 3.0 m in width with an average of 0.31 m
(see news release June 12, 2017).

Preliminary interpretation of the structural setting at Aurora
suggests that the better grades seem preferentially located in
north-west oriented flexures developed within the north-south
mineralized trend(s). These flexures are interpreted to occur at where
regional-scale structures intersection with the north-south trend(s),
and where the north-south trend intersects an arcuate shaped feature
speculated to mark part of a "ring fault", potentially developed above
the edge of a buried intrusive.  The flexures are thought to represent
sites of potential dilation and structural preparation of the host
rock(s) in the mineralized trend(s). Similar structural settings at
gold - silver deposit elsewhere in Santa Cruz province often mark the
sites for development of accumulations of mineralisation.  At Aurora,
these flexure zones will be the focus for follow-up detailed mapping
and sampling to define drill targets.

Rock chip samples assayed to date from the prospect are of oxidise
material.  In some cases oxidation may result in near surface upgrading
of gold and silver content of the samples, in comparison to the grades
in the underlying unoxidized mineralization. While Mirasol has not seen
any evidence to date that this is the case at Aurora, it is prudent to
acknowledge the possibility of this effect at this early stage of
exploration at the prospect.  Not withstanding this, the strongly
anomalous gold and silver assays returned from significant strike
extents of the vein-breccia structures, highlight Aurora as a
significant new discovery of a highly prospective, undrilled
gold-silver system, in the prolifically mineralised Santa Cruz
epithermal province.

Mirasol has continued to prospect in the Nico claims block beyond
the Aurora prospect.  Results of this exploration will be reported in
the coming weeks, as well as results of a re-evaluation of the
exploration undertaken by a previous joint venture partner at the Nico
main prospect.

Stephen Nano, President and CEO of Mirasol, has approved the
technical content of this news release and is a Qualified Person under
NI 43 -101.

Quality Assurance/Quality Control of the Nico exploration program:


All exploration on the project was supervised by Mirasol CEO
Stephen C. Nano, who is the Qualified Person under NI 43-101.

Mirasol applies industry standard exploration sampling
methodologies and techniques. All geochemical rock and drill samples
are collected under the supervision of the company's geologists in
accordance with industry practice. Geochemical assays are obtained and
reported under a quality assurance and quality control (QA/QC) program.
Samples are dispatched to an ISO 9001:2008 accredited laboratory in
Argentina for analysis. Samples are analysed by 30g fire assay for Au
and for Ag via a multi element ICP suite. If the silver assay exceeds
100 g/t, the sample is reanalysed using a gravimetric assaying method.
Assay results from surface rock, channel, trench, and drill core
samples may be higher, lower or similar to results obtained from
surface samples due to surficial oxidation and enrichment processes or
due to natural geological grade variations in the primary
mineralization.

Forward Looking Statements: The information in this news release
contains forward looking statements that are subject to a number of
known and unknown risks, uncertainties and other factors that may cause
actual results to differ materially from those anticipated in our
forward-looking statements. Factors that could cause such differences
include: changes in world commodity markets, equity markets, costs and
supply of materials relevant to the mining industry, change in
government and changes to regulations affecting the mining industry.
Forward-looking statements in this release include statements regarding
future exploration programs, operation plans, geological
interpretations, mineral tenure issues and mineral recovery processes.
Although we believe the expectations reflected in our forward-looking
statements are reasonable, results may vary, and we cannot guarantee
future results, levels of activity, performance or achievements.
Mirasol disclaims any obligations to update or revise any
forward-looking statements whether as a result of new information,
future events or otherwise, except as may be required by applicable
law.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

For further information:  Stephen Nano, President and CEO or John
Toporowski, Manager of Investor Relations, Tel: +1 (604) 602-9989,
Email: contact@mirasolresources.com, Website: www.mirasolresources.com

______________________________
_______________________________________________
TSX Venture closing price for MRZ-V
Date: 2017/07/04
Closing Price: 1.65
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1718500026TS11718501007-06144620170705