Source	MARKET NEWS
Date	07/05/2017
Time	05:36:41 AM

Company	 Silver Range Resources Ltd.
Title	Defines High grade Drill Targets At Strongbox





    CDNX Symbol: SNG











Press Release





Defines High grade Drill Targets At Strongbox --->@NEWS RELEASE
SILVER RANGE RESOURCES LTD ("SNG-V;SLRRF-0")
- Defines High-grade Drill Targets At Strongbox

Silver Range Resources Ltd. ("Silver Range") is pleased to provide
results from a geological and geophysical program conducted at the
Strongbox Property in Esmeralda County, Nevada. Property highlights
include:

//st

* widespread surface gold mineralization grading up to 27.1 g/t gold;
and,
* geophysical surveys that define large target areas below and along
strike of known high-grade mineralization.

//et

The Strongbox Property covers a system of gold veins that straddle
Tule Canyon, located 55 kilometres by road south of the town of
Goldfield. Despite being the target of several placer and small-scale
hard rock mining operations since the mid-1800s, Strongbox has seen
little modern exploration, and Silver Range has found no evidence of
drilling.

A total of 42 grab and chip samples were collected during the
recent program, 16 of which assayed greater than 1 g/t Au and 9 of
which assayed greater than 5 g/t Au. The best sample returned 18.7 g/t
Aufrom vein material that was taken from a dump at the main showing
west of Tule Canyon.

Gold on the property occurs in north to northeast trending
quartz-limonite veins developed in fault zones within Jurassic granite.
Near Tule Canyon, strong veins are spaced 10 to 20 m apart within a 100
to 200 m wide kaolinite-illite-smectite-hematite-goethite alteration
zone containing local jarosite and calcite. There are workings on both
the east and west sides of the canyon. The most prominent bedrock
alteration and the highest grade gold samples are found on the west
side of Tule Canyon, while extensive narrow underground workings were
driven in more competent veins on the east side of the canyon.

Ground total magnetic field and horizontal loop electromagnetic
(HLEM) surveys were conducted to investigate the mineralization. The
veins and alteration on the west side of Tule Canyon occur along the
southern margin of a large west-trending magnetic low.

The HLEM resistivity data delineated features that are directly
associated with the surface gold mineralization and which extend along
strike of and below known showings. The geophysical survey results
delineate bedrock structures and define compelling drill targets. Maps
and a video presentation on the Strongbox Property describing the
geophysical results and drill targets can be viewed on the property
page at www.silverrangeresources.com.

The work program described in this press release was conducted by
Aurora Geosciences Ltd. with sampling conducted under the supervision
of Roger Hulstein, P.Geo. Technical information in this news release
has been approved by Mike Power, M.Sc., P.Geo., CPG, President and CEO
of Silver Range Resources Ltd. and a Qualified Person for the purposes
of National Instrument 43-101.

Silver Range is a precious metals prospect generator working in
Nevada, Nunavut and the Northwest Territories. The company is actively
seeking joint venture partners to explore the assets in its portfolio.

ON BEHALF OF SILVER RANGE RESOURCES LTD.
"Mike Power"
President, C.E.O. & Director

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release may contain forward looking statements based on
assumptions and judgments of management regarding future events or
results that may prove to be inaccurate as a result of exploration and
other risk factors beyond its control, and actual results may differ
materially from the expected results.

Contact Information:

For further information concerning Silver Range or its exploration projects
please contact:

Investor Inquiries
Richard Drechsler
Vice-President, Communications
Tel: (604) 687-2522
NA Toll-Free: (888) 688-2522
rdrechsler@silverrangeresources.com
http://www.silverrangeresources.com
______________________________
_______________________________________________
TSX Venture closing price for SNG-V
Date: 2017/07/04
Closing Price: 0.21
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1718500018TS11718500739-05333520170705