Source	MARKET NEWS
Date	07/10/2017
Time	06:54:33 AM

Company	 Golden Predator Mining Corp.
Title	Intersects 6.86 M Of 20.15 G/t Gold At The 3 Ace





    CDNX Symbol: GPY











Press Release





Intersects 6.86 M Of 20.15 G/t Gold At The 3 Aces Project Jack AndAce Of 
Spades Zones Merging --->@NEWS RELEASE
GOLDEN PREDATOR MINING CORP ("GPY-V;NTGSF-0")
- Intersects 6.86 M Of 20.15 G/t Gold At The 3 Aces Project
- Jack And Ace Of Spades Zones Merging

Golden Predator Mining Corp. (the "Company" or "Golden Predator")
is pleased to report assay results for 23 reverse circulation (RC)
drill holes completed as of May 15, 2017 at the 3 Aces Project in
southeast Yukon, Canada. Current results expand the zone of
mineralization in the Ace and Jack of Spades zone to 137+m (450+ feet)
in a southeasterly direction (down dip) and 61+m (200+ feet) along
strike and it remains open. In addition to the already identified high
grade underground targets, the drilling results suggest a merging into
a single gently dipping zone, providing a potential near surface bulk
mineable. These drill results are part of a fully funded 40,000 m drill
program, which will continue throughout 2017.

Significant results include:

//st

* Hole 3A17-100 intersected 6.86 m of 20.15 g/t gold from a depth of 19.05
m, including 1.53 m of 42.59 g/t gold;
* Hole 3A17-106 intersected 1.52 m of 54.25 g/t gold from a depth of 2.29
m, and 1.53 m of 8.89 g/t gold from 8.38 m, and 1.53 m of 14.26 g/t gold
from 12.95 m;
* Hole 3A17-125 intersected 2.29 m of 35.35 g/t gold from a depth 9.14 m,
including 0.76 m of 59.30 g/t gold;
* Hole 3A17-127 intersected 6.10 m of 22.30 g/t gold from a depth of 12.95
m;
* Hole 3A17-126 intersected 1.52 m of 72.25 g/t gold from a depth of 14.48
m.

//et

To view maps of the 3 Aces Project outlining the results in this
release please visit:

http://www.goldenpredator.com/_resources/maps/3Aces_20170710_PressReleaseMa
ps.pdf

2017 3 Aces Exploration Program
The 2017 drill program, commenced in February, is initially
focusing on the Spades Zone then expanding to other areas of the
property. Drilling in the Spades Zone is intended to test targets
including the depth and strike extensions of the Ace of Spades vein,
stockwork mineralization encountered below the Ace of Spades vein, and,
to conduct initial drilling at the Jack, Queen, Seven and Three of
Spades. The 2017 drill program will then focus on identifying and
testing new mineralized vein targets combined with expanding the
current gold targets in the Clubs, Hearts and Spades zones.

Forty-three reverse circulation holes were drilled in the first
round of the 2017 program, completed on May 15, 2017, from an area
measuring over 450 x 700 m (1,475 x 1,300 feet) in the Spades Zone.
Results from four additional holes are pending.

Since June 1, 2017, an additional 13 RC holes for 718 m (2,355
feet) and 20 PQ diamond core holes for 1,906 m (6,253 feet) have been
drilled in the Spades Zone to complete the second round, results
pending. The current RC drilling will also focus on down-dip and along
strike of the Ace of Hearts vein, the Queen of Clubs vein and the Seven
of Spades zone. Initial drilling will be conducted at the northeast
extension of the Ace of Spades, a newly discovered vein at the Three of
Spades, the Queen of Hearts, the Six of Clubs and the Ten of Clubs.

Gold mineralization in the Spades zone is localized in the
footwall of an east-west trending, south dipping shear zone which
approximates a strongly sheared and folded phyllite/sandstone contact.
Lenticular quartz veins and associate gold mineralization are best
developed along north-northeast and north-northwest trending structures
dipping 50 SE and 60-80 SW respectively. The gold bearing vein system
is developed within a moderately dipping, southeast plunging syncline
with a phyllite hanging wall and sandstone footwall. The best
grade/thickness gold mineralization appears to be developed within the
syncline fold axis and similar structural settings are being targeted
for drilling immediately northwest and southeast of the Spades zone. In
addition to the higher-grade intervals reported here, there are
extensive zones in the current drilling that contain near surface
intervals ranging from 0.25 g/t gold up to 3.0 g/t gold.

A second gold in soil anomaly is developed 400 m west of the Ace
of Spades vein within a similar setting with arsenopyrite-bearing
quartz veins developed along phyllite/sandstone contacts. The gold in
soil anomaly has a strike length of approximately 250 m with gold
values to 4.61 g/t gold and rock chip sample assays are pending.
Arsenopyrite-bearing quartz veins have been recently discovered 450 m
east of the Ace of Spades zone along the east-west shear zone and rock
assays from recently excavated trenches are pending.

Soil sampling, trenching, road construction and property-wide
geochemical grid surveying over favourable terrain have commenced for
the 2017 season.

//st

Significant Results Drill Table - Spades Zone

Hole ID 1                  Sample    From      To (m)   Drilled    Gold
Type 2    (m)                Width      g/t 3
(m)

3A17-100                   RC        19.05     25.91    6.86       20.15

and                        RC        77.72     78.49    0.77       3.79*

3A17-101                   RC        3.81      4.57     0.76       13.80

and                        RC        88.39     89.92    1.53       4.11

and                        RC        129.54    131.06   1.52       4.85

and                        RC        137.16    137.92   0.76       6.23

3A17-102                   RC        25.15     26.67    1.52       6.19

3A17-103                   RC        12.19     12.95    0.76       8.90*

and                        RC        22.10     22.86    0.76       14.95

and                        RC        24.38     25.91    1.53       3.39

3A17-104                   RC        48.77     49.53    0.76       10.95

and                        RC        100.58    101.35   0.77       7.74

3A17-106                   RC        2.29      3.81     1.52       54.25

and                        RC        8.38      9.91     1.53       8.89

and                        RC        12.95     14.48    1.53       14.26

including   RC        13.72     14.48    0.76       24.90

and                        RC        45.72     46.48    0.76       7.88

3A17-107                   RC        6.10      6.86     0.76       26.90

3A17-108                   RC        10.67     11.43    0.76       7.24

and                        RC        15.24     16.00    0.76       3.86

3A17-109                   RC        25.15     25.91    0.76       4.47

and                        RC        27.43     28.19    0.76       14.40

and                        RC        43.43     44.20    0.77       7.96

3A17-114                   RC        35.05     36.58    1.53       6.55

and                        RC        54.10     54.86    0.76       4.03*

3A17-115                   RC        26.67     27.43    0.76       4.92

3A17-118                   RC        48.01     48.77    0.76       13.05

and                        RC        51.05     51.82    0.77       12.60

and                        RC        66.29     67.06    0.77       3.06*

and                        RC        75.44     76.20    0.76       4.51*

3A17-119                   RC        30.48     31.24    0.76       3.94*

and                        RC        40.39     41.15    0.76       5.90*

3A17-120                   RC        21.34     22.10    0.76       4.26*

and                        RC        24.38     25.15    0.77       5.58*

and                        RC        36.58     38.86    2.28       7.73*

including   RC        36.58     37.34    0.76       15.40*

3A17-125                   RC        9.14      11.43    2.29       35.35

and                        RC        49.53     51.05    1.52       4.39*

and                        RC        97.54     98.30    0.76       4.98*

3A17-126                   RC        14.48     16.00    1.52       72.25

including   RC        14.48     15.24    0.76       109.00

3A17-127                   RC        12.95     19.05    6.10       22.30

and                        RC        35.05     35.81    0.76       3.83

3A17-128                   RC        16.00     17.53    1.53       11.36

and                        RC        23.62     24.38    0.76       4.99

and                        RC        25.15     25.91    0.76       4.31

and                        RC        32.00     34.29    2.29       6.10

and                        RC        76.96     77.72    0.76       3.00

and                        RC        84.58     85.34    0.76       3.05

//et

//st

1   Only Spades area holes with a drilled interval assaying =3.0 g/t gold
are reported in table;

Hole 3A17-100's significant intercept from 19.05m to 25.91m
includes 0.76m of 0.77 g/t Au at 22.10m depth

Holes 3A17-105, 3A17-112, 3A17-113, 3A17-116 and 3A17-117 returned
multiple intervals =1.0 g/t but = 3.0 g/t Au

2   Sample Type 'RC' is whole 5.5" (139.7mm) reverse circulation cuttings

3   All intervals are reported as drilled thicknesses; true thicknesses
are estimated to be 50-100% of drilled thicknesses

4   Reported Au assay grade sourced from ALS using Au-SCR24B method (*
indicates finalized Au-AA26 results are used)

//et

3 Aces Project, Yukon

The 3 Aces Project includes the 3 Aces, Reef, and Hy Jay
properties consisting of 1,734 claims covering 357 km (35,700 hectares)
in southeast Yukon. The project is located along the all-season Cantung
Mine Road which accesses the Cantung Mine, 40 km to the north. The 3
Aces Project, which includes the two highest grade surface discoveries
to date in the Yukon, has over 25 mineralized veins that have been
discovered through sampling, trenching, roadwork and drilling over 762
m (2,500 feet) of elevation within the Central Core area.

Surface outcrops of gold bearing quartz veins were discovered on
the property, then advanced with extensive soil sampling and helicopter
supported core drilling, which outlined significant gold anomalies over
a Central Core Area of 10.5 km2. Previous exploration work by Golden
Predator in 2015 and 2016, which included metallurgical studies, rotary
air blast (RAB) drilling, RC drilling, diamond drilling and bulk
sampling, focused on establishing reproducible gold grades and
continuity of the Ace of Spades vein where previous diamond drilling
had returned inconsistent grades. This work confirmed the high gold
grades of the vein by better targeting and utilization of a sampling
and assaying protocol derived from metallurgical studies.

The 3 Aces property is in the traditional territory of the Kaska
Nation. In January 2013, Golden Predator signed an Exploration
Agreement with the Kaska Nation, as represented by the Ross River Dena
Council and the Liard First Nation, with respect to activities within
their traditional territories. The 3 Aces Project operates under a
Class 4 Mining Land Use Permit.

Sampling Methodology, Quality Control and Assurance

Because of the high-grade gold encountered at 3 Aces to date, the
Company has taken steps to ensure that its sampling and assaying
procedures can be depended upon. The Company has utilized larger
diameter drilling to provide sample material for
comparative/effectiveness analysis of past drilling programs, including
sampling protocols, assay methods and QA/QC procedures, and to more
confidently estimate grades of high-grade veins containing coarse gold.


All analyses for the drill samples from the program were performed
by ALS with sample preparation in Whitehorse, YT, Terrace, B.C. or
North Vancouver, B.C. and assaying in North Vancouver, B.C. Drill
samples were analyzed using a 50 g fire assay with atomic absorption
(AA) finish. If the procedure returned a value of 2.0 g/t gold or
greater it is re-run using a 2kg screen metallic gold method
(Au-SCR24).

The screen metallic procedure utilizes a two-kilogram split from
each crushed sample, which is pulverized and passed through a 150-mesh
screen. The material remaining on the screen (Plus fraction) is
analyzed in its entirety by fire assay with gravimetric finish. The
material that passed through the screen (Minus fraction) is homogenized
and two 50 g subsamples are analyzed by fire assay with AA finish and
averaged. The Plus and Minus fraction gold analyzes are weight averaged
to obtain a final gold determination for the sample. Quality control
and assurance (QA/QC) included 12% of the samples, consisting of reject
duplicates, blank and certified reference materials.

Due to the lengthy delay in the receipt of final assays and their
reporting, the Company has, upon completion of a sampling assessment
and error study, altered its existing drill sampling and assaying
protocol. The Company has implemented several changes to its protocol,
effective immediately, and is confident this will result in a
significantly reduced timeline in terms of receiving and reporting
assays from the Company's drilling. The Company will also experience a
significant cost reduction associated with these changes.

The technical content of this news release has been reviewed and
approved by Mark C. Shutty, CPG, a Qualified Person as defined by
National Instrument 43-101 and an employee of the Company.

Golden Predator Mining Corp.

Golden Predator Mining Corp. is a well-financed Canadian gold
mineral exploration company expanding its surface discoveries, at the 3
Aces Project in Canada's Yukon, through focused drilling. The 3 Aces
property is a high-grade gold in quartz project with an exploration
program underway that includes sampling, trenching, drilling and bulk
sampling to define and interpret the project. The Company also holds
the Brewery Creek Project in Canada's Yukon.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release. No
stock exchange, securities commission or other regulatory authority has
approved or disapproved the information contained herein. This press
release contains forward-looking information that involve various risks
and uncertainties regarding future events. Such forward-looking
information can include without limitation statements based on current
expectations that the private placement will complete as described
herein, that the Project will advance through permitting and
feasibility.  Actual results and future events could differ materially
from those anticipated in such information. These and all subsequent
written and oral forward-looking information are based on estimates and
opinions of management on the dates they are made and are expresslyqualified in 
their entirety by this notice. Except as required by law,
the Company assumes no obligation to update forward-looking information
should circumstances or management's estimates or opinions change.

Golden Predator Press Release dated May 3, 2017
TSX Venture closing price for GPY-V
Date: 2017/07/07
Closing Price: 1.06

TEL:  (604) 260-0289   Janet Lee- Sheriff, Chief Executive Officer
E-mail: info@goldenpredator.com
Internet: www.goldenpredator.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1719000035TS11719001139-06513120170710