Source	MARKET NEWS
Date	07/10/2017
Time	06:15:34 AM

Company	 Hannan Metals Ltd.
Title	Maiden 
Mineral Resource Estimate for Kilbricken





    CDNX Symbol: HAN











Press Release




[200/News Release]HANVHANNAN METALS LTDJUL 10 2017  06:12 AMMaiden 
Mineral Resource Estimate for Kilbricken in Ireland --->@NEWS RELEASE
HANNAN METALS LTD ("HAN-V;HANNF-0")
- Maiden Mineral Resource Estimate for Kilbricken in Ireland

Hannan Metals Limited ("Hannan" or the "Company") is pleased to
announce a maiden resource estimate for its 100%-owned Kilbricken
zinc-lead-silver-copper deposit in Ireland.

Highlights include:

//st

* Total indicated mineral resource of 2.7 million tonnes at 8.8% zinc
equivalent ("ZnEq"), including 1.4 millions tonnes at 10.8% Zneq;
* Total inferred mineral resource of 1.7 million tonnes at 8.2% ZnEq,
including 0.6 million tonnes at 10.4% Zneq;
* This resource estimate is the first for the Kilbricken deposit, and
immediately ranks it as one of the top ten base metal deposits discovered
in Ireland by tonnes and grade (data sourced from the Irish Exploration,
Mining Division website);
* Two styles of mineralization are evident at Kilbricken. The upper
Chimney Zone demonstrates the classic high-grade ()10% Zneq) Irish
stratabound mineralization targeted by Hannan. This body has been drilled
within an area of 750 metres by 200 metres and averages 12 metres
thickness. The lower Fort Zone was found later than the Chimney zone and
has been tested with fewer drill holes. It is structurally hosted, lower
grade, but thicker, averaging 40 metres, and drilled within a 400 metre by
200 metres area.
* Importantly, the initial resource is expandable at all scales, from
near resource to prospect scale, and Hannan has already commenced a drill
resource expansion program;

//et

Mr. Michael Hudson, CEO and Chairman, states: "The maiden resource
is an important milestone for Hannan.  It demonstrates the high-grade
potential of the deposit and immediately ranks Kilbricken as one of the
top ten base metal deposits discovered to date in Ireland.  This is
significant initial achievement in a country that is ranked first in
the world in terms of zinc discovered per square kilometre since the
1950's.

While this resource is substantial, it is also lies open in all
directions with excellent potential for expansion.  We currently have
one drill rig operating a resource expansion program and we will soon
be mobilizing additional drill rigs.  We are able to approach our
exploration and expansion programs with the benefit of extensive
technical databases and an increased understanding of the controls on
mineralization, providing an excellent chance for continued discovery."


Resource Expansion Drilling Update

Importantly, the initial resource is expandable at all scales,
from near resource to prospect scale, and Hannan has already commenced
a drill resource expansion program.  The objectives of the 2017 drill
program are three-fold:

//st

* To further delineate the underground potential around the current
resource area as shown in Figure 1. Drilling is now ongoing within this
area and initial drill results are expected within the next three weeks. To
date two holes have been completed for 1,365 metres.
* To test conceptual and advanced exploration targets within 1-5
kilometres defined by recent structural and stratigraphic interpretation of
re-processed 2D and 3D seismic data, lithogeochemistry and soil
geochemistry as shown in Figure 2.
* Test for first order mineralization within the 40 kilometre
under-tested Waulsortian host horizon that exists within Hannan's 100%
owned 32,223 hectares of prospecting licences.

//et

Tables 1, 2 and 3 below outline global indicated and inferred
resources for each mineralized body as well as a breakdown of resources
by location for various lower cut off grades.  Figures 1 and 2 show the
mineral resource areas, resource expansion targets, diamond holes and
historic prospects at different scales.

//st

Table 1: Kilbricken Deposit Indicated Mineral Resources Base Case 5% ZnEq
Lower Cut Off Grade

Zone     Category   Cutoff  Tonnes    Zn% Pb% Ag  Cu% ZnEq% SG
g/t           ZnEq%

Chimney  Indicated  5       1,369,000 5.6 4.2 66  0.1 10.8  3.5

Fort     Indicated  5       1,287,000 3.7 1.4 34  0.5 6.7   3.0

Total    Indicated  5       2,656,000 4.7 2.9 50  0.3 8.8   3.2

Table 2: Kilbricken Deposit Inferred Mineral Resources Base Case 5% ZnEq
Lower Cut Off Grade

Zone     Category  Cutoff Tonnes    Zn% Pb% Ag  Cu%  ZnEq%  SG
g/t             ZnEq%

Chimney  Inferred  5      635,000   5.9 3.6 61  0.1  10.4   3.4

Fort     Inferred  5      1,046,000 3.4 2.5 30  0.3  6.8    3.0

Total    Inferred  5      1,681,000 4.4 2.9 41  0.2  8.2    3.1

//et

//st

Table 3: Kilbricken Deposit Indicated and Inferred Mineral Resources for
the
Chimney and Fort Zones at Various ZnEq Lower Cut Off Grades. The 5% ZnEq
base
case is highlighted.

Zone    Category   Cutoff  Tonnes     Zn%  Pb%  Ag   Cu%  ZnEq  SG
g/t       %

Chimney Indicated  4       1,444,000  5.4  4.1  64   0.1  10.4  3.4

Fort    Indicated  4       1,452,000  3.6  1.4  33   0.5  6.5   2.9

Chimney Inferred   4       682,000    5.7  3.5  58   0.1  10.0  3.3

Fort    Inferred   4       1,194,000  3.2  2.4  30   0.3  6.5   3.0

Chimney Indicated  5       1,369,000  5.6  4.2  66   0.1  10.8  3.5

Fort    Indicated  5       1,287,000  3.7  1.4  34   0.5  6.7   3.0

Chimney Inferred   5       635,000    5.9  3.6  61   0.1  10.4  3.4

Fort    Inferred   5       1,046,000  3.4  2.5  30   0.3  6.8   3.0

Chimney Indicated  6       1,291,000  5.8  4.4  67   0.1  11.1  3.5

Fort    Indicated  6       790,000    4.4  1.5  34   0.5  7.5   3.0

Chimney Inferred   6       586,000    6.1  3.8  63   0.1  10.8  3.4

Fort    Inferred   6       876,000    3.5  2.7  31   0.3  7.0   3.0

Chimney Indicated  7       1,173,000  6.0  4.5  70   0.1  11.5  3.5

Fort    Indicated  7       407,000    4.8  1.3  43   0.8  8.5   3.0

Chimney Inferred   7       536,000    6.3  3.9  66   0.1  11.2  3.4

Fort    Inferred   7       267,000    4.2  2.6  44   0.5  8.3   3.0

//et

//st

Note:The zinc equivalent (ZnEq) value was calculated using the following
formula: ZnEq% = Zn % + (Cu% * 2.102) + Pb% * 0.815) + (Ag g/t * 0.023)
with assumed prices of Zn $2587/t; Cu $5437/t; Pb $2108/t and Ag $18.44/oz.

//et

Details of the Mineral Resource Estimate

The National Instrument 43-101 Mineral Resource estimate was
calculated by Mr. Geoff Reed, MAUSIMM (CP), of Reed Leyton Consulting
Pty Ltd ("Reed Leyton") from Sydney, Australia.  The resource has an
effective date of 10 July, 2017.

Reed Leyton estimated the Kilbricken Mineral Resource using a
drill database of 222 drill holes for 118,000 metres produced by Lundin
Mining Ltd, drilled from 2010 to 2012.  The resource was calculated
using mineralized intercepts from 76 drillholes and a comprehensive
re-interpretation of the geology by Hannan.  The resource does not
include any 2017 drilling by Hannan.

A set of cross-sections and level plans were used to construct
three-dimensional wireframe models at approximate cut-offs of 1% and 3%
ZnEq for both the Chimney and Fort zones.  All assays were composited,
with a majority composited to two metre lengths, with a minimum half
metre length.  No upper cut-off was applied to zinc but an upper cut
off was used for lead and copper mineralization at the Chimney zone and
to lead, copper and silver at the Fort zone.

Block model grades within the wireframe models were interpolated
in Vulcan by Ordinary Kriging with secondary check models by inverse
distance squared.  Classic density measurements (specific gravity of
"SG") were performed on all samples.  Indicated Mineral Resources were
defined by at least 2 holes falling within a 30 metres sample distance,
with the remainder of mineralization greater than 30 metres sample
distance categorized as Inferred Mineral Resources.

The base case mineral resources reported above use a lower cut-off
grade of 5% ZnEq or approximately US$60 per tonne net smelter return
value based on potential underground mining scenarios.

The zinc equivalent (ZnEq) value was calculated using the
following formula: ZnEq% = Zn % + (Cu% * 2.102) + Pb% * 0.815) + (Ag
g/t * 0.023) with assumed prices of Zn $2587/t; Cu $5437/t; Pb $2108/t
and Ag $18.44/oz. Equivalent recovery for all metals is assumed.

CIM definitions were followed for Mineral Resources. Mineral
Resources are not Mineral Reserves and do not have demonstrated
economic viability. There is no certainty that all or any part of the
Mineral Resources will be converted into Mineral Reserves.

A metallurgical gap analysis was performed for Hannan and reported
on 30 March 2017, by Dr. Kurt Forrester of ARN Perspective Ltd, based
on a report by SGS Mineral Services, Lakefield Facility, dated
September 2010 and titled: "An Investigation by High Definition
Mineralogy into the mineralogical characteristics of Fourteen Rock
Samples from A Carbonate Hosted Base Metal Deposit, Ireland, prepared
for Lundin Mining Exploration". The key finding, based on available
information, is that it is likely a conventional lead-zinc flotation
circuit at Kilbricken would achieve saleable mineral concentrates.
Therefore, it is assumed that lead and silver will be recovered in a
lead concentrate, and a separate copper circuit may be required.

About the Kilbricken Project

The Kilbricken project lies within the Clare
zinc-silver-lead-copper property which consists of 9 prospecting
licences ("PLs") for a total of 32,223 hectares.  The project is in
County Clare, Ireland, the western edge of which lies 1.5 km east of
the town of Ennis.

The Property is underlain by an Upper Devonian to Lower
Carboniferous sequence of sandstone and limestones.  The stratigraphy
appears simple, where units are upright and typically of consistent in
thickness across the property.  Syn-rift and/or later structures appear
to complicate the geological framework, particularly in mineralized
areas.  The Lower Carboniferous sequence includes the Waulsortian
Limestone, which hosts most of Ireland's important zinc-lead sulphide
deposits, such as the Lisheen (pre-mining resource 18.9 Mt @ 15.0%
Zn+Pb) and Galmoy (pre-mining resource of 6.2 Mt @ 12.4% Zn+Pb)
deposits.  This data has been sourced from the Irish Exploration,
Mining Division website http://www.mineralsireland.ie/.

Two mineralized bodies are present at Kilbricken, the upper
Chimney Zone and the lower Fort Zone. Both show an association with
NW-SE striking extensional faults.  The Chimney Zone, being the initial
discovery area, has been most intensively drilled within an area of 750
metres by 200 metres, between 440-530 metres below surface and averages
12 metres thickness. Mineralization is controlled by a failed relay
ramp between two extensional fault segments. It is stratabound at the
base of the Waulsortian limestone.  The Fort Zone was found later in
the Lundin program and is drilled over an area of 400 metres by 200
metres, between 480-720 metres below surface with an average thickness
of 40 metres. The mineralized body is wedge shaped and transgressive to
the host rock. It follows an area of extensive dissolution of the host
limestone and structurally it is located adjacent to the zone of
maximum displacement of a south dipping extensional fault.

Qualified Person - Mineral Resources: The Mineral Resources
disclosed in this press release have been estimated by Mr. Geoff Reed,
MAUSIMM (CP), owner of Reed Leyton Consulting Pty Ltd and independent
of Hannan Metals Ltd and have an effective date of 10 July 2017.  By
virtue of his education and relevant experience, Mr. Reed is a
"Qualified Person" for the purpose of National Instrument 43-101. The
Mineral Resources have been classified in accordance with CIM
Definition Standards for Mineral Resources and Mineral Reserves adopted
by the CIM council on May 10, 2014. Mr. Reed, MAUSIMM (CP), has read
and approved the contents of this press release as it pertains to the
disclosed Mineral Resource estimates.

A National Instrument 43-101 Technical Report will be filed on
SEDAR within 45 days.

About Hannan Metals Limited (TSX.V:HAN)Hannan Metals Limited has
100% ownership of the County Clare Zn-Pb-Ag-Cu project in Ireland,
which consists of 9 prospecting licences for 32,223 hectares.  Zinc
remains in tight supply amidst rising demand and stagnant supply.
Ireland is a leading global jurisdiction for zinc mining and
exploration. It has been stated that Irish base metal ore field is
ranked first in the world in terms of zinc discovered per square
kilometre, and second in the world with respect to lead. In 2015,
Ireland was the world's 10th largest zinc producing nation with 230,000
tonnes produced.

Over the last decade, the team behind Hannan has forged a long and
successful record of financing and discovering mineral projects in
Europe. Additionally, the team holds extensive zinc experience, gained
from the world's largest integrated zinc producer of the time, Pasminco
Ltd.

Mr. Michael Hudson FAusIMM, Hannan's CEO and Chairman, is a
Qualified Person as defined in National Instrument 43-101 and has
reviewed and approved the technical disclosure contained in this news
release.

On behalf of the Board,

"Michael Hudson"Michael Hudson, CEO & Chairman

Forward Looking Statements

Certain information set forth in this news release contains
"forward-looking statements", and "forward- looking information" under
applicable securities laws. Except for statements of historical fact,
certain information contained herein constitutes forward-looking
statements, which include the Company's expectations regarding future
performance based on current results, expected cash costs based on the
Company's current internal expectations, estimates, projections,
assumptions and beliefs, which may prove to be incorrect. These
statements are not guarantees of future performance and undue reliance
should not be placed on them. Such forward-looking statements
necessarily involve known and unknown risks and uncertainties, which
may cause the Company's actual performance and financial results in
future periods to differ materially from any projects of future
performance or results expressed or implied by such forward-looking
statement. These risks and uncertainties include, but are not limited
to: liabilities inherent in mine development and production, geological
risks, the financial markets generally, and the ability of the Company
to raise additional capital to fund future operations. There can be no
assurance that forward-looking statements will prove to be accurate,
and actual results and future events could differ materially from those
anticipated in such statements. The Company undertakes no obligation to
update forward-looking statements if circumstances or management'sestimates or 
opinions should change except as required by applicable
securities laws. The reader is cautioned not to place undue reliance on
forward-looking statements.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release.

Contact Information:

For further information:  www.hannanmetals.com, 1305 - 1090 West Georgia
St., Vancouver, BC, V6E 3V7, Mariana Bermudez, Corporate Secretary, +1
(604) 685 9316, info@hannanmetals.com
______________________________
_______________________________________________
TSX Venture closing price for HAN-V
Date: 2017/07/06
Closing Price: 0.40
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1719000022TS11719000962-06125720170710