Source	Marketwire
Date	07/09/2017
Time	09:01:43 PM

Company	 MILLENNIAL LITHIUM CORP.
Title	Millennial Lithium: Extended Pumping Tests indicate Robust Pasto Grandes 
Lithium Aquifer





    CDNX Symbol: ML











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Millennial Lithium Corp.

TSX VENTURE SYMBOL: ML
OTCQB SYMBOL: MLNLF
FRANKFURT SYMBOL: A3N2

July 10, 2017

Millennial Lithium: Extended Pumping Tests indicate Robust Pasto Grandes 
Lithium Aquifer


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 10, 2017) - Millennial Lithium 
Corp. (TSX VENTURE:ML)(FRANKFURT:A3N2)(OTCQB:MLNLF) ("Millennial" or the 
"Company") is pleased to report encouraging results from an extended pumping 
test of the first production scale well at its Pastos Grandes Project in Salta, 
Argentina. Pumping well PGPW16-01 was installed in late 2016 to complete 
extended pumping of the lithium brine to determine the robustness and chemical 
variation of the aquifer over an extended period. At a pumping rate of 27.7 
litres/second (l/s), the lithium content remained very consistent over the 60 
hour period. The drawdown over 24 hours was approximately 9 metres (m) with 
very rapid recovery.

Millennial CEO, Farhad Abasov, commented: "Millennial is very pleased with the 
results of this first pumping test. The test indicates strong brine flow rates 
of 27.7 l/s at the maximum capacity of the pumping equipment with only minor 
draw-down, and consistent lithium concentrations suggest a robust aquifer. 
Strong lithium values remained relatively consistent throughout the duration of 
the pumping test suggesting lithium distribution is widespread. Brine from well 
PGPW16-01 is now being used to feed a series of trial evaporation ponds as part 
of Millennial's ongoing development of the Pastos Grandes project."

Well PGPW16-01 was drilled at a diameter of 17 inches to a depth of 125m and 
then 13.5 inches to the total depth of 351m. The well was completed with 
slotted casing (screen) at 10 inch and 6 inch diameters with gravel pack from 
top to bottom in the annulus in order to capture brine from the numerous 
permeable layers. The pumping rate for the test period was 27.7 l/s, the 
capacity of the equipment on site. Table 1 contains a summary of the main 
results of the test work.

Table 1. Summary of Pumping Test at Well PGPW16-01

/T/

----------------------------------------------------------------------------
PUMPING           AVERAGE                 DRAWDOWN
DURATION           PUMPING           AFTER 24 HOURS
WELL ID                   (hours)       RATE (l/s)2      OF PUMPING (metres)
----------------------------------------------------------------------------
PGPW16-01                      60              27.7                     9.04
----------------------------------------------------------------------------

/T/

Measurements of brine levels during the pumping test indicate a drawdown of 
approximately 9m over a 24 hour period. In addition, continued measurements 
after termination of the pumping test showed a recovery of the brine level to 
within 0.5m of its original position after the 60 hour recovery period. The 
drawdown data is the basis for the calculation of the aquifer transmissivity, 
the rate at which the brine moves through the aquifer. Based on early testing, 
the transmissivity of Pastos Grandes is conservatively estimated to be very 
good at 550 square metres per day (m2/d).

Brine sampling during the pumping test was completed every 6 hours for a better 
understanding of the variation in brine chemical composition as the aquifer was 
tested. In general, the chemistry is consistent over the 60 hour period with 
lithium only dropping 8.2 mg/l from an initial 438.7 mg/l to 430.5 mg/l . 
Lithium to magnesium (Li/Mg), sulphate to lithium (SO4/Li) and potassium to 
lithium (K/Li) ratios also remain fairly constant over the test period.

A second pumping well is being constructed at hole PGMW17-04b where recent 
drilling has intersected extensive lithium-bearing brine (see Press Release 
dated June 27, 2017) and testing is expected to commence in the near future.

Sampling was conducted in accordance with CIM guidelines for brine resource 
evaluation, with an appropriate QA/QC program in place for ensuring accuracy 
and repeatability of the analytical results.

Alex Stewart Laboratories of Mendoza, Argentina and partner laboratory, Norlab 
S.R.L. of Palpala, Jujuy, are the primary analytical providers. The 
laboratories have extensive experience with lithium brine analyses and are 
certified under ISO 17025, and in Alex Stewart's case, specifically for 
determination of lithium and potassium in liquid brines by use of ICP-OES.

This news release has been reviewed by Iain Scarr, AIPG CPG., Chief Operating 
Officer of the Company and a qualified person as that term is defined in 
National Instrument 43-101.

To find out more about Millennial Lithium Corp. please contact Investor 
Relations at (604) 662-8184 or email info@millenniallithium.com.

MILLENNIAL LITHIUM CORP.

Farhad Abasov, CEO, Director

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

This news release may contain certain "Forward-Looking Statements" within the 
meaning of the United States Private Securities Litigation Reform Act of 1995 
and applicable Canadian securities laws. When used in this news release, the 
words "anticipate", "believe", "estimate", "expect", "target, "plan", 
"forecast", "may", "schedule" and similar words or expressions identify 
forward-looking statements or information. These forward-looking statements or 
information may relate to future prices of commodities, accuracy of mineral or 
resource exploration activity, reserves or resources, regulatory or government 
requirements or approvals, the reliability of third party information, 
continued access to mineral properties or infrastructure, currency risks 
including the exchange rate of USD$ for Cdn$, fluctuations in the market for 
lithium, changes in exploration costs and government royalties or taxes in 
Argentina and other factors or information. Such statements represent the 
Company's current views with respect to future events and are necessarily based 
upon a number of assumptions and estimates that, while considered reasonable by 
the Company, are inherently subject to significant business, economic, 
competitive, political and social risks, contingencies and uncertainties. Many 
factors, both known and unknown, could cause results, performance or 
achievements to be materially different from the results, performance or 
achievements that are or may be expressed or implied by such forward-looking 
statements. The Company does not intend, and does not assume any obligation, to 
update these forward-looking statements or information to reflect changes in 
assumptions or changes in circumstances or any other events affections such 
statements and information other than as required by applicable laws, rules and 
regulations.

- 30 -

CONTACT INFO:

Millennial Lithium Corp.
Investor Relations
(604) 662-8184
info@millenniallithium.com
www.millenniallithium.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=596210011