Source	CANADA NEWSWIRE
Date	07/12/2017
Time	06:03:12 AM

Company	 Engold Mines Ltd.
Title	EnGold Provides Lac La Hache Exploration Update





    CDNX Symbol: EGM











Press Release




" BC-EnGoldLacHacheUpdate   07-12 0826
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^EnGold Provides Lac La Hache Exploration Update@

VANCOUVER, July 12, 2017 /CNW/ - David H. Brett, President & CEO, EnGold
Mines Ltd., (TSX-V: EGM, "EnGold" or the "Company") reports that 21 drill
holes comprising 9,117.5 metres have now been completed around discovery drill
hole G16-01. 90% of the holes drilled to date have encountered skarn-style
mineralization across widths ranging from 2 to 43 m in true thickness.
Although there may be a north-east/south-west trend emerging, the geometry of
the mineralization has yet to be determined, and less than 50% of the
mag/gravity geophysical anomaly has been drilled to date. With data from the
newly completed airborne survey now being processed, modeled and interpreted,
together with the significant additional ground gravity data collected over
several weeks, EnGold's technical team will spend approximately two weeks
developing the next series of drill targets, both at the discovery area, and
at anomalies along the 5.5km anomalous trend. Two additional holes were
drilled targeting on trend gravity anomalies, bringing the total metres
drilled on gravity/mag targets to 10,182.8 m.
"Our initial drilling regime in the discovery area has validated our
geological model and encountered very impressive true-widths of the
higher-grade mineralization," said VP Exploration Rob Shives, P.Geo. "Results
clearly show that the thickness of the stratabound mineralization within the
much larger ground gravity/magnetic anomaly can vary significantly within 50 m
step-outs. Analysis of our new geophysical data will be critical to
determining optimal drill targeting in the next phase."
Results from the first 17 holes drilled have been previously reported,
including Hole G17-16 which intersected 43.45 metres (m) grading 1.31% Cu,
0.20 gpt Au, 4.06 gpt Ag & 31.14% Fe, including 24 m grading 1.67% Cu, 0.29
gpt Au, 5.09 gpt Ag & 34.55% Fe. Hole G17-16 is collared 142 metres (m)
northeast of discovery hole G16-01, which intersected 26.57 m grading 1.76%
Cu, 0.27 gpt Au, 10.29 gpt Ag, & 35.8% Fe. Holes drilled as step-outs from
G17-16 intersected discontinuous, narrow mineralized intervals. Hole G17-23,
intersected the subhorizontal main mineralized zone approximately 71 m
southwest of G17-04, appearing as several semi-massive magnetite-chalcopyrite
intervals totalling 14.35 m over a wider, 19 m interval. Assays are pending
for holes G17-18 through -23. As soon as ongoing access and power difficulties
related to forest fires in the region are resolved, the cores from hole G17-23
will be split and samples delivered to the lab on an expedited basis for rush
assay. An updated plan map of the drill hole collars has been added to the
Company's website www.engold.ca
"Particularly in light of recent fire activity in the area, the timing is
good to pause drilling to fully leverage the significant new geophysical data
we have in hand," said EnGold President & CEO David Brett. "EnGold is fully
funded for its next phase of drilling, following up on the very compelling
intercepts we have encountered to date and branching out to test the numerous
anomalies on trend."
Quality Control/Quality Assurance Program
EnGold Mines Ltd follows procedures which ensure sample security, chain
of custody and Quality Assurance/Quality Control for all drilling and
geochemical sampling, conforming to industry practices defined by Canadian
Institute for Mining, Metallurgy (CIMM) standards, and required for TSX-listed
companies by National Instrument 43-101.
All core was logged and photographed. Sampled intervals were sawed in
half, bagged, sealed and sent securely to ALS Canada Ltd for analyses.
Half-gram samples were digested with aqua regia acid then analysed by
inductively coupled plasma-atomic emission spectrometry (ICP-AES) for 35
elements (ME-ICP41). A 30 gram split is analyzed for gold by fire assay with a
gravimetric finish (ME-GRA21). Copper values exceeding 1 percent were analyzed
using aqua regia digestion with an ICP-AES finish (ME-OG46) to improve
accuracy and precision at higher grades. As part of our comprehensive QA/QC
program, one standard, one blank and one in-line replicate were inserted into
the sample stream in each group of approximately 20 samples in each analytical
batch.
About EnGold
EnGold is focused on exploring its 100% owned mineral property located
near the town of Lac La Hache in BC's prolific Cariboo mining region. EnGold's
corporate philosophy rests on three interdependent pillars: Environment,
Engagement and Gold. Through sound environmental stewardship, commitment to
transparent engagement with local communities, the Company is dedicated to
driving exceptional shareholder and stakeholder value by discovering and
developing mineral resources.
Rob Shives P.Geo., VP Exploration and a Qualified Person as defined under
National Instrument 43-101, has reviewed and approved the technical content of
this release.
Engold Mines Ltd.Per/
David Brett, MBAPresident & CEO
This news release may contain "forward?looking statements". Readers are
cautioned that any such statements are not guarantees of future performance
and that actual development or results may vary materially from those in
these"forward looking statements."Neither the TSX Venture Exchange nor its
Regulation Services Provider (as that term is defined in the policies of the
TSX Venture Exchange) accepts responsibility for the adequacy or accuracy of
this release.
SOURCE Engold Mines Ltd.



View original content with multimedia:
http://www.newswire.ca/en/releases/archive/July2017/12/c5088.html

-0-                           07/12/2017
/For further information: David Brett, 604-682-2421 or david(at)engold.ca/
(EGMCF EGM.)

CO:  Engold Mines Ltd.
ST:  British Columbia
IN:  MIN MNG
SU:

-30-