Source	MARKET NEWS
Date	07/12/2017
Time	06:15:47 AM

Company	 Engold Mines Ltd.
Title	Provides Lac 
La Hache Exploration Update





    CDNX Symbol: EGM











Press Release





ENGOLD MINES LTD ("EGM-V;GWRRF-0")
- Provides Lac La Hache Exploration Update

David H. Brett, President & CEO, EnGold Mines Ltd., ("EnGold" or
the "Company") reports that 21 drill holes comprising 9,117.5 metres
have now been completed around discovery drill hole G16-01. 90% of the
holes drilled to date have encountered skarn-style mineralization
across widths ranging from 2 to 43 m in true thickness. Although there
may be a north-east/south-west trend emerging, the geometry of the
mineralization has yet to be determined, and less than 50% of the
mag/gravity geophysical anomaly has been drilled to date. With data
from the newly completed airborne survey now being processed, modeled
and interpreted, together with the significant additional ground
gravity data collected over several weeks, EnGold's technical team will
spend approximately two weeks developing the next series of drill
targets, both at the discovery area, and at anomalies along the 5.5km
anomalous trend.  Two additional holes were drilled targeting on trend
gravity anomalies, bringing the total metres drilled on gravity/mag
targets to 10,182.8 m.

"Our initial drilling regime in the discovery area has validated
our geological model and encountered very impressive true-widths of the
higher-grade mineralization," said VP Exploration Rob Shives, P.Geo.
"Results clearly show that the thickness of the stratabound
mineralization within the much larger ground gravity/magnetic anomaly
can vary significantly within 50 m step-outs. Analysis of our new
geophysical data will be critical to determining optimal drill
targeting in the next phase."

Results from the first 17 holes drilled have been previously
reported, including Hole G17-16 which intersected 43.45 metres (m)
grading 1.31% Cu, 0.20 gpt Au, 4.06 gpt Ag & 31.14% Fe, including 24 m
grading 1.67% Cu, 0.29 gpt Au, 5.09 gpt Ag & 34.55% Fe.  Hole G17-16 is
collared 142 metres (m) northeast of discovery hole G16-01, which
intersected 26.57 m grading 1.76% Cu, 0.27 gpt Au, 10.29 gpt Ag, &
35.8% Fe. Holes drilled as step-outs from G17-16 intersected
discontinuous, narrow mineralized intervals. Hole G17-23, intersected
the subhorizontal main mineralized zone approximately 71 m southwest of
G17-04, appearing as several semi-massive magnetite-chalcopyrite
intervals totalling 14.35 m over a wider, 19 m interval. Assays are
pending for holes G17-18 through -23.  As soon as ongoing access and
power difficulties related to forest fires in the region are resolved,
the cores from hole G17-23 will be split and samples delivered to the
lab on an expedited basis for rush assay. An updated plan map of the
drill hole collars has been added to the Company's website
www.engold.ca

"Particularly in light of recent fire activity in the area, the
timing is good to pause drilling to fully leverage the significant new
geophysical data we have in hand," said EnGold President & CEO David
Brett. "EnGold is fully funded for its next phase of drilling,
following up on the very compelling intercepts we have encountered to
date and branching out to test the numerous anomalies on trend."

Quality Control/Quality Assurance Program

EnGold Mines Ltd follows procedures which ensure sample security,
chain of custody and Quality Assurance/Quality Control for all drilling
and geochemical sampling, conforming to industry practices defined by
Canadian Institute for Mining, Metallurgy (CIMM) standards, and
required for TSX-listed companies by National Instrument 43-101.

All core was logged and photographed. Sampled intervals were sawed
in half, bagged, sealed and sent securely to ALS Canada Ltd for
analyses. Half-gram samples were digested with aqua regia acid then
analysed by inductively coupled plasma-atomic emission spectrometry
(ICP-AES) for 35 elements (ME-ICP41). A 30 gram split is analyzed for
gold by fire assay with a gravimetric finish (ME-GRA21). Copper values
exceeding 1 percent were analyzed using aqua regia digestion with an
ICP-AES finish (ME-OG46) to improve accuracy and precision at higher
grades. As part of our comprehensive QA/QC program, one standard, one
blank and one in-line replicate were inserted into the sample stream in
each group of approximately 20 samples in each analytical batch.
About EnGold

EnGold is focused on exploring its 100% owned mineral property
located near the town of Lac La Hache in BC's prolific Cariboo mining
region. EnGold's corporate philosophy rests on three interdependent
pillars: Environment, Engagement and Gold. Through sound environmental
stewardship, commitment to transparent engagement with local
communities, the Company is dedicated to driving exceptional
shareholder and stakeholder value by discovering and developing mineral
resources.

Rob Shives P.Geo., VP Exploration and a Qualified Person as
defined under National Instrument 43-101, has reviewed and approved the
technical content of this release.

Engold Mines Ltd.Per/

David Brett, MBAPresident & CEO

This news release may contain "forward-looking statements".
Readers are cautioned that any such statements are not guarantees of
future performance and that actual development or results may vary
materially from those in these"forward looking statements."Neither the
TSX Venture Exchange nor its Regulation Services Provider (as that term
is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.

For further information:  David Brett, 604-682-2421 or
david@engold.ca
______________________________
_______________________________________________
TSX Venture closing price for EGM-V
Date: 2017/07/11
Closing Price: 0.31
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1719200018TS11719200991-06141120170712