Source	MARKET NEWS
Date	07/12/2017
Time	06:15:47 AM

Company	 Ultra Lithium Inc.
Title	Drills 1.42% 
Lithium Oxide At Georgia Lake In No





    CDNX Symbol: ULI











Press Release





ULTRA LITHIUM INC ("ULI-V")
- Drills 1.42% Lithium Oxide At Georgia Lake In Northern Ontario,
- Canada

Ultra Lithium Inc. ("Ultra Lithium" or "the Company") is pleased
to announce assay results from 2017 exploration work program at its
100% owned Georgia Lake Lithium Project located in the Thunder Bay
Mining District, Northwestern Ontario, Canada. The results of four
short drill holes at various spodumene pegmatites on the property
indicate values up to 1.42% lithium oxide (Li(sub)2(/sub)O) over 5
metres.

Highlights of the drill hole assay results are (see tables 1 and 2
for details):
*  Drill Hole ULI-17-01 intersects 1.11% Li(sub)2(/sub)O over 4 m
from one metre below surface at Niemi Pegmatite
*  Drill Hole ULI-17-02 intersects 1.08% Li(sub)2(/sub)O over 5 m
from one metre below surface at Newkirk Pegmatite
*  Drill Hole ULI-17-03 intersects 0.76% Li(sub)2(/sub)O over 1 m
from 5 metres below surface at MNW Pegmatite
*  Drill Hole ULI-17-04 intersects 1.42% Li(sub)2(/sub)O over 5
metres from one metres below surface at Lucky Lake Pegmatite

(Note: All widths reported are drill core widths and have not
been converted into true width.)

The drill program was contracted to Pleson Geoscience and was
completed during April-May 2017. A Shaw diamond core drill with
internal diameter of 41 mm was used to drill the four exploration holes
down to a depth of six metres below surface. Core samples were between
30 cm and 1.5 m. The samples were assayed by Actlabs lab in Ancaster,
Ontario. Actlabs is an independent lab accredited by ISO 17025.  The
samples were digested using sodium peroxide fusion and analyzed for the
lithium by ICP (Method: FUS-MS-Na(sub)2(/sub)O(sub)2(/sub)). Actlabs
has its own quality control and quality assurance program in place.

Dr. Weiguo Lang, CEO of Ultra Lithium, stated that, "We are highly
satisfied with the results achieved for the Georgia Lake project and
will continue with deeper drilling during our 2017-18 exploration work
program. Now, with the acquisition of La Borita brine lithium project
in Argentina, the Company has a balanced lithium portfolio comprising
both hard rock and brine types of exploration deposit models."

The technical information contained in this news release has been
reviewed and approved by Afzaal Pirzada, P.Geo., a qualified person, as
defined by NI 43-101 who works as VP Exploration with the Company.

ON BEHALF OF THE BOARD OF DIRECTORS
"Kiki Smith"
Kiki Smith, CFO

About Ultra Lithium Inc.

Ultra Lithium is an exploration and development company with a
focus on the acquisition and development of lithium assets. The Company
is currently focused on acquiring promising lithium assets in Argentina
located in the famous lithium triangle while exploring its Georgia Lake
and South Big Smoky Valley Projects.

About the Georgia Lake Lithium Project:

The Company holds a 100% interest in the Georgia Lake lithium
property comprising 16 mineral claims covering approximately 2416 in
151 units, located in the Thunder Bay Mining Division, Ontario, Canada.
The project represents a stable and favourable mining jurisdiction,
supportive First Nations and excellent infrastructure. It is located
near provincial highway 11, 145 km from deep water port in Thunder Bay.
The spodumene-bearing pegmatites of this area were first discovered in
1955. Majority of pegmatites are Lithium-cesium-tantalum (LCT) type
where spodumene is the main lithium mineral.

A total of eight historically documented lithium pegmatites are
located on the property.

//st

Table 1. Drill hole assay results

Drill Hole      Sample ID   Depth       Depth To    Length      Lithium
From (m)    (m)         of          Oxide %
sample
(m)

294101      0           1           1.00        0.27

294102      1           2           1.00        1.55

ULI-17-01   294103      2           3           1.00        1.79

294104      3           4           1.00        0.46

294105      4           5           1.00        0.67

294106      5           6           1.00        0.4

Average                                         0.86

294107      1           2           1.00        0.22

294108      2           3           1.00        1.72

ULI-17-02   294109      3           4           1.00        0.35

294110      4           5           1.00        1.6

294111      5           6           1.00        1.5

Average                                         1.078

294112      2           3           1.00        0.25

ULI-17-03   294113      3           4           1.00        0.05

294114      4           5           1.00        0.04

294115      5           6           1.00        0.76

Average                                         0.275

294116      1           2           1.00        1.42

294117      2           3           1.00        1.04

ULI-17-04   294118      3           4           1.00        1.22

294119      4           5           1.00        1.7

294120      5           6           1.00        1.7

Average                                         1.416

//et

//st

Table 2: Drill Hole Collar Information

Hole ID          Easting   Northing   Azimuth   Dip   length     # of
of hole    Samples
(m)

ULI-17-01        434438    5461357    n/a       90    8          6

ULI-17-02        431260    5464049    n/a       90    6          5

ULI-17-03        426636    5453604    n/a       90    6          4

ULI-17-04        406622    5464207    n/a       90    6          5

Summary:                                              26         20

//et

For further information, please contact the Company at:

Kiki Smith, CFO
Telephone: 778 968-1176
Facsimile: 604 909-4682
Email: kiki@ultralithium.com
Website: www.ultralithium.com
















































TSX Venture closing price for ULI-V
Date: 2017/07/10
Closing Price: 0.16

TEL:  778-968-1176  ULTRA LITHIUM INC
FAX:  604-909-4682
EMAIL:  kiki@ultralithium.com
INTERNET:  www.ultralithium.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1719200020TS11719201004-06145620170712