Source	Marketwire
Date	07/25/2017
Time	05:30:44 AM

Company	 RIVERSIDE RESOURCES INC.
Title	Riverside Resources Samples Up to 5.45 G/T Gold and Establishes 5 Priority 
Drill Targets at the Cecilia Gold Project in Sonora, Mexico





    CDNX Symbol: RRI











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Riverside Resources Inc.

TSX VENTURE SYMBOL: RRI
OTC PINK SYMBOL: RVSDF
FRANKFURT SYMBOL: R99

July 25, 2017

Riverside Resources Samples Up to 5.45 G/T Gold and Establishes 5 Priority 
Drill Targets at the Cecilia Gold Project in Sonora, Mexico


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 25, 2017) - Riverside 
Resources Inc. ("Riverside" or the "Company") (TSX VENTURE:RRI)(OTC 
PINK:RVSDF)(FRANKFURT:R99), is pleased to announce that the Company has 
completed the first phase of self-funded exploration at the Cecilia Gold 
Project (the "Project") located in northeastern Sonora, Mexico. Riverside is 
targeting epithermal gold-silver mineralization within and beneath a felsic 
volcanic flow-dome complex which is similar in age and composition to the dome 
complexes that are associated with the large La Pitarrilla and San Julian 
Ag(-Au)-Pb-Zn deposits found in the Mexican state of Durango.

Highlights of Riverside's second batch of sampling results included 8.0 and 9.7 
metre wide zones of gold mineralization at the North Breccia Zone that averaged 
3.90 g/t Au and 1.18 g/t Au, respectively. These intervals encompass a total of 
8 chip-channel samples 1.80 to 3.0 metres in length. About 400 metres southwest 
of the North Breccia Zone an altered fault structure was mineralized, with a 
3.0 m wide zone showing an average grade of 5.45 g/t Au. The Company's 
exploration program has successfully outlined a number of priority drill 
targets and Riverside has now started the application process for drill 
permitting.

Riverside's President and CEO, John-Mark Staude, stated: "Riverside acquired 
the Cecilia gold Project because our geologists view the volcanic complex at 
the heart of the Project as being a prime setting for a major epithermal 
mineral system, predominantly gold-bearing at higher levels and possibly more 
silver rich at lower elevations. The fieldwork we have completed so far, 
combined with the compilation and analysis of historical data, further supports 
this view. We have at least five high-potential gold targets defined at the 
Project, which are being permitted for drilling."

A key component of Riverside's exploration program was to confirm the existence 
of multiple zones of gold-bearing hydrothermal breccia and quartz stockwork 
veining that had been sampled decades ago by other groups, including Chesapeake 
Gold Corp., Cambior Explorations and the Consejo de Recursos Minerales, the 
predecessor to Mexico's geological survey, Servicio Geologico Mexicano. (for 
details, see Project History on the Company's website). Riverside accomplished 
this by collecting and analyzing a total of 406 rock samples from the Project's 
four main gold zones, the North Breccia, Central, West and East Zones (see 
Figure 1, below). Bedrock exposures in areas surrounding the four prospects 
were also sampled with the objective of expanding the known zones of gold 
mineralization. The distribution of 1,443 historical rock samples plus 371 
Riverside samples is shown in Figure 1. Clusters of samples with gold 
concentrations greater than 0.3 g/t Au clearly define the above-mentioned gold 
zones. Importantly, gold mineralization at Cecilia is seen to be widespread, 
occurring over an area that is roughly 1,200 metres by 400 metres, and it is 
also found over an elevation range of more than 400 metres.

To view Figure 1: Simplified Geology Map Showing Riverside and Historical Rock 
Samples, please visit the following link: 
http://media3.marketwire.com/docs/Riverside_Figure_1.pdf

In addition to its rock sampling program, Riverside's geologists compiled and 
reviewed geological and geochemical data sets that had been generated over a 
35-year history of modern exploration at Cecilia. This database includes 
drill-hole logs and core sample analyses for 19 diamond boreholes (3,817.6m), 
maps and hundreds of rock-channel assays for twenty underground workings that 
reportedly date back to the 1940s, as well as multi-element analyses for 1,979 
surface rock samples. A basic statistical analysis of gold assays obtained by 
Riverside and two previous companies is shown in Table 1.

Table 1. Summary of Gold Assay Results From Rock-Chip Sampling at Cecilia

/T/

----------------------------------------------------------------------------
# of% of Total
# of       # of    Samples      that
Samples    Samples   assaying   assayed
assaying   assaying    greater   greater
Total #    Type of  0.30-0.991.0-3.0 g/t   than 3.0  than 0.3
Company       Samples    Samples     g/t Au         Au     g/t Au    g/t Au
----------------------------------------------------------------------------
RIVERSIDE                  chip-
channels,
394      1-2 m         47         27         10        21%
----------------------------------------------------------------------------
CHESAPEAKE                 chip-
channels,
811      1-5 m        135         52         23      25.8%
----------------------------------------------------------------------------
CAMBIOR           674  undefined         42         12          4       8.6%
----------------------------------------------------------------------------

/T/

Specific drilling targets have now been selected at Cecilia and a work permit 
application for a drilling program is being prepared for Mexico's environmental 
agency, SEMARNAT. Such permits are typically received 2 to 3 months after 
applications are submitted. The selection of Riverside's drill targets was 
guided by gold assay data for surface and underground rock samples that were 
viewed in the context of a geological and exploration model of the Cerro 
Magallanes volcanic flow-dome complex. This model was developed by Riverside's 
geologists and is based on other flow-dome complexes in Mexico where 
economically important ore systems are found (eg. La Pitarrilla, San Julian).

Riverside's planned drill-holes have been designed to test the North Breccia, 
Central and East gold zones using borehole orientations that in most cases will 
be at least 90 degrees to the azimuth directions of the historic drill-holes, 
i.e. the planned holes will be directed to the south or southwest instead of to 
the northwest. Many of the boreholes drilled in 1995 are interpreted to have 
been oriented subparallel to the main mineralized structures, consequently 
missing their targets. Existing drill roads, with minor upgrading, will 
facilitate future drilling.

Some of Riverside's proposed drill-holes are designed to test deeper levels of 
the volcanic complex to explore for feeder structures that may control large 
epithermal quartz veins containing high-grade gold-silver mineralization. Such 
mineralization was found in boulders scattered at the entrances to a few of the 
old underground workings at the Central Zone (see press release on June 6, 
2017). Select samples of this type of quartz veining yielded gold assays of 
13.9 g/t Au 19.0 g/t Au, 55.0 g/t Au and 133.7 g/t Au, with corresponding 
silver assays of 20.7 g/t Ag, 335.0 g/t Ag, 288.0 g/t Ag and 87.8 g/t Ag.

Riverside's President and CEO, John-Mark Staude, added: "Riverside is actively 
discussing potential joint-venture partnerships with a number of parties on 
multiple projects in the Company's portfolio. We have several projects with 
high-quality drill targets and are committed to securing multiple new 
partnerships, while also completing a self-funded drill program by the end of 
the year. We believe this approach exposes our shareholders to the most 
catalysts and discovery upside."

Qualified Person & QA/QC:

The scientific and technical data contained in this news release pertaining to 
the Cecilia Project was reviewed and approved by Ron Burk, P. Eng, a 
non-independent qualified person to Riverside Resources, who is responsible for 
ensuring that the geologic information provided in this news release is 
accurate and who acts as a "qualified person" under National Instrument 43-101 
Standards of Disclosure for Mineral Projects.

The rock chip samples collected by Riverside's field crew at the Cecilia 
Project were taken from bedrock outcroppings on the slopes of the prominent 
mount of Cerro Magallanes, with the majority of individual samples consisting 
of composites of bedrock fragments hammer-chipped from 1.1 to 3.1 metre long 
intervals across rock faces showing evidence of hydrothermal alteration. A 
total of 406 rock-chip samples were collected and analyzed by Riverside, 12 of 
which consisted of select grab samples of loose quartz vein rock found on 
waste-rock dumps of small underground workings that exist at the core of the 
Project. Assay results for these select samples are not plotted on the map 
shown in Figure 1. All of Riverside's rock samples were analyzed at the 
Hermosillo and Vancouver laboratories of Bureau Veritas where gold content was 
determined by fire assaying with atomic adsorption finish and ICP-mass 
spectrometry was used to analyze for 45 other elements. For quality control 
purposes, 14 standard samples and 7 'blank' samples were included with the 
batch of 406 field samples from the Project.

About Riverside Resources Inc.:

Riverside is a well-funded prospect generator exploration company with over 
$5,000,000 in the bank and a tight share structure with fewer than 45M shares 
issued. Riverside leverages its 77,000 location Mexico mineral database, highly 
experienced and dedicated technical team and partnership network to acquire and 
develop high-potential projects. The Company increases the chances of discovery 
by advancing multiple assets simultaneously through partnerships, allowing 
Riverside to mitigate risk and conserve capital. Riverside has a diverse 
portfolio of gold, silver and copper properties throughout North America. 
Riverside has additional properties available for option with more information 
available on the Company's website at www.rivres.com.

ON BEHALF OF RIVERSIDE RESOURCES INC.

Dr. John-Mark Staude, President & CEO

Certain statements in this press release may be considered forward-looking 
information. These statements can be identified by the use of forward looking 
terminology (e.g., "expect"," estimates", "intends", "anticipates", "believes", 
"plans"). Such information involves known and unknown risks -- including the 
availability of funds, the results of financing and exploration activities, the 
interpretation of exploration results and other geological data, or 
unanticipated costs and expenses and other risks identified by Riverside in its 
public securities filings that may cause actual events to differ materially 
from current expectations. Readers are cautioned not to place undue reliance on 
these forward-looking statements, which speak only as of the date of this press 
release.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

John-Mark Staude
President & CEO
Riverside Resources Inc.
(778) 327-6671
Fax: (778) 327-6675
info@rivres.com
www.rivres.com

or

Raffi Elmajian
Corporate Communication
Riverside Resources Inc.
(778) 327-6671 / TF: (877) RIV-RES1
relmajian@rivres.com
www.rivres.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=596800374