Source	MARKET NEWS
Date	07/27/2017
Time	10:17:44 AM

Company	 Scorpio Gold Corporation
Title	2017 Phase I 
Drilling Encounters High Grade Gold





    CDNX Symbol: SGN











Press Release





SCORPIO GOLD CORP ("SGN-V")
- 2017 Phase I Drilling Encounters High-Grade Gold Proximal to
- Underground Mine Workings at the Goldwedge Project, Nevada

Scorpio Gold Corporation ("Scorpio Gold" or the "Company") is
pleased to report final results from its 2017 Phase I exploration
drilling program at the Goldwedge project, located in Manhattan,
Nevada.

The drill program was designed to target the extension of the
favorable lithologic unit in the Goldwedge Mine, specifically the
Zanzibar limestone bound within the Reliance Fault Zone. This zone
plunges northward into the Manhattan caldera margin. Seven RC holes
totaling 7,530 ft (2,295 m) were drilled from 5 pad locations.

Significant mineralization was encountered in 3 of the holes
(GW17024, GW17026 and GW17029) that intercepted the targeted Zanzibar
limestone within the Reliance Fault Zone. GW17029 targeted an area near
elevated underground rib samples west of the Reliance Fault Zone, and
intersected significant mineralization within 65 feet of the
mineralized rib and above the lowest working underground level.

//st
Table 1. 2017 Goldwedge Surface RC Drilling
- Significant Results ()0.1 oz/t)

Hole    Azm  Dip  From To  Width From   To     Width Gold   Gold
No.    (deg)(deg)(ft) (ft)(ft)  (m)    (m)    (m)   (oz/t) (g/t)

GW17024 192 90    725  730  5    221.00 222.50 1.52  0.274  9.39
GW17026 225 55    460  470 10    140.21 143.26 3.05  0.324 11.11
GW17029 040 55    265  280 15     80.77  85.34 4.57  0.325 11.14
620  625  5    188.98 190.50 1.52  0.157  5.38
//et

Three of the 7 holes (GW17027, GW17028, and GW17030) deviated and
stayed in the Tertiary volcanic rock and did not drill the intended
target. A fourth hole (GW17025) was drilled to intercept the Zanzibar
limestone outside of the Reliance Fault Zone. No significant
mineralization was encountered in these four holes.

Map Links:
Drill Hole Plan
Drill Hole Cross Section

All holes presented in Table 1 were completed by reverse
circulation ("RC") drilling. Widths are presented as down hole lengths;
true widths are unknown at this time. Analytical results were performed
by ALS Minerals in Reno, Nevada, an ISO/IEC 17025:2005 accredited
facility.  Further details are presented in the Company's quality
assurance and quality control program for the Goldwedge project
available at: GW QAQC.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge
gold mining operation located in Esmeralda County, Nevada with joint
venture partner Elevon, LLC (30%). Mineral Ridge is a conventional open
pit mining and heap leach operation. The Mineral Ridge property is host
to multiple gold-bearing structures, veins and lenses at exploration,
development and production stages. Scorpio Gold also holds a 100%
interest in the advanced exploration-stage Goldwedge property in
Manhattan, Nevada, with a fully permitted underground mine and 400 ton
per day mill facility. The Goldwedge mill facility has been placed on a
care and maintenance basis and can be restarted immediately when
needed.

Scorpio Gold's Chairman, Peter J. Hawley, PGeo, is a Qualified
Person as defined by National Instrument 43-101 and has reviewed and
approved the content of this release.

ON BEHALF OF THE BOARD
SCORPIO GOLD CORPORATION

Brian Lock,
Interim CEO

Website: www.scorpiogold.com

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

The Company relies on litigation protection for forward-looking
statements. This news release contains forward-looking statements that
are based on the Company's current expectations and estimates.
Forward-looking statements are frequently characterized by words such
as "plan", "expect", "project", "intend", "believe", "anticipate",
"estimate", "suggest", "indicate" and other similar words or statements
that certain events or conditions "may" or "will" occur, and include,
without limitation, statements regarding the Company's plans with
respect to the exploration, development and exploitation of its
Goldwedge project. Such forward-looking statements involve known and
unknown risks, uncertainties and other factors that could cause actual
events or results to differ materially from estimated or anticipated
events or results implied or expressed in such forward-looking
statements, including risks involved in mineral exploration and
development programs and those risk factors outlined in the Company's
Management Discussion and Analysis as filed on SEDAR. Any
forward-looking statement speaks only as of the date on which it is
made and, except as may be required by applicable securities laws, the
Company disclaims any intent or obligation to update any
forward-looking statement, whether as a result of new information,
future events or results or otherwise. Forward-looking statements are
not guarantees of future performance and accordingly undue reliance
should not be put on such statements due to the inherent uncertainty
thereof.

For further information contact:
Chris Zerga, President
Tel: (819) 825-7618
Email: czerga@scorpiogold.com

Investor Relations:
Jag Sandhu, JNS Capital Corp.
Tel: (778) 218-9638
Email: jagjns@outlook.com
______________________________________
_______________________________________________
TSX Venture closing price for SGN-V
Date: 2017/07/25
Closing Price: 0.06
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1720700047TS11720702004-10152120170727