Source	CANADA NEWSWIRE
Date	07/17/2017
Time	04:03:16 AM

Company	 Tinka Resources Limited
Title	Tinka announces new step out holes extend zinc at South Ayawilca by 200
metres and high-grade silver highlights new style of zinc mineralization





    CDNX Symbol: TK











Press Release




" BC-TinkaResourceAyawilca   07-17 2423
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Tinka announces new step out holes extend zinc at South Ayawilca by 200
metres and high-grade silver highlights new style of zinc mineralization@

22.8 METRES GRADING 8.4% ZINC IN HOLE A17-071, MINERALIZATION REMAINS
OPEN11.5 METRES GRADING 780 GRAMS PER TONNE SILVER + 5.2 % ZINC+LEAD IN HOLE
A17-072
VANCOUVER, July 17, 2017 /CNW/ - Tinka Resources Limited ("Tinka" or the
"Company") (TSXV: TK) (OTCPK: TKRFF) is pleased to announce assay results of
five new step-out drill holes at its 100%-owned Ayawilca zinc project in
central Peru. Three holes were drilled at the South Ayawilca discovery area,
with one hole drilled at West Ayawilca (A17-074). Hole A17-073 was drilled at
Zone 3, the first hole into this new target.
Holes A17-071 and A17-075 both intersected significant thicknesses of
high grade zinc and have extended the footprint of the South Ayawilca
discovery by 200 metres to the southeast, where zinc remains open and
untested. Hole A17-072 at South Ayawilca intersected high grade silver with
moderate grade zinc-lead mineralization adjacent to an important
northeast-trending fault, which is a new style of mineralization observed at
Ayawilca, This new high-grade silver discovery opens up additional exploration
opportunities. Three rigs continue to turn at the project on multiple fronts.
Key HighlightsHole A17-071 (South Ayawilca):
<<

--  22.8 metres at 8.4 % zinc, 0.8 % lead, & 35 g/t silver from 327.2 metres
depth, including
o 12.6 metres at 11.6 % zinc, 0.9 % lead, & 35 g/t silver from 332.4 metres
depth;
>>
Hole A17-072 (South Ayawilca):
<<

--  11.5 metres at 2.9 % zinc, 2.3 % lead & 781 g/t silver from 294.5 metres
depth, including
o 2.0 metres at 5.6 % zinc, 5.5 % lead & 3167 g/t silver from 302.0 metres
depth;
>>
Hole A17-075 (South Ayawilca):
<<

--  20.8 metres(x) at 5.0 % zinc, 11 g/t silver & 44 g/t indium from 359.0
metres depth, including
--  3.5 metres at 10.2 % zinc, 17 g/t silver & 96 g/t indium from 376.3
metres depth;
>>
(x) includes 1.7 metres of no
recovery assumed zero grade
Hole A17-074 (West Ayawilca):
<<

--  2.2 metres at 31.0 % zinc, 0.1 % lead & 138 g/t silver from 71.4 metres
depth (vein), and
o 0.7 metres at 18.3 % zinc & 38 g/t silver from 148.0 metres depth (vein);
>>
Hole A17-073 (Zone 3):
The first hole at Zone 3, drilled 700 metres east of the existing East
Ayawilca Inferred Resource, was completed to a depth of 710 metres.
Replacement sulphide mineralization was encountered, mostly pyrite with minor
sphalerite, over a 15-metre interval near the base of the carbonate sequence
which hosts mineralization elsewhere. At Ayawilca, pyrite occurs on the
margins of the zinc mineralization, so we interpret this as an indication that
significant zinc mineralization may be close by. A follow-up hole (A17-081) is
in progress, with one more hole planned for Zone 3 in this program.
See drill hole and zinc grade-thickness maps (Figure 1 and Figure 2), and
a South Ayawilca cross section (Figure 3).
Dr. Graham Carman, Tinka´s President and CEO, stated: "We are very
pleased with these new drill results. The zinc discovery at South Ayawilca
continues to expand southward, and remains open in several directions (see
Figure 2). Hole A17-075 indicates that zinc may be thickening to the south on
that section. The high-grade silver (zinc-lead) discovery in A17-072 is also
exciting as it opens potential for additional bonanza-grade mineralization
along the South Ayawilca Fault, which is largely untested. High-grade silver
(zinc-lead) mineralization occurs with sulphides as cavity fillings in
recrystallized limestone with abundant quartz-carbonate alteration, quite
different to the massive sulphide mineralization associated with the
high-grade zinc."
Dr. Carman continued: "We are continuing to test zinc targets at the
project and expand the drilling effort. Step-out holes are taking place at
West and South Ayawilca, with new targets being drilled at Zone 3 and Chaucha.
The drilling at Zone 3 is progressing well. Indications are that a significant
zinc sulphide system could be nearby. Zone 3 is a large target area covering
more than 1 km2, and several holes will be needed to evaluate the full
potential of that area."
True thicknesses of the zinc intersections are estimated to be at least
85% of the downhole thickness, except where otherwise noted in footnotes to
Table 1. All significant results of the 2017 program are summarized in Table 1
with the strongest intercepts in bold text. Table 2 is a summary of all drill
collar information to date.
Table 1. Summary of 2017 Drill Results from Ayawilca

Drill hole              From m               To m     Interval m         Zn 
%    Pb %  Ag g/t   Indium g/t    Reported
(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)              (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)               (equal 
sign)(equal sign)(equal sign)(equal sign)     (equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)          (equal sign)(equal sign)(equal sign)      (equal 
sign)(equal sign)(equal sign)   (equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)   (equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)    (equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)

A17-056(1)                                  90.30         90.65          
0.35      29.0       0.4            82           443    April 3 '17

and                                        113.00        113.40          
0.40      31.2       0.0            85           759    April 3 '17

and                                        126.00        189.90         
63.90       5.6       0.1            17            29    March 6 '17

including                      127.50        145.40         17.90      
11.6       0.2            36            20    March 6 '17

including                      127.50        133.30          5.80      
22.5       0.3            77            50    March 6 '17

and                                        199.20        204.70          
5.50       5.8       0.1             6            38    April 3 '17

and                                        228.50        233.70          
5.20      12.9       0.0            11           162    March 6 '17

and                                        242.00        293.90         
51.90      10.1       0.1           624           233    April 3 '17

including                      279.00        293.90         14.90      
20.6       0.2          1524           441    April 3 '17

including                      279.00        285.40          6.40      
37.5       0.4           301           916    April 3 '17
---------                      ------        ------          ----      
----       ---           ---           ---    -----------

A17-056A                                   286.50        296.00          
9.50       9.3       0.3            19            88     May 3'17

and                                        309.00        313.10          
4.10      18.6       0.1            27           224     May 3'17

including                      310.50        313.10          2.60      
27.3       0.1            38           336     May 3'17
---------                      ------        ------          ----      
----       ---           ---           ---     --------

A17-057                                     84.90         86.35          
1.45      24.8       0.0            62           157    April 3 '17

and                                        143.70        144.50          
0.80      40.4       0.1           138           261    April 3 '17

and                                        157.60        197.70         
40.10       9.1       0.2            22           168    April 3 '17

including                      168.20        177.80          9.60      
16.8       0.1            22           299    April 3 '17

and                                        227.15        234.90          
7.75       3.5       0.2            21            85    April 3 '17

and                                        264.00        279.30         
15.30      20.0       2.5           102           263    April 3 '17

including                      265.75        269.00          3.25      
34.5       2.1            96           196    April 3 '17

including                      272.50        277.70          5.20      
32.5       1.3            69           639    April 3 '17
---------                      ------        ------          ----      
----       ---           ---           ---    -----------

A17-058                                    103.50        107.70         
4.205      20.2       4.2          3294            15     May 3'17

and                                        133.25        134.35         
1.105      30.3       3.2           500            61     May 3'17

A17-058 did not reach target, lost at 301 metres in sandstone
-------------------------------------------------------------

A17-059                                     50.30         51.10          
0.80      37.5       0.5            69            70     June 8'17

58.00         60.00          2.00       6.3       0.0            12            
30     June 8'17
-----         -----          ----       ---       ---           ---           
---     ---------

A17-060                                    262.40        264.40          
2.00      14.8       0.0            35          1178     May 3'17

and                                        275.00        279.50          
4.50      15.0       0.0            20           383     May 3'17

and                                        298.00        328.50       
30.5(2)       3.4       0.2            10            38     May 3'17

including                      303.40        312.00          8.60       
5.1       0.1            11             6     May 3'17
---------                      ------        ------          ----       
---       ---           ---           ---     --------

A17-061                                    122.70        150.50         
27.80       4.4       0.1            18            24     May 3'17

including                      145.70        147.50         1.805      
27.2       0.0            32           157     May 3'17

and                                        184.00        202.60      
18.60(3)      10.4       0.5            52            59     May 3'17

including                      196.20        198.80          2.60      
23.6       2.4           192            19     May 3'17

including                      201.90        202.60          0.70      
28.7       3.6           202            41     May 3'17

and                                        220.00        233.40         
13.40      18.7       0.9            57           463     May 3'17

including                      224.10        230.00          7.90      
29.3       0.8            71           719     May 3'17

and                                        265.00        266.80          
1.80      37.0       0.2            85           808     May 3'17
---                                        ------        ------          
----      ----       ---           ---           ---     --------

A17-062                                    152.40        153.05         
0.655      33.6       0.3           166            42    June 28'17

A17-062 was lost prior to target depth in a fault zone at 313 metres
--------------------------------------------------------------------

A17-063                                    302.20        349.90         
47.70      11.3       0.0            18           313     June 8'17

including                      303.30        313.10          9.80      
17.4       0.0            28           587     June 8'17

including                      327.40        339.60         12.20      
17.1       0.0            26           495     June 8'17
---------                      ------        ------         -----      
----       ---           ---           ---     ---------

A17-064                                    269.90        270.40          
0.50      15.6       0.0            11           304     June 8'17

and                                        277.20        277.60          
0.40      14.5       0.0            17            39     June 8'17
---                                        ------        ------          
----      ----       ---           ---           ---     ---------

A17-065                                    119.00        119.75          
0.75      36.6       0.1            88           157     June 8'17

and                                        204.00        210.00          
6.00       4.0       0.0             4             9     June 8'17

and                                        219.50        238.80         
19.30       4.7       0.0             7            93     June 8'17

including                      236.20        238.80          2.60      
20.6       0.0            23           529     June 8'17

and                                        266.40        293.00         
26.60       3.6       0.0             4            46     June 8'17

and                                        307.30        332.00         
24.70       3.8       0.0             5            51     June 8'17

and                                        340.00        346.00          
6.00       2.6       0.1             7            16     June 8'17
---                                        ------        ------          
----       ---       ---           ---           ---     ---------

A17-066                                    185.20        185.50          
0.30      37.8       0.0            40          1330     June 8'17

and                                        330.90        334.40          
3.50       7.4       0.1            24           111     June 8'17
and                                        345.00        350.00          
5.00      11.3       0.1            37           270     June 8'17
---                                        ------        ------          
----      ----       ---           ---           ---     ---------

A17-067                                    256.40        265.00          
8.60       2.7       0.2            39             0    June 28'17
-------                                    ------        ------          
----       ---       ---           ---           ---    ----------

A17-068                                    343.55        344.30          
0.75       6.1      11.6           210             7    June 28'17

and                                        382.00        388.00          
6.00       4.0       0.1            46            47    June 28'17
---                                        ------        ------          
----       ---       ---           ---           ---    ----------

A17-069                                    182.00        190.00          
8.00       3.0       0.5            13            17    June 28'17

and                                        261.60        262.30          
0.70      17.8       0.0            14            73    June 28'17

and                                        271.40        300.70         
29.30      10.4       0.1            17           278    June 28'17

including                      287.30        299.40         
mited



View original content with multimedia:
http://www.newswire.ca/en/releases/archive/July2017/17/c5607.html

-0-                           07/17/2017
/For further information: Investor Information: www.tinkaresources.com,
Rob Bruggeman 1.416.884.3556, rbruggeman(at)tinkaresources.com; Company Contact:
Mariana Bermudez,  1.604.699.0202, info(at)tinkaresources.com/
/Web Site: www.tinkaresources.com /
(TKRFF TK.)

CO:  Tinka Resources Limited
ST:  British Columbia
IN:  MNG


" BC-TinkaResourceAyawilca   07-17 2423
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Tinka announces new step out holes extend zinc at South Ayawilca by 200
metres and high-grade silver highlights new style of zinc mineralization@

22.8 METRES GRADING 8.4% ZINC IN HOLE A17-071, MINERALIZATION REMAINS
OPEN11.5 METRES GRADING 780 GRAMS PER TONNE SILVER + 5.2 % ZINC+LEAD IN HOLE
A17-072
VANCOUVER, July 17, 2017 /CNW/ - Tinka Resources Limited ("Tinka" or the
"Company") (TSXV: TK) (OTCPK: TKRFF) is pleased to announce assay results of
five new step-out drill holes at its 100%-owned Ayawilca zinc project in
central Peru. Three holes were drilled at the South Ayawilca discovery area,
with one hole drilled at West Ayawilca (A17-074). Hole A17-073 was drilled at
Zone 3, the first hole into this new target.
Holes A17-071 and A17-075 both intersected significant thicknesses of
high grade zinc and have extended the footprint of the South Ayawilca
discovery by 200 metres to the southeast, where zinc remains open and
untested. Hole A17-072 at South Ayawilca intersected high grade silver with
moderate grade zinc-lead mineralization adjacent to an important
northeast-trending fault, which is a new style of mineralization observed at
Ayawilca, This new high-grade silver discovery opens up additional exploration
opportunities. Three rigs continue to turn at the project on multiple fronts.
Key HighlightsHole A17-071 (South Ayawilca):
<<

--  22.8 metres at 8.4 % zinc, 0.8 % lead, & 35 g/t silver from 327.2 metres
depth, including
o 12.6 metres at 11.6 % zinc, 0.9 % lead, & 35 g/t silver from 332.4 metres
depth;
>>
Hole A17-072 (South Ayawilca):
<<

--  11.5 metres at 2.9 % zinc, 2.3 % lead & 781 g/t silver from 294.5 metres
depth, including
o 2.0 metres at 5.6 % zinc, 5.5 % lead & 3167 g/t silver from 302.0 metres
depth;
>>
Hole A17-075 (South Ayawilca):
<<

--  20.8 metres(x) at 5.0 % zinc, 11 g/t silver & 44 g/t indium from 359.0
metres depth, including
--  3.5 metres at 10.2 % zinc, 17 g/t silver & 96 g/t indium from 376.3
metres depth;
>>
(x) includes 1.7 metres of no
recovery assumed zero grade
Hole A17-074 (West Ayawilca):
<<

--  2.2 metres at 31.0 % zinc, 0.1 % lead & 138 g/t silver from 71.4 metres
depth (vein), and
o 0.7 metres at 18.3 % zinc & 38 g/t silver from 148.0 metres depth (vein);
>>
Hole A17-073 (Zone 3):
The first hole at Zone 3, drilled 700 metres east of the existing East
Ayawilca Inferred Resource, was completed to a depth of 710 metres.
Replacement sulphide mineralization was encountered, mostly pyrite with minor
sphalerite, over a 15-metre interval near the base of the carbonate sequence
which hosts mineralization elsewhere. At Ayawilca, pyrite occurs on the
margins of the zinc mineralization, so we interpret this as an indication that
significant zinc mineralization may be close by. A follow-up hole (A17-081) is
in progress, with one more hole planned for Zone 3 in this program.
See drill hole and zinc grade-thickness maps (Figure 1 and Figure 2), and
a South Ayawilca cross section (Figure 3).
Dr. Graham Carman, Tinka´s President and CEO, stated: "We are very
pleased with these new drill results. The zinc discovery at South Ayawilca
continues to expand southward, and remains open in several directions (see
Figure 2). Hole A17-075 indicates that zinc may be thickening to the south on
that section. The high-grade silver (zinc-lead) discovery in A17-072 is also
exciting as it opens potential for additional bonanza-grade mineralization
along the South Ayawilca Fault, which is largely untested. High-grade silver
(zinc-lead) mineralization occurs with sulphides as cavity fillings in
recrystallized limestone with abundant quartz-carbonate alteration, quite
different to the massive sulphide mineralization associated with the
high-grade zinc."
Dr. Carman continued: "We are continuing to test zinc targets at the
project and expand the drilling effort. Step-out holes are taking place at
West and South Ayawilca, with new targets being drilled at Zone 3 and Chaucha.
The drilling at Zone 3 is progressing well. Indications are that a significant
zinc sulphide system could be nearby. Zone 3 is a large target area covering
more than 1 km2, and several holes will be needed to evaluate the full
potential of that area."
True thicknesses of the zinc intersections are estimated to be at least
85% of the downhole thickness, except where otherwise noted in footnotes to
Table 1. All significant results of the 2017 program are summarized in Table 1
with the strongest intercepts in bold text. Table 2 is a summary of all drill
collar information to date.
Table 1. Summary of 2017 Drill Results from Ayawilca

Drill hole              From m               To m     Interval m         Zn 
%    Pb %  Ag g/t   Indium g/t    Reported
(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)              (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)               (equal 
sign)(equal sign)(equal sign)(equal sign)     (equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)          (equal sign)(equal sign)(equal sign)      (equal 
sign)(equal sign)(equal sign)   (equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)   (equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)    (equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)

A17-056(1)                                  90.30         90.65          
0.35      29.0       0.4            82           443    April 3 '17

and                                        113.00        113.40          
0.40      31.2       0.0            85           759    April 3 '17

and                                        126.00        189.90         
63.90       5.6       0.1            17            29    March 6 '17

including                      127.50        145.40         17.90      
11.6       0.2            36            20    March 6 '17

including                      127.50        133.30          5.80      
22.5       0.3            77            50    March 6 '17

and                                        199.20        204.70          
5.50       5.8       0.1             6            38    April 3 '17

and                                        228.50        233.70          
5.20      12.9       0.0            11           162    March 6 '17

and                                        242.00        293.90         
51.90      10.1       0.1           624           233    April 3 '17

including                      279.00        293.90         14.90      
20.6       0.2          1524           441    April 3 '17

including                      279.00        285.40          6.40      
37.5       0.4           301           916    April 3 '17
---------                      ------        ------          ----      
----       ---           ---           ---    -----------

A17-056A                                   286.50        296.00          
9.50       9.3       0.3            19            88     May 3'17

and                                        309.00        313.10          
4.10      18.6       0.1            27           224     May 3'17

including                      310.50        313.10          2.60      
27.3       0.1            38           336     May 3'17
---------                      ------        ------          ----      
----       ---           ---           ---     --------

A17-057                                     84.90         86.35          
1.45      24.8       0.0            62           157    April 3 '17

and                                        143.70        144.50          
0.80      40.4       0.1           138           261    April 3 '17

and                                        157.60        197.70         
40.10       9.1       0.2            22           168    April 3 '17

including                      168.20        177.80          9.60      
16.8       0.1            22           299    April 3 '17

and                                        227.15        234.90          
7.75       3.5       0.2            21            85    April 3 '17

and                                        264.00        279.30         
15.30      20.0       2.5           102           263    April 3 '17

including                      265.75        269.00          3.25      
34.5       2.1            96           196    April 3 '17

including                      272.50        277.70          5.20      
32.5       1.3            69           639    April 3 '17
---------                      ------        ------          ----      
----       ---           ---           ---    -----------

A17-058                                    103.50        107.70         
4.205      20.2       4.2          3294            15     May 3'17

and                                        133.25        134.35         
1.105      30.3       3.2           500            61     May 3'17

A17-058 did not reach target, lost at 301 metres in sandstone
-------------------------------------------------------------

A17-059                                     50.30         51.10          
0.80      37.5       0.5            69            70     June 8'17

58.00         60.00          2.00       6.3       0.0            12            
30     June 8'17
-----         -----          ----       ---       ---           ---           
---     ---------

A17-060                                    262.40        264.40          
2.00      14.8       0.0            35          1178     May 3'17

and                                        275.00        279.50          
4.50      15.0       0.0            20           383     May 3'17

and                                        298.00        328.50       
30.5(2)       3.4       0.2            10            38     May 3'17

including                      303.40        312.00          8.60       
5.1       0.1            11             6     May 3'17
---------                      ------        ------          ----       
---       ---           ---           ---     --------

A17-061                                    122.70        150.50         
27.80       4.4       0.1            18            24     May 3'17

including                      145.70        147.50         1.805      
27.2       0.0            32           157     May 3'17

and                                        184.00        202.60      
18.60(3)      10.4       0.5            52            59     May 3'17

including                      196.20        198.80          2.60      
23.6       2.4           192            19     May 3'17

including                      201.90        202.60          0.70      
28.7       3.6           202            41     May 3'17

and                                        220.00        233.40         
13.40      18.7       0.9            57           463     May 3'17

including                      224.10        230.00          7.90      
29.3       0.8            71           719     May 3'17

and                                        265.00        266.80          
1.80      37.0       0.2            85           808     May 3'17
---                                        ------        ------          
----      ----       ---           ---           ---     --------

A17-062                                    152.40        153.05         
0.655      33.6       0.3           166            42    June 28'17

A17-062 was lost prior to target depth in a fault zone at 313 metres
--------------------------------------------------------------------

A17-063                                    302.20        349.90         
47.70      11.3       0.0            18           313     June 8'17

including                      303.30        313.10          9.80      
17.4       0.0            28           587     June 8'17

including                      327.40        339.60         12.20      
17.1       0.0            26           495     June 8'17
---------                      ------        ------         -----      
----       ---           ---           ---     ---------

A17-064                                    269.90        270.40          
0.50      15.6       0.0            11           304     June 8'17

and                                        277.20        277.60          
0.40      14.5       0.0            17            39     June 8'17
---                                        ------        ------          
----      ----       ---           ---           ---     ---------

A17-065                                    119.00        119.75          
0.75      36.6       0.1            88           157     June 8'17

and                                        204.00        210.00          
6.00       4.0       0.0             4             9     June 8'17

and                                        219.50        238.80         
19.30       4.7       0.0             7            93     June 8'17

including                      236.20        238.80          2.60      
20.6       0.0            23           529     June 8'17

and                                        266.40        293.00         
26.60       3.6       0.0             4            46     June 8'17

and                                        307.30        332.00         
24.70       3.8       0.0             5            51     June 8'17

and                                        340.00        346.00          
6.00       2.6       0.1             7            16     June 8'17
---                                        ------        ------          
----       ---       ---           ---           ---     ---------

A17-066                                    185.20        185.50          
0.30      37.8       0.0            40          1330     June 8'17

and                                        330.90        334.40          
3.50       7.4       0.1            24           111     June 8'17
and                                        345.00        350.00          
5.00      11.3       0.1            37           270     June 8'17
---                                        ------        ------          
----      ----       ---           ---           ---     ---------

A17-067                                    256.40        265.00          
8.60       2.7       0.2            39             0    June 28'17
-------                                    ------        ------          
----       ---       ---           ---           ---    ----------

A17-068                                    343.55        344.30          
0.75       6.1      11.6           210             7    June 28'17

and                                        382.00        388.00          
6.00       4.0       0.1            46            47    June 28'17
---                                        ------        ------          
----       ---       ---           ---           ---    ----------

A17-069                                    182.00        190.00          
8.00       3.0       0.5            13            17    June 28'17

and                                        261.60        262.30          
0.70      17.8       0.0            14            73    June 28'17

and                                        271.40        300.70         
29.30      10.4       0.1            17           278    June 28'17

including                      287.30        299.40         12.10      
19.1       0.1            25           440    June 28'17
---------                      ------        ------         -----      
----       ---           ---           ---    ----------

A17-070                                    100.00        105.10          
5.10       6.3       0.6           127            82    June 28'17

and                                        306.80        308.40          
1.60      15.4       0.1            40           529    June 28'17

and                                        317.50        356.80        
39.306       7.1       0.1            13           100    June 28'17

including                      340.00        356.80         16.80      
12.9       0.1            19           183    June 28'17

including                      340.00        348.00          8.00      
20.9       0.1            19           265    June 28'17
---------                      ------        ------          ----      
----       ---           ---           ---    ----------

A17-071                                    327.20        350.00         
22.80       8.4       0.8            35            17       Here

including                      332.40        345.00         12.60      
11.6       0.9            35            30       Here
---------                      ------        ------         -----      
----       ---           ---           ---       ----

A17-072                                    104.80        105.60          
0.80      27.0       0.3            73           125       Here

and      294.50        306.00         11.50       2.9       2.3           
781             0       Here

including     302.00        304.00          2.00       5.6       5.5          
3167             0       Here
---------     ------        ------          ----       ---       ---          
----           ---       ----

A17-073                                                   no significant 
results                                            Here
-------                                                   
----------------------                                            ----

A17-074                                     71.40         73.60         
2.205      31.0       0.1           138            23       Here

and                                        148.00        148.70         
0.705      18.3       0.3            38             0       Here
---                                        ------        ------         
-----      ----       ---           ---           ---       ----

A17-075                                    359.00        379.87         
20.80       5.0       0.0            11            44       Here

including                      376.30        379.80          3.50      
10.2       0.0            17            96       Here
---------                      ------        ------          ----      
----       ---           ---           ---       ----

(1) hole lost at 293.9 metres; wedged and completed as A17-056A to 376 metres 
depth

(2) includes 0.6 m with no core recovery from 315.2 to 315.8 m; this interval 
was given a zero grade

(3) includes 3.1 m with no core recovery from 198.8 to 201.9 m; this interval 
was given a zero grade

4 includes a silver assay cut at 1000 g/t

5 high grade vein intercepts with variable true thicknesses

6 includes 4.3 m of no recovery assumed zero grade

7 includes 1.7 m of no recovery assumed zero grade

Note:  Assays are calculated using a zinc only cut-off grade of 2% over 6 metres
(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)
Notes on sampling and assaying:
Drill holes are diamond HQ or NQ size core holes with recoveries
generally above 80% and often close to 100%. The drill core is marked up,
logged, and photographed on site. The cores are cut in half at the Company's
core storage facility, with half-cores stored as a future reference. Half-core
is bagged on average over 1 to 2 metre composite intervals and sent to either
ALS or SGS laboratories in Lima for assay in batches. Standards and blanks are
inserted into each batch prior to departure from Tinka's core storage
facilities. At the laboratory samples are dried, crushed to 100% passing 2mm,
then 500 grams pulverized for multi-element analysis by ICP (MS) using
multi-acid digestion. Samples assaying over 1% zinc, lead, or copper are
re-assayed using precise ore-grade AAS techniques.
Table 2. Summary of Drill Collar Information
Drill Hole WGS84 East        WGS84 North         Total depth (m)       
Elevation (m)      Azimuth     Dip
---------- ----------        -----------          --------------       
------------       -------     ---

A17-056              333046             8845062                 
293.9               4202         300     -75
-------              ------             -------                 
-----               ----         ---     ---

A17-056A             333046             8845062                 
376.4               4202         300     -75
--------             ------             -------                 
-----               ----         ---     ---

A17-057              333046             8845062                 
477.0               4202         300     -55
-------              ------             -------                 
-----               ----         ---     ---

A17-058              332557             8845657                 
301.0               4299         040     -82
-------              ------             -------                 
-----               ----         ---     ---

A17-059              332840             8845192                 
248.9               4209         120     -85
-------              ------             -------                 
-----               ----         ---     ---

A17-060              333174             8845005                 
358.4               4218         300     -70
-------              ------             -------                 
-----               ----         ---     ---

A17-061              333058             8844996                 
326.9               4191         290     -67
-------              ------             -------                 
-----               ----         ---     ---

A17-062              333175             8845004                 
309.0               4218         000     -90
-------              ------             -------                 
-----               ----         ---     ---

A17-063              333241             8845118                 
416.6               4229         310     -70
-------              ------             -------                 
-----               ----         ---     ---

A17-064              333062             8844993                 
369.1               4191         290     -50
-------              ------             -------                 
-----               ----         ---     ---

A17-065              333174             8845090                 
366.3               4225         300     -75
-------              ------             -------                 
-----               ----         ---     ---

A17-066              333345             8845193                 
371.6               4211         310     -70
-------              ------             -------                 
-----               ----         ---     ---

A17-067              333059             8844996                 
302.8               4190         120     -85
-------              ------             -------                 
-----               ----         ---     ---

A17-068              333552             8845279                 
419.7               4185         310     -75
-------              ------             -------                 
-----               ----         ---     ---

A17-069              333114             8845103                 
374.3               4210         300     -65
-------              ------             -------                 
-----               ----         ---     ---

A17-070              333152             8845150                 
367.8               4230         310     -75
-------              ------             -------                 
-----               ----         ---     ---

A17-071              333328             8845044                 
383.3               4202         310     -70
-------              ------             -------                 
-----               ----         ---     ---

A17-072              333114             8845103                 
445.9               4233         300     -53
-------              ------             -------                 
-----               ----         ---     ---

A17-073              334458             8846616                 
710.0               4024         210     -75
-------              ------             -------                 
-----               ----         ---     ---

A17-074              332666             8845491                 
429.6               4124         015     -75
-------              ------             -------                 
-----               ----         ---     ---

A17-075              333434             8845121                 
395.3               4201         310     -70
-------              ------             -------                 
-----               ----         ---     ---

A17-076              333155             8845153                 
420.7               4230         310     -55
-------              ------             -------                 
-----               ----         ---     ---
The qualified person, Dr. Graham Carman, Tinka's President and CEO, and a
Fellow of the Australasian Institute of Mining and Metallurgy, has reviewed
and verified the technical contents of this release.
On behalf of the Board,
"Graham Carman" Graham Carman, President & CEO
About Tinka Resources LimitedTinka is an exploration and development
company with its flagship property being the 100%-owned Ayawilca carbonate
replacement deposit (CRD) in the zinc-lead-silver belt of central Peru, 200
kilometres northeast of Lima. The Ayawilca Zinc Zone has an Inferred Mineral
Resource of 18.8 Mt at 5.9 % zinc, 0.2 % lead, 15 g/t silver & 74 g/t indium,
and a Tin Zone Inferred Mineral Resource of 5.4 Mt at 0.76 % tin, 0.31 %
copper & 18 g/t silver. Both resources are open for expansion (May 25, 2016).
The Silver Zone at Colquipucro, 2 km north of the Zinc Zone, has an Indicated
Mineral Resource of 2.9 Mt at 112 g/t silver for 10.4 Moz silver and an
Inferred Mineral Resource of 2.2 Mt at 105g/t silver for 7.5 Moz silver hosted
by oxidized lenses between the surface and 80 metres depth (Feb. 26, 2015).
Forward Looking Statements: Certain information in this news release
contains forward-looking statements and forward-looking information within the
meaning of applicable securities laws (collectively "forward-looking
statements"). All statements, other than statements of historical fact are
forward-looking statements. Forward-looking statements are based on the
beliefs and expectations of Tinka as well as assumptions made by and
information currently available to Tinka's management. Such statements reflect
the current risks, uncertainties and assumptions related to certain factors
including, without limitations, drilling results, the Company's expectations
regarding mineral resource calculations, capital and other costs varying
significantly from estimates, production rates varying from estimates, changes
in world metal markets, changes in equity markets, uncertainties relating to
the availability and costs of financing needed in the future, equipment
failure, unexpected geological conditions, imprecision in resource estimates
or metal recoveries, success of future development initiatives, competition,
operating performance, environmental and safety risks, delays in obtaining or
failure to obtain necessary permits and approvals from local authorities,
community agreements and relations, and other development and operating risks.
Should any one or more of these risks or uncertainties materialize, or 
shouldany underlying assumptions prove incorrect, actual results may vary 
materially
from those described herein. Although Tinka believes that assumptions inherent
in the forward-looking statements are reasonable, forward-looking statements
are not guarantees of future performance and accordingly undue reliance should
not be put on such statements due to the inherent uncertainty therein. Except
as may be required by applicable securities laws, Tinka disclaims any intent
or obligation to update any forward-looking statement.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release
SOURCE Tinka Resources Li
mited



View original content with multimedia:
http://www.newswire.ca/en/releases/archive/July2017/17/c5607.html

-0-                           07/17/2017
/For further information: Investor Information: www.tinkaresources.com,
Rob Bruggeman 1.416.884.3556, rbruggeman(at)tinkaresources.com; Company Contact:
Mariana Bermudez,  1.604.699.0202, info(at)tinkaresources.com/
/Web Site: www.tinkaresources.com /
(TKRFF TK.)

CO:  Tinka Resources Limited
ST:  British Columbia
IN:  MNG