Source	Marketwire
Date	07/19/2017
Time	04:01:29 AM

Company	 SRG GRAPHITE INC.
Title	SRG's Drill Results Returned Numerous Drill Intersects Above 10% Cg, 
Including 4.5 Meters at 36.97% Cg





    CDNX Symbol: SRG











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: SRG Graphite Inc.

TSX VENTURE SYMBOL: SRG

July 19, 2017

SRG's Drill Results Returned Numerous Drill Intersects Above 10% Cg, Including 
4.5 Meters at 36.97% Cg


MONTREAL, QUEBEC--(Marketwired - July 19, 2017) - SRG GRAPHITE INC. (TSX 
VENTURE:SRG) ("SRG" or the "Company") today announced drilling results, which 
continue to expand the potential of the Company's Lola Graphite project in 
Eastern Guinea, West Africa. Assay results from 27 boreholes continue to 
confirm the high-grade potential of the Lola Graphite deposit with ten 
intercepts grading above 10% graphitic carbon ("Cg"). Composite results are 
shown in Table 1.

Highlights:

/T/

--  Surface weathered profile thicknesses are 32% thicker than the initially
estimated 20 meters
--  Borehole LL45-011373 returned 31 meters grading 5.76% Cg, including
14.67 meters at 9.80% Cg
--  Borehole LL44-768470 returned 13 meters grading 14.22% Cg, including
4.50 meters at 36.97% Cg
--  Borehole LL45-011592 returned 19 meters grading 7.2% Cg, including 7.00
meters at 14.80% Cg

/T/

The current drilling program aims at producing the first mineral estimates for 
the property's surface weathered profile, which will be included in a 
preliminary economic assessment scheduled for Q4 2017. The weathered profile is 
approximately 32% thicker than the Company's initial estimate of 20 meters, 
with several holes demonstrating thicknesses of up to 50 meters. The drilling 
program will cover approximately 16% of the total surface area of deposit as 
defined by geological mapping, a geophysical Max-Min survey and previous 
drilling and pitting.

"Drill results continue to reaffirm our belief in the quality of this 
remarkable graphite asset," stated Dr. Marc-Antoine Audet, President and Chief 
Executive Officer, SRG.

Table 1: Composite Results

The following table presents a summary of the 27 drill hole results. 
Mineralized intervals were defined using 1.0% Cg cut-off grades ("cog").

/T/

----------------------------------------------------------------------------
FROM      LENGTH          CG
HOLE-ID                                          (m)         (m)         (%)
LL44-768470                                    23.00       13.00       14.22
Including(1)                                              4.50       36.97
LL45-028438                                     0.00       26.50        5.09
Including(1)                                             10.50        8.00
Including(2)                                              3.00       10.90
LL45-052446                                     0.00       34.50        3.16
Including(1)                                              4.50       10.70
Including(2)                                              1.50       17.10
LL45-070451                                     0.00       39.00        3.34
Including(1)                                              9.00        6.20
LL45-011373                                     3.00       31.00        5.76
Including(1)                                             14.67        9.80
Including(2)                                              5.00       16.32
LL45-094198                                     0.00       33.00        4.30
Including(1)                                              9.50        9.00
Including(2)                                              3.50       12.41
LL45-112206                                     0.00       34.50        5.36
Including(1)                                             21.75        7.60
Including(2)                                              1.00       10.90
Including(2)                                              1.00       18.50
LL45-131212                                     0.00       22.70        4.56
Including(1)                                              9.00        6.60
LL45-148219                                     0.00       15.00        5.33
Including(1)                                              9.00        7.50
Including(2)                                              1.50       11.40
Including(2)                                              1.50       11.20
LL44-782476                                     3.00       18.00        2.17
Including(1)                                              1.35       10.50
LL45-033503                                     0.00       23.60        2.65
LL45-075510                                     0.00       24.50        5.38
Including(1)                                              6.50       12.09
LL45-004489                                     9.00       17.50        4.88
LL45-002536                                     7.50       24.00        6.82
LL45-174598                                     1.50       19.50        4.34
LL45-181651                                     1.50       16.60        5.09
LL45-162645                                    16.50       13.00        6.25
LL45-105625                                    12.00        7.50        4.68
LL45-067612                                    15.00       13.90        4.91
LL45-011592                                     3.00       19.00        7.02
Including(1)                                              7.00       14.46
LL45-030598                                     3.00       27.00        2.53
LL45-170756                                     0.00       14.50        5.66
LL47-796005                                     0.00       27.00        3.65
LL48-015012                                     0.00       24.30        7.27
LL48-033019                                     0.00       23.00        3.76
Including(1)                                              9.00        4.74
Including(1)                                              2.50        7.64
LL48-052026                                     4.00       20.00        4.97
LL48-071033                                     0.00       16.50        3.41
----------------------------------------------------------------------------
(1) 3% Cg cog.
(2) 10% Cg cog.

/T/

The Lola Graphite Project is 100% owned by Sama Resources Guinea SARL, a fully 
owned subsidiary of the Company. The Graphite Project is located near the town 
of Lola in eastern Guinea and within 50 km from the border with Cote d'Ivoire.

Core logging and sampling was performed at SRG's facility in the Lola village. 
Sample preparations were performed at Veritas Laboratory in Abidjan, Ivory 
Coast. Sample pulps were delivered to Activation Laboratories Ltd., Ancaster, 
Ontario, Canada. The samples were treated through a multistage furnace process 
to remove organic carbon and carbonate carbon. The remaining graphitic carbon 
was measured as carbon dioxide in the infrared ("IR") cell as gases flow 
through the cell. Carbon dioxide absorbs IR energy at a precise wavelength 
within the IR spectrum. All analysis were performed using Eltra instruments.

About SRG Graphite Inc. (SRG)

SRG is a Canadian-based company focused on developing the Lola Graphite 
deposit, located in the Republic of Guinea, West Africa. SRG is committed to 
operate in a socially, environmentally and ethically responsible manner.

For additional information, please visit SRG's website at www.srggraphite.com.

Neither the TSX Venture Exchange nor its Regulation Services provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Forward-Looking Statements

Certain of the statements made and information contained herein are 
"forward-looking statements" within the meaning of Canadian securities 
legislation or "forward-looking information" within the meaning of the Ontario 
Securities Act and the Securities Act (British Columbia).  This includes 
statements concerning the Company's plans at its mineral properties, which 
involve known and unknown risks, uncertainties and other factors which may 
cause the actual results, performance or achievements of the Company, or 
industry results, to vary or be materially different from any future results, 
performance or achievements expressed or implied by such forward-looking 
statements or forward-looking information. Information regarding drilling 
results may also be deemed to be forward-looking statements or forward-looking 
information in that they reflect a prediction of what may be found to be 
present when and if a project is actually developed.

Forward-looking statements and forward-looking information are subject to a 
variety of risks and uncertainties which could cause actual events or results 
to differ from those reflected in the forward-looking statements or 
forward-looking information, including, without limitation, the availability of 
financing for activities, risks and uncertainties relating to the 
interpretation of drill results and the estimation of mineral resources and 
reserves, the geology, grade and continuity of mineral deposits, the 
possibility that future exploration, development or mining results will not be 
consistent with the Company's expectations, metal price fluctuations, 
environmental and regulatory requirements, availability of permits, escalating 
costs of remediation and mitigation, risk of title loss, the effects of 
accidents, equipment breakdowns, labour disputes or other unanticipated 
difficulties with or interruptions in exploration or development, the potential 
for delays in exploration or development activities, the inherent uncertainty 
of cost estimates and the potential for unexpected costs and expenses, 
commodity price fluctuations, currency fluctuations, expectations and beliefs 
of management and other risks and uncertainties.

In addition, forward-looking statements and forward-looking information are 
based on various assumptions. Should one or more of these risks and 
uncertainties materialize, or should underlying assumptions prove incorrect, 
actual results may vary materially from those described in forward-looking 
information or forward-looking statements. Accordingly, readers are advised not 
to place undue reliance on forward-looking statements or forward-looking 
information. Except as required under applicable securities legislation, the 
Company undertakes no obligation to publicly update or revise forward-looking 
statements or forward-looking information, whether as a result of new 
information, future events or otherwise.

- 30 -

CONTACT INFO:

SRG Graphite Inc. (SRG)
Dr. Marc-Antoine Audet
President & CEO
(514) 726-4158
ceo@srggraphite.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=596521201