Source	MARKET NEWS
Date	07/19/2017
Time	07:16:53 AM

Company	 Mundoro Capital Inc.
Title	Drilling 
Results From Tilva Rosh Prospect In Ser





    CDNX Symbol: MUN











Press Release




[200/News Release]MUNVMUNDORO CAPITAL INCJUL 19 2017  07:13 AMDrilling 
Results From Tilva Rosh Prospect In Serbia --->@NEWS RELEASE
MUNDORO CAPITAL INC ("MUN-V;MUNMF-0")
- Drilling Results From Tilva Rosh Prospect In Serbia

Mundoro Capital Inc. (www.mundoro.com) ("Mundoro" or the "Company")
is pleased to announce drilling results from the Tilva Rosh prospect
within the 100% controlled Savinac exploration license in north-eastern
Serbia. The Savinac license covers 90 km and is located in the Timok
Magmatic Belt, approximately 20 km southeast of the Bor mining camp.

Teo Dechev, CEO and President of Mundoro commented, "This Phase II
drilling program at Tilva Rosh was designed to test mineralization
along 400 m of strike to an average depth of 100 m as follow-up to the
discovery trench, which contained a 12 m interval of 30 g/t gold and
171 g/t silver, and to the initial drill testing of this area. Results
from drilling, trenching, geochemical soil sampling and alteration
mapping have successfully demonstrated a gold system associated with
three identified structures. Exploration has also identified a large
intact lithocap extending approximately 650 m to the north of the
current drilling for follow-up exploration. As a result mineralization
remains open to the north, south and at depth."

Phase II Drill Program

The Phase II drill program at Tilva Rosh comprised 14 inclined
reverse circulation drill holes totalling 1144 m to test the extent of
the previously identified gold mineralisation laterally, along strike
and at depth. The system was first supported by high grade trenching
results of 12 m @ 33.03 g/t AuEq (30.39 g/t Au, 171.27 g/t Ag) (see
October 21, 2013 press release) and later by Phase 1 drill testing (see
August 19, 2014 press release). Highlights from Phase II drilling at
Tilva Rosh are shown in Table 1. Collar locations are shown on Figure 1
-Tilva Rosh Drill Plan.

//st

Table 1: Summary of significant results from drill holes SAV01 to SAV06.

-------------------------------------------------------------------------
From      To Interval     Au     Ag     Cu    AuEq  CuEq
Drill Hole ID       (m)     (m)      (m)  (g/t)  (g/t)    (%)   (g/t)   (%)
---------------------------------------------------------------------------
-
17-SAV_07          20.0    24.0      4.0   0.52   2.83   0.47    1.21  0.88

-------------------------------------------------------------
35.0    41.0      6.0   1.29     11    0.8    2.56  1.86

-------------------------------------------------------------
Including        35.0    36.0      1.0   1.53    8.8   1.91    4.28  3.12

-------------------------------------------------------------
Including        40.0    41.0      1.0   1.28    8.1   1.46    3.41  2.48
---------------------------------------------------------------------------
-
17-SAV_08         101.0   104.0      3.0   3.72  22.67   0.19    4.33  3.16
---------------------------------------------------------------------------
-
17-SAV_09          25.0    30.0      5.0   0.32   3.48      -    0.37  0.27
---------------------------------------------------------------------------
-
17-SAV_010         63.0    78.0     15.0   0.37    2.2   0.24    0.73  0.54

-------------------------------------------------------------
Including        64.0    71.0      7.0   0.63   4.39   0.43    1.29  0.94

-------------------------------------------------------------
Including        65.0    66.0      1.0   1.25    7.2   1.12    2.90  2.11

-------------------------------------------------------------
88.0    92.0      4.0   0.45   1.45      -    0.47  0.34
---------------------------------------------------------------------------
-
17-SAV_011         35.0    39.0      4.0   0.57    0.5   0.13    0.76  0.55

-------------------------------------------------------------
Including        38.0    39.0      1.0   1.91    1.1   0.23    2.24  1.64

-------------------------------------------------------------
139.0   145.0      6.0   0.45    1.8      -    0.48  0.35
---------------------------------------------------------------------------
-
17-SAV_12           5.0    11.0      6.0   0.65   7.97      -    0.77  0.56
---------------------------------------------------------------------------
-
17-SAV_13          34.0    42.0      8.0   0.92    8.1      -    1.06  0.76
---------------------------------------------------------------------------
-
17-SAV_15          88.0    94.0      6.0   0.74    7.5      -    0.86  0.62
---------------------------------------------------------------------------
-
17-SAV_17          50.0    60.0     10.0   0.54    4.8   0.23    0.93  0.68

-------------------------------------------------------------
Including        55.0    60.0      5.0   0.95   0.45   0.95    1.71  1.25

-------------------------------------------------------------
Including        55.0    56.0      1.0   1.16   1.29   1.16    3.33  2.43

-------------------------------------------------------------
62.0    82.0     20.0   0.67   0.12   0.67    0.89  0.65

-------------------------------------------------------------
Including          65.0    70.0      5.0   2.02   0.34   2.02    2.69  1.96
---------------------------------------------------------------------------
-
17-SAV_20          72.0    83.0     11.0   0.54  -----   0.54    0.60  0.44

-------------------------------------------------------------
Including        76.0    77.0      1.0   3.68   0.12   3.68    4.21  3.07
---------------------------------------------------------------------------
-

//et

//st

Gold Equivalent ("AuEq.") is calculated using the formula AuEq = (g/t/Au)
+ (g/t/Ag) + ($/ozAu)/65 + [(%Cu) x (22.0462) x ($/lbCu)] [(1/31.1035) x
($/ozAu)]. Copper equivalent (CuEq%) is calculated using the formula CuEq
= (%Cu) + [(g/t/AuEq) x (1/31.1035) x ($/ozAu)] [(22.0462) x ($/lbCu)].
Metal prices used are: gold price of US$1300/oz, copper price of
US$2.6/lb, and silver price US$20/oz. All thicknesses from intersections
from drill holes are down-hole drilled thicknesses or outcrop sample
length thickness and not true widths.

//et

Drill holes 17-SAV_16; 17-SAV_18; 17-SAV_19 contain anomalous Au-Ag
and Cu but did not return significant intersections.

Interpretation of Phase II Drill Results

Phase II results support the continuation of the main north-south
trending mineralised structure over a length of at least 250 m. The
surface trace of the structure strikes towards the north and under the
lithocap (see Figure 2 - Geology, Alteration and Geochemistry at Tilva
Rosh). The lithocap appears to be displaced by late east-west faults
resulting in uplifting the southern portion and uncovering Tilva Rosh
mineralisation. A significant portion of the lithocap over the larger
northern block appears to be preserved. It continues for at least
another 650 m from the edge of the intersected mineralised structure
and is marked by a gold-silver-in-soil anomaly with elevated
molybdenum. The Tilva Rosh lithocap is zinc free but bordered by a
prominent (100-600 ppm) zinc anomaly reminiscent of the zinc
distribution in porphyry copper systems.

Recent detailed mapping of the lithocap revealed patchy alteration
texture composed of pyrophyllite-replaced clasts in a silicified matrix
and banded quartz veinlets. This is a promising sign that a porphyry
copper centre could occur at depth in the general vicinity of the
lithocap.

Prior Exploration at Tilva Rosh by Mundoro

During the 2013 and 2014 field seasons, Mundoro conducted
geochemical, mapping, trenching, ground magnetic surveys over the
Savinac license as well as compiling historic data, targeting
epithermal and porphyry copper-gold systems. This work outlined the
Savinac mineralised belt (9 km by 2 km) which includes the Tilva Rosh
epithermal system expressed on the surface with a large area of
advanced argillic alteration covering 4 km by 1 km. The Tilva Rosh
prospect was explored previously in late 1970's and early 2000's but
significant gold mineralisation and porphyry Cu-Au potential was not
identified until Mundoro's exploration program in Q4-2013.

The Phase I drill program, comprising six inclined RC drill holes
totalling 917.8 m, was drilled at the southern portion of Tilva Rosh
system to test the vertical extent of gold mineralization discovered
through previously reported trenching which returned 12m of 30.39 g/t
gold and 171.27 g/t silver (see press release dated October 21, 2013).
Highlights from Phase I drilling are shown in Table 2.

The Tilva Rosh prospect was originally outlined by a gold-in-soil
anomaly of 600 m by 150 m and confirmed with follow up trenching in
Q4-2013 and Q2-2014. The Company also completed ground magnetics in
Q1-2014. These initial drill results at Tilva Rosh are encouraging and
are interpreted to be proximal to a copper-gold porphyry system related
to a large area of advanced argillic lithocaps to the north.

//st

Table 2: Summary of significant results from Phase I drill holes SAV01 to
SAV06.

---------------------------------------------------------------------------
-
From      To Interval     Au     Ag     Cu    AuEq  CuEq
Drill Hole ID       (m)     (m)      (m)  (g/t)  (g/t)    (%)   (g/t)   (%)
---------------------------------------------------------------------------
-
SAV_01               11      18        7   7.90  46.74      -    8.62     -

-------------------------------------------------------------
Including          13      15        2  24.98 128.05      -   26.95     -

-------------------------------------------------------------
Including          13      14        1  42.90    199      -   45.96     -

-------------------------------------------------------------
126     133        7   0.35   2.76      -    0.39
---------------------------------------------------------------------------
-
SAV_02               30      40       10   0.34   2.16      -    0.37     -

-------------------------------------------------------------
67.7    71.8      4.1   0.62   2.36      -    0.66     -

-------------------------------------------------------------
95.6   100.0      4.4   0.54   6.38      -    0.64     -
---------------------------------------------------------------------------
-
SAV_03             71.0    76.0      5.0   2.54  15.54   0.59    3.59  2.61

-------------------------------------------------------------
Including        74.0    74.7      0.7  10.35  50.10   1.47   13.14  9.58
---------------------------------------------------------------------------
-
SAV_04             42.2    51.3      9.1   1.24   9.00   0.33    1.83  1.34

-------------------------------------------------------------
Including        43.3    47.3      3.0   1.45  14.60   0.58    2.47  1.80
---------------------------------------------------------------------------
-
SAV_05               29    50.2     21.2   0.25   1.78      -    0.28     -

-------------------------------------------------------------
Including        30.4    36.0      5.6   0.43   3.30      -    0.48     -

-------------------------------------------------------------
Including        46.2    50.2      4.0   0.35   3.88   0.14    0.60  0.44
---------------------------------------------------------------------------
-
SAV_06            38.50   42.90      4.4   0.59  14.95   0.21    1.11  0.81
---------------------------------------------------------------------------
-




//et

//st

Gold Equivalent ("AuEq.") is calculated using the formula AuEq = (g/t/Au)
+ (g/t/Ag) + ($/ozAu)/65 + [(%Cu) x (22.0462) x ($/lbCu)] [(1/31.1035) x
($/ozAu)]. Copper equivalent (CuEq%) is calculated using the formula CuEq
= (%Cu) + [(g/t/AuEq) x (1/31.1035) x ($/ozAu)] [(22.0462) x ($/lbCu)].
Metal prices used are: gold price of US$1300/oz, copper price of
US$2.6/lb, and silver price US$20/oz. All thicknesses from intersections
from drill holes are down-hole drilled thicknesses or outcrop sample
length thickness and not true widths.

//et

Sampling, Analysis and Qualified Person

Entire 1m interval RC cuttings are collected from the cyclone in
pre-numbered (from/to) large plastic bag. The sample is weighed.
Company technician sieves a small sample from the bag to generate a
chip log and places it in a pre-numbered (from/to) chip box. The sample
is passed through riffle splitter between 1 and 2 times until a ~3-4kg
sample is obtained and sent to ALS Bor prep lab. Duplicate sample is
kept in company core shed for future reference.

All samples are assayed using 50-gram fire assay with atomic
absorption finish and ME-ICP61 by ALS Romania. The entire sample was
crushed to 2mm, then split off a 1 kg sample and pulverized the split
to better than 85% passing 75 microns. Quality Assurance and Quality
Control procedures include the systematic insertion of standards and
duplicates into the sample streams. Duplicate samples are taken every
25 samples and standards and blanks are inserted after every 20th
sample. All data collected from detailed logging and assay results from
the laboratories are routinely verified and entered in an Access
database.

Technical information contained in this Press Release has been
reviewed and approved by Mr. G. Magaranov, P. Geo., Qualified Person as
defined by National Instrument 43-101.

On behalf of the Company,

Teo Dechev, Chief Executive Officer, President and Director

About Mundoro Capital Inc.

Mundoro is a well-funded, Canadian based, company focused on
mineral acquisition, exploration, and development. Our primary focus is
advancing our properties on the Tethyan Belt in Southeastern Europe.
Mundoro has methodically acquired a district-scale land position on
this prolific mineral belt which hosts significant Gold-Copper porphyry
and related epithermal deposits. Our strong project pipeline, which
also includes assets in Mexico and China, is positioned to drive
long-term, sustainable growth in order to attain production and
shareholder return.

Caution Concerning Forward-Looking Statements

Information included, attached to or incorporated by reference
into this News Release may contain forward-looking statements. All
statements, other than statements of historical fact, included or
incorporated by reference in this News Release are forward-looking
statements, including, without limitation, statements regarding
activities, events or developments that the Board expects or
anticipates may occur in the future. These forward-looking statements
can be identified by the use of forward-looking words such as "will",
"expect", "intend", "plan", "estimate", "anticipate", "believe" or
"continue" or similar words or the negative thereof. The material
assumptions that were applied in making the forward looking statementsin this 
News Release include expectations as to the Company's future
strategy and business plan and execution of the Company's existing
plans. There can be no assurance that the plans, intentions or
expectations upon which these forward-looking statements are based will
occur. We caution readers of this News Release not to place undue
reliance on forward looking statements contained in this News Release,
which are not a guarantee of performance and are subject to a number of
uncertainties and other factors that could cause actual results to
differ materially from those expressed or implied by such
forward-looking statements. These factors include general economic and
market conditions, changes in law, regulatory processes, the status of
Mundoro's assets and financial condition, actions of competitors and
the ability to implement business strategies and pursue business
opportunities. The forward-looking statements contained in this News
Release are expressly qualified in their entirety by this cautionary
statement. The forward-looking statements included in this News Release
are made as of the date of this News Release and the Board undertakes
no obligation to publicly update such forward-looking statements to
reflect new information, subsequent events or otherwise, except as
required by law. Shareholders are cautioned that all forward-looking
statements involve risks and uncertainties and for a more detailed
discussion of such risks and other factors that could cause actual
results to differ materially from those expressed or implied by such
forward-looking statements, refer to the Company's filings with the
Canadian securities regulators available on www.sedar.com.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.






















TSX Venture closing price for MUN-V
Date: 2017/07/17
Closing Price: 0.17

TEL:  +1-604-669-8055  Teo Dechev, CEO, President and Director
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1719900024TS11719901403-07135920170719