Source	CANADA NEWSWIRE
Date	07/20/2017
Time	10:52:03 AM

Company	 Hannan Metals Ltd.
Title	Hannan Drills 3.2 Metres (at) 8% Zinc, 73% Lead and 388 g/t Silver and 18.8
Metres (at) 9% Zinc, 1% Lead, 19 g/t Silver at Kilbricken in Ireland





    CDNX Symbol: HAN











Press Release




" BC-HannanDrill-resultsIR   07-20 2002
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Hannan Drills 3.2 Metres (at) 8% Zinc, 73% Lead and 388 g/t Silver and 18.8
Metres (at) 9% Zinc, 1% Lead, 19 g/t Silver at Kilbricken in Ireland@

VANCOUVER, July 20, 2017 /CNW/ - Hannan Metals Limited ("Hannan" or the
"Company") (TSX.V: HAN) (OTCPK: HANFF) is pleased to announce very high grade
and thickness drill results from the first drill hole completed in its
resource expansion program at the 100%-owned Kilbricken
zinc-lead-silver-copper deposit in Ireland.
Hannan's first diamond drill hole at Kilbricken, DH 17-3679-217
("DH217"), is one of the most mineralized ever drilled at the property.
Highlights include:
<<

o 8.0 metres (at) 4.1% Zn, 33.7% Pb and 174 g/t Ag (37.9% Zn+Pb) from 528 
metres,
including 3.2 metres (at) 8.4% Zn, 72.8% Pb and 388 g/t Ag (81.2% Zn+Pb) from
528 metres;
o 3.4 metres (at) 5.2% Zn, 4.3% Pb and 33 g/t Ag (9.5% Zn+Pb) from 570 metres;
o 26.6 metres (at) 7.5% Zn, 0.9% Pb and 14 g/t Ag (8.4% Zn+Pb) from 588 metres,
including 18.8 metres (at) 8.8% Zn, 1.1% Pb, 19 g/t Ag (9.9% Zn+Pb) from 588
metres;
--  A 2.2 metre interval from 528 metres assayed 86% lead which approximates
pure galena (PbS, Photo 1);
--  DH217 was completed at 714 metres into the Fort Zone at Kilbricken. Base
metal mineralization was intersected over a total downhole length of 128
metres with multiple intervals exceeding the grade and thickness cut-off
for the mineral resource area;
--  DH217 was a 20 metre step out from drill hole DH167 which intersected a
lower zone of mineralization that returned 4.5m (at) 0.8% Zn, 2.6% Pb,
18.91% Cu, 867.6g/t Ag from 616.5m;
--  The initial drill program by Hannan is focused on expansion of the
current mineral resource and extraction of metallurgical samples. To
date two holes have been completed for 1,365 metres. Drilling will
continue until August 2017. The next hole drilled, DH218 is a 50 metre
step out, located 70 metres up dip from DH217 (Figure 1).
>>
Mr. Michael Hudson, CEO and Chairman, states: "Hannan's first drill hole
(DH217) is a clear demonstration of the very high grades that are found at
Kilbricken, and the strength of the mineralization process with 3.2 metres (at)
81.2% zinc plus lead and 388 g/t silver. The higher-grade mineralization shows
good lateral continuity and is contained within a broader mineralized zone
totaling 79 metres down hole length. DH217 was not included in the maiden
resource calculation announced on July 10, 2017 and this result will add to
the existing indicated and inferred mineral resources. This is a great start
to our resource expansion drill program."
A plan and cross section view of the drill results is provided in Figure
1. Table 1 shows highlight intersections and Tables 2 and 3 include all
relevant collar and assay information. The true thickness of mineralized
intervals at Kilbricken is interpreted to be approximately 95% of the sampled
thickness.
Technical BackgroundOne diamond drill rig from Priority Drilling Limited
with water recirculation and drill cuttings collection systems was used for
the drill results reported here. Core diameter is NQ2 (50.6 mm). Core
recoveries were excellent and average close to 95-100% in fresh rock. After
photographing and logging, core intervals averaging 1-2 metre for mineralized
samples were cut in half at Hannan's core facilities in Ennis, Co. Clare,
Ireland. The remaining half core is retained for verification and reference
purposes.
Analytical samples were transported by Hannan personnel from site to the
ALS Loughrea located at Dublin Road, Loughrea, Co. Galway, Ireland. At the
laboratory samples are dried, crushed to 100% passing 2mm, then 500 grams
pulverized for multi-element analysis by method ME-MS6, a four-acid digest
performed on 0.25g of sample to quantitatively dissolve most geological
materials. Analysis is via ICP-MS + ICP-AES. Samples assaying over range 1%
zinc, lead, or copper and 100g/t silver were re-assayed using methods
Ag/Pb/Zn-OG62, a precise mineralization grade method to determine lead, zinc
and silver by HF-HNO3-HClO4 Digest, HCl leach and ICP-AES. For lead >20% and
<80% method Pb-AAORE <80% was applied. This is a high precision analysis of
lead mineralization, where lead was released with a strong oxidizing attack
and analyzed by AAS. For lead >80%, method ME-CON02 was selected where lead is
normally determined in concentrates by a combination of acid digests with
spectroscopy finish.
The QA/QC program of Hannan consists of the systematic insertion of
certified reference material of known base metal content and blanks at the
start of each batch and within interpreted mineralized rock. In addition, ALS
inserts blanks and standards into the analytical process.
Table 1: Highlight intersections from DH 217. Lower cut-off 5% ZnEq
applied except where (x) noted.
Hole_ID                   From                To                 
Width                    Zn%              Pb%      Ag g/t           Cu%       
Pb+Zn
-------                   ----                ---                
-----                    ---               ---       ------           
---        -----

217                528.0               536.0                   
8.0               4.1               33.7              174       0.1          
37.9
-----               -----                   ---               ---               
----              ---       ---          ----

including                528.0               531.2                   
3.2               8.4               72.8              388       0.1          
81.2
-----               -----                   ---               ---               
----              ---       ---          ----

217                570.0               573.4                   
3.4               5.2                4.3               33       0.1           
9.5
-----               -----                   ---               
---                ---              ---       ---           ---

217                588.0               614.6                  
26.6               7.5                0.9               14       0.1           
8.4
-----               -----                  ----               
---                ---              ---       ---           ---

including                588.0               606.8                  
18.8               8.8                1.1               19       0.1           
9.9
-----               -----                  ----               
---                ---              ---       ---           ---

217(x)                622.6               656.4                  
33.8               0.0                0.1               11       0.3           
0.1
-----               -----                  ----               
---                ---              ---       ---           ---

Note: The zinc equivalent (ZnEq) value was calculated using the following 
formula: ZnEq% (equal sign) Zn % + (Cu% (x) 2.102) + Pb% (x) 0.815) + (Ag g/t 
(x)
0.023) with assumed prices of Zn $2587/t; Cu $5437/t; Pb $2108/t and Ag 
$18.44/oz.

About Hannan Metals Limited (TSX.V:HAN)
Hannan Metals Limited has 100% ownership of the County Clare Zn-Pb-Ag-Cu
project in Ireland, which consists of 9 prospecting licences for 32,223
hectares. Zinc remains in tight supply amidst rising demand and stagnant
supply. Ireland is a leading global jurisdiction for zinc mining and
exploration. In 2015, Ireland was the world's 10th largest zinc producing
nation with 230,000 tonnes produced.
This maiden mineral resource for was published in July 2017, and
immediately ranks Kilbricken as one of the top ten base metal deposits
discovered in Ireland by tonnes and grade. Total indicated mineral resource
were calculated as 2.7 million tonnes at 8.8% zinc equivalent ("ZnEq"),
including 1.4 million tonnes at 10.8% Zneq and total inferred mineral resource
of 1.7 million tonnes at 8.2% ZnEq, including 0.6 million tonnes at 10.4%
ZnEq. Importantly, the initial resource is expandable at all scales, from near
resource to prospect scale.
Over the last decade, the team behind Hannan has forged a long and
successful record of financing and discovering mineral projects in Europe.
Additionally, the team holds extensive zinc experience, gained from the
world's largest integrated zinc producer of the time, Pasminco Ltd.
Mr. Michael Hudson FAusIMM, Hannan's CEO and Chairman, is a Qualified
Person as defined in National Instrument 43-101 and has reviewed and approved
the technical disclosure contained in this news release.
On behalf of the Board,
"Michael Hudson"Michael Hudson, CEO & Chairman
Forward Looking Statements
Certain information set forth in this news release contains
"forward-looking statements", and "forward- looking information" under
applicable securities laws. Except for statements of historical fact, certain
information contained herein constitutes forward-looking statements, which
include the Company's expectations regarding future performance based on
current results, expected cash costs based on the Company's current internal
expectations, estimates, projections, assumptions and beliefs, which may prove
to be incorrect. These statements are not guarantees of future performance and
undue reliance should not be placed on them. Such forward-looking statements
necessarily involve known and unknown risks and uncertainties, which may cause
the Company's actual performance and financial results in future periods to
differ materially from any projects of future performance or results expressed
or implied by such forward-looking statement. These risks and uncertainties
include, but are not limited to: liabilities inherent in mine development and
production, geological risks, the financial markets generally, and the ability
of the Company to raise additional capital to fund future operations. There
can be no assurance that forward-looking statements will prove to be accurate,
and actual results and future events could differ materially from those
anticipated in such statements. The Company undertakes no obligation to update
forward-looking statements if circumstances or management's estimates or
opinions should change except as required by applicable securities laws. The
reader is cautioned not to place undue reliance on forward-looking statements.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
Table 2: Collar Information for Resource Expansion Program at the
Kilbricken Project
HoleID East            North            Azimuth     Dip     RL         Depth
------ ----            -----            -------     ---     ---        -----

DH217       139133.223       176005.973         020     -82     22.433       714
----------       ----------         ---     ---     ------       ---

DH218        139165.47        176035.14         010     -81     22.735       651
---------        ---------         ---     ---     ------       ---

Table 3: Individual Assays for DH217 from the Kilbricken Project
SampleID From        To       Interval     Zn%    Pb%      Ag g/t       Cu%
-------- ----       ---       --------     ---     ---       ------       ---

20310        524.0     525.7          1.7    0.7      0.5            3       0.0
-----     -----          ---    ---      ---          ---       ---

20311        525.7     526.4          0.7    0.4      0.2            2       0.0
-----     -----          ---    ---      ---          ---       ---

20312        526.4       528          1.6    1.8      1.6           10       0.0
-----       ---          ---    ---      ---          ---       ---

20313        528.0     529.0            1    0.7     86.6          425       0.0
-----     -----          ---    ---     ----          ---       ---

20314        529.0     530.2          1.2    0.0     85.9          460       0.0
-----     -----          ---    ---     ----          ---       ---

20315        530.2     531.2          1.0   25.0     45.3          273       0.3
-----     -----          ---   ----     ----          ---       ---

20317        531.2     533.0          1.8    1.9      0.1            4       0.0
-----     -----          ---    ---      ---          ---       ---

20318          533     534.4          1.4    1.4     16.1           63       0.1
---     -----          ---    ---     ----          ---       ---

20319        534.4     536.0          1.6    0.6      8.9           37       0.0
-----     -----          ---    ---      ---          ---       ---

20320        536.0     537.8          1.8    0.2      0.2            2       0.0
-----     -----          ---    ---      ---          ---       ---

20321        537.8     539.7          1.9    1.4      2.7           14       0.1
-----     -----          ---    ---      ---          ---       ---

20322        539.7     541.7            2    0.0      0.0            0       0.0
-----     -----          ---    ---      ---          ---       ---

20323        541.7     543.7            2    0.0      0.0            2       0.1
-----     -----          ---    ---      ---          ---       ---

20324        543.7     545.7            2    0.0      0.0            1       0.0
-----     -----          ---    ---      ---          ---       ---

20326        545.7     547.7            2    0.0      0.0            1       0.0
-----     -----          ---    ---      ---          ---       ---

20327        547.7     549.1          1.4    0.0      0.0            2       0.1
-----     -----          ---    ---      ---          ---       ---

20328        549.1     550.6          1.5    0.0      0.0            1       0.0
-----     -----          ---    ---      ---          ---       ---
20329        550.6     552.0          1.4    0.0      0.0            7       0.3
-----     -----          ---    ---      ---          ---       ---

20330        552.0     554.0            2    0.0      0.0            5       0.2
-----     -----          ---    ---      ---          ---       ---

20331        554.0     556.0            2    0.3      0.2            4       0.1
-----     -----          ---    ---      ---          ---       ---

20332        556.0     558.0            2    0.0      0.1            2       0.1
-----     -----          ---    ---      ---          ---       ---

20333        558.0     560.0            2    0.2      0.1            2       0.0
-----     -----          ---    ---      ---          ---       ---

20334        560.0     562.0            2    1.3      0.5            9       0.0
-----     -----          ---    ---      ---          ---       ---

20335        562.0     564.0            2    1.6      1.0           10       0.0
-----     -----          ---    ---      ---          ---       ---

20336        564.0     566.0            2    0.5      0.3            3       0.0
-----     -----          ---    ---      ---          ---       ---

20337        566.0     568.0            2    1.1      0.6            6       0.0
-----     -----          ---    ---      ---          ---       ---

20338        568.0     570.0            2    0.9      0.4            4       0.0
-----     -----          ---    ---      ---          ---       ---

20339        570.0     571.0            1    7.3      2.6           27       0.1
-----     -----          ---    ---      ---          ---       ---

20340        571.0     572.8          1.8    0.0      0.0            2       0.0
-----     -----          ---    ---      ---          ---       ---

20341        572.8    

" BC-HannanDrill-resultsIR   07-20 2002
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Hannan Drills 3.2 Metres (at) 8% Zinc, 73% Lead and 388 g/t Silver and 18.8
Metres (at) 9% Zinc, 1% Lead, 19 g/t Silver at Kilbricken in Ireland@

VANCOUVER, July 20, 2017 /CNW/ - Hannan Metals Limited ("Hannan" or the
"Company") (TSX.V: HAN) (OTCPK: HANFF) is pleased to announce very high grade
and thickness drill results from the first drill hole completed in its
resource expansion program at the 100%-owned Kilbricken
zinc-lead-silver-copper deposit in Ireland.
Hannan's first diamond drill hole at Kilbricken, DH 17-3679-217
("DH217"), is one of the most mineralized ever drilled at the property.
Highlights include:
<<

o 8.0 metres (at) 4.1% Zn, 33.7% Pb and 174 g/t Ag (37.9% Zn+Pb) from 528 
metres,
including 3.2 metres (at) 8.4% Zn, 72.8% Pb and 388 g/t Ag (81.2% Zn+Pb) from
528 metres;
o 3.4 metres (at) 5.2% Zn, 4.3% Pb and 33 g/t Ag (9.5% Zn+Pb) from 570 metres;
o 26.6 metres (at) 7.5% Zn, 0.9% Pb and 14 g/t Ag (8.4% Zn+Pb) from 588 metres,
including 18.8 metres (at) 8.8% Zn, 1.1% Pb, 19 g/t Ag (9.9% Zn+Pb) from 588
metres;
--  A 2.2 metre interval from 528 metres assayed 86% lead which approximates
pure galena (PbS, Photo 1);
--  DH217 was completed at 714 metres into the Fort Zone at Kilbricken. Base
metal mineralization was intersected over a total downhole length of 128
metres with multiple intervals exceeding the grade and thickness cut-off
for the mineral resource area;
--  DH217 was a 20 metre step out from drill hole DH167 which intersected a
lower zone of mineralization that returned 4.5m (at) 0.8% Zn, 2.6% Pb,
18.91% Cu, 867.6g/t Ag from 616.5m;
--  The initial drill program by Hannan is focused on expansion of the
current mineral resource and extraction of metallurgical samples. To
date two holes have been completed for 1,365 metres. Drilling will
continue until August 2017. The next hole drilled, DH218 is a 50 metre
step out, located 70 metres up dip from DH217 (Figure 1).
>>
Mr. Michael Hudson, CEO and Chairman, states: "Hannan's first drill hole
(DH217) is a clear demonstration of the very high grades that are found at
Kilbricken, and the strength of the mineralization process with 3.2 metres (at)
81.2% zinc plus lead and 388 g/t silver. The higher-grade mineralization shows
good lateral continuity and is contained within a broader mineralized zone
totaling 79 metres down hole length. DH217 was not included in the maiden
resource calculation announced on July 10, 2017 and this result will add to
the existing indicated and inferred mineral resources. This is a great start
to our resource expansion drill program."
A plan and cross section view of the drill results is provided in Figure
1. Table 1 shows highlight intersections and Tables 2 and 3 include all
relevant collar and assay information. The true thickness of mineralized
intervals at Kilbricken is interpreted to be approximately 95% of the sampled
thickness.
Technical BackgroundOne diamond drill rig from Priority Drilling Limited
with water recirculation and drill cuttings collection systems was used for
the drill results reported here. Core diameter is NQ2 (50.6 mm). Core
recoveries were excellent and average close to 95-100% in fresh rock. After
photographing and logging, core intervals averaging 1-2 metre for mineralized
samples were cut in half at Hannan's core facilities in Ennis, Co. Clare,
Ireland. The remaining half core is retained for verification and reference
purposes.
Analytical samples were transported by Hannan personnel from site to the
ALS Loughrea located at Dublin Road, Loughrea, Co. Galway, Ireland. At the
laboratory samples are dried, crushed to 100% passing 2mm, then 500 grams
pulverized for multi-element analysis by method ME-MS6, a four-acid digest
performed on 0.25g of sample to quantitatively dissolve most geological
materials. Analysis is via ICP-MS + ICP-AES. Samples assaying over range 1%
zinc, lead, or copper and 100g/t silver were re-assayed using methods
Ag/Pb/Zn-OG62, a precise mineralization grade method to determine lead, zinc
and silver by HF-HNO3-HClO4 Digest, HCl leach and ICP-AES. For lead >20% and
<80% method Pb-AAORE <80% was applied. This is a high precision analysis of
lead mineralization, where lead was released with a strong oxidizing attack
and analyzed by AAS. For lead >80%, method ME-CON02 was selected where lead is
normally determined in concentrates by a combination of acid digests with
spectroscopy finish.
The QA/QC program of Hannan consists of the systematic insertion of
certified reference material of known base metal content and blanks at the
start of each batch and within interpreted mineralized rock. In addition, ALS
inserts blanks and standards into the analytical process.
Table 1: Highlight intersections from DH 217. Lower cut-off 5% ZnEq
applied except where (x) noted.
Hole_ID                   From                To                 
Width                    Zn%              Pb%      Ag g/t           Cu%       
Pb+Zn
-------                   ----                ---                
-----                    ---               ---       ------           
---        -----

217                528.0               536.0                   
8.0               4.1               33.7              174       0.1          
37.9
-----               -----                   ---               ---               
----              ---       ---          ----

including                528.0               531.2                   
3.2               8.4               72.8              388       0.1          
81.2
-----               -----                   ---               ---               
----              ---       ---          ----

217                570.0               573.4                   
3.4               5.2                4.3               33       0.1           
9.5
-----               -----                   ---               
---                ---              ---       ---           ---

217                588.0               614.6                  
26.6               7.5                0.9               14       0.1           
8.4
-----               -----                  ----               
---                ---              ---       ---           ---

including                588.0               606.8                  
18.8               8.8                1.1               19       0.1           
9.9
-----               -----                  ----               
---                ---              ---       ---           ---

217(x)                622.6               656.4                  
33.8               0.0                0.1               11       0.3           
0.1
-----               -----                  ----               
---                ---              ---       ---           ---

Note: The zinc equivalent (ZnEq) value was calculated using the following 
formula: ZnEq% (equal sign) Zn % + (Cu% (x) 2.102) + Pb% (x) 0.815) + (Ag g/t 
(x)
0.023) with assumed prices of Zn $2587/t; Cu $5437/t; Pb $2108/t and Ag 
$18.44/oz.

About Hannan Metals Limited (TSX.V:HAN)
Hannan Metals Limited has 100% ownership of the County Clare Zn-Pb-Ag-Cu
project in Ireland, which consists of 9 prospecting licences for 32,223
hectares. Zinc remains in tight supply amidst rising demand and stagnant
supply. Ireland is a leading global jurisdiction for zinc mining and
exploration. In 2015, Ireland was the world's 10th largest zinc producing
nation with 230,000 tonnes produced.
This maiden mineral resource for was published in July 2017, and
immediately ranks Kilbricken as one of the top ten base metal deposits
discovered in Ireland by tonnes and grade. Total indicated mineral resource
were calculated as 2.7 million tonnes at 8.8% zinc equivalent ("ZnEq"),
including 1.4 million tonnes at 10.8% Zneq and total inferred mineral resource
of 1.7 million tonnes at 8.2% ZnEq, including 0.6 million tonnes at 10.4%
ZnEq. Importantly, the initial resource is expandable at all scales, from near
resource to prospect scale.
Over the last decade, the team behind Hannan has forged a long and
successful record of financing and discovering mineral projects in Europe.
Additionally, the team holds extensive zinc experience, gained from the
world's largest integrated zinc producer of the time, Pasminco Ltd.
Mr. Michael Hudson FAusIMM, Hannan's CEO and Chairman, is a Qualified
Person as defined in National Instrument 43-101 and has reviewed and approved
the technical disclosure contained in this news release.
On behalf of the Board,
"Michael Hudson"Michael Hudson, CEO & Chairman
Forward Looking Statements
Certain information set forth in this news release contains
"forward-looking statements", and "forward- looking information" under
applicable securities laws. Except for statements of historical fact, certain
information contained herein constitutes forward-looking statements, which
include the Company's expectations regarding future performance based on
current results, expected cash costs based on the Company's current internal
expectations, estimates, projections, assumptions and beliefs, which may prove
to be incorrect. These statements are not guarantees of future performance and
undue reliance should not be placed on them. Such forward-looking statements
necessarily involve known and unknown risks and uncertainties, which may cause
the Company's actual performance and financial results in future periods to
differ materially from any projects of future performance or results expressed
or implied by such forward-looking statement. These risks and uncertainties
include, but are not limited to: liabilities inherent in mine development and
production, geological risks, the financial markets generally, and the ability
of the Company to raise additional capital to fund future operations. There
can be no assurance that forward-looking statements will prove to be accurate,
and actual results and future events could differ materially from those
anticipated in such statements. The Company undertakes no obligation to update
forward-looking statements if circumstances or management's estimates or
opinions should change except as required by applicable securities laws. The
reader is cautioned not to place undue reliance on forward-looking statements.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
Table 2: Collar Information for Resource Expansion Program at the
Kilbricken Project
HoleID East            North            Azimuth     Dip     RL         Depth
------ ----            -----            -------     ---     ---        -----

DH217       139133.223       176005.973         020     -82     22.433       714
----------       ----------         ---     ---     ------       ---

DH218        139165.47        176035.14         010     -81     22.735       651
---------        ---------         ---     ---     ------       ---

Table 3: Individual Assays for DH217 from the Kilbricken Project
SampleID From        To       Interval     Zn%    Pb%      Ag g/t       Cu%
-------- ----       ---       --------     ---     ---       ------       ---

20310        524.0     525.7          1.7    0.7      0.5            3       0.0
-----     -----          ---    ---      ---          ---       ---

20311        525.7     526.4          0.7    0.4      0.2            2       0.0
-----     -----          ---    ---      ---          ---       ---

20312        526.4       528          1.6    1.8      1.6           10       0.0
-----       ---          ---    ---      ---          ---       ---

20313        528.0     529.0            1    0.7     86.6          425       0.0
-----     -----          ---    ---     ----          ---       ---

20314        529.0     530.2          1.2    0.0     85.9          460       0.0
-----     -----          ---    ---     ----          ---       ---

20315        530.2     531.2          1.0   25.0     45.3          273       0.3
-----     -----          ---   ----     ----          ---       ---

20317        531.2     533.0          1.8    1.9      0.1            4       0.0
-----     -----          ---    ---      ---          ---       ---

20318          533     534.4          1.4    1.4     16.1           63       0.1
---     -----          ---    ---     ----          ---       ---

20319        534.4     536.0          1.6    0.6      8.9           37       0.0
-----     -----          ---    ---      ---          ---       ---

20320        536.0     537.8          1.8    0.2      0.2            2       0.0
-----     -----          ---    ---      ---          ---       ---

20321        537.8     539.7          1.9    1.4      2.7           14       0.1
-----     -----          ---    ---      ---          ---       ---

20322        539.7     541.7            2    0.0      0.0            0       0.0
-----     -----          ---    ---      ---          ---       ---

20323        541.7     543.7            2    0.0      0.0            2       0.1
-----     -----          ---    ---      ---          ---       ---

20324        543.7     545.7            2    0.0      0.0            1       0.0
-----     -----          ---    ---      ---          ---       ---

20326        545.7     547.7            2    0.0      0.0            1       0.0
-----     -----          ---    ---      ---          ---       ---

20327        547.7     549.1          1.4    0.0      0.0            2       0.1
-----     -----          ---    ---      ---          ---       ---

20328        549.1     550.6          1.5    0.0      0.0            1       0.0
-----     -----          ---    ---      ---          ---       ---
20329        550.6     552.0          1.4    0.0      0.0            7       0.3
-----     -----          ---    ---      ---          ---       ---

20330        552.0     554.0            2    0.0      0.0            5       0.2
-----     -----          ---    ---      ---          ---       ---

20331        554.0     556.0            2    0.3      0.2            4       0.1
-----     -----          ---    ---      ---          ---       ---

20332        556.0     558.0            2    0.0      0.1            2       0.1
-----     -----          ---    ---      ---          ---       ---

20333        558.0     560.0            2    0.2      0.1            2       0.0
-----     -----          ---    ---      ---          ---       ---

20334        560.0     562.0            2    1.3      0.5            9       0.0
-----     -----          ---    ---      ---          ---       ---

20335        562.0     564.0            2    1.6      1.0           10       0.0
-----     -----          ---    ---      ---          ---       ---

20336        564.0     566.0            2    0.5      0.3            3       0.0
-----     -----          ---    ---      ---          ---       ---

20337        566.0     568.0            2    1.1      0.6            6       0.0
-----     -----          ---    ---      ---          ---       ---

20338        568.0     570.0            2    0.9      0.4            4       0.0
-----     -----          ---    ---      ---          ---       ---

20339        570.0     571.0            1    7.3      2.6           27       0.1
-----     -----          ---    ---      ---          ---       ---

20340        571.0     572.8          1.8    0.0      0.0            2       0.0
-----     -----          ---    ---      ---          ---       ---

20341        572.8     573.4          0.6   17.1     20.1          134       0.4
-----     -----          ---   ----     ----          ---       ---

20342        573.4     574.9          1.5    2.6      0.6           22       0.0
-----     -----          ---    ---      ---          ---       ---

20343        574.9     576.1          1.2    3.3      0.8           10       0.0
-----     -----          ---    ---      ---          ---       ---

20344        576.1     578.0          1.9    0.0      0.0            0       0.0
-----     -----          ---    ---      ---          ---       ---

20345        578.0     580.0            2    0.0      0.0            0       0.0
-----     -----          ---    ---      ---          ---       ---

20346        580.0     582.0            2    0.0      0.0            0       0.0
-----     -----          ---    ---      ---          ---       ---

20347        582.0     584.0            2    0.2      0.1            1       0.0
-----     -----          ---    ---      ---          ---       ---

20348        584.0     586.0            2    0.9      0.3            3       0.0
-----     -----          ---    ---      ---          ---       ---

20349        586.0     588.0            2    0.2      0.0            0       0.0
-----     -----          ---    ---      ---          ---       ---

20351        588.0     590.0            2    6.7      1.4           16       0.1
-----     -----          ---    ---      ---          ---       ---

20352        590.0     592.0            2    4.8      0.8            9       0.0
-----     -----          ---    ---      ---          ---       ---

20353        592.0     594.0            2    1.0      0.4            6       0.0
-----     -----          ---    ---      ---          ---       ---

20354        594.0     596.0            2    4.6      1.3           16       0.1
-----     -----          ---    ---      ---          ---       ---

20355        596.0     598.0            2    7.3      1.9           17       0.1
-----     -----          ---    ---      ---          ---       ---

20356        598.0     600.0            2    8.9      1.7           20       0.1
-----     -----          ---    ---      ---          ---       ---

20357        600.0     602.0            2    8.5      1.9           36       0.2
-----     -----          ---    ---      ---          ---       ---

20358        602.0     604.0            2   13.3      0.4           19       0.2
-----     -----          ---   ----      ---          ---       ---

20359        604.0     605.5          1.5   27.4      0.9           34       0.3
-----     -----          ---   ----      ---          ---       ---

20360        605.5     606.8          1.3   10.4      0.2           17       0.1
-----     -----          ---   ----      ---          ---       ---

20361        606.8     608.2          1.4    3.3      0.5            8       0.1
-----     -----          ---    ---      ---          ---       ---

20362        608.2     610.2            2    0.5      0.0            1       0.0
-----     -----          ---    ---      ---          ---       ---

20363        610.2     612.1          1.9    3.3      0.0            2       0.0
-----     -----          ---    ---      ---          ---       ---

20364        612.1     613.7          1.6    1.9      0.2            3       0.0
-----     -----          ---    ---      ---          ---       ---

20365        613.7     614.6          0.9   22.6      0.7           15       0.1
-----     -----          ---   ----      ---          ---       ---

20366        614.6     616.6            2    0.0      0.0            1       0.0
-----     -----          ---    ---      ---          ---       ---

20367        616.6     618.6            2    0.0      0.0            1       0.0
-----     -----          ---    ---      ---          ---       ---

20368        618.6     620.6            2    0.1      0.0            0       0.0
-----     -----          ---    ---      ---          ---       ---

20369        620.6     622.6            2    0.0      0.0            0       0.0
-----     -----          ---    ---      ---          ---       ---

20370        622.6     624.6            2    0.1      0.7           15       0.5
-----     -----          ---    ---      ---          ---       ---

20371        624.6     626.2          1.6    0.0      0.1            3       0.1
-----     -----          ---    ---      ---          ---       ---

20372        626.2     627.6          1.4    0.0      0.0            4       0.3
-----     -----          ---    ---      ---          ---       ---

20373        627.6     629.4          1.8    0.0      0.0           28       0.5
-----     -----          ---    ---      ---          ---       ---

20374        629.4     631.4            2    0.0      0.0           21       0.2
-----     -----          ---    ---      ---          ---       ---

20376        631.4     633.4            2    0.0      0.0           37       0.5
-----     -----          ---    ---      ---          ---       ---

20377        633.4     635.4            2    0.0      0.0           19       0.3
-----     -----          ---    ---      ---          ---       ---

20378        635.4     637.4            2    0.0      0.0            7       0.1
-----     -----          ---    ---      ---          ---       ---

20380        637.4     640.4            3    0.0      0.0            4       0.1
-----     -----          ---    ---      ---          ---       ---

20381        640.4     643.4            3    0.0      0.0            8       0.2
-----     -----          ---    ---      ---          ---       ---

20382        643.4     646.4            3    0.0      0.1           13       0.4
-----     -----          ---    ---      ---          ---       ---

20383        646.4     649.4            3    0.0      0.0           10       0.2
-----     -----          ---    ---      ---          ---       ---

20384        649.4     652.4            3    0.0      0.0            1       0.1
-----     -----          ---    ---      ---          ---       ---

20385        652.4     654.4            2    0.0      0.0            4       1.0
-----     -----          ---    ---      ---          ---       ---

20386        654.4     656.4            2    0.0      0.0            4       0.3
-----     -----          ---    ---      ---          ---       ---

SOURCE Hannan Metals Ltd.



View original content with multimedia:
http://www.newswire.ca/en/releases/archive/July2017/20/c8239.html

-0-                           07/20/2017
/For further information: www.hannanmetals.com, 1305 - 1090 West Georgia
St., Vancouver, BC, V6E 3V7, Mariana Bermudez, Corporate Secretary, +1 (604)
685 9316, info(at)hannanmetals.com/
(HAN.)

CO:  Hannan Metals Ltd.
ST:  British Columbia
IN:  MIN
SU:

-30-