Source	Marketwire
Date	07/20/2017
Time	04:00:19 AM

Company	 SAN MARCO RESOURCES INC.
Title	Chunibas Drill Program Expanded After Discovery of Large Intrusive Breccia 
System





    CDNX Symbol: SMN











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: San Marco Resources Inc.

TSX VENTURE SYMBOL: SMN

July 20, 2017

Chunibas Drill Program Expanded After Discovery of Large Intrusive Breccia 
System


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 20, 2017) - San Marco 
Resources Inc. (TSX VENTURE:SMN) ("San Marco" or "the Company") has increased 
the Chunibas HQ core drilling program from four to six holes following the 
discovery of an extensive, previously unknown, intrusive breccia associated 
with mineralization encountered during the current drill phase. Management 
considers this to be a very important discovery and is working on multiple 
fronts to ascertain how to best explore it and determine its economic 
significance.

Bob Willis, San Marcos CEO stated,

"It is very early days, but we don't want to understate the potential 
significance of this discovery. It's too early to classify this new discovery 
though it has affinities to both breccia-hosted and intrusive-hosted systems, 
which are host to some large gold and gold-copper discoveries worldwide made in 
the recent past.

"Our core drilling, the first on the property, allowed us to log long 
contiguous sections of rock unaffected by surface weathering, something 
unavailable to past workers. This led to the discovery of the new intrusive 
breccia in all holes drilled so far, extending from the top to the bottom of 
the holes in most cases. Subsequent prospecting confirmed the breccia extends 
at least 200 metres west and 300 metres south of the Hole 1 and Hole 4 areas 
and it remains wide open. The area will be remapped to determine the surface 
extent of the breccia but early indications from our widely spaced drill holes 
is that it is fairly large. While we need to understand zoning or other 
possible controls on gold emplacement, we are highly encouraged that all core 
containing breccia assayed to date exhibits at least anomalous (greater than 50 
ppb) gold values. It will be exciting times as we work to define the magnitude 
of the system, refine and better understand the geological model and locate 
zones of mineralization with economic interest. San Marco is taking this 
discovery very seriously and shareholders should expect more reporting on it in 
coming weeks."

As indicated in the Company's News Release dated May 31, 2017, the primary 
objective of the current drill program was to confirm the presence of higher 
grade mineralization within narrow (1 - 2 metres wide) shear zones, and 
possibly low-grade mineralization in the flanking wall rock. Exploration by 
previous property owners consisted exclusively of surface work and RC drilling. 
They concluded the Chunibas system was of the low sulphidation, epithermal type 
with mineralized shears / veins hosted in a monzonite intrusion. The San Marco 
core-drilling program was designed to test three separate areas of old workings 
and presumed shearing along approximately 1,000 metres of north-south strike.

Upon commencement of drilling and logging of the core, it immediately became 
apparent that the dominant rock type in the drill core is a multi-lithic 
(breccia fragments of different compositions) highly altered, intrusive 
breccia, and NOT monzonite. Two holes (drilled to the east at - 60 degrees) 
around the southernmost workings intersected breccia from the collars to total 
depth (154 metres and 201 metres respectively). Additional holes completed to 
date have intersected breccia as well. Drilling has now been concluded, with 
approximately 860 metres completed in the six core holes, see map Chunibas 
Geology and Drill hole location July 20-17(i), for locations of drill collars 
from the current program as well as historic drilling. Following are the 
results of three holes, one each in the three areas of old workings over 1000 
metres of strike. Results of remaining holes will be released when all assays 
are received and analyzed.

Highlights are:

Hole CHD -01 39.0 metres of 0.67 grams per tonne gold

- Including 20.0 metres of 1.05 grams per tonne gold, 2.15 metres of 1.97 grams 
per tonne gold and 1.0 metre of 4.55 grams per tonne gold

Hole CHD - 02 21.0 metres of 0.58 grams per tonne gold,

- Including 1 metre of 6.78 grams per tonne gold, 1.20 metres of 2.42 grams per 
tonne gold at the bottom of the hole (i.e. hole ended in mineralization)

Hole CHD - 03 3.3 metres of 5.05 grams per tonne gold. Hole ended in 
mineralization with the final 2.2 metres grading 1.05 g/t gold (a separate 
interval)

Note: Hole CHD-03 intersected primarily diorite host rock rather than breccia, 
thus gold mineralization is primarily restricted to the higher-grade shear zone.

Early interpretation of these results indicates discovery of a breccia body, 
which has a significant footprint horizontally and vertically. Although breccia 
was previously identified in isolated outcrops, it was not systematically 
mapped nor recognized as an important host rock to mineralization. Holes CHD 01 
and CHD 02 also exhibit anomalous gold (0.12 - 0.14 g/t over 30 -35 metres, 
higher up in the drill hole) in core, which does not appear to contain 
structures, suggesting gold may be disseminated in the breccia. All gold 
intercepts so far received are consistent with historical Reverse Circulation 
drill hole assay grades. The current drill program confirms gold mineralization 
exists from surface to approximately 75 metres below surface, and is open to 
depth, and in all directions laterally.

Based on review of the drill core and potential size implications of the 
breccia body, the next exploration steps will include;

/T/

--  Receipt of and plotting / compilation of all drill holes assays.
--  Merger of historic data together with 2017 results to generate 3D
Leapfrog model to create a solid basis for additional exploration.
--  Remapping of the surface geology, with particular attention to the
distribution and types of breccia.
--  Continue petrographic studies with emphasis on host rock textures,
character of hydrothermal alteration, and the distribution and controls
to gold mineralization
--  Remodelling of all surface geochemical data to investigate potential
pathfinder elements better suited to delineate the footprint of the
breccias and identify / vector towards areas with higher grade
mineralization.

/T/

Follow up drilling is expected to be commenced once targeting based on the new 
model is completed. Please see table below for complete listing of significant 
assays from holes reported today.

/T/


----------------------------------------------------------------------------
DH           From (m)     To (m)       Interval (m) Au (g/t)
----------------------------------------------------------------------------
CHD-01       88.00        127.0        39.0         0.67
----------------------------------------------------------------------------
Including    93.0         113.0        20.0         1.05
----------------------------------------------------------------------------
And          93.85        96.0         2.15         1.97
----------------------------------------------------------------------------
And          111.0        112.0        1.0          4.55
----------------------------------------------------------------------------
CHD-02       45.0         66.0         21.0         0.58
----------------------------------------------------------------------------
Including    51.0         52.0         1.0          1.01
----------------------------------------------------------------------------
And          60.0         61.0         1.0          6.78
----------------------------------------------------------------------------
And          109.0        110.2        1.2          2.42 (last sample at the
end of the hole)
----------------------------------------------------------------------------
CHD-03       30.0         43.3         3.3          5.08
----------------------------------------------------------------------------
Including    40.0         42.0         2.0          6.74
----------------------------------------------------------------------------
And          118.0        120.2        2.2          1.05 (last sample at the
end of the hole)
----------------------------------------------------------------------------
CHD-04       -            -            -            Assays Pending
----------------------------------------------------------------------------
CHD-05       -            -            -            Assays Pending
----------------------------------------------------------------------------
CHD-06       -            -            -            Assays Pending
----------------------------------------------------------------------------
All holes were drilled at - 60 degrees inclination and azimuths of CHD-01:
90 degrees; CHD-02: 305 degrees; and CHD-03: 90 degrees. True widths are
presently unknown, as the discovery holes do not have enough information yet
to identify where the holes are located in the mineralized system.

/T/

Assaying for this drill program is being done by ALS Chemex located in 
Vancouver, B.C. Sample preparation is done at the Chemex lab in Hermosillo, 
Mexico, pulps are then shipped to Vancouver for analysis. Prepared samples are 
analyzed for gold by the Au - ICP21 method and multi-elements by ME - MS61, 
preparation 31B.

Drill core was sawn in half by a gas-powered diamond saw, then photographed and 
logged. One half of the core is sent for assay analysis and the other retained 
at the Company's secure exploration facility in Sahuripa, Mexico.

The QA/QC program consists of submission of duplicate samples and insertion of 
certified reference material and blanks inserted at regular intervals. These 
are inserted every 10 samples, or 10% of the total. Samples are bagged and 
tagged at the Company's core facility in Sahuripa, Mexico and held in a secure 
environment, until picked up by ground transport of ALS Chemex.

About San Marco

San Marco Resources Inc. is a Canadian mineral exploration company with a 
portfolio of promising projects in mining-friendly Mexico, including the 
Chunibas, Mariana and 1068 Projects in Sonora State.

San Marco actively pursues strategic project generation program focused on 
high-caliber, low acquisition cost opportunities in the North-western Mexico. 
The Company has a committed management team with extensive experience in Mexico 
and a proven track record of building shareholder value.

San Marco currently has 56,051,832 issued and outstanding shares.

On behalf of the Board of Directors,

Robert Willis, P. Eng.
President & CEO

National Instrument 43-101 Disclosure

This news release has been approved by San Marco's CEO, Robert D. Willis, P. 
Eng. a "Qualified Person" as defined in National Instrument 43-101, Standards 
of Disclosure for Mineral Projects of the Canadian Securities Administrators. 
He has verified the data disclosed, including sampling, analytical and test 
data, underlying such technical information by reviewing the assay reports 
provided to San Marco by its independent testing laboratory.

San Marco has implemented quality assurance ("QA") and quality control ("QC") 
programs to ensure sampling and analysis of all exploration work is conducted 
in accordance with the best possible practices. All sampling programs are 
carried out in a careful and diligent manner using scientifically established 
sampling practices designed and tested to ensure that the results are 
representative and reliable. Quality control programs appropriate to the type 
of sample and the mineralization are implemented, including such measures as 
external blanks, standards and duplicate samples. The security of samples from 
sample acquisition to analysis is a vital component of the sampling process. 
Procedures include the use of secure core logging, sampling, storage and 
preparation facilities as appropriate and the prompt, secure and direct 
shipping of samples to the laboratories. Appropriate sample security procedures 
are employed given the geographic and topographic conditions and the logistics 
created by the site location.

Forward-Looking Information

Information set forth in this document may include forward-looking statements. 
While these statements reflect management's current plans, projections and 
intents, by their nature, forward-looking statements are subject to numerous 
risks and uncertainties, some of which are beyond the control of San Marco. 
Readers are cautioned that the assumptions used in the preparation of such 
information, although considered reasonable at the time of preparation, may 
prove to be imprecise and, as such, undue reliance should not be placed on 
these forward-looking statements. San Marco's actual results, programs, 
activities and financial position could differ materially from those expressed 
in or implied by these forward-looking statements.

Neither the TSX Venture Exchange nor the Investment Industry Regulatory 
Organization of Canada accepts responsibility for the adequacy or accuracy of 
this release.

- 30 -

CONTACT INFO:

Nancy Curry
info@sanmarcocorp.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=596565954