Source	MARKET NEWS
Date	07/24/2017
Time	05:59:08 AM

Company	 Endurance Gold Corporation
Title	Identifies 
Four Chargeability Anomalies on the E





    CDNX Symbol: EDG











Press Release





ENDURANCE GOLD CORP ("EDG-V")
- Identifies Four Chargeability Anomalies on the Elephant
- Property, Alaska; All Four Gold Targets Prioritized for Drilling

Endurance Gold Corporation ("Endurance") is pleased to report the
results of the induced polarization ("IP") and ground magnetic surveys
that were undertaken on the Elephant Property located 76 miles (123
kilometres ("km")) northwest of Fairbanks within the
Rampart-Eureka-Manley Hot Springs placer gold mining district near
Eureka, Alaska.

A total of about 43 line-km of IP and 39 line-km of magnetic
surveying were completed during the 2017 IP program. The surveys
successfully identified four prioritized resistivity and chargeability
anomalies that warrant drill testing. Plan maps and sections showing
the four IP targets are available at www.endurancegold.com.

The 2017 resistivity survey is dominated by a linear east-west
trending low that entirely bisects the survey area. This dominant
anomaly is readily discernible on the 5th level resistivity contour
plan and is interpreted to represent the resistivity expression of the
Elephant Mountain Fault traversing the intrusive. In addition, at least
three less dominant linear northwesterly trending resistivity lows
intersect the Elephant Mountain Fault complex. Two of these
northwesterly trending resistivity lows are coincident with anomalous
gold-in-soil, including the high priority South Zone soil anomaly.

Adjacent and extending northwards from the Elephant Mountain Fault
in the northern part of the grid is a two-lobed well-defined
chargeability feature estimated at 1,200 x 600 metres ("m") in size
associated with pervasively sericite altered granodiorite and 1 to 3%
disseminated sulphides, quartz veinlets and sulphide-quartz veinlets
with associated gold. This chargeability anomaly is directly associated
with a km-scale, greater than 100 parts per billion ("ppb")
gold-in-soil anomaly, and was partially tested with Endurance's 2016
drill hole EL 16-13, which returned 0.40 grams per tonne (gpt) gold
over 147.1 m including 0.63 gpt gold over 48.2 m.

For targeting purposes this chargeability feature has been broken
into two separate lobes defined by east-west oriented areas of higher
chargeability. These targets are the North Zone Target and the Pump
Zone Target. A portion of the North Zone Target was tested by the
Company's 2016 drill hole and partially tested with drill holes by
previous operators in 1992 and 2000. Large portions of the stronger
chargeability features associated with the North Zone Target remain
untested by drilling. The Pump Zone Target is newly recognized and
remains untested by either trenching or drilling.

South of the Elephant Mountain Fault, one of the northwesterly
trending narrow resistivity low features is contained within a 1,000 x
250 m gold-in-soil anomaly, where values exceeded 100 ppb, known as the
South Zone Target. This resistivity anomaly estimated to be at least
350 m in strike length is associated with the South Zone discovery hole
EL 16-14A which returned 4.09 gpt gold over 4.6 m hosted in an altered
shear zone with bands of massive arsenopyrite and stibnite. Adjacent
and on the east side of this resistivity feature and discovery drill
hole is a near surface chargeability feature with a strike length of
between 100 and 200 m. This South Zone chargeability feature remains
untested by drilling.

Elevated chargeabilities were noted on the largest separation
readings on the north side and within the Elephant Mountain fault
between the South Zone and combined North Zone-Pump Targets. This area
also has some anomalous gold-in-soil and is referred to as the Central
Zone Target. This target expresses itself at depth because it is
interpreted to be beneath an area of deeper oxidation associated with
the fault.

A magnetic survey confirmed low magnetic susceptibility associated
with the intrusive and higher magnetic susceptibility associated with
the hornfels altered sediments. The North Zone and the Pump Zone
Targets are associated with the lowest magnetic susceptibility areas of
the intrusive complex while the South Zone Target is associated with
the border phases of the intrusive complex which have been observed to
contain xenoliths of hornfels that increase the relative magnetic
susceptibility within the South Zone Target area.

Peter Walcott and Associates was engaged to complete the 2017 time
domain pole-dipole IP and magnetics surveys. The 2017 surveys were
completed at 50 m dipole spacing on 200 m spaced lines for the entire
approximate five (5) square km grid. In the South Zone Target, tighter
25 m dipole spacing was completed over several of the 200 m spaced
lines as well as five additional shorter 50 m spaced lines on which
only 25 m dipole spacing was completed.

In 2004, Aurora Geosciences completed a combined 18.75 line-km IP
and 36.75 line-km magnetics surveys on the Elephant Property. The 2004
IP survey area (at 25 m dipole spacing) is located southwest and west
of the 2017 IP and mag surveys. Evaluation of the Aurora IP survey data
has identified a chargeability anomaly that represents a western
extension and expansion of the Pump Zone Target identified in the 2017
survey. The results and data from an IP survey completed by Placer Dome
Inc. in 1992 was not available to the Company.

Next Steps - The size of the North Zone and Pump Zone
chargeability targets combined with the associated wide low-grade gold
intersections and gold-in-soil anomalies is evidence of an exploration
potential for discovery of a large-tonnage low-grade gold resource at
the North Zone, Pump Zone, and Central Zone Targets. Recommended drill
testing of these targets north of the Elephant Mountain Fault will
focus on discovery of the feeder zones and/or oxidized lower grade gold
zones which have potential for higher grades or lower grade
mineralization with favourable recovery characteristics. At the South
Zone Target, south of the Elephant Mountain Fault, recommended drill
testing will focus on expanding on the South Zone Discovery drill hole
and identifying the source of the near surface chargeability anomaly
which may represent a currently unrecognized sulphide bearing shear
zone.

The Elephant Property is the anchor property of the three
properties that form the Elephant Mountain Project which can be easily
accessed by the all-weather Elliott Highway. The Elephant Mountain
Project includes at least six (6) km-scale gold targets associated with
a Cretaceous aged intrusive complex and associated alteration that
extends over a strike length of about twelve (12) km. Five (5) of these
km-scale gold targets are associated with gold-in-soil (greater than
100 ppb gold with peak values up to 1,880 ppb gold) and rock grab
samples up to 11.98 gpt gold. A map showing the location of the
properties and targets is also available at www.endurancegold.com. For
a descriptive summary of the gold targets on the Trout and Wolverine
Properties, please refer to the Company's news release dated April 3,
2017.

About Endurance

Endurance Gold Corporation is a company focused on the
acquisition, exploration and development of highly prospective North
American mineral properties with the potential to develop world-class
deposits. The company also owns a significant shareholding in Inventus
Mining Inc.(IVS-TSXV) which controls the entire Pardo paleoplacer gold
district near Sudbury, Ontario and owns shares in GFG Resources Inc.
(GFG-TSXV) which controls the entire Rattlesnake Hills gold district in
Wyoming.

ENDURANCE GOLD CORPORATION
Robert T. Boyd

FOR FURTHER INFORMATION, PLEASE CONTACT
Endurance Gold Corporation
(604) 682-2707,
info@endurancegold.com
www.endurancegold.com

Robert T. Boyd, P.Geo. is a qualified person as defined in
National Instrument 43-101 and supervised the compilation of the
information forming the basis for this release. The drill intersections
in this release may not represent the true width of the intersection.
The split drill core samples from the 2016 drill program were analyzed
at ALS Minerals using Au-AA23, Au-GRA21 ()10 g/t), and ME-MS61L.
Confirmation standards were inserted within sample shipments by
Endurance as well as ALS Minerals inserted standards with each shipment
analyzed. Bedrock grab samples mentioned in this release are selective
by nature and are unlikely to represent average grades within the
bedrock when drilled.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release. This news release may contain forward looking statements
based on assumptions and judgments of management regarding future
events or results that may prove to be inaccurate as a result of
factors beyond its control, and actual results may differ materially
from the expected results

ENDURANCE GOLD CORP
Tel: (604) 682-2707
Fax: (604) 681-0902
______________________________________
_______________________________________________
TSX Venture closing price for EDG-V
Date: 2017/07/21
Closing Price: 0.06
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1720400011TS11720400828-05571120170724