Source	CANADA NEWSWIRE
Date	07/24/2017
Time	06:03:47 AM

Company	 Mirasol Resources Ltd.
Title	Mirasol Resources Defines Three Porphyry Copper Targets at 100% Owned
Rubi Project, Northern Chile





    CDNX Symbol: MRZ











Press Release




" BC-Mirasol-Rubi-Project   07-24 1573
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Mirasol Resources Defines Three Porphyry Copper Targets at 100% Owned
Rubi Project, Northern Chile@

VANCOUVER, July 24, 2017 /CNW/ - Mirasol Resources Ltd. (TSX-V: MRZ,
OTCPK: MRZLF "Mirasol") is pleased to announce that it has defined three
large-scale porphyry Cu-Mo-Au targets, and also expanded its claim holdings,
at its 100% owned Rubi Project ("Rubi") situated adjacent to the giant El
Salvador copper mining district in northern Chile.
Rubi (Figure 1) lies at relatively low elevation within 20 km of El
Salvador and Portrerillos porphyry Cu-Mo-Au mines, with highly favourable
infrastructure advantages such as year-round access, adjacent townships with a
trained mining workforce, nearby roads, power, water grid and an operating
mill and smelter.
Rubi has a prospective geological setting centered on structural
intersections with the Domeyko Fault System, a through-going regional-scale
structure and the Ojos del Salado trans-orogen structure, interpreted to have
influenced the emplacement of the near-by giant El Salvador and Potrerillos
Cu-Mo-Au deposits.
Mirasol has systematically consolidated claims holdings at Rubi over the
past 12 months and has expanded the claim area to a total of nearly 26,000 ha.
Mirasol recently completed field evaluation and targeting programs at
Rubi identifying three large-scale Cu-Mo-Au targets at the Lithocap, Zafiro,
and Portezuelo prospects (Figure 1). The targets were defined by integrated
analysis, including re-logging of drill holes and the re-interpretation of
geophysics and geochemistry from previous Joint Venture (JV) partner
exploration at Rubi. This was combined with recent Mirasol geological mapping,
rock chip sampling and target vector modelling from field-based measurements
of alteration minerology.
"The company has rapidly built a portfolio of quality copper targets at
Rubi and at its recently announced Odin project located 35 km north of BHP's
Escondida Mine. These and other recently staked copper projects strategically
position Mirasol in the premier copper belt of northern Chile." stated Stephen
Nano the company's CEO and President.
Lithocap
The Rubi Lithocap ("Lithocap") target (Figure 2) covers a 3.5 km by 2.0
km area centred on a large, deeply weathered, advanced argillic alteration
zone, surrounded by thin gravel cover. Geochemically barren Lithocap
alteration zones of the type seen at Rubi can form above or adjacent to large
porphyry copper deposits.
At Lithocap, previous explorers have drilled peripheral to, but not
beneath or adjacent to the post-mineral gravel covered western edge of the
anomaly. New Mirasol mapping and re-logging of previous drill holes has
defined veining and brecciation with anomalous Cu and Mo mineralization and
alteration patterns that vector toward potentially concealed porphyry
mineralization to the north and north-west of the previous drill holes. The
southern edge of Lithocap was "clipped" by a previous JV partner´s IP
geophysical survey, which identified a large open-ended chargeability anomaly
extending from 200 m to more than 400 m depth beneath the cap.
This pattern suggests the presence of a deep weathering profile overlying
a buried source of the chargeability anomaly, which may indicate the presence
of sulphide(s) in the unoxidized basement rocks. This type of deep weathering
in porphyry environments in northern Chile is often conducive for the
development of supergene enriched Cu mineralization as at the nearby El
Salvador mining district.
Zafiro
The Zafiro prospect (Figure 3) features a 2.8 km by 2.2 km gravel covered
area characterized by a subtle circular magnetic high surrounded by an
incomplete, doughnut-shaped magnetic low. This magnetic signature may be
indicative of a large gravel-covered intrusive with an alteration halo. The
gravel cover in this area ranges from approximately 25 m to more than 200 m in
thickness concealing the central target area. However, a large canyon 1 km to
the north of the target cuts through the gravel profile exposing the basement
rock. Mirasol's stream sediment sampling of gullies that traverse this area
have returned widespread strongly anomalous Cu up to 1,030 ppm (0.1%),
suggesting either an "exotic" source of copper in the gravels and / or a
primary porphyry source for the Cu in the gravel-covered basement of the
Zafiro prospect.
Reconnaissance mapping of the basement rocks in the area of the stream
sediment anomalies has identified pervasive propylitic and advanced argillic
alteration and zones of breccia and quartz-carbonate veins and stock-working
that have returned strongly anomalous Cu-Mo-Pb-Zn (Au-Ag-Sb) rock chip assays.
These types of alteration and mineralization may be found in the halo to
porphyry copper deposits and suggest a vector to the south under gravel cover,
which supports the concept for a concealed porphyry in the area of the Zafiro
prospect.
High grade "exotic" copper or a supergene enriched porphyry are both
attractive exploration targets at the Zafiro prospect. Significant ore bodies
of these types of mineralization occur at the nearby El Salvador mining
district.
Portezuelo
At the Portezuelo prospect (Figure 4), the 4.5 km by 2.7 km target area
is characterized by relatively thin gravel cover and intermittent outcropping.
Analysis of Mirasol and previous JV partner data shows widespread anomalous Cu
and Mo in soils, spatially associated with an oval-shaped magnetic feature
that may represent a partially gravel-covered intrusive complex. Strongly
oxidized, porphyry-like stock-works and sheeted veining with anomalous Mo and
Cu, is locally exposed in road cuts and has been recently identified by
Mirasol outcropping in creek beds in the north of the target area.
A limited number of reverse circulation (RC) holes from prior operators
were drilled into the southern part of the Portezuelo target prior to Mirasol
staking these claims. The holes are estimated to have been drilled in the late
1980's to early 90's. The assays for these drill holes are not available to
Mirasol, however sampling of residual RC chips on the drill pads returned
anomalous Mo and Cu assays. Reconnaissance mapping and sampling to the
southwest of the target has identified a multi-kilometre long zone of Au-Ag
base metal veinlets that may represent a style of polymetallic mineralization
commonly developed in the halo surrounding a porphyry centre. No systematic
geological mapping, rock chip sampling or electrical geophysics has yet been
undertaken at Portezuelo by the Company or its previous JV partners. Mirasol
believes this large prospect warrants detailed exploration to define drill
targets.
Mr. Nano added: "Mirasol's Rubi and Odin projects have received strong
interest and we are actively seeking JV partners to drill test and develop
these projects".
Stephen Nano, Vice President of Exploration for the Company, a Qualified
Person under NI 43-101, is responsible for the technical content of this
release
Information on the Inca Trail:
Remnants of the Inca Trail are recorded over a 30,000 sq km area of
western South America. A strand of the trail network passes in proximity to
the El Salvador mine and the Inca de Oro mine development near the Rubi
Project. A 7.6 km segment of the trail, passes through the Rubi Project.
Where preserved at Rubi the trail in seen as 2 to 3 m wide earth path.
The exploration targets identified by Mirasol in this news release are
separated from the Trail. Mirasol and its previous Joint Venture partner
engaged independent Archaeological consultants to survey the Trail marking its
location and to recommend preservation protocols to safeguard the Trail.
In 2014 Mirasol's joint venture partner drilled tested a series of
targets at the Rubi project operating under the Chilean exploration drilling
permitting call a "carta de pertinencia". As part of the permitting process
the archaeological report was presented to the Chilean environmental and
cultural authorities who ratified the drill program and the procedures to
preserve the Trail.
Quality Assurance/Quality Control of the Rubi exploration program:
All exploration on the project was supervised by Mirasol CEO Stephen C.
Nano, who is the Qualified Person under NI 43-101. Mirasol applies industry
standard exploration sampling methodologies and techniques. All geochemical
rock and drill samples are collected under the supervision of the company's
geologists in accordance with industry practice. Geochemical assays are
obtained and reported under a quality assurance and quality control (QA/QC)
program. Samples are dispatched to an ISO 9001:2008 accredited laboratory in
Chile for analysis. Assay results from surface rock, channel, trench, and
drill core samples may be higher, lower or similar to results obtained from
surface samples due to surficial oxidation and enrichment processes or due to
natural geological grade variations in the primary mineralization.
Forward Looking Statements: The information in this news release contains
forward looking statements that are subject to a number of known and unknown
risks, uncertainties and other factors that may cause actual results to differ
materially from those anticipated in our forward-looking statements. Factors
that could cause such differences include: changes in world commodity markets,
equity markets, costs and supply of materials relevant to the mining industry,
change in government and changes to regulations affecting the mining industry.
Forward-looking statements in this release include statements regarding future
exploration programs, operation plans, geological interpretations, mineral
tenure issues and mineral recovery processes. Although we believe the
expectations reflected in our forward-looking statements are reasonable,
results may vary, and we cannot guarantee future results, levels of activity,
performance or achievements. Mirasol disclaims any obligations to update or
revise any forward-looking statements whether as a result of new information,
future events or otherwise, except as may be required by applicable law.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Mirasol Resources Ltd.



View original content:
http://www.newswire.ca/en/releases/archive/July2017/24/c1902.html

-0-                           07/24/2017
/For further information: Stephen Nano, President and CEO, or Jonathan
Rosset, Manager of Corporate Development, Tel: +1 (604) 602-9989, Email:
contact(at)mirasolresources.com, Website: www.mirasolresources.com/
/Web Site: http://www.mirasolresources.com /
(MRZ. MRZLF)

CO:  Mirasol Resources Ltd.
ST:  British Columbia
IN:  MNG
SU:

-30-