Source	Marketwire
Date	07/25/2017
Time	01:32:33 PM

Company	 ANFIELD GOLD CORP.
Title	Anfield Gold Announces Positive Feasibility Results at its Coringa Project





    CDNX Symbol: ANF











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Anfield Gold Corp.

TSX VENTURE SYMBOL: ANF

July 25, 2017

Anfield Gold Announces Positive Feasibility Results at its Coringa Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 25, 2017) - Anfield Gold Corp. 
("Anfield" or the "Company") (TSX VENTURE:ANF) announces the results of the 
Feasibility Study (the "Study"), prepared in accordance with National 
Instrument 43-101 Standards of Disclosure for Mineral Projects ("NI 43-101"), 
for its 100%-owned Coringa Project ("Coringa" or the "Project"). The Study was 
compiled by MTB Project Management Professionals Inc. ("MTB") and demonstrates 
that Coringa has the potential to be an economic, high-grade underground gold 
mine.

Marshall Koval, Chairman and CEO, commented: "We are pleased to deliver a 
report that confirms strong economics at Coringa and believe that the Project 
has the potential to add substantial value to shareholders and the surrounding 
community over the coming years. Once Anfield receives the required permits 
from the Brazilian authorities, our experienced operating team led by Andrew 
Storrie can commence re-constructing the same plant that he and his team 
operated while working at the nearby Andorinhas mine."

Anfield will continue to explore for areas where value can be added to the 
Project. There are approximately 40,000 gold ounces of the estimated Inferred 
mineral resource, which are not included in the Study's mine plan,(1) that are 
adjacent to areas mined as part of the Study. In addition, the Company controls 
a twenty kilometre area in the district with delineated gold soil anomalies, of 
which, the drill-defined mineral resource strike length is approximately two 
kilometres.

/T/

1.  Inferred mineral resources are considered too speculative geologically
to have the economic considerations applied to them that would enable
them to be categorized as mineral reserves. There is no certainty that
any or all mineral resources can be upgraded to mineral reserves through
continued exploration.

/T/

Feasibility Study Summary

The Study was initiated in June 2016 by MTB, with contribution by several 
consultants that have extensive expertise in their respective fields. Further 
details on the contributors can be found in the Qualified Persons section of 
this news release.

All currencies are in United States dollars unless otherwise specified. Base 
case economics are based on a gold price of $1,250 per ounce ("oz"), silver 
price of $18.00 per oz and an exchange rate of 3.2 (US$:R$). The effective date 
of the Study is July 1, 2017 and it incorporates all expenditures prior to that 
date. A technical report relating to the Study will be filed on SEDAR within 45 
days of this news release.

The Study and Project highlights include the following estimates:

/T/

--  Gold production of approximately 32 koz per year averaged over a 4.8
year mine life
--  Average life of mine process fully-diluted gold grade of 6.5 grams per
tonne ("g/t")
--  Post-tax internal rate of return of 30.8%
--  Post-tax net present value of $31.0 million at a 5% discount rate
--  Initial capital costs of $28.8 million
--  Average net cash operating costs of $585/oz and all-in sustaining costs
of $783/oz
--  Probable mineral reserves of 161 koz of gold and 324 koz of silver
--  23% of engineering for the process plant and related infrastructure has
been completed and 100% of engineering for the tailings storage facility
has been completed

/T/

Table 1: Summary of Coringa Economic Results by Gold Price

/T/

----------------------------------------------------------------------------
Gold Price (per oz)                Units     $1,125     $1,250     $1,375
----------------------------------------------------------------------------
Pre-Tax NPV (5%)                    $M        $17.6      $34.0      $50.3
----------------------------------------------------------------------------
Pre-Tax IRR                          %        19.6%      32.9%      45.5%
----------------------------------------------------------------------------
Post-Tax NPV (5%)                   $M        $16.0      $31.0      $45.2
----------------------------------------------------------------------------
Post-Tax IRR                         %        18.4%      30.8%      41.7%
----------------------------------------------------------------------------

/T/

Table 2: Coringa Life of Mine Capital Expenditure Estimate Breakdown

/T/

----------------------------------------------------------------------------
Initial Capital ($M)
----------------------------------------------------------------------------
Process & Infrastructure                                  $13.3
----------------------------------------------------------------------------
Pre-production Mine Development                           $3.5
----------------------------------------------------------------------------
Equipment                                                 $1.9
----------------------------------------------------------------------------
Direct and Indirect Owner Costs                           $8.1
----------------------------------------------------------------------------
Contingency (7.5%)                                        $2.0
----------------------------------------------------------------------------
Total Initial Capital (excluding working                  $28.8
capital)
----------------------------------------------------------------------------
Working Capital                                           $1.5
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Sustaining Capital ($M)
----------------------------------------------------------------------------
Life of Mine Sustaining Capital                          $28.7M
----------------------------------------------------------------------------
Average Annual Life of Mine Sustaining                    $5.9M
Capital
----------------------------------------------------------------------------

/T/

Table 3: Summary of Coringa Operating Cost Estimates and Cash Costs

/T/

----------------------------------------------------------------------------
Average Life-of-Mine Operating Costs per Tonne Milled
----------------------------------------------------------------------------
Mining Costs                                             $41.68
----------------------------------------------------------------------------
Processing Costs                                         $33.51
----------------------------------------------------------------------------
General, Administrative and Site Costs                   $33.14
----------------------------------------------------------------------------
Total Operating Costs                                    $108.33
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Average Life-of-Mine Cash Costs per Ounce
----------------------------------------------------------------------------
Operating Costs                                           $558
----------------------------------------------------------------------------
Silver By-Product Credits                                 ($23)
----------------------------------------------------------------------------
Sandstorm 2.5% NSR Royalty                                 $31
----------------------------------------------------------------------------
Government 1.5% NSR Royalty (1)                            $19
----------------------------------------------------------------------------
C1 Cash Costs Net of By-products (2)                      $585
----------------------------------------------------------------------------
Sustaining Capital and Closure Costs                      $197
----------------------------------------------------------------------------
All-in Sustaining Cash Cost (3)                           $783
----------------------------------------------------------------------------

/T/

(1): Includes 1.0% NSR royalty to the Brazilian government and 0.5% NSR royalty 
payment for surface rights
(2): (Refining Costs + Insurance + Transport Costs + Third Party Royalties + 
Operating Costs) / Payable Au oz
(3): (Refining Costs + Insurance + Transport Costs + Third Party Royalties + 
Operating Costs + Sustaining and Closure Capital Costs) / Payable Au oz

Coringa Estimated Mineral Reserves and Resources

The estimated mineral reserves for Coringa are based on the conversion of 
Indicated mineral resources to Probable mineral reserves based on the Study's 
estimated mine plan. The total fully-diluted mineral reserves for the Coringa 
Project are shown in Table 4.

Table 4: Coringa Estimated Mineral Reserves and Resources

/T/

----------------------------------------------------------------------------
Classification                                         Contained   Cut-off
Tonnes Au Grade Ag Grade Contained    Silver     Grade
(000's)   (g/t)    (g/t)  Gold (koz)   (koz)     (g/t Au)
----------------------------------------------------------------------------
Serra Probable      498      6.0     12.8       97        204       2.50
Reserves
----------------------------------------------------------------------------
Meio Probable       196      7.4     14.6       46         92       2.38
Reserves
----------------------------------------------------------------------------
Galena Probable      74      7.1     11.2       17         27       2.50
Reserves
----------------------------------------------------------------------------
Total Probable      769      6.5     13.1       161       324
Reserves
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Total Indicated     726      8.4     17.0       195       396       2.00
Resource
----------------------------------------------------------------------------
Total Inferred     1,301     4.3      5.1       181       215       2.00
Resource
----------------------------------------------------------------------------

/T/

General Note: Additional information, including with respect to the mineral 
resource estimate, metallurgy, data verification and quality control measures, 
can be found in Anfield's technical report titled "Coringa Gold Project, 
Brazil, NI 43-101 Technical Report" with an effective date of May 3, 2017, 
which is filed on SEDAR at www.sedar.com. Totals in the above table may not add 
due to rounding.
Resource Notes: Minimum thickness is 0.8 m horizontal. Effective date of May 3, 
2017. Indicated mineral resources are inclusive of mineral reserves.
Reserve Notes: Effective date of July 1, 2017. Grades are reported on a 
fully-diluted basis.

Mining

The Study contemplates underground mining using a 100% owner operated equipment 
fleet, most of which was acquired from Troy Resources Limited's ("Troy 
Resources") Andorinhas mine and is on site. The three mining areas that make up 
the Project will use a shrink stoping method to extract ore. Coringa has been 
designed to deliver an average of 159 thousand tonnes per year (approximately 
460 tonnes per day) of mill feed. The Study contemplates a mine that will 
extract ore over a 4.8-year period with a delivered fully-diluted gold head 
grade of 6.5 g/t. Ore will be sourced from the Serra zone in years 1 to 4, the 
Meio zone in years 3 and 4 and the Galena zone in the final year of mining.

Metallurgy

Extensive feasibility level test work was completed by C.H. Plenge & CIA S.A. 
at its laboratory in Lima, Peru, using representative composites, that 
confirmed the material from Coringa is amenable to a conventional crush, grind, 
gravity concentration and carbon-in-leach flow sheet.

Test work results indicated that 40% to 50% of the gold will be recovered in a 
gravity concentrate. The overall estimated gold and silver recovery based on 
all ore types being processed during the life of mine is 95.4% and 61.2% 
respectively.

Infrastructure

The Coringa Project is located in Para State, approximately 70 kilometres 
south-east of the city of Novo Progresso. Access to the mine site from the city 
of Novo Progresso is by way of existing paved and gravel roads and the driving 
time from Novo Progresso to the Coringa camp is typically two hours.

Camp and Existing Infrastructure:

The existing Coringa camp has been upgraded with the addition of new 
accommodations for 212 permanent operations staff and a new cafeteria/kitchen 
facility to serve the expected workforce. Additionally, a leased and 
contract-catered camp for construction contractors, capable of accommodating 
128 individuals, has been retained at Coringa following the completion of 
infill drilling. The entire camp complex has been secured with perimeter 
fencing, perimeter lighting, and access control by security staff.

Power for the Camp and Mine:

Total Project electrical demand during full mine and process plant operation is 
3,039 kilowatts ("kW") (3,799 kilovolt amps "kva").

Initially, until commercial power can be designed, permitted, constructed, and 
supplied by CELPA (the regional utility), power supply for the plant, mine, and 
camp will be supplied by seven diesel generators (six operating and one on 
standby), each rated at 750 kva. Power will be distributed from a central power 
station at the plant site via an overhead 34.5 kilovolt transmission line to 
the mine portals and to the camp. Completion of the incoming CELPA transmission 
line is expected to take 12-18 months.
The camp load of 90 kW (112.5 kva) has been, and will continue to be, provided 
by a 310 kva generator with a 500 kva generator as back-up. Both camp 
generators were obtained from Troy Resources. The power supply for the camp 
will continue to be supplied by generators until the power station at the plant 
and the overhead transmission line from the plant to the camp have been 
completed.

Water Requirements for the Camp and Mine:

During production, the mine, plant, and camp water requirements will be 
approximately 140m3/day, 770m3/day, and 35m3/day, respectively. Additionally, 
approximately 40m3/day will be needed during the six-month dry season each year 
for dust control on site roads and in working areas to maintain safe and 
healthy working conditions.

Mine and plant water needs will be sourced from mine dewatering, which is 
modelled to significantly exceed the total requirements for both. Camp water 
needs are expected to be sourced from a well near the camp.

During the three to six months of plant startup when reclaimed water from the 
tailings storage facility is not yet available, water to the process plant will 
be sourced from behind a temporary coffer dam constructed within the tailings 
storage facility footprint to provide a dry area for construction of the 
tailings embankment.

Approximately 520m3/day of the 770m3/day required for plant operation will come 
from reclaim of process water from the tailings storage facility. Only 
250m3/day of raw water from mine dewatering will be required for plant makeup 
water.

Taxes

The Study incorporates assumptions about Anfield's ability to use income tax 
deductions made available under a government economic stimulus program to 
companies for industrial projects developed in the Amazon region of Brazil. The 
program reduces the Brazilian corporate income tax rate by 75%. The assumed 
income tax rate used in the financial model is 15.25%.

Construction Timeline and Permitting

The Study evaluates a construction period of ten months from start to 
completion. The Company continues to engage with the Secretaria de Estado de 
Meio Ambiente e Sustentabilidade ("SEMAS") to receive the required permits to 
commence construction and hope they will be forthcoming in the near-future.

Qualified Persons

The scientific and technical information contained in this news release 
pertaining to the Project has been reviewed and approved by the following 
Qualified Persons as defined by NI 43-101: Robert Sim, P.Geo. (Mineral 
Resource), of SIM Geological Inc.; Neil Prenn, P.Eng. and Edwin Peralta, P.Eng. 
(Mining), of Mine Development Associates; Robert Michel, SME Registered Member 
(Economic Analysis and Infrastructure) of Robert Michel Enterprises; Nelson 
King, SME Registered Member (Metallurgy and Process); Mark Smith, P.E. 
(Tailings Management Facility) of RRD International LLC and Larry Breckenridge, 
P.E. (Hydrology, Hydrogeology, Geochemistry, and Infrastructure) of Global 
Resource Engineering, Ltd. All of the Qualified Persons are independent of 
Anfield.

About Anfield Gold

Anfield Gold Corp. (TSX VENTURE:ANF) is a Vancouver, Canada based precious 
metal exploration and development company focused on the development of the 
Coringa Project located in Para State, Brazil. Anfield's strategic plan 
includes the acquisition of other gold projects with the goal of becoming a 
mid-tier gold mining company.

Further details are available on the Company's website at 
https://anfieldgold.com

Anfield Gold Corp.

Marshall Koval, Chairman & CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

Certain statements and information herein, including all statements that are 
not historical facts, contain forward-looking statements and forward-looking 
information within the meaning of applicable securities laws. Often, but not 
always, forward-looking statements can be identified by the use of words such 
as "plans", "will", "expected" or variations of such words. Forward looking 
statements or information in this press release include, but are not limited 
to, Anfield's strategic plan to acquire other gold projects with the goal of 
becoming a mid-tier gold mining company; the mineral resource and mineral 
reserve estimates for the Project; that the Project has strong economics; the 
internal rate of return of the Project; the annual production of the Project; 
the net present value of the Project; the life of mine of the Project; the 
capital costs, operating costs and other costs estimated for the Project; 
required infrastructure for the Project; how infrastructure for the Project 
will be sourced; the timing required to complete construction at the Project; 
and that construction of the Project will occur at all. In making the 
forward-looking statements in this release, Anfield has applied certain factors 
and assumptions that are based on information currently available to Anfield as 
well as Anfield's current beliefs and assumptions (including Anfield's belief 
in the results of the Study). Although Anfield considers these beliefs and 
assumptions to be reasonable based on information currently available to it, 
they may prove to be incorrect, and the forward-looking statements in this 
release are subject to numerous risks, uncertainties and other factors that may 
cause future results to differ materially from those expressed or implied in 
such forward-looking statements.
Such risk factors include, among others, actual ore mined varying from 
estimates of grade, tonnage, dilution and metallurgical and other 
characteristics; the inherent uncertainty of production and cost estimates, and 
the potential for unexpected costs and expenses; risks associated with the 
estimation of mineral reserves and mineral resources, and the grade and 
continuity of mineral deposits; the timing of mining the three zones of the 
Project; the annual mill feed for the Project; gold recovery rates; power and 
water requirements for the Project; that mineral resources may never become 
mineral reserves and do not demonstrate economic viability, Anfield may not be 
able to achieve the base case during actual mining at the Project, risks 
associated with the business of Anfield, risks relating to exploration and 
potential development of the Company's projects; risks related to obtaining the 
permits and approvals necessary to develop and commission the Project on terms 
that are acceptable to Anfield; risks related to Anfield identifying suitable 
acquisition targets; business and economic conditions in the mining industry 
generally; the supply and demand for labour and other project inputs; prices 
for commodities to be produced and changes in commodity prices; changes in 
interest and currency exchange rates; risks relating to inaccurate geological 
and engineering assumptions (including with respect to the tonnage, grade and 
recoverability of mineral resources and mineral reserves); risks relating to 
unanticipated operational difficulties (including failure of plant, equipment 
or processes to operate in accordance with specifications or expectations, cost 
escalation, unavailability of materials and equipment, government action or 
delays in the receipt of government approvals, industrial disturbances or other 
job action, and unanticipated events related to health, safety and 
environmental matters); risks relating to adverse weather conditions; political 
risk and social unrest; changes in general economic conditions or conditions in 
the financial markets; and changes to business and economic conditions in the 
mining industry generally.
Forward-looking information and statements are in addition based on various 
estimates, forecasts and projections as well as expectations, beliefs and 
assumptions including, without limitation, the expectations and beliefs of 
management, the assumed long-term price of gold; that the Company can access 
financing and that the political environment where the Company operates will 
continue to support the development and operation of mining projects. Although 
Anfield has attempted to identify important factors that could cause actual 
results to differ materially from those contained in forward-looking 
information, there may be other factors that cause results not to be as 
anticipated, estimated or intended. There can be no assurance that such 
information will prove to be accurate, as actual results and future events 
could differ materially from those anticipated in such statements. Accordingly, 
readers should not place undue reliance on forward-looking information. Anfield 
does not undertake to update any forward-looking information, except in 
accordance with applicable securities laws.

- 30 -

CONTACT INFO:

Anfield Gold Corp.
Scott Hicks
+604  646-1884
Fax: +604  687-7041
https://anfieldgold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=596840529


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Anfield Gold Corp.

TSX VENTURE SYMBOL: ANF

July 25, 2017

Anfield Gold Announces Positive Feasibility Results at its Coringa Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 25, 2017) - Anfield Gold Corp. 
("Anfield" or the "Company") (TSX VENTURE:ANF) announces the results of the 
Feasibility Study (the "Study"), prepared in accordance with National 
Instrument 43-101 Standards of Disclosure for Mineral Projects ("NI 43-101"), 
for its 100%-owned Coringa Project ("Coringa" or the "Project"). The Study was 
compiled by MTB Project Management Professionals Inc. ("MTB") and demonstrates 
that Coringa has the potential to be an economic, high-grade underground gold 
mine.

Marshall Koval, Chairman and CEO, commented: "We are pleased to deliver a 
report that confirms strong economics at Coringa and believe that the Project 
has the potential to add substantial value to shareholders and the surrounding 
community over the coming years. Once Anfield receives the required permits 
from the Brazilian authorities, our experienced operating team led by Andrew 
Storrie can commence re-constructing the same plant that he and his team 
operated while working at the nearby Andorinhas mine."

Anfield will continue to explore for areas where value can be added to the 
Project. There are approximately 40,000 gold ounces of the estimated Inferred 
mineral resource, which are not included in the Study's mine plan,(1) that are 
adjacent to areas mined as part of the Study. In addition, the Company controls 
a twenty kilometre area in the district with delineated gold soil anomalies, of 
which, the drill-defined mineral resource strike length is approximately two 
kilometres.

/T/

1.  Inferred mineral resources are considered too speculative geologically
to have the economic considerations applied to them that would enable
them to be categorized as mineral reserves. There is no certainty that
any or all mineral resources can be upgraded to mineral reserves through
continued exploration.

/T/

Feasibility Study Summary

The Study was initiated in June 2016 by MTB, with contribution by several 
consultants that have extensive expertise in their respective fields. Further 
details on the contributors can be found in the Qualified Persons section of 
this news release.

All currencies are in United States dollars unless otherwise specified. Base 
case economics are based on a gold price of $1,250 per ounce ("oz"), silver 
price of $18.00 per oz and an exchange rate of 3.2 (US$:R$). The effective date 
of the Study is July 1, 2017 and it incorporates all expenditures prior to that 
date. A technical report relating to the Study will be filed on SEDAR within 45 
days of this news release.

The Study and Project highlights include the following estimates:

/T/

--  Gold production of approximately 32 koz per year averaged over a 4.8
year mine life
--  Average life of mine process fully-diluted gold grade of 6.5 grams per
tonne ("g/t")
--  Post-tax internal rate of return of 30.8%
--  Post-tax net present value of $31.0 million at a 5% discount rate
--  Initial capital costs of $28.8 million
--  Average net cash operating costs of $585/oz and all-in sustaining costs
of $783/oz
--  Probable mineral reserves of 161 koz of gold and 324 koz of silver
--  23% of engineering for the process plant and related infrastructure has
been completed and 100% of engineering for the tailings storage facility
has been completed

/T/

Table 1: Summary of Coringa Economic Results by Gold Price

/T/

----------------------------------------------------------------------------
Gold Price (per oz)                Units     $1,125     $1,250     $1,375
----------------------------------------------------------------------------
Pre-Tax NPV (5%)                    $M        $17.6      $34.0      $50.3
----------------------------------------------------------------------------
Pre-Tax IRR                          %        19.6%      32.9%      45.5%
----------------------------------------------------------------------------
Post-Tax NPV (5%)                   $M        $16.0      $31.0      $45.2
----------------------------------------------------------------------------
Post-Tax IRR                         %        18.4%      30.8%      41.7%
----------------------------------------------------------------------------

/T/

Table 2: Coringa Life of Mine Capital Expenditure Estimate Breakdown

/T/

----------------------------------------------------------------------------
Initial Capital ($M)
----------------------------------------------------------------------------
Process & Infrastructure                                  $13.3
----------------------------------------------------------------------------
Pre-production Mine Development                           $3.5
----------------------------------------------------------------------------
Equipment                                                 $1.9
----------------------------------------------------------------------------
Direct and Indirect Owner Costs                           $8.1
----------------------------------------------------------------------------
Contingency (7.5%)                                        $2.0
----------------------------------------------------------------------------
Total Initial Capital (excluding working                  $28.8
capital)
----------------------------------------------------------------------------
Working Capital                                           $1.5
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Sustaining Capital ($M)
----------------------------------------------------------------------------
Life of Mine Sustaining Capital                          $28.7M
----------------------------------------------------------------------------
Average Annual Life of Mine Sustaining                    $5.9M
Capital
----------------------------------------------------------------------------

/T/

Table 3: Summary of Coringa Operating Cost Estimates and Cash Costs

/T/

----------------------------------------------------------------------------
Average Life-of-Mine Operating Costs per Tonne Milled
----------------------------------------------------------------------------
Mining Costs                                             $41.68
----------------------------------------------------------------------------
Processing Costs                                         $33.51
----------------------------------------------------------------------------
General, Administrative and Site Costs                   $33.14
----------------------------------------------------------------------------
Total Operating Costs                                    $108.33
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Average Life-of-Mine Cash Costs per Ounce
----------------------------------------------------------------------------
Operating Costs                                           $558
----------------------------------------------------------------------------
Silver By-Product Credits                                 ($23)
----------------------------------------------------------------------------
Sandstorm 2.5% NSR Royalty                                 $31
----------------------------------------------------------------------------
Government 1.5% NSR Royalty (1)                            $19
----------------------------------------------------------------------------
C1 Cash Costs Net of By-products (2)                      $585
----------------------------------------------------------------------------
Sustaining Capital and Closure Costs                      $197
----------------------------------------------------------------------------
All-in Sustaining Cash Cost (3)                           $783
----------------------------------------------------------------------------

/T/

(1): Includes 1.0% NSR royalty to the Brazilian government and 0.5% NSR royalty 
payment for surface rights
(2): (Refining Costs + Insurance + Transport Costs + Third Party Royalties + 
Operating Costs) / Payable Au oz
(3): (Refining Costs + Insurance + Transport Costs + Third Party Royalties + 
Operating Costs + Sustaining and Closure Capital Costs) / Payable Au oz

Coringa Estimated Mineral Reserves and Resources

The estimated mineral reserves for Coringa are based on the conversion of 
Indicated mineral resources to Probable mineral reserves based on the Study's 
estimated mine plan. The total fully-diluted mineral reserves for the Coringa 
Project are shown in Table 4.

Table 4: Coringa Estimated Mineral Reserves and Resources

/T/

----------------------------------------------------------------------------
Classification                                         Contained   Cut-off
Tonnes Au Grade Ag Grade Contained    Silver     Grade
(000's)   (g/t)    (g/t)  Gold (koz)   (koz)     (g/t Au)
----------------------------------------------------------------------------
Serra Probable      498      6.0     12.8       97        204       2.50
Reserves
----------------------------------------------------------------------------
Meio Probable       196      7.4     14.6       46         92       2.38
Reserves
----------------------------------------------------------------------------
Galena Probable      74      7.1     11.2       17         27       2.50
Reserves
----------------------------------------------------------------------------
Total Probable      769      6.5     13.1       161       324
Reserves
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Total Indicated     726      8.4     17.0       195       396       2.00
Resource
----------------------------------------------------------------------------
Total Inferred     1,301     4.3      5.1       181       215       2.00
Resource
----------------------------------------------------------------------------

/T/

General Note: Additional information, including with respect to the mineral 
resource estimate, metallurgy, data verification and quality control measures, 
can be found in Anfield's technical report titled "Coringa Gold Project, 
Brazil, NI 43-101 Technical Report" with an effective date of May 3, 2017, 
which is filed on SEDAR at www.sedar.com. Totals in the above table may not add 
due to rounding.
Resource Notes: Minimum thickness is 0.8 m horizontal. Effective date of May 3, 
2017. Indicated mineral resources are inclusive of mineral reserves.
Reserve Notes: Effective date of July 1, 2017. Grades are reported on a 
fully-diluted basis.

Mining

The Study contemplates underground mining using a 100% owner operated equipment 
fleet, most of which was acquired from Troy Resources Limited's ("Troy 
Resources") Andorinhas mine and is on site. The three mining areas that make up 
the Project will use a shrink stoping method to extract ore. Coringa has been 
designed to deliver an average of 159 thousand tonnes per year (approximately 
460 tonnes per day) of mill feed. The Study contemplates a mine that will 
extract ore over a 4.8-year period with a delivered fully-diluted gold head 
grade of 6.5 g/t. Ore will be sourced from the Serra zone in years 1 to 4, the 
Meio zone in years 3 and 4 and the Galena zone in the final year of mining.

Metallurgy

Extensive feasibility level test work was completed by C.H. Plenge & CIA S.A. 
at its laboratory in Lima, Peru, using representative composites, that 
confirmed the material from Coringa is amenable to a conventional crush, grind, 
gravity concentration and carbon-in-leach flow sheet.

Test work results indicated that 40% to 50% of the gold will be recovered in a 
gravity concentrate. The overall estimated gold and silver recovery based on 
all ore types being processed during the life of mine is 95.4% and 61.2% 
respectively.

Infrastructure

The Coringa Project is located in Para State, approximately 70 kilometres 
south-east of the city of Novo Progresso. Access to the mine site from the city 
of Novo Progresso is by way of existing paved and gravel roads and the driving 
time from Novo Progresso to the Coringa camp is typically two hours.

Camp and Existing Infrastructure:

The existing Coringa camp has been upgraded with the addition of new 
accommodations for 212 permanent operations staff and a new cafeteria/kitchen 
facility to serve the expected workforce. Additionally, a leased and 
contract-catered camp for construction contractors, capable of accommodating 
128 individuals, has been retained at Coringa following the completion of 
infill drilling. The entire camp complex has been secured with perimeter 
fencing, perimeter lighting, and access control by security staff.

Power for the Camp and Mine:

Total Project electrical demand during full mine and process plant operation is 
3,039 kilowatts ("kW") (3,799 kilovolt amps "kva").

Initially, until commercial power can be designed, permitted, constructed, and 
supplied by CELPA (the regional utility), power supply for the plant, mine, and 
camp will be supplied by seven diesel generators (six operating and one on 
standby), each rated at 750 kva. Power will be distributed from a central power 
station at the plant site via an overhead 34.5 kilovolt transmission line to 
the mine portals and to the camp. Completion of the incoming CELPA transmission 
line is expected to take 12-18 months.
The camp load of 90 kW (112.5 kva) has been, and will continue to be, provided 
by a 310 kva generator with a 500 kva generator as back-up. Both camp 
generators were obtained from Troy Resources. The power supply for the camp 
will continue to be supplied by generators until the power station at the plant 
and the overhead transmission line from the plant to the camp have been 
completed.

Water Requirements for the Camp and Mine:

During production, the mine, plant, and camp water requirements will be 
approximately 140m3/day, 770m3/day, and 35m3/day, respectively. Additionally, 
approximately 40m3/day will be needed during the six-month dry season each year 
for dust control on site roads and in working areas to maintain safe and 
healthy working conditions.

Mine and plant water needs will be sourced from mine dewatering, which is 
modelled to significantly exceed the total requirements for both. Camp water 
needs are expected to be sourced from a well near the camp.

During the three to six months of plant startup when reclaimed water from the 
tailings storage facility is not yet available, water to the process plant will 
be sourced from behind a temporary coffer dam constructed within the tailings 
storage facility footprint to provide a dry area for construction of the 
tailings embankment.

Approximately 520m3/day of the 770m3/day required for plant operation will come 
from reclaim of process water from the tailings storage facility. Only 
250m3/day of raw water from mine dewatering will be required for plant makeup 
water.

Taxes

The Study incorporates assumptions about Anfield's ability to use income tax 
deductions made available under a government economic stimulus program to 
companies for industrial projects developed in the Amazon region of Brazil. The 
program reduces the Brazilian corporate income tax rate by 75%. The assumed 
income tax rate used in the financial model is 15.25%.

Construction Timeline and Permitting

The Study evaluates a construction period of ten months from start to 
completion. The Company continues to engage with the Secretaria de Estado de 
Meio Ambiente e Sustentabilidade ("SEMAS") to receive the required permits to 
commence construction and hope they will be forthcoming in the near-future.

Qualified Persons

The scientific and technical information contained in this news release 
pertaining to the Project has been reviewed and approved by the following 
Qualified Persons as defined by NI 43-101: Robert Sim, P.Geo. (Mineral 
Resource), of SIM Geological Inc.; Neil Prenn, P.Eng. and Edwin Peralta, P.Eng. 
(Mining), of Mine Development Associates; Robert Michel, SME Registered Member 
(Economic Analysis and Infrastructure) of Robert Michel Enterprises; Nelson 
King, SME Registered Member (Metallurgy and Process); Mark Smith, P.E. 
(Tailings Management Facility) of RRD International LLC and Larry Breckenridge, 
P.E. (Hydrology, Hydrogeology, Geochemistry, and Infrastructure) of Global 
Resource Engineering, Ltd. All of the Qualified Persons are independent of 
Anfield.

About Anfield Gold

Anfield Gold Corp. (TSX VENTURE:ANF) is a Vancouver, Canada based precious 
metal exploration and development company focused on the development of the 
Coringa Project located in Para State, Brazil. Anfield's strategic plan 
includes the acquisition of other gold projects with the goal of becoming a 
mid-tier gold mining company.

Further details are available on the Company's website at 
https://anfieldgold.com

Anfield Gold Corp.

Marshall Koval, Chairman & CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

Certain statements and information herein, including all statements that are 
not historical facts, contain forward-looking statements and forward-looking 
information within the meaning of applicable securities laws. Often, but not 
always, forward-looking statements can be identified by the use of words such 
as "plans", "will", "expected" or variations of such words. Forward looking 
statements or information in this press release include, but are not limited 
to, Anfield's strategic plan to acquire other gold projects with the goal of 
becoming a mid-tier gold mining company; the mineral resource and mineral 
reserve estimates for the Project; that the Project has strong economics; the 
internal rate of return of the Project; the annual production of the Project; 
the net present value of the Project; the life of mine of the Project; the 
capital costs, operating costs and other costs estimated for the Project; 
required infrastructure for the Project; how infrastructure for the Project 
will be sourced; the timing required to complete construction at the Project; 
and that construction of the Project will occur at all. In making the 
forward-looking statements in this release, Anfield has applied certain factors 
and assumptions that are based on information currently available to Anfield as 
well as Anfield's current beliefs and assumptions (including Anfield's belief 
in the results of the Study). Although Anfield considers these beliefs and 
assumptions to be reasonable based on information currently available to it, 
they may prove to be incorrect, and the forward-looking statements in this 
release are subject to numerous risks, uncertainties and other factors that may 
cause future results to differ materially from those expressed or implied in 
such forward-looking statements.
Such risk factors include, among others, actual ore mined varying from 
estimates of grade, tonnage, dilution and metallurgical and other 
characteristics; the inherent uncertainty of production and cost estimates, and 
the potential for unexpected costs and expenses; risks associated with the 
estimation of mineral reserves and mineral resources, and the grade and 
continuity of mineral deposits; the timing of mining the three zones of the 
Project; the annual mill feed for the Project; gold recovery rates; power and 
water requirements for the Project; that mineral resources may never become 
mineral reserves and do not demonstrate economic viability, Anfield may not be 
able to achieve the base case during actual mining at the Project, risks 
associated with the business of Anfield, risks relating to exploration and 
potential development of the Company's projects; risks related to obtaining the 
permits and approvals necessary to develop and commission the Project on terms 
that are acceptable to Anfield; risks related to Anfield identifying suitable 
acquisition targets; business and economic conditions in the mining industry 
generally; the supply and demand for labour and other project inputs; prices 
for commodities to be produced and changes in commodity prices; changes in 
interest and currency exchange rates; risks relating to inaccurate geological 
and engineering assumptions (including with respect to the tonnage, grade and 
recoverability of mineral resources and mineral reserves); risks relating to 
unanticipated operational difficulties (including failure of plant, equipment 
or processes to operate in accordance with specifications or expectations, cost 
escalation, unavailability of materials and equipment, government action or 
delays in the receipt of government approvals, industrial disturbances or other 
job action, and unanticipated events related to health, safety and 
environmental matters); risks relating to adverse weather conditions; political 
risk and social unrest; changes in general economic conditions or conditions in 
the financial markets; and changes to business and economic conditions in the 
mining industry generally.
Forward-looking information and statements are in addition based on various 
estimates, forecasts and projections as well as expectations, beliefs and 
assumptions including, without limitation, the expectations and beliefs of 
management, the assumed long-term price of gold; that the Company can access 
financing and that the political environment where the Company operates will 
continue to support the development and operation of mining projects. Although 
Anfield has attempted to identify important factors that could cause actual 
results to differ materially from those contained in forward-looking 
information, there may be other factors that cause results not to be as 
anticipated, estimated or intended. There can be no assurance that such 
information will prove to be accurate, as actual results and future events 
could differ materially from those anticipated in such statements. Accordingly, 
readers should not place undue reliance on forward-looking information. Anfield 
does not undertake to update any forward-looking information, except in 
accordance with applicable securities laws.

- 30 -

CONTACT INFO:

Anfield Gold Corp.
Scott Hicks
+604  646-1884
Fax: +604  687-7041
https://anfieldgold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=596840529