Source	MARKET NEWS
Date	08/08/2018
Time	07:18:09 AM

Company	 Orsu Metals Corporation
Title	Intercepted a 
Voluminous 200-m-Wide Gold-Mineral





    CDNX Symbol: OSU











Press Release





ORSU METALS CORP ("OSU-V")
- Intercepted a Voluminous 200-m-Wide Gold-Mineralized Stockwork
- In the North of the Klyuchi West Zone, Sergeevskoe Gold Project,
- Russia

Orsu Metals Corporation ("Orsu" or the "Company") is excited to
announce excellent drill results at the Klyuchi West Zone of its
Sergeevskoe Gold Project in Russia.



Highlights:
* Drilling identified a 200 m width of steeply-dipping gold
stockwork in the north of Klyuchi West.
* Hole SDH18-39 intercepted:
- 2.03 g/t Au over 10.15 m from 45.9 m,
- 5.83 g/t Au over 5.55 m from 89.95 m, and
- 2.64 g/t Au over 10.55 m from 119.95 m.
* Hole SDH18-40 intercepted:
- 0.82 g/t Au over 46.45 m from 39.8 m,
- 2.3 g/t Au over 9.4 m from 94.65 m, and
- 1.76 g/t Au over 10.9 m from 186.75 m,
* Hole SDH18-34 intercepted:
- 1.17 g/t Au over 31.75 m from 4.1 m (including 2.06 g/t Au
over 9 m).
* Hole SDH18-35 intercepted:
- 1.27 g/t Au over 58.5 m from 83.05 m, including 2.63 g/t Au
over 10.5 m.
* Hole SDH18-41 intercepted:
- 1.0 g/t Au over 41.1 m from 140.2 m,
- 1.5 g/t Au over 15.9 m from 190.9 m, including 2.03 g/t Au
over 4.55 m, and
- 3.33 g/t Au over 9.85 m from 245.9 m.

Dr. Alexander Yakubchuk, Director of Exploration of Orsu
commented: "Although Orsu identified a gold-mineralized stockwork at
Klyuchi West in 2017, its extent remained unknown. New drilling in 2018
intercepted a 200-m-wide envelope with voluminous disseminated
porphyry-like gold mineralization, superimposed by a linear 75-m-wide
stockwork of northwest-trending gold-quartz veins. The highest gold
grades tend to appear near the contact between granite and granodiorite
porphyry intrusions. The stockwork trends towards the central part of
the Kozie prospect, located some 250 m northwest from Klyuchi West. The
area in between was never drilled or trenched in the past, and Orsu is
currently drill-testing this area".

Dr. Sergey Kurzin, the Executive Chairman of the company added:
"This is great news, we have not yet seen that sheer volume of
mineralization at Sergeevskoe deposit. It is hoped that results from
further drilling will connect this stockwork with the Kozie occurrence,
to potentially double the expected size and tonnage of the Klyuchi West
zone. We are nearing completion of the 2018 exploration program having
drilled 8000 out of 10500 planned meters. I am very happy with what we
have seen so far. All three zones that we worked on this year - Zone
23, Adit 5 and Klyuchi West - comfortably met and more often exceeded
our expectations by a margin. Orsu is firmly on track to deliver the
resource statement in Q4 2018. "

The license of the Sergeevskoe Gold Project occurs east from the
Alexandrovskoe open pit and gold plant owned by Zapadnaya Gold Mining
Ltd and immediately to the west from the Klyuchevskoe gold license
owned by Sun Gold Mining (Figure 1). The Klyuchevskoe (Klyuchi) gold
deposit represents a +6 Moz gold endowment (see Orsu press-release
dated September 21, 2016). Orsu owns a 90% interest in the Sergeevskoe
Gold Project (see press release dated November 6, 2017).



Figure 1. An outline of the 7.6 sq km Sergeevskoe license area with
location of principal gold prospects and two adjacent gold open pits.

At Klyuchi West, the Company previously reported encouraging
intercepts in surface trenches and drillholes SDH17-3 and SDH17-7, as
well as in (see press release November 13, 2017), as well as in
drillholes SDH17-13 and SDH17-14 (see press release January 25, 2018),
which demonstrated a 200 m vertical extent of gold mineralization, but
its width was not constrained.

As part of the ongoing ~10,500 m drilling program, Orsu drilled 8
holes, totaling 2283.7 m in three north-south fences, approximately 40
m apart, starting near the eastern license boundary. The mineralization
in the north of Klyuchi West forms a northwestern extension of gold
mineralization in the Klyuchevskoe open pit (Figures 1 & 2).

The mineralization is hosted by the Permian granite intrusion,
which is intruded by Jurassic granodiorite porphyry stock and dioritic
to hybrid porphyry dykes. The stockwork consists of
quartz-tourmaline-sulfide veins and veinlets, striking to the
northwest, often in parallel orientation with the dykes. The contact
between the granite and granodiorite porphyry is also important in
controlling the higher grade gold mineralization.



Figure 2. Surface expression of multiple northwest-trending
gold-mineralized intervals at Klyuchi West, Sergeevskoe Gold Project.
Mineralization south of Shirotnyi Fault is not shown.

Selection of mineralized intervals, presented below, is based on a
0.5g/t Au cut-off for compositing, with maximum 2 m length of 0.3-0.5
g/t Au mineralization included into mineralized interval. Composited
intervals in drillholes are presented uncapped.

Orsu received assays for all eight holes drilled in parallel
sections 9740E, 9790E and 9830E, although some assays for some
intervals are still pending (Table 1). All holes were drilled to the
south at 50 to 75 degrees and identified multiple gold-mineralized
intervals in quartz-tourmaline veins and hydrothermal breccias, with
best and/or widest intercepts in holes SDH18-39, 40, 34, 35 and 41
(Figure 3). In particular, SDH18-39 intercepted 2.03 g/t Au over 10.15
m from 45.9 m, 5.83 g/t Au over 5.55 m from 89.95 m, and 2.64 g/t Au
over 10.55 m from 119.95 m. SDH18-40 intercepted 0.82 g/t Au over 46.45
m from 39.8 m, 2.3 g/t Au over 9.4 m from 94.65 m, and 1.76 g/t Au over
10.9 m from 186.75 m, whereas SDH18-34 intercepted 1.17 g/t Au over
31.75 m from 4.1 m (including 2.06 g/t Au over 9 m), and nearby
SDH18-35 returned 1.27 g/t Au over 58.5 m from 83.05 m, including 2.63
g/t Au over 10.5 m. SDH18-41 went through 1.0 g/t Au over 41.1 m from
140.2 m, 1.5 g/t Au over 15.9 m from 190.9 m, including 2.03 g/t Au
over 4.55 m, and 3.33 g/t Au over 9.85 m from 245.9 m.




Figure 3. Gold mineralization in sections 9830E, 9790E and 9740E. Note wide
intercepts along the contact between granite and granodiorite porphyry. The
higher grade ()2 g/t Au) intercepts tend to occur in granite, and
granodiorite porphyry tends to host a bulk disseminated gold
mineralization.

Holes SDH18-37 and 38 in section 9740E, with the lowest grades (Table 1),
are interpreted to mark the southwestern flank of the mineralized stockwork
in the north of Klyuchi West.

These results revealed a 200-m-wide gold-mineralized stockwork with
multiple closely-spaced mineralized intervals. Downdip, it is drill tested
to a depth of 200 m, with consistent or somewhat higher grade at depth. Its
southwestern and northeastern parts host lower grade disseminated
mineralization. In the center are the higher-grade gold veins, trending
northwest towards the central part of the Kozie prospect. The 250 m strike
length in between Kozie and Klyuchi West was never trenched or drilled in
the past. It coincides with a
low resistivity anomaly, identified by Orsu during the 2017 PD-IP electric
surveying. Orsu is currently drilling scout holes in this area.

//st



Table 1. Mineralized intercepts at Klyuchi West (above 0.5 g/t Au cut-off).





Section 9830E
SDH18-39 (210.7 m)  12.65    1 6.5 5  3.9     3 . 4  0.6 5
26.9     30 .7 5  3.8 5   3.3    0.54
45.9     56.05    10.15   9.0    2.03
89.95    95. 5    5 .55   4.8    5.83
119. 95  130. 5   1 0.55  9.2    2.64
125.8    130.5    4.7     4.2    5.29
1 5 1.1  153.05   1.95    1.6    0 .9
1 6 1.7  165.7    4. 0    3.5    1. 5 7
202.65   204.85   2 . 2   1.8    0.65
SDH18-40 (241.2 m)  9.7      12.11    2.41    1.4    0.56
29.15    31.05    1.9     1.1    3.47
39.8     86.25    46.45   27.0   0.82
65.3     76.1     10.8    7.0    1.2
94.65    104.05   9.4     6.6    2.3
145.65   149.05   3.4     2.2    1.4
153.65   162.2    8.55    5.8    0.64
186.75   197.65   10.9    6.6    1.76
191.2    197.65   6.45    4.2    2.57
202.4    203.45   1.05    0.7    11.3
SDH18-42 (291.8 m)  24.6     27.65    3.05    2.4    1.63
31.4     33.9     2.5     2.0    0.57
50.15    79.3     29.15   23.0   0.61
81.35    98.35    17.0    13.5   pending
98.35    100.75   2.4     2.0    0.55
113.6    152.4    38.8    31.0   0.88
142.25   149.3    7.05    5.6    1.61
163.0    165.0    2.0     1.6    0.76
178.85   181.05   2.2     1.7    0.7
215.4    222.95   7.55    6.0    0.96
241.55   246.5    4.95    4.0    1.69
276.15   284.0    7.85    6.3    3.7
Section 9790E
SDH18-34 (141.6 m)  4.1      40.85    31.75   27.0   1.17
28.6     37.6     9.0     7.6    2.06
94.7     96.3     1.6     1.4    2.72
103.9    106.0    2.1     1.8    0.63
SDH18-35 (235.4 m)  11.0     14.5     3.5     2.5    0.89
23.25    26.8     3.55    2.5    1.22
34.15    55.6     21.45   14.5   0.89
48.5     55.6     7.1     5.0    1.01
83.05    141.55   58.5    18.5   1.27
101.6    109.7    10.5    3.5    2.63
161.05   163.4    2.35    0.8    2.4
170.55   172.2    1.65    0.55   0.63
179.8    183.55   3.75    1.2    1.55
SDH18-41 (293.8 m)  35.75    37.4     1.65    1.0    1.24
58.0     63.7     5.7     3.8    0.55
72.45    79.9     7.45    5.0    0.82
90.6     103.85   13.25   8.8    0.66
110.75   140.2    35.2           pending
140.2    181.3    41.1    28.0   1.0
190.9    206.8    15.9    11.0   1.5
201.35   205.9    4.55    3.5    2.03
226.8    232.5    5.7     4.3    0.62
245.9    255.75   9.85    7.0    3.33
273.4    275.8    2.4     1.9    0.75
Section 9740E
SDH18-37 (187 m)    37.05    39.7     2.65    2.2    3.29
45.95    55.15    9.2     7.8    0.5
65.15    75.0     9.85    8.2    0.65
81.85    86.4     4.55    3.8    0.54
88.65    96.65    8.0     6.8    0.68
100.0    104.0    4.0     3.4    0.6
SDH18-38 (150.7 m)  25.35    27.8     2.45    1.3    0.58
47.15    56.9     9.75    5.0    0.55
61.6     78.4     16.85   9.0    0.65
64.25    68.15    3.9     2.2    1.23
88.1     90.85    2.75    1.5    0.57
102.0    103.8    1.8     1.1    1.39
122.65   128.1    5.45    3.0    0.62
136.9    147.0    10.1    6.0    0.73
174.3    180.0    5.7     3.2    0.81
//et

Quality Assurance - Quality Control ("QA/QC")

Drillcore samples were submitted directly to the ALS Limited
laboratories in Chita, Russia, which are independent from Orsu, for
sample preparation and analysis. Analysis for Au is performed using
fire assay method with atomic absorption ("AA") finish and with a
gravimetric finish for samples exceeding 10g/t Au. Results published
are from the gravimetric finish if above 10g/t Au and from the AA
finish if lower than 10g/t Au.



Qualified Person
This release and the technical data reported have been reviewed
and approved by Alexander Yakubchuk, Director of Exploration of the
Company, also a Qualified Person as defined in NI 43-101.



Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Cautionary Statement:
This news release contains forward-looking statements that are
based on the Company's current expectations and estimates.
Forward-looking statements are frequently characterized by words such
as "plan", "expect", "project", "intend", "believe", "anticipate",
"estimate", "suggest", "indicate" and other similar words or statements
that certain events or conditions "may" or "will" occur. Such
forward-looking statements involve known and unknown risks,
uncertainties and other factors that could cause actual events or
results to differ materially from estimated or anticipated events or
results implied or expressed in such forward-looking statements. There
may be other factors that cause actions, events or results not to be as
anticipated, estimated or intended. Any forward-looking statement
speaks only as of the date on which it is made and, except as may be
required by applicable securities laws, the Company disclaims any
intent or obligation to update any forward-looking statement, whether
as a result of new information, future events or results or otherwise.
Forward-looking statements are not guarantees of future performance and
accordingly undue reliance should not be put on such statements due to
the inherent uncertainty therein.



Alexander Yakubchuk, Director of Exploration, Orsu Metals Corporation

Doris Meyer, Corporate Secretary, Orsu Metals Corporation

Tel: +1-604-536-2711 ext 6

www.orsumetals.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1821900021TS11821901196-07144420180808