Source	MARKET NEWS
Date	07/19/2018
Time	06:45:16 AM

Company	 Cabral Gold Inc.
Title	New Discovery 
of High Grade Vein Mineralization





    CDNX Symbol: CBR











Press Release




[200/News Release]CBRVCABRAL GOLD INCJUL 19 2018  06:41 AMNew Discovery 
of High Grade Vein Mineralization at Machichie ReturnsGrades up to 336g/t 
(10.8 oz/t) Gold at Cabral's Cuiu Cuiu Projectin Brazil --->@NEWS RELEASE
CABRAL GOLD INC ("CBR-V;CBGZF-0")
- New Discovery of High-Grade Vein Mineralization at Machichie
- Returns Grades up to 336g/t (10.8 oz/t) Gold at Cabral's Cuiu Cuiu
- Project in Brazil

Cabral Gold Inc. ("Cabral" or the "Company")  is pleased to
announce initial sampling and exploration results from an ongoing
program assessing the potential of newly discovered high-grade veins at
the Machichie Prospect, within the Cuiu Cuiu Project, Para State,
northern Brazil.

Initial results have highlighted a newly recognized mineralized
trend with no previous drilling that is located only 500m north of the
Cabral's MG deposit (Figure 1). MG is one of four deposits with defined
resources at Cuiu Cuiu.

The newly discovered Machichie mineralized structures extend at
least 300m and lie along an easterly trend, roughly parallel to MG. The
discovery is highlighted by a line of recently sunk artisanal shafts
that are exploiting high-grade gold-bearing quartz veins hosted in
soft, shallow weathered bedrock. The structure is defined as a subtle
magnetic low that corresponds to a coincident gold-in-soil geochemical
anomaly (100-315ppb Au). Both the veins and wall-rock alteration are
sulphide rich, which appears to correlate to a pronounced off-grid IP
chargeability response interpreted from a 2006 IP test survey covering
part of the MG deposit to the south.

Highlights

//st

* A composite grab sample of mineralized rock returned 336 g/t Au from a 1m
wide quartz-pyrite vein in an artisanal shaft at Machichie.
* Channel sample results include 54.6 g/t Au over 0.80m, 13.2 g/t Au over
0.75m, 13.8 g/t Au over 1.5m and 5.8 g/t Au over 1.75m

//et

Figure 1: Location of the Machichie target relative to the other
gold deposits and targets in the central part of the Cuiu Cuiu
property.

To view an enhanced version of  Figure 1, please visit:
http://orders.newsfilecorp.com/files/3900/36078_a1531969804946_19.jpg

Background

The Cuiu Cuiu Project covers the largest of the historical placer
gold camps in the Tapajos region of northern Brazil, having yielded an
estimated 2MMoz of gold from the overall 20-30MMoz gold produced during
the Tapajos gold rush1 from the late-1970's though the mid-1990's.
Placer workings cover over 850ha on the property but are largely
exhausted. The few remaining artisanal workers now process gold from
palaeo-valley placer deposits and in places exploit high-grade gold
mineralization from quartz veins in saprolite (shallow highly weathered
bedrock).

Exploration work from 2006 through 2012 successfully identified
multiple bedrock sources for a number of the placer workings, largely
discovered by following up pronounced surface gold-in-soil geochemical
anomalies. Many potential source areas remain untested, and recent work
by artisanal workers is uncovering additional new targets.

Earlier this year, Cabral reported an updated NI 43-101 Mineral
Resource Estimate2 totalling 5.9MM tonnes grading 0.9 g/t Au
(Indicated) and 19.5MM tonnes grading 1.2 g/t Au (Inferred), or 0.2MM
ounces and 0.8MM ounces of gold, respectively. That estimate was based
on four deposits drilled prior to the cessation of drilling in 2012.

The Company's current program is designed to improve understanding
and expand existing prospects, evaluate newly identified discoveries,
prioritize drill targets, and to build upon the existing resource
inventory.

One focus is on the definition of gold targets that are
strategically close to existing resources. The Machichie area is one
such target, as it lies within 500m of the MG deposit (Figure 1).

Currently MG is assigned an Inferred Resource of 8.6MMt @ 1.45g/t
Au (0.4MMoz of gold) 3. To date, drilling at MG is wide-spaced.  The
deposit remains open at depth. The resource is quite sensitive to
top-end cuts, with 73% more gold reporting to an estimate provided
without top-end cuts. Additional strategic drilling this fall will be
targeted to better define high-grade shoots at MG in order to improve
the gold grade, and thereby the size of the gold resource.

Any nearby resources outlined at Machichie would be expected to
improve the economic prospects of MG.

Machichie Target Area

Placer deposits were mined for gold in the Machichie area during
the main phase of the Tapajos gold rush. Principal placer workings
extended over 1km along a valley system to the north of Cabral's MG
deposit.

Artisanal workers later found multiple northeast trending
gold-bearing vein systems in weathered bedrock immediately to the
northwest of the east-trending MG deposits. There, several substantial
artisanal pits were eventually developed ranging up to 120m in strike
length that exploited the saprolite-hosted gold mineralization. These
pits are now flooded, and are no longer accessible to sampling, having
been worked to the water table. A channel sample taken during whilst
one of these pits was active returned 16.0 g/t Au over 5.8m. While the
MG deposit was being drilled in 2009, a single historical hole
(CC-52-09) tested below these pits, returning 7.4g/t Au over 3.3m,
approximately 50m along strike from the channel sample. Despite these
initial strong results, emphasis at the time was on MG and no further
work was done at Machichie.

In early March 2018, Cabral's first field visit to Machichie
identified extensive new artisanal workings on a previously unknown
easterly trend that is roughly parallel to MG (Figure 2). These include
a key area where artisanal gold mining and processing is being
conducted on quartz veins hosted in saprolite that were recently
exposed following a renewed phase of colluvial mining of
overburden-covered placer mineralization.

Cabral commenced a review of the new Machichie discovery area in
April 2018. There are currently at least ten active shafts, four of
which are in active production and are developed on vein-hosted gold
mineralization. These shafts are all developed along an east -trending
structural corridor, which cuts across the previously discovered
northeast-trending vein set. The majority of these shafts have only
been developed in the last six months. The western extension of the
vein system remains concealed by a soil profile typically 6-8 m thick.
The eastern extension, identified with the more recent advancement of
colluvial mining, remains partly covered by tailings and stockpiles.

Cabral's initial work has included: detail drone aerial
photography to map the artisanal workings, rock-chip sampling and
channel sampling of veins exposed in shafts, stockpile and grab
sampling of material extracted from shafts, and trenching and channel
sampling between the workings where topography and overburden thickness
allows access. The geophysical and geochemical work completed by the
previous operator has also been reassessed.

Figure 2: Drone orthophoto of the MG-Machichie Area showing the
new discovery trend and historic drilling and sampling and the outline
of the MG mineralisation trend.

To view an enhanced version of  Figure 2, please visit:
http://orders.newsfilecorp.com/files/3900/36078_a1531969805290_93.jpg

Reprocessed ground magnetic data clearly shows a subtle easterly
trending magnetic low  along which the shafts align (Figure 3).
Additional magnetic lows are evident that have not yet been evaluated.

A strong gold-in-soil anomaly directly correlates to the area of
the new discovery (Figure 3), and there are several other untested
anomalies that have yet to be evaluated, including:

//st

* A soil anomaly at a 100ppb Au threshold extending ~400m WNE of the
western-most shaft.
* The 100ppb Au geochemical anomaly persists 300m ESE from the easternmost
shaft, and untested satellite anomalies are present extending over
distances between 200 and 800m
* A smaller satellite soil anomaly further to the west converges towards
the Jerimum Baixo area.

//et

Figure 3: Geochemical anomalies associated with trends in
reprocessed ground magnetics. The shafts at Machichie align with an
easterly trend along which untested gold in soil geochemical anomalies
are distributed. Additional targets are represented by magnetic lows,
which need to be tested for indications of alteration related to the
mineralization event.

To view an enhanced version of Figure 3, please visit:
http://orders.newsfilecorp.com/files/3900/36078_a1531969805602_85.jpg

Figure 4: Detailed drone orthophoto view of the new Machichie
discovery area with sample results pit, trench and shaft locations,
along with photos of samples and workings.

To view an enhanced version of  Figure 4, please visit:
http://orders.newsfilecorp.com/files/3900/36078_a1531969805884_44.jpg

Figure 4 shows a more detailed view of the new Machichie discovery
area. The eastern-most shaft has been developed to the top of fresh
bedrock at the water table, exposing a 1m wide quartz-pyrite vein. A
composite sample of from the run-of-mine material excavated from the
working face returned an assay result of 336 g/t Au. The artisanal
workers pass the crushed vein material through a sluice box four times.
Sampling of rejects from the first, second and third stages of washing
returned grades of 25.7, 14.2, and 12.9 g/t Au respectively.

The vein was observed to be 1m wide in the working, and is
enveloped by a strongly silicified wall rock with disseminated pyrite.
Grab samples of the pyrite-altered wall rock returned grades of 1.0 to
4.4 g/t Au. This material is not targeted for processing and exposure
is limited, such that the width of this zone around the vein has yet to
be established.

Four of the new shafts to the west have been accessed for
sampling. Results of channel samples across the face of these western
shafts were:

//st

* 54.6 g/t Au over 0.80m
* 13.8 g/t Au over 1.5m
* 13.2 g/t Au over 0.75m
* 5.8 g/t Au over 1.75m

//et

These channel samples are all open across strike, as all were
constrained to the available width of the narrow working face. A deep
soil profile and topography prevents trenching in the immediate
vicinity of these E-W veins. The potential for additional cross-strike
mineralization will be tested with drilling as will the unmined
wall-rock alteration.

Figure 5: -100m Chargeability grid from a 2006 IP test survey
superimposed on the 2018 MG-Machichie area drone orthophoto.
Geophysical exploration targets are preliminary in nature and not
conclusive evidence of the likelihood of a mineral deposit.

To view an enhanced version of  Figure 5, please visit:
http://orders.newsfilecorp.com/files/3900/36078_a1531969806212_70.jpg

Higher grade mineralization in the east-trending MG deposit
exhibited considerably more sulphide in veins and wall-rock alteration
than the other known deposits on the property.  Higher grade
mineralization examined from the new Machichie discovery appears to
have even stronger sulphide alteration.  Furthermore, that strong
pyrite wall-rock alteration is coupled with large accessory molybdenite
grains, and traces of chalcopyrite. Fluorite is also present in the
vein and alteration halo. Given this strong sulphide content, results
from a test IP (induced polarisation) geophysical survey completed in
2006 were re-examined.  The results, interpreted at that time,
indicated a strong chargeability anomaly trending towards the new
Machichie discovery area (Figure 5).

The new Machichie discovery area is shaping up to be a primary
drill target area for Cabral's initial drill program planned later this
year. In the meantime, additional multi-element geochemistry will also
be conducted in the area, focusing initially on stream sediments to
assess whether the copper- molybdenum signature can be traced over a
broader area. Auger lines are planned to further define the lateral
extensions of the zone. And; finally, an expanded IP survey over the
MG-Machichie area is being considered as an option for defining the
extensions of the structure under-cover, and to target rocks with
chargeability response consistent with heavier sulphide contents, that
in the Cuiu Cuiu setting generally correlate with higher grade lode
positions.

Alan Carter, President & CEO commented "The Machichie results are
redefining our ideas of the variety of target styles that are yet to be
drilled at Cuiu Cuiu. Past exploration has focussed on the lower-grade
stockwork-style vein systems. These new results highlight the potential
of more discrete vein structures with exceptionally high-grades. The
new processing and review of our geophysical database has added
valuable context of interpreted structures correlative with geochemical
anomalies which can now be seen to extend from this trend. Our next
steps are to further screen these targets using auger drilling, and
potentially geophysics to complete the definition of drill targets
along this newly recognized corridor. We look forward to drill-testing
the new Machichie discovery later this year".

About Cabral Gold Inc.

The Company is a junior resource company and is engaged in the
identification, exploration and development of mineral properties, with
a primary focus on gold properties located in Brazil.  The Company owns
the Cuiu Cuiu gold project located in the Tapajos Region within the
state of Para in northern Brazil.

FOR FURTHER INFORMATION PLEASE CONTACT:

Alan Carter President and Chief Executive Officer Cabral Gold Inc.
Tel: 604.676.5660

Dr. Adrian McArthur, B.Sc. Hons, PhD. FAusIMM., a consultant to
the Company as well as a Qualified Person as defined by National
Instrument 43-101, supervised the preparation of the technical
information in this news release.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as such term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Forward-looking Statements

This news release contains certain forward-looking information and
forward-looking statements within the meaning of applicable securities
legislation (collectively "forward-looking statements").  The use of
the words "will", "expected" and similar expressions are intended to
identify forward-looking statements.  These statements involve known
and unknown risks, uncertainties and other factors that may cause
actual results or events to differ materially from those anticipated in
such forward-looking statements.  Such forward-looking statements
should not be unduly relied upon.  This news release contains
forward-looking statements and assumptions pertaining to the following:
strategic plans and future operations, and results of exploration. Actual 
results achieved may vary from the information provided herein
as a result of numerous known and unknown risks and uncertainties and
other factors.  The Company believes the expectations reflected in
those forward-looking statements are reasonable, but no assurance can
be given that these expectations will prove to be correct.

Notes

Gold analysis has been conducted by SGS method FAA505 (fire assay
of 50g charge), with higher grade samples checked by FAA525 or screen
fire assay. Analytical quality is monitored by certified references and
blanks. Until dispatch, samples are stored under the supervision the
Company's exploration office. The samples are couriered to the assay
laboratory using a commercial contractor. Pulps are returned to the
Company and archived. Channel sampling is conducted using a
hand-trenching tool over exposed faces to maintain a consistent sample.
The high-grade Machichie sample was collected from the 2mm crushed
run-of-mine feed stream of an artisanal processing operation. Under the
agreement with the Cuiu Cuiu condominium, local artisanal operators can
process mineralization to a depth of 30m, unless otherwise negotiated.
Shafts generally stop at or above the depth at the depth around the
water-table. Historical drilling results are reports as down-hole
length weighted intersections unless otherwise stated.

1 DNPM (National Department of Mining Production) 2 Micon NI
43-101 resource estimate reported June 7 2018. 3 Micon NI 43-101
resource estimate reported June 7 2018.

TEL: 604-676-5663    CABRAL GOLD INC
FAX: 780-439-7308
E-mail: alan@cabralgold.com
Website: https://www.cabralgold.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1819900026TS11819900841-06414620180719