Source	MARKET NEWS
Date	08/02/2018
Time	07:03:20 AM

Company	 Abraplata Resource Corp.
Title	Evaluating Underground Exploitation Potential of





    CDNX Symbol: ABRA











Press Release





Evaluating Underground Exploitation Potential of High GradeMineralization 
--->@NEWS RELEASE
ABRAPLATA RESOURCE CORP ("ABRA-V;ABBRF-0")
- Evaluating Underground Exploitation Potential of High Grade
- Mineralization

AbraPlata Resource Corp. ("AbraPlata" or the "Company") is pleased
to announce an update on its Diablillos property, located in
northwestern Argentina.  The Company has been conducting a review of
historical drill data to determine if higher grade silver and gold
zones could potentially be exploited using underground mining methods.
An underground mining approach could entail significantly less initial
capital than the large open pit approach contemplated in the Company's
2018 Preliminary Economic Analysis ("PEA") on the Diablillos project.
The PEA demonstrated that Diablillos has the potential to product an
average of 9.8 million silver-equivalent ounces per year over an eight
year mine with robust economics.  Building such a large operation would
require estimated initial capital of US$293 million.  (Refer to
technical report filed April 16, 2018, on SEDAR.com for full details of
the PEA.)

The comprehensive drill database review by AbraPlata follows the
identification by Nick Tate, the Company's consulting geologist and
epithermal specialist, that high grade mineralized cores are strongly
correlated with steeply dipping, tabular hydrothermal breccia bodies in
the main Oculto deposit (Figure 1).  Historical drilling, which totals
about 88,000m in 450 drill holes, intercepted these breccias in
numerous drill holes with the best mineralization being encountered at
the intersection of the Main Breccia Zone and the Cross Breccia Zone.

Highlights of historical drill the core of the Oculto deposit are
provided in Table 1. The collars of the drill holes listed in Table 1
cover a strike length of over 400 metres and a width of over 200
metres, suggesting that Oculto has a thick, high grade core where there
is pervasive brecciation.

Table 1 - Historical drill intercepts from the high grade core of
the Oculto Deposit

Table is available at
https://globenewswire.com/news-release/2018/08/02/1546218/0/en/Evaluating-U
nderground-Exploitation-Potential-of-High-Grade-Mineralization.html



Notes

*  Intervals are down-the-hole and do not represent True Widths (*
true width of broad intercept in hole DDH-93-001 is estimated to be
42.5% of reported interval, or 41.9m)
*  No grade capping has been applied
*  Equivalent grades (AgEq or AuEq) have been calculated on the
basis of Au:Ag = 75:1

"The implications from the improved geological understanding of
the Oculto deposit are that the near-vertical breccia bodies are
largely untested at depth and, as indicated in our April 30, 2018, news
release, we believe that Oculto has the potential to host high grade
gold mineralization below the current mineral resource," commented
Willem Fuchter, President and CEO of AbraPlata.  "An underground option
may indicate a processing plant of reduced capacity and increased
recoveries due to a higher grade feed, and would require less capital.
In addition, significant pre-stripping of waste material would no
longer be necessary, resulting in further savings and the high grade
zones at depth can then be tested from underground.  Furthermore, in
the event that Oculto makes sense as an underground operation, then the
potential high grade gold mineralization at depth becomes significantly
more compelling than in an open pit approach.  While we believe the
open pit approach to Diablillos remains a viable option, the Company
plans to conduct additional work to assess if an underground mining
approach that is less capital intensive may be a viable alternative and
if a PEA on such a scenario is warranted."

Diablillos Overview The Diablillos property hosts high
sulphidation epithermal Ag-Au mineralization associated with a large
epithermal system underlying the property.  The great majority of
resources reported from the property are located in the Oculto deposit
(Figure 1) which is centered over the core of the epithermal system.

Figure 1 - Surface Geology of the Oculto Deposit showing the
outline of the PEA pit shell

The higher grade mineralization at Oculto tends to be structurally
controlled. AbraPlata has done considerable work over the past year
mapping the surface and re-logging  of  key drill holes in order to
interpret the structural geology at Oculto and arrive at a geological
and geometrical model of the mineralized zones.  The most important
mineral bearing zones are the Main, Cross, and West Zones, although
mineralization has been intercepted in the other zones.  In addition,
breccia zones have been also identified in the satellite occurrences
surrounding Oculto, notably at, Fantasma, Laderas, Enigmatica,
Concepcion, and Nebulosa.

More specifically, mineralization appears to be controlled by NW-
and NE-trending structures along which significant tabular zones of
hydrothermal breccia have been developed that, in turn, host the high
grade mineralization.  To date, six specific breccia zones have been
identified at Oculto: Main Breccia Zone; Cross Breccia Zone; East
Breccia Zone; West Breccia Zone; NW Breccia Zone; and North Breccia
Zone (Figure 1).   The Main Breccia Zone and the Cross Breccia Zone
have an estimated strike extent of at least 800m.  The East and West
Zones have strikes of 650m and 450m respectively.  The Main and Cross
Breccia Zones form a continuous zone of mineralization which extends
for more than 1000m (Figure 2), and a significant vertically dipping
pipe-like body over 80m in diameter and extending some 150m in depth
lies at the intersection of the Main and Cross Zones (Figure 3a).  This
mineralized plug is open at depth.  Likewise, the general lack of
drilling below the current PEA pit shell together with the results of
few deep holes that have been continued below the current pit depth
such as DDH-97-007A (see Figure 3b) indicate the considerable potential
for the definition of additional resources at depth in the basement
rocks.

Figure 2 - Long Section A-A' of the Oculto deposit showing drill
intercepts through the Main and Cross Breccia Zones (looking northwest)
with intercepts over 200 g/t Ag and 2.5 g/t Au indicated

A photo accompanying this announcement is available at
http://www.globenewswire.com/NewsRoom/AttachmentNg/58cd1642-8792-4211-afbc-
4773d65c044b

Figure 3a - Section B-B' through the pipe-like body at the
intersection of the Main and Cross Breccia Zones

A photo accompanying this announcement is available at
http://www.globenewswire.com/NewsRoom/AttachmentNg/a65935d4-dc3e-4fc0-bc06-
20f0b030fc5d

Figure 3b - Section C-C' through the West Breccia Zone, showing
the high grade gold potential below the pit

A photo accompanying this announcement is available at
http://www.globenewswire.com/NewsRoom/AttachmentNg/8fb5d861-7704-45b6-a505-
a1a317e257a9

Given the fact that mineralization at Oculto is of an epithermal,
high sulphidation nature, mineralization may extend for hundreds of
meters below the current pit shell.  This creates the potential of
increasing resources from Oculto significantly, especially gold
resources.  High grade gold-rich zones are associated with hydrothermal
breccias at the interface of the basement rocks with the overlying
volcanics and volcaniclastics  and confined to tight structures within
the basement.  Oculto has multiple characteristics of a gold deposit
with a silver cap.

The long section through the Main and Cross Zones (Figure 2) shows
elevated levels of silver and gold mineralization occurring in a zone
that is 5 to 30m in thickness and occurs approximately 90 to 120m below
current topography and just below the current water table (blue line on
sections), which lies about 80m below the surface.  This enriched
mineralized zone has been interpreted as a supergene enrichment zone
developed just below the water table during emplacement.  Numerous high
grade silver and gold drill intercepts have been encountered in this
zone with grades reporting over 200g/t AgEq.  Sample intercepts from
historical drilling of the high grade silver and gold mineralization in
the enrichment zone are shown in Table 2.

Table 2 - Significant intercepts in the supergene enrichment zone

Table is available at
https://globenewswire.com/news-release/2018/08/02/1546218/0/en/Evaluating-U
nderground-Exploitation-Potential-of-High-Grade-Mineralization.html



Notes:

*  Intervals are down-the-hole and do not represent True Widths

*  No grade capping has been applied

*  Equivalent grades (AgEq or AuEq) have been calculated on the
basis of Au:Ag = 75:1

A gold-rich zone lies at an angle to the silver zone, and is
generally better developed at depth.  Much of the gold in this zone is
hosted by breccia bodies both within the NE-trending structures and
also in breccias developed at the intersection of the basement rocks
and overlying volcanics and volcaniclastics.  At depth, the gold
generally occurs in the vicinity of the oxide-sulphide interface
(maroon line on the  sections) and is interpreted to represent hypogene
mineralization.  Examples of historical drill intercepts in breccia
zones of the gold rich zones are shown in Table 3.

Table 3 - Gold intercepts near the oxide-sulphide interface

Table is available at
https://globenewswire.com/news-release/2018/08/02/1546218/0/en/Evaluating-U
nderground-Exploitation-Potential-of-High-Grade-Mineralization.html



Notes

*  Intervals are down-the-hole and do not represent True Widths
*  No grade capping has been applied
*  Equivalent grades (AgEq or AuEq) have been calculated on the
basis of Au:Ag = 75:1

The Diablillos property has an Indicated Mineral Resource Estimate
of 27.1 million tonnes grading 93.1g/t Ag and 0.84g/t Au containing
80.9 million oz Ag and 732,000 oz Au (136Moz AgEq or 1.81Moz AuEq using
Au:Ag of 75:1).  Further details can be found in technical reports from
November 2016 and April 2018 which are available from the Company's
profile on SEDAR.com.

Qualified Person All scientific and technical information in this
news release has been approved by Willem Fuchter, PhD PGeo, President &
CEO of AbraPlata Resource Corp and a qualified person as defined by
National Instrument 43-101.

About AbraPlata AbraPlata is a junior mining exploration company
focused on delivering shareholder returns by unlocking mineral value in
Argentina.  The Company's experienced management team has assembled an
outstanding portfolio of gold, silver and copper exploration assets,
and is focused on advancing its flagship Diablillos silver-gold
property  through the various stages of feasibility.  In addition,
AbraPlata owns the highly prospective Cerro Amarillo property with its
cluster of five mineralized Cu-(Mo-Au) porphyry intrusions located in a
mining camp hosting the behemoth El Teniente, Los Bronces, and Los
Pelambres porphyry Cu-Mo deposits. As well, the Company is exploring
Aguas Perdidas, its wholly owned Patagonia-style epithermal Au-Ag
property.

ON BEHALF OF THE BOARD  ABRAPLATA RESOURCE CORP. "Willem Fuchter"
Willem Fuchter  President & Chief Executive Officer

//st

For further information concerning this news release, please
contact:

Willem Fuchter - President & CEO        Rob Bruggeman - Investor
Tel: +54.11.5258.0920 E-mail:           Relations Tel: +1.416.884.3556
willem@abraplata.com                    Email: rob@abraplata.com

//et

This news release includes certain "forward-looking statements"
under applicable Canadian securities legislation. Forward-looking
statements are necessarily based upon a number of estimates and
assumptions that, while considered reasonable, are subject to known and
unknown risks, uncertainties, and other factors which may cause the
actual results and future events to differ materially from those
expressed or implied by such forward-looking statements. All statements
that address future plans, activities, events or developments that the
Company believes, expects or anticipates will or may occur are
forward-looking information. There can be no assurance that such
statements will prove to be accurate, as actual results and future
events could differ materially from those anticipated in such
statements. Accordingly, readers should not place undue reliance on
forward-looking statements. The Company disclaims any intention or
obligation to update or revise any forward-looking statements, whether
as a result of new information, future events or otherwise, except as
required by law.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

For further information about AbraPlata and its projects, please
visit the Company's website at www.abraplata.com.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1821300014TS11821301107-06594520180802