Source	MARKET NEWS
Date	08/02/2018
Time	03:20:27 PM

Company	 West Kirkland Mining Inc.
Title	Reports on Metallurgy of High Grade Surface Gold





    CDNX Symbol: WKM











Press Release





Reports on Metallurgy of High Grade Surface Gold at Gold MountainTarget 
Hasbrouck Gold Project, Tonopah, Nevada --->@NEWS RELEASE
WEST KIRKLAND MINING INC ("WKM,WKM-V;WSKKF,WKLDF-0")
- Reports on Metallurgy of High-Grade Surface Gold at
- Gold Mountain Target Hasbrouck Gold Project, Tonopah, Nevada

West Kirkland Mining Inc. ("West Kirkland", "WKM" or the "Company")
reports the results of preliminary metallurgical tests on
representative samples taken from the high-grade surface gold
mineralization the Company is currently investigating on Gold Mountain.
The samples were taken along a 3,000 ft (900 m) zone defined by surface
sampling lines. The Company is currently drilling this area with the
objective to add to its gold reserves in the district

These metallurgical results support the premise that the wide-spread
surface gold that the Company has located at high elevations on Gold
Mountain may be recoverable by heap leaching. Definitive testwork to
confirm that this material can be heap-leached will be performed
following drilling and successful resource definition. The current test
results are encouraging for the potential to add to the Company's heap
leach type reserves in the Tonopah District.

The Tonopah District is located in Southwest Nevada where there is
currently increased gold exploration interest.

Metallurgical Test Results

96-hour bottle roll tests performed by Kappes Cassiday & Associates
indicate a rapid recovery of over 90% gold and 50% silver at 0.15 mm
crush size, with low-to-moderate reagent consumption. Further tests
will be performed to understand metallurgical performance at coarser
crush sizes and to see if silver recovery further improves with
increased cyanide tenor.

//st

KCA        Calculated     Au Extracted, %    Calculated    Ag Extracted, %
Sample     Head, g                           Head, g
No.        Au/tonne                          Ag/tonne

82111 A    0.464          97             %   73.66         62            %

82112 A    1.040          96             %   302.25        58            %

82113 A    2.189          96             %   69.33         46            %

82114 A    0.481          94             %   18.31         30            %

82115 A    1.624          94             %   41.23         34            %

82116 A    2.005          94             %   79.42         56            %

82117 A    0.288          95             %   11.98         32            %

82118 A    1.549          95             %   74.71         70            %

82119 A    2.534          92             %   87.64         71            %

//et

Composite samples were taken from locations on Gold Mountain shown
here:

A photo accompanying this announcement is available at
http://www.globenewswire.com/NewsRoom/AttachmentNg/ac4c9328-93f3-4841-b9db-
7a3d30551a26

ABOUT THE HASBROUCK GOLD PROJECT

The Company holds a 75% interest in the Hasbrouck Gold Project with
a permit to construct and operate the first part of the mine. The
Company holds a 100% option interest in the new Gold Mountain area
contiguous with the Hasbrouck pit reserves. The Hasbrouck Gold Project
contains Proven & Probable Reserves of 784,000 gold equivalent oz,
(45,270,000 tons at 0.6 Au g/t for 762,000 contained Au oz; 8.0 Ag g/t
for 10,569,000 contained Ag ounces. NPV5 Post Tax estimated at US$120M,
IRR 43% (US$1,275/oz Au) (Technical Report and Updated Preliminary
Feasibility Study for The Hasbrouck and Three Hills Gold-Silver
Project, Esmeralda County, Nevada, USA, Report Date: September 14,
2016).

QUALIFIED PERSON

R. Michael Jones P.Eng., CEO of West Kirkland Mining, is a
non-independent Qualified Person as defined by NI 43-101. He has
reviewed the information contained in this news release and has
verified the data by hiring qualified geologists and engineers and has
completed a review of the detailed technical information. Mineral
Reserve information in this news release relating to the Hasbrouck Gold
Project has been developed and approved by Thomas L. Dyer, P.E., of MDA
following CIM standards.

QUALITY ASSURANCE/QUALITY CONTROL

West Kirkland Mining utilizes a well-documented system of inserting
blanks and standards into the assay stream and has a strict chain of
custody for samples taken by WKM.  Assays by WKM are completed at
independent laboratories which have internal quality assurance and
quality control systems and procedures.  Assays were performed by ALS
Chemex Labs Ltd., by fire assay and ICP methods. The metallurgical
results were completed by Kappes Cassiday & Associates an experienced
lab in heap leach recovery.

On behalf of West Kirkland Mining Inc.  "R. Michael Jones"  Chief
Executive Officer

For further information, please see the Company's website at
www.wkmining.com or contact us by email at info@wkmining.com.

Disclaimer for Forward-Looking Information

This press release contains forward-looking information or
forward-looking statements (collectively "forward-looking information")
within the meaning of applicable securities laws. Forward-looking
information is typically identified by words such as: "believe",
"expect", "anticipate", "intend", "estimate", "postulate" and similar
expressions, or are those, which, by their nature, refer to future
events.  Forward-looking information in this news release includes,
without limitation, the exploration and project approach of a
Prefeasibility Study.  Historical mineral title also has risk of an
unrecorded claim. The Company cautions investors that any
forward-looking information provided by the Company is not a guarantee
of future results or performance, and that actual results may differ
materially from those in forward-looking information as a result of
various factors, including, but not limited to, the state of the
financial markets for the Company's equity securities, the state of the
market for gold or other minerals that may be produced generally,
variations in the nature, quality and quantity of any mineral deposits
that may be located, the Company's ability to obtain any necessary
permits, consents or authorizations required for its activities, to
raise the necessary capital or to be fully able to implement its
business strategies and other risks associated with the exploration and
development of mineral properties.  The reader is referred to the
Company's public filings for a more complete discussion of such risk
factors and their potential effects which may be accessed through the
Company's profile on SEDAR at www.sedar.com.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TEL: 604-685-8311    WEST KIRKLAND MINING INC
FAX: 604-484-4710
E-mail: info@wkmining.com
Website: http://www.wkmining.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1821300043TS11821302340-15183120180802