Source	MARKET NEWS
Date	08/07/2018
Time	05:02:55 AM

Company	 Stratabound Minerals Corp.
Title	Golden 
Culvert Project Update, Yukon Territory





    CDNX Symbol: SB











Press Release





STRATABOUND MINERALS CORP ("SB-V")
- Golden Culvert Project Update, Yukon Territory

Stratabound Minerals Corp. ("Stratabound" or "the Company") is
pleased to provide a progress report for the ongoing exploration
campaign on its Golden Culvert Project located in the Hyland Valley
gold district of the southeast Yukon Territory.  Key features of the
Project are the 250 metre wide by 3 kilometre long +30 parts per
billion (ppb) gold-in-soil anomaly and the exposed quartz veins in
outcrop assaying up to 23.8 gpt gold.  The exploration target is
orogenic-type broad, low grade gold mineralization in sediment hosted
wall rocks centred around higher grade gold bearing quartz veins.  The
Hyland Gold District also includes Goldstrike Resources Ltd.'s Plateau,
Golden Predator Mining Corp.'s 3 Aces and Banyan Gold's Hyland
projects, all located within the Hyland Group of sedimentary rocks.

Road and Trenching:

As previously reported, the 2 kilometre road to the work site was
completed in mid-June.  Since then the road has been extended to access
6 trenches across 800 metres strike of the strongest portion of the
gold-in-soil anomaly to the southeast of the main discovery showing.
Shallow trenching totaling 1.6 kilometres over six trenches has now
been recently completed of which 750 metres have exposed the bedrock
sufficiently for mapping and sampling.  From the trenching a total of
515 samples have been collected to date, of which only 17% of these
assays have been received.  The Company is expecting further assay
results in the next 2-3 weeks.
Geological Mapping and Early Interpretations:

First pass geological mapping of the first six trenches has
identified a very large pervasive hydrothermal system of sericite,
silica and sulphide altered phyllite host rocks that is greater than
0.5 km wide and open beyond the 800 m of strike mapped to date.  The
+30 ppb gold-in-soil anomaly is zoned within the larger newly
identified hydrothermal system.

Also, very significantly, the system hosts a 400 metre wide
corridor of at least 7 major quartz veins up to 3 metres wide that are
traced continuously beyond the 800 metres of strike length of trenching
completed so far.  Oxidized and sulphidized quartz vein surface float
is observed to extend beyond the 800 metres of mapped areas along and
across strike.

The veins have the same 310-330 orientation as the gold-in-soil
anomaly and are mineralized with oxidized sulphides to a varying
degree. Most significantly, the quartz veins when accompanied by the
stronger oxidation/sulphidation mineralization are coincident with the
higher gold-in-soil anomaly trends.

The dip of the veins averages -80 both east and west.  The veins
are oriented parallel to the regional foliation fabric.   The primary
near-vertical quartz veins are accompanied in places by sets of 1 mm
sheeted veins, or "flats".  These extension veinlets into the wall rock
are known from previous work to occasionally host gold mineralization.
More work is required to understand the gold deposition within the
entire system as the veins pass through the gold-in-soil anomaly.

It is important to note that the vein corridor is not only traced
along strike but also vertically between the 1500 metre elevation at
trench TR1801 and the 1800 metre elevation at trench TR1808 (800 metres
to the south), providing a determination of a minimum 300 metre
vertical, 400 metre wide and 800 metre long horizontal strike extent
where it remains open beyond that mapped to date.

Diamond Drilling:

The diamond drill arrived on site July 24th and commenced drilling
on July 27th.  About 1,000 metres of drilling is planned to cover about
500 metres of strike length to a vertical depth of about 180 metres
from surface.  It is expected that core will be logged and split by the
end of August.  Drill results are expected by the middle of September.

President and CEO R. Kim Tyler commented, "We have made some very
exciting new discoveries on Golden Culvert so far and are very pleased
with the progress and quality of work performed by our contractors and
suppliers.  Besides the very large hydrothermal envelope that hosts and
helps explain the large gold-in-soil anomaly, we have also confirmed a
coincident large multi-quartz vein corridor that has proved to be much
larger, more continuous and more extensive than first thought.  The
strongest gold mineralization indicated by the gold-in-soil anomaly is
also visually coincident with strong oxidized sulphide mineralization
associated with the quartz veining in the corridor, all good
indicators.  The few assay results received to date indicate gold
mineralization exists outside the known gold-in-soil anomaly.  We look
forward to receiving all the trench assay results so that we can put
the full picture together.  Diamond drilling is now proceeding as
planned."

Mr. R. Kim Tyler, P.Geo., President and CEO of Stratabound, is a
"Qualified Person" for the purpose of NI 43-101 and has reviewed and
approved the contents of this news release.

About the Golden Culvert and Little Hyland Properties

Golden Culvert and Little Hyland cover 83.8 square kilometres in
the southeast Yukon Territory across a 24-kilometre strike located
approximately 20 kilometres northeast of and parallel to Golden
Predator Mining Corp.'s 3 Aces property.  Work filed in Yukon mineral
claims assessment reports has outlined a northerly trending, 3
kilometre by 250 metre, +30 ppb Au up to 791 ppb Au gold-in-soil
anomaly that remains open at both ends.  The soil anomaly is centred
around partially exposed primary gold-bearing quartz veins grading
between 7.7 to 22.8 gpt gold over 1 metre and complimentary
gold-bearing quartz vein stockwork within a larger silicified, altered,
sulphide and gold-bearing wallrock grading up to 2.27 gpt gold over 0.5
metre.

Prior to this summer's exploration program a total of $564,400 of
work had been done on the Property, including 3,645 soil samples, 48
stream samples, 239 rock samples,  19.4 line-km of ground magnetic
survey and 18.5 line-km of VLF survey.  This summer's program of $1.1
million includes trenching and drilling to further define the highly
mineralized areas of the property.

About Stratabound

Stratabound Minerals Corp. is a Canadian exploration and
development company focused on the Yukon Territory and to a lesser
extent the Bathurst Mining Camp in New Brunswick.  Stratabound
management has a diversified track record of exploration, development
and operating successes that will facilitate the development of the
Company's exploration projects.

For further information, please see the Golden Culvert
presentation and the NI 43-101 technical report on the Stratabound web
site, www.stratabound.com.



R. Kim Tyler, President and CEO

Ritu Gupte, Investor Relations Consultant
rgupte@stratabound.com
647-267-5380
www.stratabound.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

WARNING: the Company relies upon litigation protection for
"forward looking" statements. The information in this release may
contain forward-looking information under applicable securities laws.
This forward-looking information is subject to known and unknown risks,
uncertainties and other factors that may cause actual results to differ
materially from those implied by the forward-looking information.
Factors that may cause actual results to vary materially include, but
are not limited to, inaccurate assumptions concerning the exploration
for and development of mineral deposits, currency fluctuations,
unanticipated operational or technical difficulties, changes in laws or
regulations, failure to obtain regulatory, exchange or shareholder
approval, the risks of obtaining necessary licenses and permits,
changes in general economic conditions or conditions in the financial
markets and the inability to raise additional financing. Readers are
cautioned not to place undue reliance on this forward-looking
information. The Company does not assume the obligation to revise or
update this forward-looking information after the date of this release
or to revise such information to reflect the occurrence of future
unanticipated events, except as may be required under applicable
securities laws.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1821700001TS11821700698-07333720180806