Source	MARKET NEWS
Date	08/09/2018
Time	08:33:50 AM

Company	 Nortec Minerals Corp.
Title	Provides 
Revised Model and Defines New Targets o





    CDNX Symbol: NVT











Press Release





NORTEC MINERALS CORP ("NVT-V;NMNZF-0")
- Provides Revised Model and Defines New Targets on the Tomboko Permit

NORTEC MINERALS CORP. (the "Company" or "Nortec") announces
that staff have defined a new structural interpretation of the geology
at the TOM 1 North gold target on the Tomboko exploration project. The
Tomboko Permit is located in North Eastern Guinea, West Africa (Figure
1).



Figure 1: Location Map. Guinea, West Africa




(img
src='https://www.thenewswire.com/data/tnw/clients/img/2e0163705359f099f51db
66de7c16009_.png' /) @
https://www.thenewswire.com/data/tnw/clients/img/2e0163705359f099f51db66de7
c16009.png' target='_blank
Click Image To View Full Size



1.Phase I exploration drilling at TOM 1 North produced significant
@ ' target='_blank results with grades of 9 m at 2.74 g/t gold from 32
m, including 3.57 m at 3.91 g/t gold from 36 m and 7 m at 3.57 g/t gold
from 43 m, including one m at 17.1 g/t gold from 45 m.

2.Phase II, follow up RAB drilling did not produce expected
results

3.Phase III trenching produced 24m@3.66g/t incl. 4m@10g/t from
18m;

4.Starting in June of 2018 Dr Serigne Dieng and staff have worked
to build a structural and lithological model to explain the broader
results as well as defined vectors for expanding the high grade results
obtained in drill core and trenches.




This work has resulted in a clear and coherent model for
structurally-controlled gold mineralization hosted in faulted and
sheared contact between volcano-clastic successions extending along a
NNW-striking, NE-steeply dipping structure that is offset by a series
of parallel NE-trending late fault systems (Figures 2 & 3).

(img
src='https://www.thenewswire.com/data/tnw/clients/img/d7d217cb9c0465eec46b9
35bdbec64cd_.png' /) @
https://www.thenewswire.com/data/tnw/clients/img/d7d217cb9c0465eec46b935bdb
ec64cd.png' target='_blank
Click Image To View Full Size          (img
src='https://www.thenewswire.com/data/tnw/clients/img/15ff1c90e44e07b8b1bd8
111689e6ea3_.png' /) @
https://www.thenewswire.com/data/tnw/clients/img/15ff1c90e44e07b8b1bd811168
9e6ea3.png' target='_blank
Click Image To View Full Size

(img
src='https://www.thenewswire.com/data/tnw/clients/img/6d25397a6aa20237daae8
5147590cb3f_.png' /) @
https://www.thenewswire.com/data/tnw/clients/img/6d25397a6aa20237daae851475
90cb3f.png' target='_blank
Click Image To View Full Size

Figure 2: Geological and structural map of the TOM 1 North gold
target

(img
src='https://www.thenewswire.com/data/tnw/clients/img/b62059973610bccf99743
4272145d6d3_.png' /) @
https://www.thenewswire.com/data/tnw/clients/img/b62059973610bccf9974342721
45d6d3.png' target='_blank
Click Image To View Full Size

Figure 3: Geological Cross-Section and Plan view map at TOM 1
North gold Target

Dr Dieng explains on the new model, "This new model suggests that
the Tomboko gold deposit is a classical greenstone - orogenic-type gold
deposit hosted in faulted and sheared contact between volcano-clastic
successions. The gold mineralization is structurally-controlled and
occurs in deformed zones of large and highly hydrothermally altered,
NNW-striking, NE-steeply-dipping, structural corridors that contain a
complex network of extensional dilation fracture systems associated
with the Late Birimian tectonism that have affected the West African
Shield. New outcrops discovered south and north of the drilled area
indicate that the deposit could have a strike length of about 3
kilometers. All of these new insights show that the Tomboko deposit has
a very high potential for hosting multi-million ounce gold
mineralization. Further aggressive exploration programs including
extensive RC drilling is highly recommended to define and delineate
resources of the Tomboko deposit"

Dr. Dieng, Ph.D., AusIMM, has and is conducting the structural
studies of all the data to date. Serigne has 20 years' experience in
geological and structural interpretation, modelling and target
generation in West Africa. He is a registered qualified professional
geoscientist in accordance with NI 43-101 and JORC standards. He
received his Ph.D. in Structural Geology, Exploration Geochemistry and
Ore Deposit Genesis from Queens University, Kingston, Ontario, Canada
(see News Release June 6, 2018).

Interpretation

The diamond drilling and RAB drilling programs consisting of
approximately 1900 meters and 4000 meters respectively focused on the
original interpretation that the mineralization was dipping to the
southwest at 45 to 50 degrees.

Dr. Dieng examined the drill core in detail, carried out field
work in the Tom 1 North area and carried out detailed interpretation of
the structural controls of mineralization. He arrived at the following
conclusions:




1the gold mineralization is structurally-controlled and hosted in
faulted and sheared contact between volcano-clastic successions that
are composed of Ash tuffs and lapilli tuffs;

2the shear zone that control the gold mineralization strikes NNW
(N350) and steeply dips NE at 75, (not 45 West as previously
interpreted), (Figures 2 & 3);

3the gold mineralization is associated with pervasive magnetite,
chlorite, tourmaline, carbonate, quartz and disseminated pyrite and
arsenopyrite (Figure 4);

4several parallel late post-mineralization NE-trending fault
systems offset and displace the gold bearing structure (Figure 2);

5the sedimentary rocks are composed of siltstone and sandstone
layers; the volcanoclastic rocks consist of tuffs and pyroclastic
rocks; and,

6on the light of this investigations, the Tomboko deposit has a
very good potential for hosting an economic gold mineralization.




(img
src='https://www.thenewswire.com/data/tnw/clients/img/495d31f9f4e7b24710be7
2a670f8f83e_.png' /) @
https://www.thenewswire.com/data/tnw/clients/img/495d31f9f4e7b24710be72a670
f8f83e.png' target='_blank
Click Image To View Full Size

Figure 4: Gold mineralization in drill core associated with
pyrite, chlorite, magnetite and quartz.

Conclusions & Recommendations

In view of the new interpretation of structural controls of the
gold mineralization in the Tom 1 North target, an infill termite
geochemical survey (Figures 5 & 6) was initiated to confirm the
mineralized structure over the potential deposit area and the expected
extensions. The results will be released on receipt.

(img
src='https://www.thenewswire.com/data/tnw/clients/img/8bef3a34d725e7a98ab03
a6f71ee6896_.png' /) @
https://www.thenewswire.com/data/tnw/clients/img/8bef3a34d725e7a98ab03a6f71
ee6896.png' target='_blank
Click Image To View Full Size

Figure 5: Highly altered, sheared and gossanous rocks with
pervasive magnetite and sulphide boxworks outcrop north and south of
the main zone over a strike length of about 3 kilometers.

(img
src='https://www.thenewswire.com/data/tnw/clients/img/2bb57eddaa4a533b6c065
9f42276a55d_.png' /) @
https://www.thenewswire.com/data/tnw/clients/img/2bb57eddaa4a533b6c0659f422
76a55d.png' target='_blank
Click Image To View Full Size

Figure  @ ' target='_blank1: Infill termite mound sampling program
to define the extensions of the gold zone.




For quality control, the drill cores were sawed in half and the
chip samples were split in half.  A duplicate, a blank and a standard
were inserted every 10th sample for quality control. Samples are
processed by Fire Assay with A.A. finish under the SGS FAA505 protocol.
The samples were analysed by SGS Labs, an accredited laboratory in
Bamako, Mali. RAB samples were also logged in detail, split into 2 kg
to 3 kg samples and also analysed by SGS Labs.

Mohan R. Vulimiri, M.Sc., P.Geo, CEO, Director and Michael
Collins, B.Sc (Honours), P.Geo. Director are Qualified Persons as
defined by NI 43-101. Mr. Vulimiri and Mr. Collins have approved the
corporate and technical content contained in this press release.

About Nortec Minerals Corp.

Nortec is a mineral exploration and development company based in
Vancouver, British Columbia.  Nortec earned a 51% interest in the
Tomboko project.

The Company also has a 20% interest in the Tammela Lithium and
Gold Project in South-West Finland. Sunstone has completed more than
3,000 meters diamond drilling on the Kietyonmaki Lithium prospect and
the Satulinmaki and Riukka gold prospects that comprise the Tammela
Project.

Detailed information on the Company's projects have been posted on
the Company's website www.nortecminerals.com.
//st

--------------------------------------
|On behalf of the Board of Directors,|
|Nortec Minerals Corp.               |
|Mohan R. Vulimiri                   |
|Mohan R. Vulimiri, CEO and Chairman |
|                                    |
--------------------------------------

//et

@ ' target='_blankThe TSX Venture Exchange has not reviewed and
does not accept the responsibility for the adequacy or accuracy of this
news release.  @ ' target='_blank @ ' target='_blank

This press release contains certain forward looking statements
which involve known and unknown risks, delays and uncertainties not
under the Company's control which may cause actual results,
performances or achievements of the Company to be materially different
from the results, performances or expectations implied by these forward
looking statements. This news release does not constitute an offer to
sell or a solicitation of an offer to buy any of the securities in the
United States.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1822000033TS11822001244-08314620180809