Source	MARKET NEWS
Date	07/31/2018
Time	05:22:32 AM

Company	 Juggernaut Exploration Ltd.
Title	Commences Inaugural Drill Campaign On Its Empire





    CDNX Symbol: JUGR











Press Release





Commences Inaugural Drill Campaign On Its Empire Property --->@NEWS RELEASE
JUGGERNAUT EXPLORATION LTD ("JUGR-V")
- Commences Inaugural Drill Campaign On Its Empire Property

Juggernaut Exploration Ltd. (the "Company" or "Juggernaut") is
pleased to report it has commenced diamond drilling and IP programs on
its Empire property, 40 km northeast of Terrace British Columbia.

JUGGERNAUT PROGRAM HIGHLIGHTS:

*  Inaugural drill program started on Empire at the MaxMin zone
*  2018 IP survey at Big One identifies significant chargeability
anomaly in the subsurface coincident with the airborne EM anomaly
*  New Jay-Bear zoned discovered on Empire that is situated on
regional northwest trending geophysically indicated structure
*  Diamond drilling will commence August 7th on Midas.

MAX MIN AND METALWORKS ZONE EXPLORATION UPDATE

The drill program will start on the Max Min Zone (Link to Drill
Pad photo at Max Min) which measures 170 m by 100 m and remains open in
all directions, including to depth. Channel highlights from Max Min
include 4.8 gpt Au, 0.26 % Cu, 3.73 % Zn, 4.85 % Pb over 4.6 meters
that ended in mineralization (see Nov 29th Press Release).

The Empire inaugural drill program will focus on targeting the
widespread gold and polymetallic mineralized zones along the 5.5 km
Inca Trend (link to new Empire map). The mineralization and alteration
at Max Min and Metalworks (Link to Drill Pad Photos at Metalworks) at
the northern end of the Inca Trend, strongly indicates the presence of
a polymetallic feeder system at depth. Towards the southern end on the
Inca Trend, at Rockstar, the mineralization and alteration are more
typical of a volcanic massive sulphide mineralizing system; the same
can also be said for the Big One zone to the north.

BIG ONE EXPLORATION UPDATE

The Big One target is a strongly conductive, subsurface tabular
body consistent with a VMS target (see Feb 12th Press Release) (Link to
3D Big One Video). The 2018 ground IP program just completed on the Big
One target also identified a significant chargeability anomaly in the
subsurface that is coincident with the 2017 SkyTem survey EM anomaly.
Drill collars and pads are being sited and built in preparation for
drilling this VMS target in the immediate future.

ROCKSTAR ZONE UPDATE

Mapping, prospecting, IP, and channel sampling remains ongoing
over an area of 1.5 km by 550 metres, and many new areas containing
mineralization have been found in 2018. Drill collars and pads are
being sited and built in preparation for testing the mineralization to
depth and along strike (link to new Rockstar discovery video).

NEWLY DISCOVERED J-BEAR ZONE ON EMPIRE PROPERTY

Initial prospecting on Empire has already resulted in the
discovery of the new J-Bear Zone in an area of receding snowpack and
ice. The J-Bear Zone was discovered along a regional northwest trending
magnetic high. Grab and channel samples from this zone contained
massive chalcopyrite and bornite and were collected over an area of
approximately 150 metres by 20 metres (link to new J-Bear zone video).
The J-Bear Zone remains open and the area will be mapped and prospected
as the snow and ice continue to recede. Assays results are pending.

MIDAS PROPERTY EXPLORATION UPDATE

The Midas property is located in a world class geologic setting
and contains the King Solomon zone, a 2.1 by 1.6 km region that is
defined by widespread bedrock-hosted, polymetallic and gold mineralized
channel, chip and grab samples. The widespread gold and polymetallic
mineralized showings, anomalous soil geochemistry and extensive
alteration suggest the King Solomon Zone may be the surface expression
of a significant hydrothermal system.

Juggernaut plans to begin its inaugural drill program on Midas
with a second drill rig set to start within a week. Drilling will
target several zones of bedrock polymetallic and gold mineralization on
the King Solomon Zone that contains channel cuts of up to 4.43 meters
of 10.28 grams per tonne gold (see Jan 15th Press Release).

Mr. Dan Stuart, Director, President and CEO of Juggernaut states:

"We look forward to reporting drill results from these exciting
new discoveries from both the Empire and Midas properties with much
anticipation."

Qualified Person

Stefan Kruse, Ph.D., P. Geo., Chief Geologist, is the qualified
person as defined by National Instrument 43- 101, for Juggernaut
Exploration projects, and supervised the preparation of, and has
reviewed and approved, the technical information in this release.

Other

All rock, channel and talus fine samples were crushed and
pulverized at ALS Canada Ltd.'s lab in Terrace, BC or in Reno Nevada.
ALS is either Certified to ISO 9001:2008 or Accredited to ISO
17025:2005 in all of its locations. The resulting sample pulps were
analyzed for gold by fire assay in Reno, Nevada or in Vancouver, BC.
The pulps were also assayed using multi-element aqua regia digestion at
ALS Canada Ltd.'s lab in Vancouver, BC. The silt samples were sieved
and assayed at ALS Canada Ltd.'s lab in Vancouver, BC. The coarse
reject portions of the rock, channel and talus fine samples, as well as
the pulps, were shipped to J2 Syndicate's storage facility in Terrace,
BC. The silt samples were disposed of after analysis. All samples were
analyzed using ALS Canada Ltd.'s assay procedure ME-ICP41, a 1:1:1 aqua
regia digestion with inductively-coupled plasma atomic emission
spectrometry (ICP-AES) or inductively-coupled plasma mass spectrometry
(ICP-MS) finish for 35 elements as well as the Au-AA24 lead-collection
fire assay fusion procedure with atomic absorption spectroscopy (AAS)
finish. Any results greater than 100 ppm for silver or 10,000 ppm
copper, lead and zinc were additionally assayed using ALS's OG46 method
particular to each element. This method used an HNO(sub)3(/sub)-HCl
digestion followed by ICP-AES (or titrimetric and gravimetric
analysis). Gold values of greater than 10 ppm Au were assayed by the
Au-GRA22 method which includes a fire-assay fusion procedure with a
gravimetric finish. Blanks and duplicates QA/QC samples were inserted
into channels sample laboratory batches. Additionally, and 10%
sub-sample of pulp and reject material was sent to Activation
Laboratories in Ancaster Ontario, for check-analysis.

The reader is cautioned that grab samples are spot samples which
are typically, but not exclusively, constrained to mineralization. Grab
samples are selective in nature and collected to determine the presence
or absence of mineralization and are not intended to be representative
of the material sampled.

For more information please contact:

Juggernaut Exploration Ltd.
Mr. Dan Stuart
President and Chief Executive Officer
Tel: (778) 223-0293
dan@juggernautexploration.com
Website: JuggernautExploration.com

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
RELEASE.

FORWARD LOOKING STATEMENTS

Certain disclosure in this release may constitute forward-looking
statements that are subject to numerous risks and uncertainties
relating to Juggernaut's operations that may cause future results to
differ materially from those expressed or implied by those
forward-looking statements, including its ability to complete the
contemplated private placement. Readers are cautioned not to place
undue reliance on these statements. NOT FOR DISSEMINATION IN THE UNITED
STATES OR TO U.S. PERSONS OR FOR DISTRIBUTION TO U.S. NEWSWIRE
SERVICES. THIS PRESS RELEASE DOES NOT CONSTITUTE AN OFFER TO SELL OR AN
INVITATION TO PURCHASE ANY SECURITIES DESCRIBED IN IT.

TEL:  (778) 223-0293  Mr. Dan Stuart
President and Chief Executive Officer
Juggernaut Exploration Ltd.
EMAIL:  dan@juggernautexploration.com
WEBSITE:  JuggernautExploration.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1821100002TS11821100385-05213120180731