Source	MARKET NEWS
Date	07/31/2018
Time	06:46:58 AM

Company	 Pangolin Diamonds Corp.
Title	Drills 
into Kimberlite Dyke, Botswana Africa; Mi





    CDNX Symbol: PAN











Press Release





PANGOLIN DIAMONDS CORP ("PAN-V;KGHZF-0")
- Drills into Kimberlite Dyke, Botswana Africa; Mini-Bulk
- Sample of 100 Tonnes Planned to Determine Diamond Content

Pangolin Diamonds Corp. (the "Company" or "Pangolin") is pleased
to provide an update on the drilling programme at Pangolin's 100% owned
Malatswae Diamond Project, Botswana, Africa.

-Two diamonds recovered at surface in excess of 1mm in long axis
size
-BH1 - Kimberlitic garnets with Class 1 surface textures recovered
at a vertical depth between 21.6 and 26.9 m
-BH2 - Kimberlitic garnets with primary surface textures recovered
at a vertical depth between 47.6 m and 52.8 m
-BH3 - Kimberlitic garnets with primary surface textures recovered
at a vertical depth between 21.6 and 26.9 m
-The combination of the soil sample and drilling results are
indicative of a diamondiferous kimberlite dyke system at MAL 001
-Once core drilling is completed, a mini-bulk sample of at least
100 tonnes will be undertaken to determine the diamond content for the
kimberlite

Following a 24-month soil sample programme sampling the same 4
hectare grid monthly, a well defined kimberlite indicator anomaly was
identified in the MAL 001 area of the Malatswae Diamond Project.  The
indicators were analysed and reported on 08 May 2018 (see news release
- May 8 2018). The majority of the indicators analysed are garnets (93)
and consist predominantly of peridotitic garnets which include 4 x G10
garnets and an additional 41 garnets consistent with a derivation from
the diamond stability field.

Two diamonds, both in excess of 1mm in long axis size, were also
recovered from the soil samples at MAL001.  The presence of the
diamonds is consistent with the observed garnet compositions above.

A detailed groundmagnetic survey has been completed over the 4
hectare area and no magnetic anomaly is present.  The distribution of
the recovered diamonds and indicators are concentrated in the central
part of the area covered by the groundmagnetic survey and suggests that
the source of the indicators extends beyond the northern and southern
limit of the survey area.

Borehole MAL 001/BH1 was drilled with an air percussion drill at
an angle of 60 degrees from the horizontal in a southwesterly direction
to intersect possible source rocks below the indicator anomaly.
Geological logging of the percussion chips from this borehole indicate
that Kalahari sediments depth and the top of the surrounding Karoo
rocks is at a vertical depth of 17.3m at this position. Samples were
collected on a 6m interval basis and processed through a mini-DMS 1 tph
plant for indicator minerals. Garnets with Class 1 surface textures
were recovered from the drilled material between the drill hole depth
intersection of 25m to 31m, which is equivalent to a vertical depth
between 21.6 and 26.9 m.

Boreholes MAL 001/BH2 and MAL 001/BH3 were drilled 50 metres to
the south east from MAL 001/BH1 with an air percussion drill at an
angle of 60 degrees from the horizontal in a northeasterly direction to
intersect possible source rocks below the indicator anomaly.  Samples
were collected on a 6m interval basis and processed through a mini-DMS
1 tph plant for indicator minerals.

Garnets with primary surface texture were recovered from the
drilled material of borehole MAL 001/BH2 between the drill hole depth
intersection of 55m to 61m, which is equivalent to a vertical depth
between 47.6 m and 52.8 m.

Borehole MAL 001/BH3 was drilled 15 m to the northeast of borehole
MAL 001/BH2. In both holes, geological logging of the percussion chips
from this borehole indicate that Kalahari sediments depth and the top
of the surrounding Karoo rocks is at a vertical depth of 19.0m at this
position. Garnets with primary surface textures were recovered from the
depth interval of 25 to 31 m, which is equivalent to a vertical depth
between 21.6 and 26.9 m.  This positive recovery is vertically
correlated with the positive recovery of indicators in borehole MAL
001/BH2.

The combination of the soil sample and drilling results are
indicative of a diamondiferous kimberlite dyke system at MAL 001.  A
systematic programme to assess the economic potential of the dyke
system will be undertaken.  Initially, a core drilling programme will
be undertaken to determine the width and extent of the dyke system.
Once the core drilling programme has been completed a mini-bulk sample
of at least 100 tonnes will be undertaken to confirm and determine the
diamond content for the kimberlite.

In addition, following the Marsfontein model where an enlargement
was discovered on a diamondiferous dyke system, a programme to search
for an enlargement on the MAL 001 dyke system has commenced.  Soil
sampling will be extended to the north and the south of the current
sampling grid.  An extended groundmagnetic survey has produced an
anomaly of approximately 1.5 hectares on strike about 500 m to the
southeast of borehole MAL 001/BH3.  A detailed soil sample programme
over the groundmagnetic anomaly has been initiated.

Kimberlite dykes have been successfully mined in South Africa for
more than sixty years. The Bellsbank dykes have been mined for diamonds
since 1956.  Other kimberlite dyke mines in South Africa are
Swartruggens, Sover, Star and Klipspringer.  Enlargements in the form
of small pipes have been found at Bellsbank, Star and Marsfontein.

DRILLING UPDATE

Drilling on PAN Projects in Botswana continues in the third
quarter. Due to large sample backlogs at laboratories, analytical
results from the drilling conducted earlier in the year have not been
received. Results will be announced once the analytical data is
available and has been assessed.

Quality Control and Quality Assurances Quality assurance
procedures, security, transport, storage, and processing protocols
conform to chain of custody requirements.

The technical disclosure in this news release has been reviewed and
approved by Miracle Muusha MSc and a Qualified Person as defined by
National Instrument 43-101.

About Pangolin Diamonds Corp. and Our Social Connections For more
information on Pangolin Diamonds Corp., please visit our website at
http://pangolindiamonds.com

Follow us on Twitter @pangolindiamond and Facebook at Pangolin
Diamonds Corp

Pangolin Diamonds Corp.

Contact Information:

Contact:Scott Young, Investor Relations
Phone: +1.705.888.2756
Email: syoung@pangolindiamonds.com

Graham C. Warren, Chief Financial Officer
Phone: +1.416.594.0473
Fax: +1.416.594.1630
Email: gwarren@pangolindiamonds.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1821100019TS11821100819-06435820180731