Source	MARKET NEWS
Date	08/27/2018
Time	10:29:28 AM

Company	 Namibia Critical Metals Inc.
Title	Identifies Multiple Targets from Airborne EM Sur





    CDNX Symbol: NMI











Press Release





Identifies Multiple Targets from Airborne EM Survey Over KuneneCobalt Copper 
Project --->@NEWS RELEASE
NAMIBIA CRITICAL METALS INC ("NMI-V")
- Identifies Multiple Targets from Airborne EM Survey Over Kunene
- Cobalt-Copper Project

Namibia Critical Metals Inc. ("Namibia Critical Metals" or the
"Company") announced that the SkyTEM airborne geophysical survey has
been completed over the Kunene Cobalt-Copper project in northern
Namibia. Preliminary data has been provided and an initial evaluation
of the electromagnetic ("EM") responses shows clear conductive trends
associated with favourable sedimentary horizons and structures known to
be associated with cobalt-copper mineralization (Figure 1). Of
particular interest are the prolific number of responses along a 20
kilometer-long segment of the interpreted extension of the Dolomite Ore
Formation ("DOF") and along a 15 kilometer-long segment of the
Okanihova lineament. The DOF hosts the Opuwo cobalt-copper-zinc deposit
of Celsius Resources, and historic drilling by First Quantum Minerals
intersected anomalous copper and cobalt along the Okanihova lineament
(Figure 2). Two more isolated targets have been identified at Okanihova
East and Olulilwa Southwest.  Secondary targets are associated with
contact zones along the Western Target magnetic anomaly and in
sedimentary horizons parallel to the interpreted DOF extension in the
northwest over a strike length of 20 kilometers.

Don Burton, President of Namibia Critical Metals, stated "The
SkyTEM survey has exceeded our expectations in terms of the prolific
number of targets it has identified and the detail in which it has
mapped the favourable sedimentary formations and structures. This is a
very preliminary assessment of an invaluable database that immediately
provides us with the ability to pinpoint drill targets on the ground.
We will undertake a systematic reconnaissance drilling approach,
utilizing one diamond drill and one reverse circulation drill rig to
test multiple targets to accelerate the opportunity for deposit
discoveries. We are looking at a drill start up before the end of
September. Geophysical interpretations will be refined upon delivery of
final products from SkyTEM and this will include a more comprehensive
study for deep conductors."

To view the graphic in its original size, please click here

Figure 1 - Kunene Co-Cu Project Area showing SkyTEM airborne
survey area (white dash) and preliminary EM conductor picks for 5-10
channel and ) 10 channels responses. Responses for ( 5 channels not
shown. Channel responses are provided in picovolts/meter. Background
image is total magnetic intensity from the Namibian Geological Survey
database combined with satellite surface topography.

Airborne Survey Objectives and Outcomes

The Kunene project area covers over 720 km2 and is characterized
by widespread base metal and associated mineralization occurring in
discrete sedimentary horizons such as the DOF where Co-Cu is associated
with disseminations and veinlets of sulphide minerals, as well as
orogenic copper, and stratabound Zn-Pb mineralization. The stratabound
DOF hosts the Opuwo Co-Cu-Zn deposit which occurs on the contiguous
ground held by Celsius Resources ("Celsius") where it has been traced
for over 35 kilometers. This stratigraphic package is interpreted to
continue across the Kunene Project area and given the nature of the
mineralization and host lithologies (black shales with graphitic
members) it was decided to fly the area with EM.

The objectives of the airborne EM survey were to refine geological
and structural mapping under the largely covered areas, to delineate
conductive sedimentary horizons, to isolate conductive bodies that may
be indicative of near surface mineral deposits, and to detect sulphide
deposits and stockworks at depth. Previous work had identified three
large target areas primarily associated with Co-Cu anomalies identified
from regional soil sample surveys (Figure 2) which were confirmed by
detailed soil sampling (Figure 3). These areas were referred to as the
DOF Extension, the Western Targets and the Okanihova Targets. A primary
objective of the airborne EM survey was to delineate specific targets
within these regional geochemical anomalies for drilling.

To view the graphic in its original size, please click here

Figure 2 - Kunene Co-Cu Project Area showing principal targets
associated with DOF Horizon, structural lineaments, and  cobalt
anomalies (soil ICP) at regional 1 kilometer spacing. Celsius
Resources' land position to the east in cross hatching with the Opuwo
Deposit area in red rectangle.

Celsius has reported that the Opuwo deposit hosts a maiden JORC
compliant resource of 72.0 million tonnes at a grade of 0.11% cobalt,
0.42% copper and 0.41% zinc in the Indicated category, and a further
40.5 million tonnes at a grade of 0.12% cobalt, 0.41% copper and 0.46%
zinc in the Inferred category. It is noted that the mineralization on
the Celsius property may not be indicative of mineralization that may
be found on the Kunene project area held by Namibia Rare Earths.

SkyTEM ApS was contracted to fly the survey at a flight line
spacing of 200 meters on north-south oriented lines across the entire
project area. SkyTEM utilized their most powerful time domain EM system
(SkyTEM 312 HP) which provides superior resolution in the near-surface
environment (0-100 vertical meters) and comparable depth penetration
(300-400 vertical meters) when compared to its peers. The platform
included a Geometrics total intensity magnetometer and was installed on
an Astar 350 B3 helicopter operated by Savannah Helicopters. The survey
was flown in cooperation with similar coverage over the Celsius ground
which reduced survey costs related to mobilization and de-mobilization
charges and mitigated standby charges for weather days over mountainous
ground due to high winds. Total line kilometers flown on the Namibia
Critical Metals ground amounted to about 4,150 kilometers.

To view the graphic in its original size, please click here

Figure 3 - Kunene Co-Cu Project Area showing airborne survey area
(white border) and cobalt anomalies from detailed soil geochemical
surveys. Background image is total magnetic intensity from the Namibian
Geological Survey database combined with satellite surface topography.

The preliminary data was received on a bi-weekly basis and quality
control and assurance ("QAQC") was monitored by Robert E. Gillick and
Associates Ltd. ("Gillick") who are also providing independent
interpretations of the geophysical results. The SkyTEM system operates
in 2 transmission modes: a low magnetic moment transmission ("LM")
using 2 transmitter coil turns at 5 amperes, and a high magnetic moment
transmission ("HM") using 5 transmitter coil turns at 100 amperes.  The
HM mode is designed to energize and map deeper conductors; the LM mode
is designed for mapping weaker conductive sources nearer to the
surface. The final products will include inversion model resistivity
sections and plans incorporating both the HM and LM data. Gillick has
provided the preliminary EM response picks for the z-component of the
HM data as shown in Figure 1. The preliminary picks are qualitative at
this stage and do not take into account calculated source depths or
source conductivities. A more detailed quantitative interpretation will
be undertaken once final products are delivered.

Preliminary Drill Targets

A more comprehensive assessment of drill targets will be
undertaken once the final data is received however the preliminary
assessment clearly provides immediate targets along the DOF Extension,
in the southwest extension of the Okanihova lineament, at Okanihova
East and at Olulilwa Southwest.  Immediate focus will be given to these
targets and access tracks are in preparation. This first phase of
drilling will likely comprise 4,000 m of the available 7,500 m budget
and should be started before the end of September. Details of the drill
program and scheduling will be provided following further
interpretations and awarding of the drill contract.

Evaluation of Vanadium Anomaly with Coincident EM

Soil sample analyses show anomalous concentrations of vanadium on
the northern EPL 4347. Now that the SkyTEM survey has identified
conductive trends, it is apparent that there are several coincident
vanadium soil anomalies (100-250 ppm) in close proximity to the
interpreted DOF Extension. Elevated vanadium is also characteristic of
the Western Targets magnetic anomaly along with cobalt which was
previously noted from the regional and detailed soil surveys (Figure 3
and Figure 4). The Western Targets magnetic anomaly does not have any
internal EM conductors but there are indications of conductors along
its margins. Field crews will investigate these vanadium anomalies
further and drill target positioning will take this into account.

To view the graphic in its original size, please click here

Figure 4 - Kunene Co-Cu Project Area showing airborne survey area
(white dash) and vanadium anomalies from detailed soil geochemical
surveys. Note concentrations of vanadium anomalies proximal to DOF
Extension and with the Western Areas magnetic anomaly.  Background
image is total magnetic intensity from the Namibian Geological Survey
database combined with satellite surface topography.

Sample preparation and analyses of soil samples were carried out
by Activation Laboratories Ltd. (Windhoek, Namibia and Ancaster,
Ontario) employing appropriate ICP techniques and following strict
internal QAQC procedures inserting standards and duplicates.

Donald M. Burton, P.Geo. and President of Namibia Critical Metals
Inc., is the Company's Qualified Person and has reviewed and approved
this press release.

About Namibia Critical Metals Inc.

Namibia Critical Metals Inc. holds a diversified portfolio of
exploration and advanced stage projects in the country of Namibia
focused on the development of sustainable and ethical sources of metals
for the battery, electric vehicle and associated industries. The common
shares of Namibia Critical Metals Inc. trade on the TSX Venture
Exchange under the symbol "NMI".

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

For more information please contact -
//st

Namibia Critical Metals Inc. Don Burton, President Tel: +01 (902)
835-8760 Fax: +01 (902) 835-8761 Email: Info@NamibiaREE.com Web site:
www.NamibiaCriticalMetals.com

//et

The foregoing information may contain forward-looking information
relating to the future performance of Namibia Rare Earths Inc.
Forward-looking information, specifically, that concerning future
performance, is subject to certain risks and uncertainties, and actual
results may differ materially. These risks and uncertainties are
detailed from time to time in the Company's filings with the
appropriate securities commissions.

To view the original release (with media), please click here
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1823800044TS11823801392-08225120180827