Source	MARKET NEWS
Date	08/22/2018
Time	02:31:48 PM

Company	 GGX Gold Corp.
Title	Drilling 
Intersects 54.9 g/t Gold and 379 g/t Si





    CDNX Symbol: GGX











Press Release





GGX GOLD CORP ("GGX-V;GGXXF-0")
- Drilling Intersects 54.9 g/t Gold and 379 g/t Silver over
- 1.47 Meters Gold Drop Property, Southern British Columbia

GGX Gold Corp. (the "Company" or "GGX") is pleased to announce it
has received additional analytical results from its diamond drilling
program on the Gold Drop property, located near Greenwood, B.C. Drill
core analytical results have been received for 2018 drill holes
COD18-46 to COD18-48 which tested the COD Vein. The COD gold bearing
vein is located in the Gold Drop Southwest Zone.

Gold bearing quartz vein with high grade gold in drill hole
COD18-46

(54.9 g/t gold over 1.47meters)

To view the graphic in its original size, please click here

The highlight from these analytical results is an intersection of
54.9 grams per tonne (g/t) gold and 379 g/t silver over 1.47 meter core
length in drill hole COD18-46 which tested the COD Vein, including 223
g/t gold, 1,535 g/t silver and )500 g/t tellurium over 0.30 meter core
length. This gold-bearing intersection of quartz veins and minor
altered granodiorite in COD18-46 is located at approximately 25 meter
vertical depth. This drill intersection is approximately 5 meters below
the high grade intersection of drill hole COD-18-45 (50.1 g/t gold and
375 g/t silver over 2.05 meter core length as was reported in the
Company's News Release of August 15, 2018). Both COD18-45 and COD18-45
are approximately 160 meters southwest of the area of 2017 trenching at
the COD Vein and approximately 220 meters southwest of drill hole
COD17-14 which intersected the 4.59 g/t gold over 16.03 meters,
including 10.96 g/t gold over 5.97 meters (News Release of September 7,
2017).

The 2018 drilling program focused on testing and defining the COD
Vein, a Dentonia/Jewel style quartz vein. Trenching during 2017 exposed
the northeast - southwest striking COD Vein for over 160 meter strike
length. The 2018 drilling program also tested the continuation of the
Everest Vein, which is located approximately 600 meters southwest of
the COD Vein worksite. The Everest Vein was first discovered by Company
prospectors during the 2017. Chip samples collected in 2017 across the
approximate 0.4 meter wide vein exposure returned up to 52.8 g/t gold
and 377 g/t silver while a grab sample of a quartz vein boulder broken
off the outcrop by the excavator returned 81.8 g/t gold and 630 g/t
silver (News Release of August 21, 2017).

The analytical results listed below are highlights from drill
holes COD18-46 to COD18-48 (intersections greater than 1 g/t gold),
testing the continuation of the COD Vein south-southwest of the 2017
trench. Since true widths cannot be accurately determined from the
information available the core lengths (meters) are reported. The gold,
silver and tellurium analyses are reported in grams per tonne (g/t).

//st

Hole ID     From (m)   To (m)   Interval      Au (g/t)   Ag     Te
Length (m)               (g/t)  (g/t)

COD18-46    29.57      31.04    1.47          54.9       379

including   29.57      29.86    0.29          5.57       22.2   16.85

including   30.30      30.60    0.30          34.8       239    191

including   30.60      30.90    0.30          223        1535   )500

including   30.90      31.04    0.14          11.4       127    95.1

//et

Previous drill core analytical results from the 2018 drilling
program are reported in News Releases of May 29, June 14, June 27, July
11, July 19, July 25, August 1, August 9 and August 15. The
close-spaced intersections of drill holes COD18-45 and COD-18-46 at the
COD Vein is the highlight of the 2018 drilling program to date and
represents significant intersections with high grade gold southwest of
the 2017 trench. Prior to the receipt of analytical results for these
holes, the highlight of the 2018 drilling program was 14.62 g/t gold,
150.2 g/t silver and 102.0 g/t tellurium over 2.1 meter core length in
drill hole COD18-3 at the COD Vein, located in the area of the 2017
trench and vicinity of drill hole COD17-14. The following map of the
COD Vein work area includes some of the more significant 2017 - 2018
drill intersections.

Drill core from the 2018 program was geologically logged and
sampled. Drill core was sawn in half with half core samples submitted
for analysis and remaining half core stored in a secure location. Core
samples were delivered to the ALS Minerals laboratory in Vancouver to
be analyzed for gold by Fire Assay - AA. Samples exceeding 100 g/t gold
were re-analyzed for gold by Fire Assay - Gravimetric Finish. The
samples were also analyzed for 48 Elements by Four Acid ICP-MS. Samples
exceeding 100 g/t silver were re-analyzed for silver by Four Acid
ICP-AES. One sample from COD18-46 exceeded 1500 g/t silver and was
re-analyzed for silver by Fire Assay - Gravimetric Finish. Quality
control (QC) samples were inserted at regular intervals.

David Martin, P.Geo., a Qualified Person as defined by NI 43-101,
is responsible for the technical information contained in this News
Release.

To view the Original News release with pictures please go to the
website or contact the company.

On Behalf of the Board of Directors,

Barry Brown, Director

604-488-3900

Office@GGXGold.com

Investor Relations:

Mr. Jack Singh, 604-488-3900   ir@GGXgold.com

" We don't have to do this, we get to do this "

The Crew

Forward Looking Information

This news release includes certain statements that constitute
"forward-looking information" within the meaning of applicable
securities law, including without limitation, the Company's information
and statements regarding or inferring the future business, operations,
financial performance, prospects, and other plans, intentions,
expectations, estimates, and beliefs of the Company. Such statements
include statements regarding the completion of the proposed
transactions. Forward-looking statements address future events and
conditions and are necessarily based upon a number of estimates and
assumptions. These statements relate to analyses and other information
that are based on forecasts of future results, estimates of amounts not
yet determinable and assumptions of management. Any statements that
express or involve discussions with respect to predictions,
expectations, beliefs, plans, projections, objectives, assumptions or
future events or performance (often, but not always, using words or
phrases such as "expects" or "does not expect", "is expected",
"anticipates" or "does not anticipate", "plans", "estimates" or
"intends", or stating that certain actions, events or results "may",
"could", "would", "might" or "will" be taken, occur or be achieved),
and variations of such words, and similar expressions are not
statements of historical fact and may be forward-looking statements.
Forward-looking statement are necessarily based upon several factors
that, if untrue, could cause the actual results, performances or
achievements of the Company to be materially different from future
results, performances or achievements express or implied by such
statements. Such statements and information are based on numerous
assumptions regarding present and future business strategies and the
environment in which the Company will operate in the future, including
the price of gold and other metals, anticipated costs and the ability
to achieve goals, and the Company will be able to obtain required
licenses and permits. While such estimates and assumptions are
considered reasonable by the management of the Company, they are
inherently subject to significant business, economic, competitive and
regulatory uncertainties and risks including that resource exploration
and development is a speculative business; that environmental laws and
regulations may become more onerous; that the Company may not be able
to raise additional funds when necessary; fluctuating prices of metals;
the possibility that future exploration, development or mining results
will not be consistent with the Company's expectations; operating
hazards and risks; and competition. There can be no assurance that
economic resources will be discovered or developed at the Gold Drop
Property. Accordingly, actual results may differ materially from those
currently anticipated in such statements. Factors that could cause
actual results to differ materially from those in forward looking
statements include continued availability of capital and financing and
general economic, market or business conditions, the loss of key
directors, employees, advisors or consultants, equipment failures,
litigation, competition, fees charged by service providers and failure
of counterparties to perform their contractual obligations. Investors
are cautioned that forward-looking statements are not guarantees of
future performance or events and, accordingly are cautioned not to put
undue reliance on forward-looking statements due to the inherent
uncertainty of such statements. The forward-looking statements included
in this news release are made as of the date hereof and the Company
disclaims any intention or obligation to update or revise any
forward-looking statements, whether as a result of new information,
future events or otherwise, except as expressly required by applicable
securities legislation.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TEL: 604-488-3900    GGX GOLD CORP
FAX: 604-488-3910
E-mail: info@poly-pacific.com
Website: http://www.ggxgold.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1823300001TS11823300378-04382520180822