Source	MARKET NEWS
Date	08/22/2018
Time	02:46:27 PM

Company	 Guyana Goldstrike Inc.
Title	Completes 
Sampling and Mapping of Trench TTR 18





    CDNX Symbol: GYA











Press Release





GUYANA GOLDSTRIKE INC ("GYA-V")
- Completes Sampling and Mapping of Trench TTR-18-9 at Toucan
- Ridge Area, Marudi Gold Project, Guyana

Guyana Goldstrike Inc. (the "Company" or "Guyana Goldstrike") is
pleased to report that the geological team has completed sampling and
mapping of trench TTR-18-9 at the Toucan Ridge area on its Marudi Gold
Project ("Marudi" or the "Property") located in the Guiana Gold Belt,
Guyana, South America.

Mr. Locke Goldsmith P Eng. P Geo., VP of Exploration states,
"Trench TTR-18-9 has exposed 6 intervals of quartzite-metachert host
rock, with each interval containing visible gold from pan concentrates.
We continue to successfully follow the host rock horizon along the
Toucan Ridge area of interest with the commencement of trench
TTR-18-10."

Toucan Ridge Trench TTR-18-9 Highlights

At trench TTR-18-9 298.3 metres was trenched, 114 samples were
taken for fire assay, and selected samples will be re-assayed for total
metallic content. The quartzite-metachert host rock in trench TTR-18-9
has been trenched and exposed at surface over 6 intervals for a total
length of 58.4 metres. Please see below an updated map of the Toucan
Ridge area with the location of trench TTR-18-9.

Significant Gold Discoveries to Date

To date, the Company has trenched four areas of interest: Paunch,
Pancake, Marudi-North West Extension and Toucan Ridge, the current area
trenched.

In May 2018, trench samples from the Paunch area returned the
program's first significant gold discovery with high-grade assay
results of 7.45 g/t and 5.98 g/t gold over 2 metres respectively.

(See news release dated May 15, 2018: "Guyana Goldstrike Assays up
to 7.45 g/t in New Discovery of Gold Mineralization at Paunch Area,
Marudi Gold Project, Guyana @
https://www.guyanagoldstrike.com/index.php/news/2018-news-release/105
and,

News release dated May 30, 2018: "Guyana Goldstrike Continues with
Gold Discovery: Assays up to 5.98 g/t Gold at Paunch Area, Marudi Gold
Project, Guyana @
https://www.guyanagoldstrike.com/index.php/news/2018-news-release/110

In July 2018, samples at Toucan Ridge returned the trenching
program's second significant gold discovery with trench TTR-8-6
returning a total metallic weighted average assay of 1.27 g/t over 4.5
metres.

(See news release dated August 2, 2018: "Guyana Goldstrike
Confirms Second Gold Discovery: Assays up to 1.53 g/t Gold in Trench
TTR-18-6 at Toucan Ridge Area, Marudi Gold Project, Guyana @
https://www.guyanagoldstrike.com/index.php/news/2018-news-release/132-guyan
a-goldstrike-confirms-second-gold-discovery-assays-up-to-1-53-g-t-gold-in-t
rench-ttr-18-6-at-toucan-ridge-area-marudi-gold-project-guyana

In August 2018, samples at Toucan Ridge from trench TTR-18-8
returned high-grade assay values of 1.38 g/t gold over 16 metres
including 5.4 g/t gold over 3 metres.

(See news release dated August 14, 2018: "Guyana Goldstrike
Reports Initial Assays of 1.38 g/t Gold Over 16 Metres Including 5.4
g/t Gold Over 3 Metres at Toucan Ridge Area, Marudi Gold Project,
Guyana @
https://www.guyanagoldstrike.com/index.php/news/2018-news-release/144

Toucan Ridge Area Location and Trenching

To date, a total of 998 metres of trenching has been completed in
the Toucan Ridge area. 379 samples have been taken. The exploration
team will continue to explore along the ridge progressing in an
eastward direction with each new trench site stepping out roughly in
50-100 metre intervals, mainly perpendicular to the ridge.

The initial area of trenching at Toucan Ridge began on the western
end with trench TTR-18-05 which is located approximately one kilometre
east of the Marudi North zone and one kilomtetre north of the Mazoa
Hill zone. The Mazoa Hill zone contains the project's current mineral
resource estimate: 259,100 indicated gold ounces within 4,428,000
tonnes grading 1.8 g/t and 86,200 inferred gold ounces within 1,653,000
tonnes grading 1.6 g/t.

The Toucan Ridge area of interest continues for more than 1.75
kilometres to the east of the first trench - TTR-18-05. Trench sites
are planned in intervals along the length of the ridge where
quartzite-metachert is exposed or interpreted to occur beneath the
transported overburden. The eastern part of Toucan Ridge is
approximately 400 metres south of the Paunch area which was trenched in
May of this year and returned the Company's first significant gold
discovery and approximately 350 metres north of alluvial workings at
Toucan Creek.

About Quartzite-metachert (Host Rock) at Marudi

At Marudi, all important gold mineralization discovered to date is
associated with the medial quartzite-metachert (host rock) unit of the
Marudi Mountain Formation. Gold occurs within the magnetite-hematite
rich quartzite and in the magnetite-silicate iron formation.
Mineralization of the host rock may be affected at surface by the
erosion at different levels of the strata. Therefore, all discoveries
of quartzite-metachert on the Property are considered important for the
potential of containing mineralization at surface and/or at depth and
should be explored through trenching and drilling. When discovered
these areas are assigned high levels of priority for further
exploration work, including drilling in the Company's planned drill
program.

TOUCAN RIDGE LOCATION MAP

(img
src='https://www.thenewswire.com/data/tnw/clients/img/dc6fb3ea4e79365b635d5
e6f97d7f56c_.png' /) @
https://www.thenewswire.com/data/tnw/clients/img/dc6fb3ea4e79365b635d5e6f97
d7f56c.png

Historical Trenching

Previous operators at Marudi reported 3,327.40 metres of trenching
and assayed 1,069 samples with gold values assayed up to 11 g/t of
gold. (Source: D. Strickland P. Geo NI 43-101 Technical Report,
November 30, 2016)

Marudi Geology

Gold mineralization at Marudi is regarded as being related to
iron-formation-hosted gold ("IFG") deposits that occur in other
cratonic greenstone belts around the world. These deposits can be
remarkably long-lived with sizeable gold production. They have a strong
association between gold and iron sulfide minerals, the presence of
gold bearing quartz veins and structures, the occurrence of deposits in
structurally complex terranes, and the absence of lead and zinc
enrichment.

Examples of some existing IFG deposits are: the Homestake Mine,
Lupin Mine, and Musselwhite Mine.

The Homestake Mine is located in South Dakota USA and was the
largest and deepest gold mine in North America. It has reported
production of 43.9 million ounces of gold and was in production from
1878-2001. (source:
https://en.wikipedia.org/wiki/Homestake_Mine_(South_Dakota)

The Lupin Mine located in Nunavut, Canada, no longer in
production, produced approximately 3 million ounces of gold. (source:
http://www.kinross.com/news-and-investors/news-releases/press-release-detai
ls/2003/Suspension-of-Operations-at-the-Lupin-Mine/default.aspx)

The Mussellwhite mine located in Ontario, Canada has estimated
reserves of 2.29 million ounces of gold and is owned and operated by
Goldcorp and will be in production until 2020. (source:
https://en.wikipedia.org/wiki/Musselwhite_mine)

About the Marudi Gold Project

The Company is developing the Marudi Gold Project located in
Guyana, South America. The project has 18-year mining license in good
standing, all-season road access, infrastructure in place, with an
established camp serviced by employees, service buildings, and a
full-time camp manager. The Property has three known gold bearing
areas: the alluvial areas, the saprolite, and the underlying hard-rock.


There has been 42,000 metres of historic diamond drilling (141
holes) completed on the project by prior operators that have delineated
two zones of mineralization: Mazoa Hill and Marudi North zones. The
Company has recently completed a mineral resource estimate on the Mazoa
Hill zone containing 259,100 indicated gold ounces within 4,428,000
tonnes grading 1.8 g/t and 86,200 inferred gold ounces within 1,653,000
tonnes grading 1.6 g/t. There exists excellent exploration upside
through the development of previously and newly identified mineralized
bedrock targets on the project.

For information concerning the mineral resource estimate and the
project, readers are encouraged to review "Technical Report: Marudi
Property Mazoa Hill Mineral Resource Estimate", a technical report
prepared for the Company by Global Mineral Resource Services and is
available at
http://www.guyanagoldstrike.com/images/pdf/43101_Report_Guyana_Goldstrike_M
azoa_Hill_Zone_Jan_2018.pdf  and under the Company's profile on SEDAR
www.sedar.com. @ http://www.sedar.com.

Sampling and Assaying

All samples collected during this program were delivered to
Activation Laboratories Ltd. (Actlabs) located in Georgetown, Guyana
for gold content by Fire Assay (FA) and Total Metallics. Actlabs is ISO
17025 accredited and/or certified to 9001:2008. With 25+ years'
experience, with full analytical laboratories that perform high quality
analysis for many industries around the world.

Quality Assurance / Quality Control

Actlabs is an ISO 9001:2008 qualified assayer that performs and
makes available internal assaying controls. Certified blanks and
standards are systematically used as part of Guyana Goldstrike's
quality assurance/quality control (QA/QC) program with one blank and
standard inserted at every 20 sample intervals.

About Guyana Goldstrike Inc.

Guyana Goldstrike Inc. is a Canadian based junior gold company
focused on the exploration, development, and operation of the Marudi
Gold Project in Guyana, South America.

Please visit us at:

www.guyanagoldstrike.com

http://www.guyanagoldstrike.com

About Guyana

The Republic of Guyana is located in South America adjacent to
Suriname. The country is English speaking and under British Common Law
with a democratically-elected government. It has an established mining
act and a rich history of gold production. In 2016, 690,000 ounces of
gold was produced by operators mining in the country. The Fraser
Institute's 2016 Annual Survey of Mining listed Guyana as the third
best mining jurisdiction with regards to investment attractiveness in
the Latin America and Caribbean Basin sub-group. The Guiana Shield is
the geographic gold-hosting region, and is world-recognized as a
premier gold region that is highly prospective, under-explored and has
geological continuity with West Africa.* In 2016, two mines in Guyana
declared the commencement of commercial production: the Aurora deposit
(Guyana Goldfields) and the Karouni deposit (Troy Resources).

* Independent Technical and Environmental Review Karouni Gold
Project - Guyana, Behre Dolbear Australia Pty Ltd, April 29, 2016

Qualified Person

Locke Goldsmith, M.Sc., P. Eng, P. Geo, Chief Geologist and
Exploration Manager for the Company, is a Qualified Person in
accordance with National Instrument 43-101 - Standards of Disclosure
for Mineral Projects. Mr. Goldsmith has reviewed and approved the
scientific and technical content of this news release.

On behalf of the Board of Directors of

GUYANA GOLDSTRIKE INC.

Peter Berdusco
President and Chief Executive Officer

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release may contain certain "Forward-Looking Statements"
within the meaning of the United States Private Securities Litigation
Reform Act of 1995 and applicable Canadian securities laws. When used
in this news release, the words "anticipate", "believe", "estimate",
"expect", "target, "plan", "forecast", "may", "schedule" and other
similar words or expressions identify forward-looking statements or
information. These forward-looking statements or information may relate
to future prices of commodities, accuracy of mineral or resource
exploration activity, reserves or resources, regulatory or government
requirements or approvals, the reliability of third party information,
continued access to mineral properties or infrastructure, fluctuations
in the market for gold, changes in exploration costs and government
regulation in Guyana, status of artisanal mining activities and
associated rights, and other factors or information. Such statements
represent the Company's current views with respect to future events and
are necessarily based upon a number of assumptions and estimates that,
while considered reasonable by the Company, are inherently subject to
significant business, economic, competitive, political and social
risks, contingencies and uncertainties. Many factors, both known and
unknown, could cause results, performance or achievements to be
materially different from the results, performance or achievements that
are or may be expressed or implied by such forward-looking statements.
The Company does not intend, and does not assume any obligation, to
update these forward-looking statements or information to reflect
changes in assumptions or changes in circumstances or any other events
affections such statements and information other than as required by
applicable laws, rules and regulations.

Copyright (c) 2018 TheNewswire - All rights reserved.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1823300039TS11823301434-08322120180822