Source	MARKET NEWS
Date	08/15/2018
Time	05:12:58 AM

Company	 Orsu Metals Corporation
Title	Hits 2.62 g/t 
Au over 22.2 Metres and Proves Hig





    CDNX Symbol: OSU











Press Release





ORSU METALS CORP ("OSU-V;ORSUF-0")
- Hits 2.62 g/t Au over 22.2 Metres and Proves Higher Gold Grades
- at Zone 23, Sergeevskoe Gold Project, Russia

Orsu Metals Corporation ("Orsu" or the "Company") is delighted to
announce excellent drilling results from hole SDH18-43 at Zone 23, as
part of the 10,500 meters ('m') drilling program at its Sergeevskoe
Gold Project in Russia. The program is designed to deliver an
estimation of a maiden resource by Q4 2018.

Highlights:

//st

* The assay results from hole SDH18-43 returned 2.62 g/t Au over 22.2 m in
the Main stockwork at Zone 23

//et

//st

* The average grade of the Main stockwork in five sections over a 280 m
strike length averages 2.45 g/t Au over 19.35 m

//et

//st
* The average grade of the Main and Southern stockworks in five sections is
1.89 g/t Au over a combined average drill width of 33.08 m

//et

Dr. Alexander Yakubchuk, Director of Exploration of Orsu
commented: "Orsu successfully started testing the western extent of
gold mineralization at Zone 23. It is encouraging to see that SDH18-43
returned 22.2 m grading 2.62 g/t Au versus the previously reported
total average drill width of the Main stockwork of 16.5 m at 2.23 g/t
of Au (see Orsu press-release July 16, 2018). This hole lifts the
average gold grade in the Main stockwork to 2.45 g/t Au, demonstrating
consistent presence of the higher gold grades in the system. Both Main
and Southern stockworks of Zone 23 continue to the west, totaling 280 m
vis-a-vis 240 m reported by Orsu only three weeks ago (see Orsu
press-release July 16, 2018). Their average combined drill width
reaches 33.08 m averaging 1.89 g/t Au at the upper range of the 1.5-2.0
g/t Au guidance estimated based on 2017 drilling and trenching results
prior to commencement of the 2018 program. The Company continues to do
step-out drilling at Zone 23 both eastwards and westwards and expects
to report shortly further results for gold mineralization at the
western and eastern extents of Zone 23".

Dr. Sergey Kurzin added: "This drill hole SDH18-43 delivered one
of the best intervals that we have seen in the Main stockwork at Zone
23. We have historical evidence to believe that Zone 23 can reach
500-to-600 meters along the strike vis-a-vis currently drill proven 280
m and this is what we focus on now at Zone 23. We also see continuing
exploration success at Klyuchi West where we hit over 200 m of
mineralization as reported on August 8, 2018. We are continuing to
drill with a growing confidence in the quality of the soon to be
delivered maiden mineral resource statement".

The license of the Sergeevskoe Gold Project occurs immediately
east from the Alexandrovskoe open pit and gold plant owned by Zapadnaya
Gold Mining Ltd and to the west from the Klyuchevskoe gold license
owned by Sun Gold Mining (Figure 1). The Klyuchevskoe (Klyuchi) gold
deposit represents a +6 Moz gold endowment (see Orsu press-release
dated September 21, 2016). Orsu owns a 90% interest in the Sergeevskoe
Gold Project (see Orsu press-release December 1, 2017).

Figure 1. An outline of the 7.6 sq km Sergeevskoe license area
with location of principal gold prospects and two adjacent open pits.

To view the graphic in its original size, please click here

Orsu identified and reported gold mineralization at Zone 23 in
four sections (see Orsu press-release June 19, 2018) to the south of
the Shirotnyi fault (Figure 2). The quartz-tourmaline-sulfide
stockworks are locally present in the granodiorite porphyry and
magmatic breccia stocks to the north of the fault. However, they are
best mineralized in the west-east-trending stockworks hosted in the
granite intrusion to the south of the fault.

Both Main and Southern stockworks were identified in section 9260E
(Figure 3) and were therefore traced here from section 9540E for 280 m.
Both stockworks change in width along the strike and downdip. The
average drill width of the Main stockwork can be now estimated in 19.35
m grading 2.45 g/t Au. The Southern stockwork somewhat decreases in
grade and averages 13.73 m grading 1.1 g/t Au. Therefore, the combined
average drill width of the two stockworks is 33.08 m grading 1.89 g/t
Au over a strike length of more than 280 m and some 150 to 250 m
downdip.

Figure 2. The surface expression of multiple west-east-trending
gold-mineralized intervals at Zone 23, Sergeevskoe Gold Project,
constrained by historical and Orsu data.

To view the graphic in its original size, please click here

Figure 3. Gold mineralization in sections 9260E (looking west).
Hole SDH18-22 was drilled obliquely, with its lower quarter appearing
in the section.

To view the graphic in its original size, please click here

Selection of mineralized intervals in section 9260E, presented
below, is based on a 0.5 g/t Au cut-off for compositing, with maximum 2
m length of 0.3-0.5 g/t Au mineralization included into mineralized
interval. Composited intervals in drill holes are presented uncapped.

In section 9260E (Figure 3), Orsu received complete assays for one
drill hole SDH18-43 (Table 1). This hole was drilled to a depth of 240
m southward at approximately 60 degrees, just some 40 m west from
section 9300E. Its aim was to target higher grade gold intercepts
reported in hole SDH18-15 (see Orsu press-release January 22, 2018).
The most significant intercept of 2.62 g/t Au over 22.2 m from 153.75 m
is interpreted to correspond to the Main stockwork. The Southern
stockwork is represented in this section by several intervals with a
combined with of 14.75 m grading 0.76 g/t Au.

Orsu is confident in location of the stockworks relative to the
marker of granodiorite porphyry dyke, intruding the granite. In
addition, the southern limit of the mineralized corridor can be
constrained in this section by presence of the hybrid dyke, intercepted
in the bottom of hole SDH18-43.

Table 1. Mineralized intercepts in drillhole SDH18-43 at Zone 23
(above 0.5 g/t Au cut-off).

//st

Drillhole      From (m)   To (m)   Interval (m)      True        Gold
Number                                          Width (m)      (g/t)

SDH18-43 (240    96.8       100.95   4.15           3.7          0.84
m) Section
9260E

111.2      112.9    1.7            1.5          4.05

153.75     175.95   22.2           19.0         2.62

164.65     170.65   6.0            5.2          5.57

186.75     191.75   5.0            4.4          0.7

205.5      211.4    5.9            5.3          0.79

216.95     220.8    3.85           3.4          0.79

236.0      240.0    4.0            3.5          0.66

//et

Quality Assurance - Quality Control ("QA/QC")

Thorough QA/QC protocols are followed on the project including
insertion of duplicate, blank and standard samples in all trenches.
Duplicate samples were inserted after every 20 samples. All standard
samples were inserted once per 20 samples. Blanks were also inserted
once per 20 samples and consisted of the previously assayed barren
granitoid rocks.

Drill core samples were submitted directly to the SGS Vostok
laboratories in Chita, Russia, which are independent from Orsu, for
sample preparation and analysis. Analysis for Au is performed using
fire assay method with atomic absorption ("AA") finish and with a
gravimetric finish for samples exceeding 10 g/t Au. Results published
are from the gravimetric finish if above 10 g/t Au and from the AA
finish if lower than 10 g/t Au.

Qualified Person

This release and the technical data reported have been reviewed
and approved by Alexander Yakubchuk, Director of Exploration of the
Company, also a Qualified Person as defined in NI 43-101.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Cautionary Statement:

This news release contains forward-looking statements that are
based on the Company's current expectations and estimates.
Forward-looking statements are frequently characterized by words such
as "plan", "expect", "project", "intend", "believe", "anticipate",
"estimate", "suggest", "indicate" and other similar words or statements
that certain events or conditions "may" or "will" occur. Such
forward-looking statements involve known and unknown risks,
uncertainties and other factors that could cause actual events or
results to differ materially from estimated or anticipated events or
results implied or expressed in such forward-looking statements. There
may be other factors that cause actions, events or results not to be as
anticipated, estimated or intended. Any forward-looking statement
speaks only as of the date on which it is made and, except as may be
required by applicable securities laws, the Company disclaims any
intent or obligation to update any forward-looking statement, whether
as a result of new information, future events or results or otherwise.
Forward-looking statements are not guarantees of future performance and
accordingly undue reliance should not be put on such statements due to
the inherent uncertainty therein.

ENDS

For further information, please contact:

Alexander Yakubchuk, Director of Exploration, Orsu Metals
Corporation

Doris Meyer, Corporate Secretary, Orsu Metals Corporation

Tel: +1-604-536-2711 ext 6

www.orsumetals.com

To view the original release (with media), please click here

TEL: 4402075183999    ORSU METALS CORP
FAX: 4402075183998
E-mail: info@orsumetals.com
Website: http://www.orsumetals.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1822600001TS11822600566-05102720180815