Source	MARKET NEWS
Date	08/16/2018
Time	05:57:47 AM

Company	 Novo Resources Corp.
Title	Novo 
Artemis JV Confirms Continuity of Upper Gol





    CDNX Symbol: NVO











Press Release





NOVO RESOURCES CORP ("NVO-V")
- Novo-Artemis JV Confirms Continuity of Upper Gold-Bearing
- Conglomerate From Comet Well to Purdy's Reward

Novo Resources Corp. ("Novo" or the "Company") is pleased to
announce that recent surface mapping and trenching indicates the upper
gold-bearing conglomerate at Comet Well (80% Novo; 10% Gardner Mining;
10% Smith) appears continuous with the basal gold-bearing conglomerate
at Purdy's Reward (50% Novo; 50% Artemis joint venture on conglomerate
and paleoplacer gold hereafter referred to as the "Novo-Artemis JV"), a
current explored strike of approximately 3.4 km. These gold-bearing
conglomerates remain open along strike to the northeast and southwest
and down dip to the southeast into the Fortescue Basin. At Purdy's
Reward, exploration has recently re-commenced where infill drilling and
bulk sampling is being undertaken to further evaluate the gold deposit.


*  Soon after identifying two distinct gold nugget-bearing
conglomerate units at Comet Well, Novo noted that nuggets from the
upper unit displayed similar large size and flattened shape to those
observed in the basal gold-bearing conglomerate uncovered at Purdy's
Reward in late 2017 by the Novo-Artemis JV. Novo and the Novo-Artemis
JV have recently conducted mapping and trenching in intermediate areas
indicating these conglomerates are one-in-the-same (see Figure 1
below).

*  Novo and the Novo-Artemis JV are encouraged by the apparent
continuity of these gold-bearing conglomerates over an explored strike
length of 3.4 km. They are generally shallow and accessible for bulk
sampling. Several new trenches opened up in the intermediate area
between Comet Well and Purdy's Reward reveal numerous detector strikes
(see Videos 1, 2 and 3 at https://www.youtube.com/embed/FhwufkDaugk,
https://www.youtube.com/embed/bwFfe0B6Z4g, and
https://www.youtube.com/embed/elCUB0SFuu8). Bulk samples (5-10 tonnes)
are currently being collected from newly opened areas and will be
prioritized in the processing queue.

*  The upper gold-bearing conglomerate at Comet Well is associated
with a distinct mafic volcanic tuff marker bed that helps enable its
identification in the field. As the upper gold-bearing conglomerate and
associated tuff project northeastward toward Purdy's Reward, a series
of north-northeast trending faults is encountered beyond which the
mafic tuff is no longer present. Gold-bearing conglomerates persist,
however, stepping down through the stratigraphic section to a position
directly on basement. Small fragments of what appear to be mafic tuff
occur within the basal gold-bearing conglomerate at Purdy's Reward (see
Figure 2 below).

*  Novo and the Novo-Artemis JV believe these north-northeast
faults must have been active during deposition of the conglomerate
beds. Purdy's Reward was the upthrown block, hence gold-bearing
conglomerate was deposited straight onto basement whereas Comet Well
was the downthrown block and nuggets were deposited onto older
conglomerate beds.

*  Because these gold-bearing conglomerates display good lateral
continuity and are generally shallow, Novo and the Novo-Artemis JV are
growing more confident that they will be the main focus of future
large-scale bulk sample extraction.

Re-commencement of exploration at Purdy's Reward

The Novo-Artemis JV recently commenced infill diamond drilling at
Purdy's Reward. These drill holes are utilized to gather information
about the depth and thickness of targeted conglomerate units. Given the
extremely nuggety nature of the deposit, gold grades are being assessed
by bulk sampling. Bulk samples using Novo's new 5-10 tonne sampling
protocol will soon be collected from trenches in areas near where the
Novo-Artemis JV collected 300 kg gold-bearing bulk samples in 2017.

Novo's and the Novo-Artemis JV's exploration strategy is to
generate sufficient geologic and grade data for the gold-bearing
conglomerates at Comet Well and Purdy's Reward to produce a
mineralization report, a critical item needed to convert the current
exploration licenses to mining leases. The Novo-Artemis JV's aim is to
ultimately move the project toward large-scale bulk sample extraction
and testing as a critical means of determining its potential viability
with sufficient data available for a mineralization report by the end
of 2018. For more details on the Novo-Artemis JV, please refer to the
Company's news release dated August 15, 2017.

Dr. Quinton Hennigh, the Company's, President and Chairman and a
Qualified Person as defined by National Instrument 43-101, has approved
the technical contents of this news release.

About Novo Resources Corp.

Novo's focus is to explore and develop gold projects in the
Pilbara region of Western Australia, and Novo has built up a
significant land package covering approximately 12,000 sq km with
varying ownership interests. For more information, please contact Leo
Karabelas at (416) 543-3120 or e-mail leo@novoresources.com

On Behalf of the Board of Directors,

Novo Resources Corp.

"Quinton Hennigh" Quinton Hennigh President and Chairman

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this news
release.

Forward-looking information Some statements in this news release
contain forward-looking information (within the meaning of Canadian
securities legislation) including, without limitation, statements as to
planned exploration activities. These statements address future events
and conditions and, as such, involve known and unknown risks,
uncertainties and other factors which may cause the actual results,
performance or achievements to be materially different from any future
results, performance or achievements expressed or implied by the
statements. Such factors include, without limitation, customary risks
of the mineral resource industry as well as the performance of services
by third parties.

PDFs accompanying this announcement are available at:



http://resource.globenewswire.com/Resource/Download/03ea7e29-5459-498a-811e
-31caaa9607e2



http://resource.globenewswire.com/Resource/Download/d9ffb99b-ce29-497e-93fe

TEL: 604-688-9588    NOVO RESOURCES CORP
FAX: 778-329-9361
E-mail: herrick@novoresources.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1822700013TS11822700738-05540120180816