Source	MARKET NEWS
Date	08/20/2018
Time	05:12:54 AM

Company	 Commerce Resources Corp.
Title	Provides Update on the Metallurgical Test Progra





    CDNX Symbol: CCE











Press Release





Provides Update on the Metallurgical Test Program at UniversiteLaval for the 
Ashram Rare Earth Deposit --->@NEWS RELEASE
COMMERCE RESOURCES CORP ("CCE-V;CMRZF-0")
- Provides Update on the Metallurgical Test Program at Universite
- Laval for the Ashram Rare Earth Deposit

Commerce Resources Corp. (the "Company" or "Commerce") is pleased
to provide an update on the metallurgical test program for the Ashram
Rare Earth Deposit that is being completed under the direction of the
Universite Laval ("Laval"). The test program uses an alternative
flowsheet approach with the purpose of validating a software model
simulator developed by Laval (see news releases dated May 31 and July
24, 2018). The program is fully funded through a grant received by
Laval with testwork being completed in collaboration with SGS Canada
Inc. ("SGS") at their facilities.

Since the program was first initiated in May 2018, the test work
has advanced aggressively with a bench-scale level demonstration of the
entire flowsheet now complete, including the production of several
grams of mixed rare earth oxide concentrate (see news release dated
July 24, 2018). The Company is now pleased to report that the crushing
and grinding component, as well as the large-scale flotation component
of the program, have now been completed. A total of ~1.5 tonnes of
Ashram Deposit material was processed, with the flotation component
completed using individual batches ranging from 10 kg to 30 kg. Initial
results are in line with expectations with the team now looking ahead
to the pilot-level hydrometallurgical component that will commence with
a caustic crack on an estimated 150 kg of flotation concentrate.

Company President Chris Grove states, "We continue to be impressed
with the rapid advancement of this collaboration and look forward to
the commencement of the hydrometallurgical pilot component."
The next steps of the program will use the flotation concentrate
as feed to a semi-continuous hydrometallurgical pilot operation to
produce a purified solution containing the REE. The REE solution will
then be processed through a continuous solvent extraction (SX)
separation pilot circuit to separate the LRE(1) from the SEG(2) and
HRE(3). In parallel, the solution composition will be used to simulate
the pilot scale SX separation circuit using the model simulator. The
comparison between the results of the pilot plant and the simulation
will validate the model simulator, which could then be used to further
assess the economics of the separation of the REE into individual rare
earth oxides.

//st

* LRE - Light Rare Earth
* SEG - Samarium, Gadolinium, Europium
* HRE - Heavy Rare Earth

//et

NI 43-101 Disclosure

Darren L. Smith, M.Sc., P.Geol., Dahrouge Geological Consulting
Ltd., a Qualified Person as defined by National Instrument 43-101,
supervised the preparation of the technical information in this news
release.

About Universite Laval

Universite Laval is a French-language university based in Quebec
City, QC, Canada with over 42,500 students enrolled in some 500
programs. Laval is a highly regarded academic institution at the
forefront of research and development in the country with over 60
departments and schools supporting a range of innovative initiatives.

About SGS

SGS is the world's leading inspection, verification, testing and
certification company. SGS is recognized as the global benchmark for
quality and integrity. With more than 95,000 employees, SGS operates a
network of over 2,400 offices and laboratories around the world.

About Commerce Resources Corp.

Commerce Resources Corp. is an exploration and development company
with a particular focus on deposits of rare metals and rare earth
elements. The Company is focused on the development of its Ashram Rare
Earth Element Deposit in Quebec and the Upper Fir Tantalum-Niobium
Deposit in British Columbia.

For more information, please visit the corporate website at
http://www.commerceresources.com or email info@commerceresources.com.

On Behalf of the Board of Directors

COMMERCE RESOURCES CORP.

"Chris Grove"

Chris Grove

President and Director

Tel: 604.484.2700

Email: cgrove@commerceresources.com

Web:    http://www.commerceresources.com

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Forward Looking Statements

This news release contains forward-looking information which is
subject to a variety of risks and uncertainties and other factors that
could cause actual events or results to differ from those projected in
the forward-looking statements.  Forward looking statements in this
press release include, but are not limited to, potential process
methods and mineral recoveries assumption based on limited test work
and by comparison to what are considered analogous deposits that with
further test work may not be comparable; the availability of labour,
equipment and markets for the products produced; and despite the
current expected potential of the project, conditions changing such
that the minerals on our property cannot be economically mined, or that
the required permits to build and operate the envisaged mine can be
obtained. The forward-looking information contained herein is given as
of the date hereof and the Company assumes no responsibility to update
or revise such information to reflect new events or circumstances,
except as required by law.

Commerce acknowledges its partners:

//st

To view the graphic in its original    To view the graphic in its
size, please click here                original size, please click here

//et

To view the original release (with media), please click here

TEL: 604-484-2700    COMMERCE RESOURCES CORP
FAX: 604-681-8240
E-mail: kevin@commerceresources.com
Website: http://www.commerceresources.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1823100002TS11823100657-05093920180820