Source	MARKET NEWS
Date	08/21/2018
Time	05:10:19 AM

Company	 Mkango Resources Ltd.
Title	Intersects 
Extensive Zones of Rare Earths Minera





    CDNX Symbol: MKA











Press Release





MKANGO RESOURCES LTD ("MKA-V")
- Intersects Extensive Zones of Rare Earths Mineralisation at
- the Songwe Hill Project in Malawi

Mkango Resources Ltd. (the "Company" or "Mkango") is pleased to
announce results for the first eight holes totaling 944 metres of its
targeted 10,000 metre diamond drilling programme at the Songwe Hill
Rare Earths Project ("Songwe") in Malawi. The drilling programme is a
key component of the ongoing Feasibility Study for Songwe. Highlights
from the new results are as follows:

//st

PX062    147.2 m1 grading 1.6% Total Rare Earth Oxides (TREO) (5.3 -
152.5 m end of hole (EoH)). Inclined hole (70 degrees east).

PX065    91.0 m2 grading 1.5% TREO (0.0 - 91.0 m) including 27.0 m2
grading 2.0% TREO (23.0 - 50.0 m). Inclined hole (60 degrees
west).

PX047    51.8 m grading 1.6% TREO (16.2 - 68.0 m). Inclined hole (60
degrees west).

PX046    48.0 m grading 1.2% TREO (4.0 - 52.0 m). Inclined hole (60
degrees south).

PX045b   9.2 m grading 2.0% TREO (6.1 - 15.3 m) and 27.5 m grading 1.5%
TREO (30.5 - 58.0 m EoH). Vertical hole.

PX042    19.1 m grading 1.0% TREO (18.0 - 37.1 m). Inclined hole (60
degrees west).

PX036    42.8 m grading 1.3% TREO (87.3 - 130.1 m EoH) including 6.7 m
grading 2.2% TREO (123.4 - 130.1 m EoH). Inclined hole (60
degrees west).

//et

1 Includes a 2.0m cavity not sampled. 2 Includes a 2.7m cavity not
sampled. TREO: total rare earth oxides based on total La2O3, Ce2O3,
Pr2O3, Nd2O3, Sm2O3, Eu2O3, Gd2O3, Tb2O3, Dy2O3, Ho2O3, Er2O3, Tm2O3,
Yb2O3, Lu2O3, Y2O3. These intersections are reported as down hole
widths and do not necessarily represent true thicknesses and attitude
of the mineralised zones, the estimation of which will require further
refining of the geological model.

William Dawes, Chief Executive Officer, commented: "These are an
excellent first set of results from the current programme and we look
forward to announcing results from the remaining approximately 75 drill
holes as they become available. The drill programme and planned
resource update are fully funded following investments by Talaxis
Limited totalling 6 million in January 2018. Talaxis will invest a
further 7 million to fund completion of the Feasibility Study for
Songwe on Mkango publishing a NI 43-101 technical report in relation to
the resource update."

*  The drill programme is focused on infill drilling to confirm
and upgrade the existing Indicated and Inferred Mineral Resource
Estimates, testing extensions to the mineralisation and geotechnical
drilling.
*  All eight drill holes intersected rare earth mineralisation,
with the table above highlighting intersections averaging 1% TREO or
more.
*  Drill holes PX065, PX062, PX046, PX047, PX042 and PX045b above
were focused on infill drilling. Intersections of broad zones of
mineralisation, as opposed to narrow veins or dykes, continue to
support the concept of a bulk tonnage, open pit mining operation with
low mining costs.
*  Drill hole PX036 was focused on testing the southerly extension
of mineralisation. The significance of the more than 42 m of
mineralisation intersected by PX036 at depth (87.3 - 130.1 m),
including 6.7 metres grading 2.2% TREO to the end of the hole (130.1m),
is being evaluated. This was the first hole in the project's history to
be drilled in the area near the summit of Songwe Hill. Another hole
testing the southerly extension of mineralisation, PX037, did not reach
the target depth.
*  A total of 8,466 metres of drilling, comprising 70 drill holes,
has now been completed as at August 20, 2018.

A schematic geological map illustrating the location of the drill
hole collars and estimated drill hole traces is available on the
Company's website (www.mkango.ca).

The breakdown of TREO values reported above are as follows:

//st

Drill       From    To      Interval         La2O3   Ce2O3    Pr2O3 Nd2O3
Hole

m       m       m                ppm     ppm      ppm    ppm

PX062       5.3     152.5   147.2      (i)   4,226   7,157    736   2,524

(i) Includes 2.0m cavity not
sampled.

PX065       0.0     91.0    91.0       (i)   3,600   6,594    689   2,352

including   23.0    50.0    27.0       (i)   5,595   9,574    954   3,020

(i) Includes 2.7m cavity not
sampled.

PX047       16.2    68.0    51.8             3,606   7,149    800   2,877

PX046       4.0     52.0    48.0             2,486   5,129    577   2,104

PX045b      6.1     15.3    9.2              5,257   8,278    806   2,752

30.5    58.0    27.5             3,876   6,232    617   2,075

PX042       18.0    37.1    19.1             2,490   4,263    440   1,496

PX036       87.3    130.1   42.8             2,821   5,648    636   2,279

including   123.4   130.1   6.7              5,540   10,403   1,078 3,582



Drill       Sm2O3   Eu2O3   Gd2O3   Tb2O3   Dy2O3   Ho2O3   Er2O3
Hole

ppm     ppm     ppm     ppm     ppm     ppm     ppm

PX062       364     96      225     27      113     18      43

(i) Includes 2.0m cavity not
sampled.

PX065       319     83      191     23      107     17      41

including   370     91      196     21      88      13      27

(i) Includes 2.7m cavity not
sampled.

PX047       415     115     280     36      179     29      70

PX046       317     92      227     30      146     25      60

PX045b      469     136     330     44      224     42      118

337     98      240     30      144     25      61

PX042       235     70      174     23      112     18      41

PX036       295     67      141     15      77      15      41

including   391     83      162     15      65      11      29







Drill       Tm2O3   Yb2O3   Lu2O3   Y2O3    TREO
Hole

ppm     ppm     ppm     ppm     %

PX062       5       30      4       512     1.6%

(i) Includes 2.0m cavity not
sampled.

PX065       5       29      4       489     1.5%

including   3       16      2       329     2.0%

(i) Includes 2.7m cavity not
sampled.

PX047       9       47      6       807     1.6%

PX046       8       47      6       703     1.2%

PX045b      18      112     14      1,318   2.0%

8       46      6       737     1.5%

PX042       5       31      4       486     1.0%

PX036       6       35      5       483     1.3%

including   4       28      4       357     2.2%

//et

Scientific and technical information contained in this release
including sampling, analytical, and test data underlying the
information has been approved and verified by Dr. Scott Swinden of
Swinden Geoscience Consultants Ltd, who is a "Qualified Person" in
accordance with National Instrument 43-101 - Standards of Disclosure
for Mineral Projects.

Sample preparation and analytical work for the drilling and
channel sampling programmes are being provided by Intertek-Genalysis
Laboratories (Perth, Australia) employing ICP-MS techniques suitable
for rare earth element (REE) analyses and following strict internal
QAQC procedures inserting duplicates, blanks and standards. Internal
Laboratory QAQC was also completed to include blanks, standards and
duplicates.

About Mkango Resources Limited

Mkango's primary business is exploration for rare earth elements
and associated minerals in the Republic of Malawi, a country whose
hospitable people have earned it a reputation as "the warm heart of
Africa". The Company holds interests in three exclusive prospecting
licenses in Malawi, the Phalombe licence, the Thambani licence and the
Chimimbe Hill licence.

The main exploration target in the 80% held Phalombe licence is
the Songwe Hill rare earths' deposit, which features carbonatite-hosted
rare earth mineralisation and was subject to previous exploration in
the late 1980s. Mkango completed an updated Pre-Feasibility Study for
the project in November 2015 and a Feasibility Study is currently
underway, the initial phases of which include a major drilling
programme.

Under the terms of an agreement with Talaxis, Talaxis will fully
fund the Feasibility Study for Songwe by investing 12 million for a 49%
interest in the project (via Mkango subsidiary Lancaster Exploration
Ltd). Talaxis will also have the option to acquire a further 26%
interest by arranging funding for project development including funding
the equity component thereof. If Talaxis exercises its option, Mkango
will retain a 25% interest, free carried to production. To-date,
Talaxis has invested 5 million, which is funding the initial phase of
the Feasibility Study, for a 20% interest in the project with Mkango
holding 80%.

By investing a further 2 million, Talaxis will acquire a 49%
interest in Maginito Ltd, a new subsidiary of Mkango focused on
neodymium alloy powders, magnets and other technologies. This includes
the collaboration with Metalysis Ltd announced in September 2017, which
is focused on advanced alloys using neodymium or praseodymium with
other elements for permanent magnet manufacturing. Permanent magnets
are critical materials for most electric vehicles, direct drive wind
turbines and many other high growth applications. Neodymium is a key
rare earth component at Songwe. To date, Talaxis has invested 1 million
for a 24.5% interest in Maginito with Mkango holding 75.5%.

The main exploration targets in Mkango's remaining two 100% held
licences are, in the Thambani licence, uranium, niobium, tantalum and
zircon and, in the Chimimbe Hill licence, nickel and cobalt.

For more information, please visit www.mkango.ca.

Market Abuse Regulation (MAR) Disclosure

Certain information contained in this announcement may have been
deemed inside information for the purposes of Article 7 of Regulation
(EU) No 596/2014 until the release of this announcement.

Cautionary Note Regarding Forward-Looking Statements

This news release contains forward-looking statements (within the
meaning of that term under applicable securities laws) with respect to
Mkango, its business and the Project. Generally, forward looking
statements can be identified by the use of words such as "plans",
"expects" or "is expected", "scheduled", "estimates" "intends",
"anticipates", "believes", or variations of such words and phrases, or
statements that certain actions, events or results "can", "may",
"could", "would", "should", "might" or "will", occur or be achieved, or
the negative connotations thereof. Forward looking statements in this
news release include statements with respect to the global market for
products using the rare earth metals the Company is exploring for,
completion of the feasibility study and of the transactions
contemplated in the Agreement, as well as the use of proceeds from the
investments into the Company by Talaxis and the timing of such
expenditures. Readers are cautioned not to place undue reliance on
forward-looking statements, as there can be no assurance that the
plans, intentions or expectations upon which they are based will occur.
By their nature, forward-looking statements involve numerous
assumptions, known and unknown risks and uncertainties, both general
and specific, that contribute to the possibility that the predictions,
forecasts, projections and other forward-looking statements will not
occur, which may cause actual performance and results in future periods
to differ materially from any estimates or projections of future
performance or results expressed or implied by such forward-looking
statements. Such factors and risks include, without limiting the
foregoing, market demand for the metals and associated downstream
products for which Mkango is exploring, researching and developing, the
positive results of a feasibility study on the Project, delays in
obtaining financing or governmental or stock exchange approvals. The
forward-looking statements contained in this news release are made as
of the date of this news release. Except as required by law, the
Company disclaims any intention and assumes no obligation to update or
revise any forward-looking statements, whether as a result of new
information, future events or otherwise, except as required by
applicable law. Additionally, the Company undertakes no obligation to
comment on the expectations of, or statements made by, third parties in
respect of the matters discussed above.



Mkango Resources Limited

William Dawes
Chief Executive Officer
will@mkango.ca
UK: +44 207 3722 744
Canada: +1 403 444 5979
www.mkango.ca

Alexander Lemon
President
alex@mkango.ca
@MkangoResources

Blytheweigh
Financial Public Relations
Tim Blythe, Camilla Horsfall, Julia Tilley
UK: +44 207 138 3204

SP Angel Corporate Finance LLP
Nominated Adviser and Joint Broker
Jeff Keating, Caroline Rowe
UK: +44 20 3470 0470

Alternative Resource Capital
Joint Broker
Alex Wood, Rob Collins
UK: +44 20 7186 9004; +44 20 7186 9001

The TSX Venture Exchange has neither approved nor disapproved the
contents of this press release. Neither the TSX Venture Exchange nor
its Regulation Services Provider (as that term is defined in the
policies of the TSX Venture Exchange) accepts responsibility for the
adequacy or accuracy of this release.

This press release does not constitute an offer to sell or a
solicitation of an offer to buy any equity or other securities of the
Company in the United States. The securities of the Company will not be
registered under the United States Securities Act of 1933, as amended
(the "U.S. Securities Act") and may not be offered or sold within the
United States to, or for the account or benefit of, U.S. persons except
in certain transactions exempt from the registration requirements of
the U.S. Securities Act.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1823200002TS11823200530-05072520180821