Source	MARKET NEWS
Date	08/21/2018
Time	06:43:19 AM

Company	 Millennial Lithium Corp.
Title	Update 
of Ongoing Feasibility Study and Pilot Te





    CDNX Symbol: ML











Press Release





MILLENNIAL LITHIUM CORP ("ML-V;MLNLF-0")
- Update of Ongoing Feasibility Study and Pilot Testwork at
- its Pastos Grandes Lithium Project, Argentina

Millennial Provides Update of Ongoing Feasibility Study and Pilot
Testwork at its Pastos Grandes Lithium Project, Argentina

Millennial Lithium Corp. ("Millennial" or the "Company") is
pleased to announce that there has been significant progress on its
flagship Pastos Grandes Project in Salta, Argentina.  Millennial has
initiated numerous studies in support of its ongoing basic engineering
and Feasibility Study recently initiated by WorleyParsons Chile.

Farhad Abasov, Millennial President and CEO, commented, "We are
very pleased with the progress at our Pastos Grandes Project.
WorleyParsons is advancing the Pastos Grandes Feasibility Study which
remains on schedule for completion in Q1 2019.  Technical studies in
support of the Feasibility Study, including exploration drilling,
pumping well tests and geophysics are well underway on the REMSA
license that comprises part of the Pastos Grandes Project.  The pilot
pond earthworks have been completed and lining will begin shortly
followed by filling the ponds with brine from our pumping well
PGPW18-4.  The pilot plant design is advancing and construction of the
3 tonne-per-month lithium carbonate plant is expected to begin in Q4
2018."

Drilling

Exploration drilling has been initiated in the recently acquired
REMSA license.  Thirteen additional holes are programmed in the new
area; this work is expected expand the lithium resources at the project
and, with pumping tests, establish reserves for the project.  First
drill results from the current program are expected in September, 2018.


Pumping Well Testwork

A minimum three pumping wells are planned. The first is near
previous hole PGMW17-4b which intersected an aquifer approximately
381.5m thick yielding 535 mg/l lithium.  The pumping test work is
scheduled to begin in early September 2018; the brine will be captured
in the pilot ponds located adjacent to the well to be used for
pilot-scale processing.  The additional pumping wells are planned for
the REMSA license and will be located once analytical data is received.


Pilot Pond Testwork

Pilot pond earthworks with internal baffles has been completed and
lining of the ponds with geotextile followed by HDPE liner to commence
by month end.  The main pond set, consisting of four segments, is 150m
by 150m and a second pond set measures 100m by 100m.  These ponds are
expected to provide plant grade brine via solar evaporation for a pilot
plant that is planned produce lithium carbonate production data to be
utilized in the detailed engineering for the commercial plant.
Construction of the ponds is documented in recent photos located on the
Company's web-site (www.millenniallithium.com).

Geophysical Studies

Ground geophysical studies are also underway at Millennial's
Pastos Grandes Project including a seismic survey and a TEM survey,
both designed to delineate the extension of the brine bearing horizon
on the Pastos Grandes core licenses onto the contiguous REMSA license
to the south.  The surveys are in progress with estimated completion
and interpretation delivery in September 2018.

Pilot Plant

An on-site laboratory and a pilot plant capable of producing 3
tonnes per month of lithium carbonate are in the design and
procurements stages with construction to commence early in Q4 2018.
The plant is to be operated at the project site near the pilot pond
operation and is expected to include impurity removal via solvent
extraction and, carbonation and ion exchange to produce high purity
lithium carbonate.  The plant will provide valuable data for the
detailed engineering of the commercial plant, important operational
experience for the Millennial team, and tonne-lot quantities of lithium
carbonate for customer trials.

This news release has been reviewed by Iain Scarr, AIPG CPG.,
Chief Operating Officer of the Company and a Qualified Person as that
term is defined in National Instrument 43-101.

To find out more about Millennial Lithium Corp. please contact
Investor Relations at (604) 662-8184 or email
info@millenniallithium.com.

MILLENNIAL LITHIUM CORP.

"Farhad Abasov"

CEO, Director

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
RELEASE.

This news release may contain certain "Forward-Looking Statements"
within the meaning of the United States Private Securities Litigation
Reform Act of 1995 and applicable Canadian securities laws.  When used
in this news release, the words "anticipate", "believe", "estimate",
"expect", "target, "plan", "forecast", "may", "schedule" and similar
words or expressions identify forward-looking statements or
information.  These forward-looking statements or information may
relate to future prices of commodities, accuracy of mineral or resource
exploration activity, reserves or resources, regulatory or government
requirements or approvals, the reliability of third party information,
continued access to mineral properties or infrastructure, currency
risks including the exchange rate of USD$ for Cdn$, fluctuations in the
market for lithium, changes in exploration costs and government
royalties or taxes in Argentina and other factors or information. Such
statements represent the Company's current views with respect to future
events and are necessarily based upon a number of assumptions and
estimates that, while considered reasonable by the Company, are
inherently subject to significant business, economic, competitive,
political and social risks, contingencies and uncertainties. Many
factors, both known and unknown, could cause results, performance or
achievements to be materially different from the results, performance
or achievements that are or may be expressed or implied by such
forward-looking statements. The Company does not intend, and does not
assume any obligation, to update these forward-looking statements or
information to reflect changes in assumptions or changes in
circumstances or any other events affections such statements and
information other than as required by applicable laws, rules and
regulations.

TEL: 604-662-8184    MILLENNIAL LITHIUM CORP
FAX: 604-602-1606
E-mail: gharris@redhill-resources.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1823200026TS11823201165-06395420180821