Source	MARKET NEWS
Date	08/28/2018
Time	06:09:20 AM

Company	 Algold Resources Ltd.
Title	Drilling 
Intersects 16.27 g/t Au Over 13 Meters





    CDNX Symbol: ALG











Press Release





ALGOLD RESOURCES LTD ("ALG-V;ALGDD-0")
- Drilling Intersects 16.27 g/t Au Over 13 Meters

ALGOLD RESOURCES LTD. (the "Corporation") today announced further
assay results from its Phase IV 25,000-meter drilling campaign carried
out on the Corporation's Tijirit property ("Tijirit") in Mauritania.

Highlights

*  Hole T18RC123 (Eleonore North) - 16.27 g/t Au over 13 meters,
including 32.13 g/t Au over 6 meters on section S9840, inside the open
pit limits as defined in the May 2018 Preliminary Economic Assessment.
Further down hole, an intersection of 6.50 g/t Au over 2 meters
indicates that further parallel high-grade intersections may be present
( Figures 1 and 2).

*  Hole T18RC125 (Eleonore North) - 8.80 g/t Au over 2 meters on
section S10170, located 25 meters west of hole T16RC092, which
intersected 2.41 g/t Au over 3 meters.

*  Hole T18RD071 (Eleonore South) - returned multiple high-grade
intercepts in close proximity including 1.6 g/t Au over 5.5 meters and
2.01 g/t Au over 6.2 meters, 30 meters down dip of T16RC027, which
intersected 16.4 g/t Au over 6 meters (reference Algold's Press Release
August 16, 2016). (Figure 3)

*  Hole T18RD083 (Eleonore South) - 26.7 g/t Au over 0.7 meters,
1.5 g/t Au over 3 meters and 5.15 g/t Au over 1.6 meters, 50 meters up
dip of T17RD002, which returned 10.24 g/t Au over 3.7 meters (reference
Algold's Press Release dated September 12, 2017).

Eleonore North and South zones continue to validate the spatial
continuity of the mineralization identified to date and, importantly,
demonstrate that high grades are recurrent along strike and dip.
Furthermore, the wide, high-grade intersection in hole T18RC123 at
Eleonore North indicates the formation of a wide, cigar shape, shallow
dipping structure, possibly concentrating in variable large sheared
assymetric fold hinges related to late-tectonic emplacement.

The new diamond core ("DDH") and reverse circulation ("RC")
drilling results from Eleonore North and South zones corroborate the
high-grade and spatial continuity of the mineralization tested. In
2018, as part of the Phase IV drilling program, Algold completed over
7,600 meters of DDH drilling, representing approximately 20% of all
drilling completed on the Project to date.

Mineralization in Eleonore North is defined over one kilometer,
being separate from Eleonore Central by a crosscutting diabase dyke.
Hosted within the mafic volcanics, it is contained in sub-vertical or
more mildly dipping quartz-rich shear zones locally trending N050, N070
in addition to the regional trend of N020. These zones are both
sub-vertical and more shallower dipping. Visible gold is frequently
observed in drill samples, consistent with the zones to the south. The
mineralization remains open to the north and at depth.

At Eleonore North, the presence of several significant mineralized
intervals at similar depths in the vicinity of hole T18RC123
demonstrates the likely structural control to these zones of well
developed gold mineralization.  Further drilling and borehole logging
are currently underway to aid in interpretations prior to modelling and
testing possible ore shoots.

The Eleonore South mineralization extends over 1.2 kilometers from
north to south and is the southern-most zone defined thus far on the
3.4-kilometer-long Eleonore structure. The discrete shear zones that
may control the gold mineralization remain largely untested at depth.
In addition, several near-surface targets remain untested by drilling
and represent additional opportunity for near-term resource addition.

The Phase IV 25,000-meter program was initiated on May 7, 2018
with the objective of completing an initial 15,000 meters of drilling
by mid-July in order to upgrade inferred resources to the indicated and
measured category using a 40x40-meter grid. To date, Algold has
completed 15,565 meters of reverse-circulation and 7,613 meters of
diamond drilling and is in receipt of 7,425 RC assays and 2,327 DDH
assays.

Detailed geological descriptions of all mineralized zones can be
found on Algold's website (www.algold.com) and on SEDAR (www.sedar.com)
in the report entitled, "Algold 43-101 Technical Report: Tijirit Maiden
Mineral Resources Estimates for the Tijirit Gold Project in
Mauritania".

Following completion of the initial 15,000 meters of Phase IV
drilling, Algold commenced the remaining 10,000 meters of drilling,
which is aimed at testing the depth and strike extensions at Eleonore,
as well as defining resources over new high-priority targets at
Eleonore East and Salma. Algold looks forward to updating the market
with additional exploration results in the near future.

Table 1: Assay Result Highlights - Phase IV Drilling Program

Table is available at http://algold.com/press-release/



//st

*Vertical depth of intersection below RL collar.

**Weighted average grade, composite based on a minimum grade of 0.3 g/t
Au with an internal dilution of 0.005 g/t Au over 2 meters and an edge
grade of 0.25 g/t Au permitted.

***Down-hole length (estimated between 70-90% of true width of
mineralization).

No capping of higher values has been applied.

//et

Note: Complete assay results are available on Algold's website
(www.algold.com).

Quality Assurance / Quality Control (QA/QC) Analytical work for
drill core and chips, geochemical samples and rock chip samples is
being carried out at the independent SGS Laboratories Ltd. in Bamako,
Mali.  The 50 g fire assay with ASS finish analytical services are
accredited by SANAS and are carried out with a quality assurance
protocol in line with ISO 17025:2005. Samples are stored at the
Corporation's field camps and put into sealed bags until delivered by a
geologist on behalf of Algold to the laboratory in Bamako, Mali, where
samples are prepared and analyzed. Until the end of 2016, samples were
analyzed at ALS's facility in Loughrea, Ireland. Beginning in 2017,
samples are analyzed at SGS Laboratory, Bamako. Samples are logged in
the tracking system, weighed, dried and finely crushed to better than
70%, passing a 2 mm (Tyler 9 mesh, US Std. No.10) screen. A split of up
to 1,000 g is taken and pulverized to better than 85%, passing a
75-micron (Tyler 200 mesh) screen, and a 50-gram split is analyzed by
fire assay with an AA finish.  Anomalous samples greater than 5 g/t Au
are re-analyzed by 50 g fire assay with gravimetric finish.  Selected
samples may be re-analyzed using a 1 kg cyanide leach (Bottle Roll)
using "LeachWELL" or the 1 kg screen fire assay method. Blanks,
duplicates and certified reference material (standards) are inserted to
monitor laboratory performance during the analysis.

This press release has been reviewed for accuracy and compliance
under National Instrument 43-101 by Andre Ciesielski, DSc., PGeo.,
Algold Resources Ltd Lead Consulting Geologist and Qualified Person,
and Alastair Gallaugher, C.Geo. (Chartered Geologist and Fellow of the
Geological Society of London), BSc. Geology, Algold's Exploration
Manager in Mauritania, Qualified Persons as defined by NI 43-101
Standards of Disclosure for Mineral Projects. Andre Ciesielski has
further approved the scientific and technical disclosure in the news
release.

ABOUT ALGOLD

Algold Resources Ltd is focused on the exploration and development
of gold deposits in West Africa. The board of directors and management
team are seasoned resource industry professionals with extensive
experience in the exploration and development of world-class gold
projects in Africa.

Algold is developing the Tijirit Gold Project, which represents an
area of more than 750 km2, comprise of the Tijirit Exploitation License
of 306 km2 and of the Tijirit East Exploration License of 460 km2,
situated approximately 25 kilometers southeast of the Tasiast gold
mine. Exploration is being carried out on the Eleonore, Sophie I,
Sophie II-III, Lily and Salma zones.

CAUTIONARY LANGUAGE REGARDING FORWARD-LOOKING INFORMATION

This press release contains and refers to forward-looking
information based on current expectations. All other statements other
than statements of historical fact included in this release are
forward-looking statements (or forward-looking information). The
Corporation's plans involve various estimates and assumptions and its
business is subject to various risks and uncertainties. For more
details on these estimates, assumptions, risks and uncertainties, see
the Corporation's most recent Annual Information Form and most recent
Management Discussion and Analysis on file with the Canadian provincial
securities regulatory authorities on SEDAR at www.sedar.com. These
forward-looking statements are made as of the date hereof and there can
be no assurance that such statements will prove to be accurate.
Forward-looking statements are subject to significant risks and
uncertainties, and actual results and future events could differ
materially from those anticipated in such statements. Accordingly,
readers should not place undue reliance on forward-looking statements
that are included herein, except in accordance with applicable
securities laws.




Contact:

Algold Resources Ltd. 1320, boul. Graham, bureau 132, Mont-Royal,
Quebec, H3P 3C8, www.algold.com

//st

Benoit LaSalle, FCPA, FCA              Alex Ball

Chairman and Chief Executive Officer   Executive VP, Finance and
Corporate Development

b.lasalle@algold.com                   a.ball@algold.com

+1 (514) 951-4411                      +1 (647) 919 2227

//et
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1823900024TS11823900955-06064520180828