Source	MARKET NEWS
Date	08/29/2018
Time	06:29:56 AM

Company	 Puma Exploration Inc.
Title	Puma 
Exploration And Trevali Mining Corporation





    CDNX Symbol: PUMA











Press Release




[200/News Release]PUMAVPUMA EXPLORATION INCAUG 29 2018  06:24 AMPuma 
Exploration And Trevali Mining Corporation Drilled 13.1% Zn,4.8% Pb Over 27.0 
Meters at Murray Brook Deposit --->@NEWS RELEASE
TREVALI MINING CORP ("TV-T;TREVF-0")
PUMA EXPLORATION INC ("PUMA-V")
- Puma Exploration And Trevali Mining Corporation Drilled 13.1% Zn,
- 4.8% Pb Over 27.0 Meters at Murray Brook Deposit

Puma Exploration Inc. (the "Company" or "Puma") and Trevali Mining
Corporation ("Trevali") are pleased to release the drill results for
the metallurgical drilling program conducted at the Murray Brook
Deposit. The program successfully intersected the Massive Sulphide
Deposit in each hole matching perfectly with the Resources Model and a
potential internal mine design.

The metallurgical program consisted of 1,683 meters of drilling
within seven (7) new holes collared on the Deposit. The locations,
orientations and angles of the holes were defined according to a
preliminarily mine design. The main targeted zones of the Deposit were
the High-Grade Zinc Zone, the Low-Grade Zinc Zone and the High-Grade
Copper Zone. The priority was to proceed with the High-Grade and
Low-Grade Zinc Zones recovery tests and then evaluate any potential
future benefit within the High-Grade Copper Zone, the Oxyde Zone and
the Gold recovery of the Deposit. The recovery tests are currently in
process at RPC Facility in Fredericton, New Brunswick.

Highlights of the Metallurgical Drilling Program

//st

1) A total of 898 meters of Massive Sulphide (MS) was intersected in the
holes with continuous intersections of MS ranging from 36.60 meters to
209.75 meters;

2) High-Grade Zinc intercepts over significant thickness (see Table 2):

a.   MB18-05: 6.1% Zn, 2.1% Pb
(8.3% Zn+Pb) over 120.9
meters; including 13.1% Zn,
4.8% Pb (17.9% Zn+Pb) over 27
meters.

b.   MB18-06A: 3.8% Zn, 1.2% Pb
(5.0% Zn+Pb) over 158.1
meters; including 7.6% Zn,
2.8% Pb (10.4% Zn+Pb) over 24
meters.

c.   MB18-07: 6.9% Zn, 2.4% Pb
(9.3% Zn+Pb) over 87.1 meters;
including 10.2% Zn, 3.1% Pb
(13.3% Zn+Pb) over 21 meters.

3) High-Grade Copper Zones:

d.   MB18-01: 1.4% Cu over 36.6
meters including; 4.0% Cu over
9 meters;

e.   MB18-02: 2.1% Cu over 19.0
meters including; 4.3% Cu over
5 meters;

f.   MB18-03: 2.5% Cu over 24.0
meters including; 4.0% Cu over
6 meters;

g.   MB18-04: 0.85% Cu over 75.0
meters including; 1.0% Cu over
32 meters.

//et

"We are very happy with the initial drill results of the
metallurgical drilling program. Those results represent well the
continuity and the high-grade core of the Massive Sulphide Deposit
which brings different potential mining scenarios at Murray Brook",
notes Marcel Robillard, President of Puma Exploration.

The technical team is currently logging and sampling the drill holes
of the geotechnical and exploration drill programs and are supervising
the execution of Borehole geophysical surveys. The survey is aimed at
localising new mineralised zones in proximity of the recent drill holes
and characterizing the mineralization intersected in the holes.

Table 1: Metallurgical Drill holes at the Murray Brook Deposit

//st

Drillhole   Easting   Northing   Azimuth   Dip   Length (m)

MB18-01     693363    5266826    185       -65   125

MB18-02     693192    5266696    350       -65   264

MB18-03     693192    5266696    180       -75   125

MB18-04     693197    5266798    60        -50   275

MB18-05     693190    5266852    240       -75   374

MB18-06A    693220    5266806    250       -63   242

MB18-07     693190    5266852    330       -80   278

1,683

//et

Table 2: Significant Zinc drill results at the Murray Brook Deposit

//st

DDH #        From     To (m)   Length   Pb%    Zn%    Pb+Zn%   Cu%    Ag
(m)                                                      g/t

MB-2018-01   46.7     101.0    54.4     0.57   1.23   1.80     1.16   37

including    48.0     54.0     6.0      0.83   1.71   2.54     2.00   51

including    64.4     101.0    36.6     0.63   1.38   2.01     1.35   41

inc.         86.0     100.0    14.0     0.46   1.17   1.63     2.97   42

inc.         91.0     100.0    9.0      0.26   0.68   0.94     4.00   36

MB-2018-02   19.0     228.0    209.0    0.84   2.83   3.67     0.38   33

including    19.0     88.0     69.0     1.07   3.71   4.78     0.79   31

inc.         53.0     63.0     10.0     2.23   6.23   8.46     0.17   41

including    133.0    178.0    45.0     1.13   3.72   4.85     0.12   48

inc.         136.0    140.0    4.0      2.24   6.01   8.25     0.02   58

including    168.0    177.0    9.0      1.78   6.02   7.80     0.09   74

inc.         169.0    174.0    5.0      2.70   8.33   11.03    0.06   97

including    212.0    215.0    3.0      2.42   5.49   7.91     0.15   51

MB-2018-03   11.4     110.0    98.6     0.48   2.51   2.99     0.79   29

inc.         26.0     42.0     16.0     0.75   3.70   4.45     1.01   32

inc.         26.0     34.0     8.0      1.09   5.06   6.15     1.57   39

inc.         63.0     66.0     3.0      0.28   6.77   7.05     0.15   28

Including    80.0     102.0    22.0     0.87   3.73   4.60     0.19   42

inc.         85.0     99.0     14.0     1.22   4.87   6.09     0.20   52

inc.         85.0     92.0     7.0      1.38   6.10   7.48     0.11   60

MB-2018-04   114.0    252.3    138.3    0.69   1.56   2.25     0.65   37

Including    199.0    228.0    29.0     1.16   3.08   4.24     0.22   63

inc.         218.0    228.0    10.0     1.21   3.95   5.16     0.41   65

//et

//st

MB-2018-05    109.4   230.3   120.9   2.05   6.11    8.16    0.11   70

Including     112.0   139.0   27.0    2.22   7.31    9.53    0.07   88

inc.          112.0   122.0   10.0    2.38   8.17    10.55   0.06   88

Including     179.0   230.3   51.3    3.07   8.54    11.61   0.13   93

inc.          182.0   217.0   35.0    3.84   10.72   14.56   0.15   117

inc.          190.0   217.0   27.0    4.80   13.09   17.89   0.11   142

inc.          198.0   210.0   12.0    7.38   17.25   24.63   0.12   196

inc.          204.0   207.0   3.0     8.17   20.10   28.27   0.15   207

MB-2018-06A   57.0    215.1   158.1   1.20   3.75    4.96    0.15   38

including     79.0    97.0    18.0    1.76   6.08    7.84    0.10   89

inc.          86.0    96.0    10.0    2.08   8.05    10.13   0.08   84

including     120.0   125.0   5.0     1.24   5.17    6.41    0.08   35

including     146.0   151.0   5.0     1.79   5.33    7.12    0.03   52

including     173.0   214.0   41.0    1.82   5.45    7.27    0.13   46

inc.          190.0   214.0   24.0    2.81   7.56    10.37   0.06   61

inc.          190.0   207.0   17.0    2.84   8.07    10.91   0.06   64

inc.          202.0   207.0   5.0     4.10   10.12   14.22   0.06   60

MB-2018-07    154.9   242.0   87.1    2.35   6.86    9.21    0.13   96

including     154.9   193.0   38.1    2.93   9.04    11.97   0.12   142

inc.          157.0   168.0   11.0    3.30   10.89   14.19   0.15   161

inc.          157.0   161.0   4.0     4.46   15.08   19.54   0.18   215

including     181.0   242.0   61.0    2.46   7.42    9.88    0.15   96

inc.          181.0   202.0   21.0    3.09   10.18   13.27   0.14   144

inc.          181.0   193.0   12.0    4.75   16.64   21.39   0.19   243

inc.          182.0   189.0   7.0     5.27   19.66   24.93   0.20   274

including     223.0   241.0   18.0    3.16   9.66    12.82   0.23   97

inc.          223.0   228.0   5.0     3.68   14.67   18.35   0.22   107

//et

Note: the true thickness is ranging from 70%-90% of the core
intercepts.

Table 3: Significant Copper drill results at the Murray Brook
Deposit

//st

DDH #        From     To (m)   Length   Pb%    Zn%    Pb+Zn%   Cu%    Ag
(m)                                                      g/t

MB-2018-01   48.0     54.0     6.0      0.83   1.71   2.54     2.00   51

MB-2018-01   64.4     101.0    36.6     0.63   1.38   2.01     1.35   41

including    80.0     101.0    21.0     0.65   1.46   2.11     2.18   45

inc.         91.0     100.0    9.0      0.26   0.68   0.94     4.00   36

inc.         93.0     99.0     6.0      0.18   0.53   0.71     5.13   41

//et

//st

MB-2018-02   19.0    38.0    19.0   0.61   1.85   2.46   2.11    31

including    20.0    29.0    9.0    0.70   1.99   2.69   3.12    37

inc.         21.0    26.0    5.0    0.84   2.25   3.09   4.29    40

MB-2018-02   220.0   224.0   4.0    0.15   0.25   0.40   2.20    26

MB-2018-03   12.0    36.0    24.0   0.63   3.19   3.82   2.53    41

including    12.0    26.0    14.0   0.43   2.75   3.18   3.12    42

inc.         12.0    18.0    6.0    0.61   2.84   3.45   4.00    63

MB-2018-04   114.0   189.0   75.0   0.67   1.30   1.97   0.85    33

including    114.0   128.0   14.0   0.22   0.48   0.70   1.03    20

inc.         141.0   173.0   32.0   0.68   1.41   2.09   1.01    33

MB-2018-04   240.0   252.3   12.3   0.37   0.92   1.29   1.196   13.7

//et

Note: the true thickness is ranging from 70%-90% of the core
intercepts.

QC/AC protocols

All sampling, drilling, testing and analysis are conducted using
rigorous QA/QC procedures to ensure reliability and validity of results
beyond basic regulatory guidelines. The driller is responsible for
insuring that the core placed in boxes is in correct order and marking
the length tags for each rod-length of core as well as the inside of
the core boxes where the tag is located. This step is examined by the
technician and supervised by the on-duty project geologist. The driller
picks up core boxes from the drill site and takes them to the drill
core logging facilities in Bathurst.

Boxes are then laid out on logging tables and checked to make sure
that the core is continuous and in the right order in each box.
Geological logging of core is conducted, and sample positions are
marked to conform to lithological/alteration changes. Sample numbers
are written inside of the core boxes corresponding to pre-printed
sample tags. Chalk lines are marked down to identify the axis of core,
and boxes for sampling are moved to cutting area. Diamond saw blade
cutters are used to cut the core in half.

Core boxes are returned to their places in order on the logging
tables. Strong plastic rock sample bags are labelled with sample's
number on the outside and the sample tags are inserted inside. Then,
one half of the core is placed in its respective sample bag. The second
half is kept at the Alliance warehouse for future reference.

The samples are shipped, stored and assayed at the laboratory of
the Caribou Mine site held by Trevali Mining Corporation. Trevali has
an option to acquire 75% interest in the Murray Brook Deposit from
where the drilling program was conducted. The samples are crushed and
pulverized at a range of 80 to 100 microns. The crusher and pulverizer
are cleaned with pressurized air between each sample. The samples are
assayed by Absorption Atomic for Zinc (Zn), Lead (Pb), Copper (Cu),
Silver (Ag) and Iron (Fe) content. For QA/QC, there are typically 8
standards runs for each batch of 25. A duplicate is done at least once
every 50 samples, no blanks are run. Pulps are currently stored in the
lab in labelled brown sealed bags which in turn are stored in organized
labelled boxes. Coarse rejects are stored in labelled 18L pails on
pallets inside the Alliance warehouse.

The Murray Brook Deposit The Murray Brook Deposit, which is the
essence of the Strategic Alliance between the companies, is located 10
kilometers west of Trevali's Caribou Mine and 10 kilometers east of
Trevali's Restigouche Deposit in the Bathurst Mining Camp of New
Brunswick, Canada.

The deposit has a measured mineral resource of 3.68 million tonnes
grading 5.57% Zn, 1.87% Pb, 0.36% Cu, 70.5 g/t Ag and 0.56 g/t Au, plus
indicated mineral resources of 1.60 million tonnes grading 4.48% Zn,
1.63% Pb, 0.70% Cu, 65.3 g/t Ag and 0.88 g/t Au (for a combined
measured and indicated resource of 5.28 million tonnes averaging 5.24%
Zn, 1.80% Pb, 0.46% Cu, 68.9 g/t Ag and 0.65 g/t Au containing
approximately 610 million pounds of Zinc, 209 million pounds of Lead
and 11.7 million ounces of Silver, as of December 21, 2016.

The core of the mineral resource occurs in the West Zone
(Zinc-Lead) which is 200 meters wide, extending from surface to 300
meters vertical and the true thickness of the Massive Sulphide body
varies from 75 meters to 100 meters. The East Zone (Copper-Gold) is 100
meters wide, also extending from surface to 300 vertical meters and is
mainly mineralized with Gold and Copper. On February 20th, 2017, a NI
43-101 report was filed on SEDAR.

The Caribou Mine Trevali's Caribou mine is located approximately
10 kilometers east of the Murray Brook Deposit. It comprises an
underground mine, a 3.000-tonne-per-day (tpd) processing mill, a
flotation recovery plant, metallurgical and geochemical laboratories,
as well as a tailings management facility.

About Puma Exploration Inc. Puma Exploration is a Canadian mineral
exploration company with advanced precious and base metals projects in
Canada. The Company's major assets consist of an option to acquire 100%
beneficial interest in the Murray Brook Property, the Turgeon
Zinc-Copper Project and the Nicholas-Denys Project, all located in New
Brunswick. Also, Puma owns an equity interest in BWR Resources,
Manitoba. Puma's objective is to focus its exploration efforts in New
Brunswick.

About Trevali Mining Corporation Trevali is a Zinc-focused base
metal company with four mines: the wholly-owned Santander mine in Peru,
the wholly-owned Caribou mine in the Bathurst Mining Camp of northernNew 
Brunswick, its 90% owned Rosh Pinah mine in Namibia and its 90%
owned Perkoa mine in Burkina Faso.

Qualified Persons Technical information provided in this news
release was prepared and reviewed by Marcel Robillard, P.Geo.,
President,  and Dominique Gagne, P.Geo., Vice President Exploration of
Puma Exploration, qualified persons as defined by NI 43-101. Neither
TSX Venture Exchange nor its Regulation Services Provider (as that term
is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release. Mr.
Robillard and Mr. Gagne are not independent of the Company, as both are
officers and shareholders thereof.

Learn more by consulting www.pumaexploration.com for further
information on Puma Exploration Inc. Visit us on Facebook and Twitter.
Marcel Robillard, President Tel.: (418) 724-0901  |  email :
president@explorationpuma.com

Forward-Looking Statements: This press release may contain
forward-looking statements. Such forward-looking statements involve a
number of known and unknown risks, uncertainties and other factors
which may cause the actual results, performance or achievements of Puma
Exploration Inc. to be materially different from actual future results
and achievements expressed or implied by such forward-looking
statements. Readers are cautioned not to place undue reliance on these
forward-looking statements which speak only as of the date the
statements were made, except as required by law. Puma Exploration
undertakes no obligation to publicly update or revise any
forward-looking statements. These risks and uncertainties are described
in the quarterly and annual reports and in the documents submitted to
the securities administration.

Images accompanying this announcement are available at:



http://www.globenewswire.com/NewsRoom/AttachmentNg/daf47e70-6f25-46cb-9e72-
ca1d64615e93



http://www.globenewswire.com/NewsRoom/AttachmentNg/8b8ff443-7f87-47ca-b625-

TEL: 418-724-0901    PUMA EXPLORATION INC
FAX: 418-722-0310
E-mail: cguilbaud@explorationpuma.com
Website: http://www.explorationpuma.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1824000033TS11824000988-06244520180829