Source	MARKET NEWS
Date	08/29/2018
Time	06:29:50 AM

Company	 Velocity Minerals Ltd.
Title	Receives 
Positive Metallurgical Results at Rozin





    CDNX Symbol: VLC











Press Release




[200/News Release]VLCVVELOCITY MINERALS LTDAUG 29 2018  06:24 AMReceives 
Positive Metallurgical Results at Rozino Gold Project,Southeast Bulgaria 
--->@NEWS RELEASE
VELOCITY MINERALS LTD ("VLC-V;VLCJF-0")
- Receives Positive Metallurgical Results at Rozino Gold Project,
- Southeast Bulgaria

Velocity Minerals Ltd. ("Velocity" or the "Company") announces
that it has received positive results from comminution, flotation &
gravity recovery, and leach test work on a bulk sample representative
of the entire Rozino gold project ("Rozino" or the "Project"), located
in southeast Bulgaria.

Results of this work will be incorporated into the Rozino NI
43-101 Preliminary Economic Assessment ("PEA"), which is in progress
with results expected to be released in September 2018.  Delivery of
the PEA is the mechanism by which Velocity will earn a 70% interest in
the Rozino gold deposit.

"Comprehensive metallurgical test work has provided us with
positive results for inclusion into the Rozino PEA.  The results
included here provide Velocity with a mechanism to produce a 30 g/t
gold concentrate, which is amenable to processing at the nearby Gorubso
carbon-in-leach plant," stated Keith Henderson, Velocity's President &
CEO.  "The flotation test work has demonstrated that the process
delivers a high-quality concentrate for input to the existing CIL
plant.  With extremely low sulphide contents, low carbon contents and
negligible deleterious elements, this low-volume, high-grade
concentrate should complement the development options being considered
in the PEA."

Highlights of Results

*  )98% of sulphide recoverable to produce a gold concentrate
using standard flotation
*  Low-volume, high-grade concentrate complements PEA project
development options
*  Concentrate produced typically averages 30 g/t gold
*  Flotation gold recoveries of approximately 91%
*  Extremely simple mineralogy with negligible deleterious
elements
*  Low sulphide content ((1%) and low mass pull ((5%)
*  Low carbon content (1.2%) minimizes pregnant solution robbing
during leaching
*  Environmentally benign waste tailings product
*  Results based on representative bulk sample comprised of 1,600
core samples

Simple Mineralogy at Rozino

The uncomplicated nature of mineralogy at Rozino is one of the
attractive features of the gold deposit.  The mineralization is very
simple with gold associated with pyrite, which is the only significant
sulphide mineral in the deposit.

Flotation Test Work

The test work shows that more than 98% of the sulphide is
recoverable to produce a basic gold concentrate using standard
flotation techniques, conventional flotation reagents and a grind size
of 70% passing 200 mesh. The test work concentrate typically averages
30 g/t gold with recoveries of approximately 91%.  The economics of the
grind sizing and the reagent scheme used in the test work have not yet
been optimized, but these results indicate that a simple metallurgical
flowsheet is required, which may be refined in the next phase of test
work to further enhance the operating cost inputs.

One of the scenarios being considered in the PEA will be trucking
of this concentrate to Gorubso's CIL facility in Kardzhali.  The cost
of trucking this concentrate to Velocity's partner is not expected to
be material to the economics of the project.

Leach Test Work

Cyanidation tests were carried out on whole-rock mineralized
material, at differing grind sizes, and on the flotation concentrate
described above, via 48-hour bottle roll test work.  The whole rock
tests were conducted at 60% and 80% passing 200 mesh with recoveries of
70% and 83% respectively and moderate cyanide consumptions of 2.14 and
2.23 kg/t respectively. Leach kinetics are good with leaching
effectively complete within 24 hours.

Best leach results were gained from leach tests on flotation
concentrates returning optimum leach times of 24 hours and recoveries
of 87% extraction (Table 1).  Finer grinding of the concentrate does
not appreciably increase the leach recovery.

Table 1   Leach results of gold concentrates from the Rozino
deposit

//st

Extraction             87.48%

Consumption of Na CN   3.1 kg/t

Added NaCN             7.3 kg/t

Consumption of NaOH    5.0 kg/t

//et

Bulk Sample Composition

Head grade analyses of the bulk sample concurs with previous gold
assay results:

Table 2   Feed analysis of the 130kg bulk sample used for
metallurgical test work

//st

Gold  Sulphur  Carbon  Silver  Copper  Arsenic  Lead  Antimony Zinc

Bulk      (g/t)   (%)      (%)     (g/t)   (ppm)   (ppm)   (ppm) (ppm) (ppm)
Sample
Average
Head
Grade

1.28    0.42     1.20     2.0      48      125      28         74

//et

Mineralogical analysis of the bulk sample using X-Ray Diffraction
(XRD) confirmed a very straightforward Low Sulphidation Epithermal
style of mineralization as outlined in Table 3.  Positive aspects
include extremely low sulphide contents, low carbon contents and
negligible deleterious elements. The very low carbon content will avoid
any negative impact on gold recoveries through pregnant solution
robbing during cyanide leaching. The very low sulphide content together
with very high recoveries of the sulphides ()98%) results in a low mass
pull concentrate ((5%) and leaves a waste tailings product that is
environmentally benign.

Table 3   Mineralogical composition determined by XRD

//st

Mineralogy           Weight %

Quartz               61

Mica                 18

Potassium Feldspar   11

Carbonate            9

Pyrite

//et

All of the gravity and flotation test work was carried out on a
130kg bulk sample assembled from all of the significant drill
intercepts from the 2107 and 2018 drill programs.  The sample was
carefully prepared with material from more than 1,600 core samples.

Velocity has greatly improved on the results of historical
metallurgical test work carried out by previous operators at Rozino.
In part this improvement can be attributed to the quality of the bulk
sample assembled by Velocity and the extent to which it is
representative of the deposit.

Gravity Test Work

Gravity test work demonstrated that no significant free gold is
being lost and the test work did not improve upon the overall results,
even when integrated with the flotation test work.  As a result, the
gravity option will most likely not be considered in the upcoming PEA.

Ball Mill Work Index

Initial Bond Ball Mill Work Index ("BWI") determination was
carried out on whole drill core and returned a calculated value of
14.52.  This work is preliminary in nature and further work including
SAG mill test work is required, but the results are sufficient for the
initial ball mill design to be incorporated in the PEA.  The BWI
results are included in Table 4.  Preliminary BWI test work was carried
out on whole core taken from representative intercepts.

Table 4   Initial Bond Work Index results for the Rozino
mineralization

//st

D80 particle      d80 particle      End product      WG*           WI**
size of the       size of the       specific mass
feed              end product

(mm)              (mm)              (g/rev)          (kWh/g)       (kWh/t)

1.80              0.095             1.87             5.72 x 10-3   14.52

//et

//st

* WG    - Energy consumption per g end product

** WI   - Bond Work Index

//et

Details of Flotation Test Work Results

Fifteen variations of flotation test work were carried out,
including two lock cycle tests using a variety of differing grind sizes
and reagents and the results are included in Table 5.

The locked cycle test work was carried out on a coarser grind
fraction than most of the other tests and returned an average recovery
of 91% within a concentrate grading 30 g/t using standard flotation
methodology and relatively low-cost reagents.  Finer secondary grinding
of the concentrate did not result in significant improvement in
recoveries indicating that there is no cost benefit to producing higher
grade concentrates using finer grind processes.

Owing to the efficient recovery and low starting concentrations of
pyrite the mass pull is less than 5% resulting in a low-volume
concentrate with high gold recoveries.

Table 5   Summary of flotation test work on the Rozino bulk
metallurgical sample

//st

Test    Grind     Reagents                              Recoveries
% -75
micron

Na2CO3      KIBK     Aero     BM      Au (g/t)     Au
(g/t)       (g/t)    242      (g/t)                (%)
(g/t)

1       80        850         25       25       100     23.35        89.17

2       50/80     850         50       *        10      27.71        85.10

3       90        850         25       25       50      17.0         88.19

4       50        850         25       25       25      19.80        60.65

5       Ex        850         25       25       25      37.50        53.75
grav 2

6       80        850         25       25       50      16.37        87.67

7       70        850         25       25       50      21.93        87.81

8       80        850         75       0        50      35.49        86.24

9       80        850         25       25       50      22.20        85.98
10      80        850         KXK      0        25      21.96        80.37
100

11      70        850         25       25       25      36.40        90.66
LCT#

12      70        850         75       0        50      24.10        91.45
LCT#

13      60        850         50       50       50      24.15        82.84

14      70        250         50       50       75      18.96        88.03

15      70        0           0        50       75      24.49        86.14

//et

*NaHS and CuSO4 to mill. # LCT Locked Cycle Tests

Quality Assurance / Quality Control

The metallurgical work program at Rozino was designed and is
supervised by Len Holland B.Sc., C.Eng., FIMMM., FMES, an independent
consulting metallurgist who is responsible for all aspects of the
metallurgical test work, including the quality control/quality
assurance program.

The flotation, gravity and leach test work, together with gold
deportment, mineralogical and laser sizing studies were carried out by
Eurotest Control EAD, Bulgaria on a homogenized bulk sample that was
assembled through splitting of 1,632 coarse reject samples.  The sample
splitting was carried out by Velocity's staff using Jones splitters in
accordance with best international practice.  The bulk sample was
subsequently homogenized by Eurotest according to the Australian
Standard - AS 3988-91 - Sample Preparation for the Determination of
Gold, before being divided into 1kg aliquots using a rotary splitter.
Eurotest conducted homogenization tests including Fischer dispersion
analysis and 50 chemical analyses in order to ensure that each
metallurgical sample was representative of the combined mineralized
intervals from Rozino.

The Eurotest Control laboratory is certified by LRQA to ISO 9001.
The company also holds a certificate of accreditation as a testing
laboratory pursuant to BDS EN ISO 17025.  Analyses of materials less
than 5g/t gold were carried out by ICP-OES on Aqua Regia digest.
Samples containing more than 5 g/t were analyzed by 30g Fire Assay
using an AAS finish.  Specialist determinations were carried out in
accordance with best international practice, e.g. Sulphur was
determined by the LECO technique.  Comminution studies were carried out
by Eurotest and the University of Mining and Geology in Sofia.  The
preliminary BWI determination was carried out on a 22.5kg sample of
whole drill core selected to be representative of typical
mineralization from the Rozino deposit.

Qualified Person

The technical content of this release has been approved for
disclosure by Len Holland, a Qualified Person as defined by National
Instrument 43-101.  Mr. Holland is independent of the Company.

About the Rozino Gold Project

Velocity has been exploring and drilling at Rozino since August
2017, publishing a maiden Inferred Mineral Resource Estimate in Q1
2018; 17Mt @ 1.15g/t gold for 629,000 ounces at 0.5g/t cut-off grade
with 8.2Mt @ 1.68g/t gold for 443,000 ounces at 0.8g/t cut-off grade.
Approximately 90% of estimated resources at depths of less than 110m
from surface and less than 1% below 150m from surface.  Mineralization
remains open for expansion.  The Company has completed the 2018 drill
program with a view to publishing an updated mineral resource estimate
and PEA before year end. On completion of the PEA, the Company will
exercise its option for a 70% interest in the project and will move
forward in joint venture with its Bulgarian partner.

About Velocity Minerals Ltd.

Velocity is a gold exploration and development company focused on
eastern Europe.  The Company's management and board includes mining
industry professionals with combined experience spanning Europe, Asia,
and the Americas as employees of major mining companies as well as
founders and senior executives of junior to mid-tier public companies.
The team's experience includes all aspects of mineral exploration,
resource definition, feasibility, finance, mine construction and mine
operation as well as a track record in managing publicly listed
companies.

About Bulgaria

Bulgaria is a member of NATO (2004) and a member of the European
Union (2007). The local currency (BGN) has been tied to the Euro since
1999 (1.956 BGN/EUR).  The country is served by modern European
infrastructure including an extensive network of paved roads.  Bulgaria
boasts an exceptionally low corporate tax rate of only 10%.  The
country's education system is excellent with good availability of
experienced mining professionals in a favourable cost environment.
Foreign mining companies are successfully operating in Bulgaria.  The
country's mining law was established in 1999 and updated in 2011.
Mining royalties are low and compare favourably with more established
mining countries.

On Behalf of the Board of Directors "Keith Henderson" President &
CEO

Contact Information:

Contact:

Keith Henderson Phone: +1-604-484-1233 E-mail:
info@velocityminerals.com Web: www.velocityminerals.com

Neither the TSX Venture Exchange nor its Regulation ServicesProvider (as that 
term is defined in policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

CAUTIONARY STATEMENT REGARDING FORWARD-LOOKING INFORMATION: This
news release includes certain "forward-looking statements" under
applicable Canadian securities legislation.  Forward-looking statements
include, but are not limited to, statements with respect to: future
exploration and testing carried out on the Tintyava property; use of
funds; and the future business and operations of Velocity.   Often, but
not always, forward looking statements can be identified by words such
as "pro forma", "plans", "expects", "may", "should", "budget",
"scheduled", "estimates", "forecasts", "intends", "anticipates",
"believes", "potential" or variations of such words including negative
variations thereof, and phrases that refer to certain actions, events
or results that may, could, would, might or will occur or be taken or
achieved.  Forward looking information involves known and unknown
risks, uncertainties and other factors which may cause the actual
results, performance or achievements of the Company to differ
materially from any future results, performance or achievements
expressed or implied by the forward-looking information.  Such risks
and other factors include, among others, operating and technical
difficulties in connection with mineral exploration and development and
mine development activities for the Tintyava property, including the
geological mapping, prospecting and sampling programs for the projects,
the fact that the Company's interests in the Tintyava property is only
an option and there is no guarantee that the interest, if earned, will
be certain, actual results of exploration activities, including the
program, estimation or realization of mineral reserves and mineral
resources, the timing and amount of estimated future production, costs
of production, capital expenditures, the costs and timing of the
development of new deposits, the availability of a sufficient supply of
water and other materials, requirements for additional capital to fund
the Company's business plan, future prices of precious metals, changes
in general economic conditions, changes in the financial markets and in
the demand and market price for commodities, possible variations in ore
grade or recovery rates, possible failures of plants, equipment or
processes to operate as anticipated, accidents, labour disputes and
other risks of the mining industry, delays in obtaining governmental
and regulatory approvals (including of the TSX Venture Exchange),
permits or financing or in the completion of development or
construction activities, changes in laws, regulations and policies
affecting mining operations, hedging practices, currency fluctuations,
title disputes or claims limitations on insurance coverage and the
timing and possible outcome of pending litigation, environmental issues
and liabilities, risks related to joint venture operations, and risks
related to the integration of acquisitions, as well as those factors
discussed under the heading.  "Risk Factors" in the Company's annual
management's discussion and analysis and other filings of the Company
with the Canadian Securities Authorities, copies of which can be found
under the Company's profile on the SEDAR website at www.sedar.com.

Readers are cautioned not to place undue reliance on forward
looking information.  The Company undertakes no obligation to update
any of the forward-looking information in this news release or
incorporated by reference herein, except as otherwise required by law.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1824000032TS11824000985-06244320180829