Source	MARKET NEWS
Date	08/31/2018
Time	08:20:36 AM

Company	 Azarga Metals Corp.
Title	Clarifies 
Disclsoure on Preliminary Economic Ass





    CDNX Symbol: AZR











Press Release





AZARGA METALS CORP ("AZR-V;EUUNF-0")
- Clarifies Disclsoure on Preliminary Economic Assessment (PEA) on
- Unkur Copper-Silver Project

AZARGA METALS CORP. ("Azarga Metals" or the "Company") announced
the positive findings of an independently prepared preliminary economic
assessment ("PEA") for the development of its wholly-owned Unkur
Copper-Silver Project in the Zabaikalsky administrative region of
eastern Russia on 30 August 2018. At the request of IIROC the Company
wishes to clarify certain disclosure in its August 30, 2018 news
release titled "Azarga Metals Announces Positive, Independent,
Preliminary Economic Assessment on Unkur Copper-Silver Project".

This announcement covers the PEA but has been expanded to allow
the Company and Tetra Tech, Inc. ("Tetra Tech") to make additional
comments on: (i) metallurgical process; and (ii) silver price forecast.
This release includes such additional comments along with the PEA
summary.

Regarding metallurgical process, further information and
background on the metallurgical process(es) summarized in the original
PEA announcement, used to achieve 94% recoveries for both copper and
silver and produce a very high grade concentrate product containing
approximately 75.0% copper and  6,500g/t silver have been included in
the Mining and Processing and Product and Marketing sections below.

Regarding silver price. A silver price of US$20 per ounce was used
in the PEA and while it may appear high relative to the current spot
price of less than US$15 per ounce, the forecast price is justified on
the basis that: (i) the forward curve for silver, permanently in
contango, only dropped below US$20 per ounce for the 2020-2021 period
(matching potential development timeframe for Unkur) in June 2018 and
has been above that for most of the last three years; and (ii) the
average long-term silver price forecast of a number of independent
analysts referenced (including Macquarie Bank, UBS, Credit Suisse, BMO,
ABN Amro and TD Economics) remains at approximately US$20 per ounce. It
should also be noted that copper is the primary revenue metal in the
PEA.

The PEA is based on the current Inferred Mineral Resource estimate
for Unkur of 62 million tonnes at 0.53% copper and 38.6g/t silver,
containing 328,600 tonnes (724 million pounds) of copper and 76.8
million troy ounces of silver, as announced by the Company on 27 March
2018 ("2018 Mineral Resource").

Dorian L. (Dusty) Nicol, Azarga Metals' President and CEO
commented on the PEA, "We are extremely encouraged that even based only
on our initial exploration, Unkur is able to demonstrate a positive PEA
result.". He then went on to say, "Additional exploration is expected
to significantly grow the size of the deposit and this will likely
continue to enhance the project economics when an updated PEA is
prepared."

The following table summarizes key Unkur Project PEA metrics.

//st

Table 1: Key Unkur Project PEA metrics

Parameters / metrics                    Amount1

Production

- Total mill feed                       16.9 million tonnes LOM / 2.0
million tonnes per year

- Copper feed grade (ave)               0.66%

- Silver feed grade (ave)               57.9g/t

- Initial LOM                           8-years

- LOM copper recovery                   94.0%

- LOM silver recovery                   94.0%

- Concentrate grade - copper (dry)      75%

- Concentrate grade - silver (dry)      6,500 g/t

- Total copper production               105,737 tonnes LOM / 13,217
tonnes per year (ave)

- Total silver production               29.63 million ounces LOM / 3.70
million ounces per year (ave)

- LOM strip ratio                       9.7:1

Capital and costs

- Pre-production capital                US$186.6 million (including
US$37.3 million contingency)

- LOM sustaining capital                US$14.4 million

- Closure costs                         US$3.6 million

- Copper C1 cash cost (excl. G&A)       US$0.38 per pound (assuming
silver as a by-product)

Project economics (pre-tax)             US$2.84 per pound (excluding
by-product sales)

- Copper price                          US$3.25 per pound

- Silver price                          US$20.0 per ounce

- Russian Ruble                         62.5 per US$1

- NPV                                   US$203.6 million (at 8.0%
discount rate)

- IRR                                   28.9%

- Payback                               3.0 years

Project economics (post-tax)2

- NPV                                   US$147.5 million (at 8.0%
discount rate)

- IRR                                   24.4%

Notes: 1. References to 'ounces' are troy ounces, 2. Assuming Unkur
Project qualifies for Russian Far East & Siberian tax incentives for
mineral extraction projects.

//et

MINING AND PROCESSING

The mining method selected for the PEA is open-pit mining, based
upon contract mining of mineralized material and waste.

The initial mine plan has been designed on a higher-grade sub-set
of the 2018 Mineral Resource, comprising 15.5 million tonnes of
mineralized material at a grade of 0.76% copper and 66.6g/t silver,
with an annual production rate of approximately 2 million tonnes of
mill feed per year. The overall LOM waste to mill feed material (i.e.,
strip) ratio is projected to be 9.7:1. However, it should be noted that
much of the overburden is unconsolidated moraine material that will not
require blasting.

Preliminary metallurgical test work on a bulk sample demonstrated
that 95% copper and silver extraction can be achieved using
conventional hydrometallurgical processing methods. The PEA process
plant design is based on 2 million tonne per annum capacity, with LOM
feed of average diluted copper grade of 0.66% and average diluted
silver grade of 57.9g/t. The conceptual process flowsheet consists of a
jaw crusher followed by a two-stage conventional milling
(semi-autogenous grinding mill and ball mill) in order to produce
slurry with an optimum size distribution for cyanidation. The slurry,
with a characteristic particle size of P(sub)80(/sub) = 75 m, will be
fed into pre-leach thickeners. The thickener underflows will then be
leached in agitated leach tanks and subsequently washed in a counter
current decantation circuit prior to being treated by a sulphidization,
acidification, recycling and thickening ("SART") circuit, which
produces a copper and silver concentrate and recycle cyanide. SART is
an established process based on proven chemistry employed in high
copper gold projects such as Nemont's Yanacocha and Anglo Asian's
Gedabek Projects.

The PEA assumes the proposed process plant will provide an average
silver recovery of 94.0% and an average copper recovery of 94.0%,
taking process efficiencies into account.

Tailings from the process plant will be pumped to a tailings
management facility.

PRODUCT AND MARKETING

The SART process will produce a synthetic mineral precipitate
largely consisting of chalcocite (Cu(sub)2(/sub)S) and acanthite
(Ag(sub)2(/sub)S), which will result in a high-grade copper concentrate
of approximately 75.0% copper and 6,500g/t silver. This compares
favourably with standard copper concentrates that are typically 22-24%
copper and so it should make this product very attractive to smelters.
There is also the possibility that this material may be accepted
directly at custom refiners.

OUTBOUND LOGISTICS

The PEA assumes a 12-kilometer road will be built from the
existing highway, which is also where the Baikal-Amur Mainline railway
is. The concentrate can either be sold within Russia, exported to China
(via rail or road) or other international customers (assumed to be via
rail to the Russian Pacific port of Sovetskaya Gavan a distance of some
2,300 kilometers).

INFRASTRUCTURE

Unkur Copper-Silver Project has access to infrastructure. The
project site is situated within 20 kilometers of the town of Novaya
Chara, with major road and rail access. A regional 220kVA power line
runs across a corner of the Unkur license area and the PEA assumes
construction of a 4 kilometer overhead powerline and substation to
connect the processing plant and main site to mains power.

The world's largest current copper project development is taking
place at Udokan, approximately 30 kilometers from Unkur. As a result,
substantial investment in improved ancillary infrastructure is being
made that will be of future benefit to Azarga Metals and Unkur,
including a renovation of the regional airport, roads and a significant
expansion of facilities at Novaya Chara town.

PRE-DEVELOPMENT

The PEA assumes a two-year pre-development timeline prior to first
production. Initial development in the first year consists mainly of
infrastructure works, site preparation and commencement of plant
construction. Pre-stripping and tailings storage facility development
will occur in the second pre-development year along with completion of
the processing plant.

FUTURE PEA ENHANCEMENT

This initial PEA was based on the 2018 Mineral Resource, which was
largely the product of the first modern exploration campaign conducted
at Unkur Copper-Silver Project in 2016-2017. Azarga Metals considers
that there is strong potential to grow the 2018 Mineral Resource.
Mineralization is open in both directions along strike and at depth.
Azarga Metals aims to substantially grow the mineral resource at Unkur,
with a particular initial focus on the zone of thicker and higher grade
mineralization in the northern part of the interpreted mineralized
area. Increased Mineral Resources would be highly likely to increase
the proposed mining inventory in a future subsequent PEA, with a likely
resultant improvement in project economics.

Qualified Person and NI 43-101 Disclosure

The PEA is preliminary in nature, and includes Inferred Mineral
Resources that are considered too speculative geologically to have the
economic considerations applied to them that would enable them to be
categorized as mineral reserves, and there is no certainty that the PEA
will be realized. Mineral Resources that are not Mineral Reserves do
not have demonstrated economic viability.

Dorian (Dusty) Nicol B.Sc. Geo, MA Geo the Company's President and
Chief Executive Officer and, a Qualified Person as defined by NI 43-101
has prepared, supervised the preparation, or approved the scientific
and technical disclosure in this news release.
Independent Qualified Person, Andy Carter, of Tetra Tech, Inc.,
has reviewed and approved the technical content of this news release.

About Azarga Metals Corp.

Azarga Metals is a mineral exploration and development company
that owns 100% of the Unkur Copper-Silver Project in the Zabaikalsky
administrative region in eastern Russia.

AZARGA METALS CORP.

"Dusty Nicol"

Dorian L. (Dusty) Nicol, President and CEO

For further information please contact: Doris Meyer, at +1 604
536-2711 ext 6, visit www.azargametals.com, or follow us on Twitter
@AzargaMetals.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Cautionary Statement:

This news release contains forward-looking statements that are
based on the Corporation's current expectations and estimates.
Forward-looking statements are frequently characterized by words such
as "plan", "expect", "project", "intend", "believe", "anticipate",
"estimate", "suggest", "indicate" and other similar words or statements
that certain events or conditions "may" or "will" occur. Such
forward-looking statements involve known and unknown risks,
uncertainties and other factors that could cause actual events or
results to differ materially from estimated or anticipated events or
results implied or expressed in such forward-looking statements. Such
factors include, among others: the actual results of current planned
exploration activities; conclusions of economic evaluations; changes in
project parameters as plans to continue to be refined; possible
variations in mineralized material grade or recovery rates; accidents,
labor disputes and other risks of the mining industry; delays in
obtaining governmental approvals or financing; and fluctuations in
metal prices. There may be other factors that cause actions, events or
results not to be as anticipated, estimated or intended. Any
forward-looking statement speaks only as of the date on which it is
made and, except as may be required by applicable securities laws, the
Corporation disclaims any intent or obligation to update any
forward-looking statement, whether as a result of new information,
future events or results or otherwise. Forward-looking statements are
not guarantees of future performance and accordingly undue reliance
should not be put on such statements due to the inherent uncertainty
therein.

TEL: 604-536-2711    AZARGA METALS CORP
FAX: 604-536-2788
E-mail: doris@goldenoakcorporate.com
Website: http://www.azargametals.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1824200018TS11824200905-08174620180831