Source	MARKET NEWS
Date	09/04/2018
Time	06:30:31 AM

Company	 Panoro Minerals Ltd.
Title	Increased 
Copper Recovery Estimates at Antilla C





    CDNX Symbol: PML











Press Release





PANORO MINERALS LTD ("PML-V;POROF-0")
- Increased Copper Recovery Estimates at Antilla Copper Project,
- Peru

Panoro Minerals Ltd. ("Panoro", the "Company") Panoro is pleased
to announce the final results from the recently completed leach test
from Column #4 at the 100% owned Antilla Copper Project.

The revised estimate for copper recovery from the secondary
sulphides is 79.9% in a period of 150 days. This is an increase from
the Preliminary Economic Assessment (PEA), announced in May 2018 which,
which included an estimated 72.5% copper recovery over a 200 day
period.

"The results of the Antilla column leach testing program have
demonstrated significant upside potential to the Antilla Project
economics. The project is well situated, with low capital intensity,
low operating costs and strong economics.  We are confident that the
strategic review of the projects' roadmap to feasibility and
development will yield positive outcomes in the near future," stated
Luquman Shaheen, President & CEO of Panoro Minerals.

The leach test results from Column #4 have increased the estimated
recoveries and reduced the recovery time of each of the four
mineralogical zones included in the Antilla Project mine plan in the
PEA as summarized in the table below.

//st

Mineralogical   Copper Recovery Estimates
Zone

Current Estimates    2018 PEA Estimates   Change

Cu          Period   Cu          Period   Cu         Period
Recovery    (days)   Recovery    (days)   Recovery   (days)
(%)                  (%)                  (%)

Cover           72.9        150      31.1        200      + 41.8     - 50

Leach Cap       74.4                 38.0                 + 36.4

Secondary       79.9                 72.5                 + 7.4
Sulphides

Primary         69.7                 21.2                 + 48.5
Sulphides

//et

The PEA mine plan includes 117 million tonnes of secondary
sulphides corresponding to 98% of the feed to the heap leach pad.  The
balance of the feed to the heap leach is made up of Cover, Leach Cap
and Primary Sulphides.

The recoveries estimated for the PEA were derived from bottle roll
tests and mineralogic testwork available at the time of the completion
of the PEA.  The column test program was initiated early in 2018 while
the PEA was underway. Leach tests from Columns #1, #2 and #3 were
completed in July 2018 and #4 was completed in August 2018.

The PEA recovery estimates were based on analytical extraction
data. The revised estimates are based on an assessment of the actual
and likely extractions under a thermophilic leach scenario.  Also, the
PEA estimates included days under acid leach in the laboratory
testwork. The new estimates assume bioleaching from the start.

The original objective of the test program was to determine copper
extraction from supergene (secondary sulphide) material under simulated
mesophilic bio-leach conditions (medium temperature) at a range of
crush sizes. These tests were successful and indicated that overall
process recoveries of 72.5% were achievable. Leaching of primary
sulphides such as chalcopyrite or enargite is limited under mesophilic
conditions. The leach cycle of Column #4 was extended and the column
transitioned to thermophilic conditions (up to 55C temperature) to
determine to what extent the small amounts of primary sulphides within
the material would be leached. Transitioning to thermophilic conditions
led to a significant improvement in the global leach extraction with
85% copper extraction being achieved. Overall process recovery is
estimated to be 94% of leach extraction for each zone where the leach
extraction estimates are summarized in the table below.

//st

Mineralogical Zone    Cu Extraction (%)
Cover                 77.6

Leach Cap             79.2

Secondary Sulphides   85.0

Primary Sulphides     74.2

//et

Extraction numbers are based on laboratory column leach tests of
supergene material under simulated mesophilic and thermophilic bioleach
conditions.  Additional laboratory bioleach testwork will be completed
as part of the next stage of engineering for the project. Heap
bioleaching has been successfully implemented over the past 30 years.
Examples of current and historical copper heap bioleach projects are
the Cerro Verde mine, Peru (Freeport McMoran), the La Granja project,
Peru (Rio Tinto), the Cerro Colorado mine, Chile (BHP), the Quebrada
Blanca mine, Chile (Teck Resources), the Zaldivar mine, Chile
(Barrick), the Lince II mine, Chile (Antofagasta Plc), in addition to
others.

The column leach program, together with associated mineralogical
and bottle roll leach testwork has been conducted at Aminpro
Laboratories, an ISO 9001 and 14001 Laboratory based in Lima, Peru. All
works were designed and supervised by Andrew Carter, General Manager UK
of the Mining and Minerals arm of Tetra Tech.

About Panoro

Panoro Minerals is a uniquely positioned Peru focused copper
exploration and development company.  The Company is advancing its
flagship project, Cotabambas Copper-Gold-Silver Project and its Antilla
Copper-Molybdenum Project, both located in the strategically important
area of southern Peru. The Company is well financed to expand, enhance
and advance its projects in the region where infrastructure such as
railway, roads, ports, water supply, power generation and transmission
are readily available and expanding quickly.  The region boasts the
recent investment of over US$15 billion into the construction or
expansion of four large open pit copper mines.

Since 2007, the Company has completed over 80,000 meters of
exploration drilling at these two key projects leading to substantial
increases in the mineral resource base for each, as summarized in the
table below.

Summary of Cotabambas and Antilla Project Resources

//st

Project       Resource          Million    Cu      Au       Ag       Mo
Classification    Tonnes     (%)     (g/t)    (g/t)    (%)

Cotabambas    Indicated         117.1      0.42    0.23     2.74     0.001
Cu/Au/Ag

Inferred          605.3      0.31    0.17     2.33     0.002

@ 0.20% CuEq cutoff, effective October 2013, Tetratech

Antilla       Indicated         291.8      0.34    -        -        0.01
Cu/Mo

Inferred          90.5       0.26    -        -        0.007

@ 0.175% CuEq cutoff, effective May 2016, Tetratech

//et

Preliminary Economic Assessments (PEA) have been completed for
both the Cotabambas and Antilla Projects, the key results are
summarized below.

Summary of Cotabambas and Antilla Project PEA Results

//st

Key Project Parameters                       Cotabambas       Antilla Cu
Cu/Au/Ag         Project2
Project1

Process Feed, life of mine    million        483.1            118.7
tonnes

Process Feed, daily           Tonnes         80,000           20,000

Strip Ratio, life of mine                    1.25 : 1         1.38: 1

Before Tax1         NPV7.5%   million USD    1,053            520

IRR       %              20.4             34.7

Payback   Years          3.2              2.6

After Tax1          NPV7.5%   million USD    684              305

IRR       %              16.7             25.9

Payback   Years          3.6              3.0

Annual Average      Cu        thousand       70.5             21.0
Payable Metals                tonnes

Au        thousand       95.1             -
ounces
Ag        thousand       1,018.4          -
ounces

Mo        thousand       -                -
tonnes

Initial Capital Cost          million USD    1,530            250

* Project economics estimated at commodity prices of; Cu = US$3.00/lb, Au
= US$1,250/oz, Ag = US$18.50/oz, Mo = US$12/lb * Project economics
estimated at long term commodity price of Cu = US$3.05/lb and Short term
commodity price of Cu = US$3.20, US$3.15 and US$3.10 for Years 1,2 and 3
of operations, respectively.

//et

The PEAs are considered preliminary in nature and include Inferred Mineral
Resources that are considered too speculative to have the economic
considerations applied that would enable classification as Mineral
Reserves. There is no certainty that the conclusions within the updated PEA
will be realized. Mineral Resources are not Mineral Reserves and do not
have demonstrated economic viability.

Luis Vela, a Qualified Person under National Instrument 43-101, has
reviewed and approved the scientific and technical information in this
press release.

On behalf of the Board of Panoro Minerals Ltd.

Luquman Shaheen. PEng, PE, MBA President & CEO

FOR FURTHER INFORMATION,

Contact Information:

CONTACT:

//st

Panoro Minerals Ltd. Luquman    Renmark Financial Communications Inc.
Shaheen, President & CEO        Laura Welsh Tel.: (416) 644-2020 or (416)
Phone: 604.684.4246 Fax:        939-3989 blwelsh@renmarkfinancial.com
604.684.4200 Email:             www.renmarkfinancial.com
info@panoro.com Web:
www.panoro.com

//et

CAUTION REGARDING FORWARD LOOKING STATEMENTS:   Information and
statements contained in this news release that are not historical facts
are "forward-looking information" within the meaning of applicable
Canadian securities legislation and involve risks and uncertainties.

Forward-looking statements are subject to a variety of known and
unknown risks, uncertainties and other factors which could cause actual
events or results to differ materially from those expressed or implied
by the forward-looking statements, including, without limitation:

*  risks relating to metal price fluctuations;
*  risks relating to estimates of mineral resources, production,
capital and operating costs, decommissioning or reclamation expenses,
proving to be inaccurate;
*  the inherent operational risks associated with mining and
mineral exploration, development, mine construction and operating
activities, many of which are beyond Panoro's control;
*  risks relating to Panoro's ability to enforce Panoro's legal
rights under permits or licenses or risk that Panoro's will become
subject to litigation or arbitration that has an adverse outcome;
*  risks relating to Panoro's projects being in Peru, including
political, economic and regulatory instability;
*  risks relating to the uncertainty of applications to obtain,
extend or renew licenses and permits;
*  risks relating to potential challenges to Panoro's right to
explore and/or develop its projects;
*  risks relating to mineral resource estimates being based on
interpretations and assumptions which may result in less mineral
production under actual circumstances;
*  risks relating to Panoro's operations being subject to
environmental and remediation requirements, which may increase the cost
of doing business and restrict Panoro's operations;
*  risks relating to being adversely affected by environmental,
safety and regulatory risks, including increased regulatory burdens or
delays and changes of law;
*  risks relating to inadequate insurance or inability to obtain
insurance;
*  risks relating to the fact that Panoro's properties are not yet
in commercial production;
*  risks relating to fluctuations in foreign currency exchange
rates, interest rates and tax rates; and
*  risks relating to Panoro's ability to raise funding to continue
its exploration, development and mining activities.

This list is not exhaustive of the factors that may affect the
forward-looking information and statements contained in this news
release. Should one or more of these risks and uncertainties
materialize, or should underlying assumptions prove incorrect, actual
results may vary materially from those described in the forward-looking
information.  The forward-looking information contained in this news
release is based on beliefs, expectations and opinions as of the date
of this news release. For the reasons set forth above, readers are
cautioned not to place undue reliance on forward-looking information.
Panoro does not undertake to update any forward-looking information and
statements included herein, except in accordance with applicable
securities laws.
Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1824600028TS11824601074-06270120180904