Source	MARKET NEWS
Date	09/04/2018
Time	06:47:55 AM

Company	 Rizal Resources Corporation
Title	T'Boli 
Gold Silver Project Exploration Update





    CDNX Symbol: RZL











Press Release





RIZAL RESOURCES CORP ("RZL-V")
- T'Boli Gold-Silver Project Exploration Update

Rizal Resources Corporation ("Rizal" or the "Company")

Detailed mapping highlights potential controls on the location of high
grade gold at the T'Boli Gold Silver Project ("T'Boli" or T'Boli Project").

Trial mining activities with gold mineralization separation techniques have
resulted in an improved delivered gold grade to the Processing Plant of
over 4g/t for the month of July.

Similar trial mining using the same mining method in the higher-grade South
Veins are planned in late September with the objective of improving the
grade to the Processing Plant.

Processing of bulk samples from trial mining resulted in Gold (601oz) and
Silver (1,059oz) produced and sold during the month of July with revenues
exceeding the operating costs at T'Boli. Total revenue was CAD946,209
(unaudited), while operating costs totaled CAD658,912 (unaudited).

In connection with trial mining and bulk sampling activities, refinements
to the mining method and enhancements to the processing plant are ongoing
with the objective of increasing tonnage throughput and processing
capabilities.

Planned exploration development of drives accessing the South Veins will
intersect two of the high-grade drill hole intercepts with 3.7m (true
width) @ 15g/t (uncut) from TG008 and 8.0m (true width) @ 14.2g/t (uncut)
from TG038, scheduled for completion in 2018.

Rizal has completed a further stage of underground exploration
activities including detailed mapping and assaying, data collation and
interpretation.  There has been a substantial improvement to the
understanding of the high-grade gold locations at T'Boli in recent
months which continues to build on the Company's ability to build up
the information it requires to prepare deliver a current Mineral
Resource estimate, and information required for development of a
current mine plan.

In addition, as part of the ongoing effort to gather important
geological, mining and processing information about the gold
mineralization at T'Boli, a modified approach to the trial mining
commenced in July.  The adjusted mining approach has enabled the
separation of some lower grade and higher-grade material, resulting in
a higher delivered average grade to the processing plant.

Of particular significance for the planned activities in the
coming months will be development of exploration drives providing
access to some of the better drill hole intercepts found within the
drilling database. There are a number of significant high-grade drill
hole intercepts that exist on the defined South Veins underneath the
previous development.  The planned access into the South Vein will
initially be located 10m drill hole TG038 which intersected 8.0m (True
Width) @ 14.2g/t (uncut) and with development to the east planned soon
after to access the South Veins in the vicinity of drill holes, TG079
(1.1m @ 21g/t) and TG080 (2.8m @ 8.0g/t) - see figure 4.

Growing the understanding of the high-grade gold at T'Boli

There is a general observation at the T'Boli Project that
high-grade gold assay results (over 10g/t) exist at various locations
in the drilling database and from the underground sampling data.  It is
considered that the geological understanding of these high-grade gold
locations is the key driver for any assessment of the prospects for
economic extraction of the mineralization at the T'Boli Project.
Therefore, the geological understanding and possible continuity of the
high-grade gold has been a focus of the technical work effort at T'Boli
over the past 6 months.

Earlier observations from mapping available in the North Veins had
shown that the high-grade gold corresponded with intersection points
between structures of various orientations.  It has also been observed
from the earlier underground development and sampling that the
high-grade gold locations in the South Vein were of greater consistency
and continuity than observed in the North Veins.  However, until
recently, accessing the development in the South Veins to validate the
geological structures associated with these high-grade zones was not
possible.

A more detailed review of the South Veins was recently completed
after rehabilitation of the Mofoko underground workings was completed.
This has revealed that there is a relationship between the smaller
scale north dipping veins which link closely to the dominant South
dipping veins and the locations of more consistent high-grade gold
mineralization (Figures 1 and 2).

Trial Mining Activities

Given the complex vein array and linking structures that exist at
the T'Boli mine, a modified and slightly more selective form of trial
mining commenced in July.  This approach looked at allowing sections of
the stope to be collected and sampled prior to delivery to the
processing plant.  Not all stopes could be accessed to identify the
geological location of the material derived from the open stope.
However, selected sections of material gathered from the stope were
sampled and stockpiled separately with the results used to determine
which tonnes were sent to the processing plant and which tonnes were
sent to a low grade or waste stockpile.

The bulk of the tonnes processed during July were from the 515
level access on the North Veins.  The average grade of the bulk sample
results for tonnes delivered to the processing plant are shown in
figure 3 below. The results identified for each location have now been
fully reconciled with the gold produced at the T'Boli processing plant
during the month of July (allowing for estimated gold sent to tails and
adjustments to surface stockpiles).

This approach and attempted selectivity has had an immediate
positive effect on the average grade delivered to the processing plant
in July. Prior to July, the average grade of tonnes processed was fully
reconciled to average less than 2g/t.  In July, the grade delivered to
the Processing Plant has increased to over 4g/t, with an average
reconciled head grade for the month of July of 4.2g/t.

This has also had a significant positive effect on the revenue
raised during the month of July, which has exceeded the total operating
costs at the mine site.  A summary of the total operating costs for the
trial mining activities and the recovered gold and silver for the month
of July is summarized in table 1 (all results are unaudited).

//st

Activity          Tonnes/oz   Total Costs/Revenue (CAD)      Cost per
tonne (CAD)

Total Mining      5,953t                          $319,353   $53.65/t
Costs

Total             4,705t                          $239,651   $50.94/t
Processing
Costs

Other Site        4,705t                          $ 99,909   $21.23/t
Costs &
Royalties

Total Site                                        $658,912   $125.82/t
Costs
(Operating)

Gold Produced     601oz                           $931,479

Silver Produced   1,069oz                         $ 14,730

Total Revenue                                     $946,209

//et

Note: All revenue and operating costs reported are management
prepared and unaudited

Table 1: Summary of total operating costs and Gold/Silver produced
for the month of July, 2018. Gold and Silver Revenue is based on a
realized gold price of CAD1,549.88/oz and CAD13.77/oz respectively.
All costs estimates are calculated using a CAD:PHP exchange rate of
40.63.

Future Work Program

Work at the T'Boli mine is continuing with the trial mining on the
North Veins and development is well underway to access the interpreted
higher-grade material located on the South Veins.  The initial level
access into the South Veins is planned to be at 10 to 15m vertically
beneath and in-between drill holes TG038 (Figure 4).  A second deeper
access location on the South Vein will be also developed in the coming
months which is situated 80m to the east of, and 10 to 15m beneath the
significant drill hole intersection identified in TD008 (Figure 4).

Important note regarding Mining and Processing Activities at
T'Boli

Note that the T'Boli Project does not have a current Mineral
Resource estimate or Mineral Reserves and that the absence of a
feasibility study of mineral reserves demonstrating economic and
technical viability is associated with an increased risk of failure of
the mining operation due to increased uncertainty of results.  Mining
and processing activity at the T'Boli Project is ongoing on a
small-scale basis associated with the Company's underground exploration
activities and this should not be construed as Rizal having made a
commercial production decision.

Quality Control

Channel sampling undertaken within the exploration development
drives are consistently taken on a horizontal line as rock chip samples
between 1m to 1.5m above the floor of the development which is
approximately perpendicular to the dominant dip of the mineralized
structures.  The dominant geological domains and mineralized structures
dip to the South at between 60 and 90 degrees.  Sample intervals vary
from between 0.2m and 1.0m in width with the sample boundaries obeying
the observed geological contacts.

Drill cores from the prior drilling programs were HQ, NQ and BQ in
size.   For drill core that was HQ or NQ size, selected sampling
intervals were sub-sampled using different techniques depending on the
nature of the drill core.  Competent drill core was cut longitudinally
in half with a core saw; Clay dominant or soft core was divided into
two halves using a spatula; Broken core or rubble was physically
separated into 2 separate and equal halves.  For drill core that was BQ
in size, the whole sample interval was taken for analysis.  Sample
intervals taken were predominantly at 1m or less, with sample interval
boundaries selected to ensure that the sampling interval did not cross
over a defined geological contact.

Of particular note with regard to the quality control of the prior
drill core samples is that for many of the sampling locations the core
recovery was reported to be poor.  Based on the observations of the
mineralized structures from the underground development this is
interpreted to be a result of some clay rich sections that occur in
close proximity to the mineralized structures.  The underground channel
sampling has also identified that the clay rich locations often contain
significant gold mineralization.  The above observations indicate that
the core loss recorded in the prior drilling is due to the poor capture
of the mineralized clay rich material surrounding parts of the larger
structures at T'Boli.  The loss of mineralized material may result in
an underestimation of the gold content within some of the reported
drilling intercepts.

Prior drilling samples were analysed by Interteck, which is an
independent external laboratory, with the processing laboratory
situated in Manila, Philippines.

Sampling preparation and analysis for the channel samples are
undertaken at the Company's internal laboratory situated at T'Boli.

For both the prior drilling and the current channel samples from
the exploration development, the Company has maintained quality control
systems which includes the insertion of blanks, standards and pulp
duplicates.  The control samples from the prior drilling information
have been reviewed for any possible lab bias.  The review has concluded
that there are no material biases or inaccuracies in the assay
database, with additional check data required to confirm an observation
that there may be a slight bias of results on the low side resulting in
a slight understatement in the reported gold assay information.

Qualified Persons

Steven Olsen, member of AIG, has reviewed the exploration data and
prepared the scientific and technical information regarding exploration
results contained within this news release.  Steven Olsen, an
Independent Consultant, is a "Qualified Person" as such term is defined
in National Instrument 43-101 and he has verified and approved the
contents of this news release.

About Rizal

Rizal is an exploration and development Company with a focus on
its flagship T'Boli Project situated in the Philippines.  The Company
is using underground development to explore and define the extensive
gold mineralization that exists at T'Boli.

Peter Main President and CEO pmain@rizalresources.com

For further information please visit our website at
www.rizalresources.com, Email us at info@rizalresources.com, Phone:
778-370-1372 Fax: 604-608-5442

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Photos accompanying this announcement are available at
http://www.globenewswire.com/NewsRoom/AttachmentNg/91dec7f4-2125-49b8-8120-
1991de1eb065



http://www.globenewswire.com/NewsRoom/AttachmentNg/0e34aeb2-6eee-4156-9f9c-
eba7cbe50860



http://www.globenewswire.com/NewsRoom/AttachmentNg/ce729d30-9192-42fc-a289-
b322e9166375



http://www.globenewswire.com/NewsRoom/AttachmentNg/54c45c37-6ce2-481a-a06e-
883db2d634c9
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1824600034TS11824601175-06474220180904