Source	MARKET NEWS
Date	09/04/2018
Time	06:48:31 AM

Company	 Tethyan Resources PLC
Title	Drills 
12 m of 22.03 % Zinc, 10.29 % Lead and 16





    CDNX Symbol: TETH











Press Release





TETHYAN RESOURCES PLC ("TETH-V")
- Drills 12 m of 22.03 % Zinc, 10.29 % Lead and 167 g/t
- Silver at the Kizevak Project, Serbia

Tethyan Resources plc ("Tethyan" or the "Company") is pleased to
announce results from its initial diamond drill programme at the
Kizevak zinc-lead-silver project in Southwest Serbia. Tethyan drilled
four holes for a total of 957.3 metres, targeting an area of anomalous
zinc, lead and silver in soil located 1 km southeast of an historic
past producing open pit mine (Figure 1). All assays have now been
received and drilling has returned broad zones of polymetallic vein and
breccia type mineralisation in all holes, with highlights including:

//st

* 12.0 m @ 22.03 % zinc, 10.29 % lead, 167 g/t silver and 0.18 g/t gold for
35.09 % ZnEq (Hole KSEDD002, from 130 m)
* 43.0 m @ 4.30 % zinc, 2.49 % lead, 26 g/t silver and 0.21 g/t gold for
7.39 % ZnEq (Hole KSEDD001, from 193 m)
* including 13.1 m @ 11.28 % zinc, 5.05 % lead, 57 g/t silver and 0.32
g/t gold for 17.44 % ZnEq (from 221 m)

* 40.0 m @ 4.35 % zinc, 2.14 % lead, 27 g/t silver and 0.34 g/t gold for
7.37 % ZnEq (Hole KSEDD003, from 137 m)
* 22.2 m @ 2.95 % zinc, 2.41 % lead, 41 g/t silver and 0.18 g/t gold for
6.23 % ZnEq (Hole KSEDD003, from 160 m)

//et

Holes were drilled on two sections 80 m apart with a spacing of 40
m between the holes. All holes intercepted significant mineralisation
between 85 and 190 m below surface, and mineralisation remains open in
all directions (Figures 2 and 3). Collar details are given in Table 1
and significant intercepts, including estimated true width intervals,
are given in Table 2.

Fabian Baker, President and CEO of Tethyan commented, "We are
delighted with the results of our first drill programme at Kizevak,
which returned some exceptional grades over substantial widths. These
first results are particularly encouraging as they are from only a
small part of the large zinc, lead, silver, gold soil anomaly. We are
immediately planning to commence induced polarisation and ground
magnetic geophysical programmes as well as trenching to refine drill
targets in advance of a second drill programme later this year."

Tethyan has already constructed and permitted seven additional
drill pads at Kizevak to test over a total of 200 metres along strike
from the recently completed holes. Tethyan is also preparing to submit
samples from drill core for preliminary metallurgical test work to
understand baseline zinc, lead and silver recoveries to concentrates,
as well as gold deportment.

Table 1: Drill Collar Data

//st

Hole ID    Easting   Northing   Elevation   Depth    Azimuth   Inclination
(m)       (m)         (m)       (m)       ()          ()

KSEDD001   476507    4792486       912      257.60     225         -55

KSEDD002   476485    4792456       909      226.10     230         -53

KSEDD003   476431    4792507       896      212.60     230         -55

KSEDD004   476459    4792533       904      261.00     230         -60

//et

Note: Coordinates are shown using the UTM WGS84 projection, Zone
34 Northern Hemisphere

Table 2: Significant Intercepts

//st

Hole ID     From    To (m)   Apparent   Zinc    Lead    Silver   Gold  Zinc
(m)               Width      (%)     (%)    (g/t)    (g/t)  Eq.
(m)                                      (%)

KSEDD001    128.00   129.50     1.5      4.36    2.02      30     0.09  6.92

KSEDD001    160.00   181.00     21.0     1.02    4.68      60     0.17  6.69

including   161.00   166.60     5.6      1.50    16.13    213     0.19 20.51

KSEDD001    187.00   188.00     1.0      2.15    2.90      23     0.30  5.68

KSEDD001    193.00   236.00     43.0     4.30    2.49      26     0.21  7.39

including   221.00   234.10     13.1     11.28   5.05      57     0.32 17.44

KSEDD002    130.00   142.00     12.0     22.03   10.49    167     0.18 35.09

KSEDD002    188.50   189.50     1.0      1.73    3.64      26     0.41  6.16

KSEDD003     1010    101.50     0.5      9.42    3.94      51     0.14 14.20

KSEDD003    105.00   127.20     22.2     2.95    2.41      41     0.18  6.23

including   116.00   117.50     1.5      15.30   6.29     135     0.24 24.09

and      123.70   125.20     1.5      4.63    5.30     154     0.40 13.23

and      126.70   127.20     0.5      3.61    29.30    437     0.39 39.27

KSEDD003    137.00   177.00     40.0     4.35    2.14      27     0.34  7.37

including   151.20   154.00     2.8      18.34   5.49      77     0.45 25.54

and      166.30   168.00     1.7      17.08   10.94    126     1.82 32.41

KSEDD004    116.50   118.00     1.5      2.64    1.16      12     0.11  4.09

KSEDD004    159.80   181.00     21.2     1.75    0.74      6      0.13  2.74

including   167.10   170.60     3.5      6.09    2.23      17     0.22  8.77

KSEDD004    223.00   228.00     5.0      1.96    1.35      11     0.40  4.03

KSEDD004    248.50   251.00     2.5      2.47    0.02      27     0.34  3.63

//et

Notes

//st

* Zinc Equivalent (Zinc Eq.) metal grade was calculated using assumed metal
prices of $1250/oz gold; $16/oz silver; $2100/t lead and $2400/t zinc.
* Metal recoveries of 100% were applied in the metal equivalent
calculations.
* Zinc equivalent (%) was calculated using the following formula: Zinc Eq.
(%) = 100 x ((Au price (g) x Au grade) + (Ag Price (g) x Ag grade) + (Pb
price x Pb grade/100) + (Zn price x Zn grade/100))/Zn price.
* Numbers may not add up due to rounding.
* The true thickness of mineralised zones is estimated to vary between 70
to 95% of apparent width. Due to currently limited drilling data, early
stage of exploration, variable geometry of the mineralisation and lack of
outcrop, the Company is currently unable to accurately estimate true
widths.

//et

Figure 1: Location of the four drill holes shown in relation to
the zinc and gold in soil anomalies and historic open pit mine.

To view an enhanced version of Figure 1, please visit:
https://orders.newsfilecorp.com/files/5611/38443_tethyan1enhanced.jpg

Figure 2: Cross-section "A" showing results and geology for drill
holes KSEDD001 and KSEDD002

To view an enhanced version of Figure 2, please visit:
https://orders.newsfilecorp.com/files/5611/38443_tethyan2enhanced.jpg

Figure 3: Cross-section "B" showing results and geology for drill
holes KSEDD003 and KSEDD004

To view an enhanced version of Figure 3, please visit:
https://orders.newsfilecorp.com/files/5611/38443_tethyan3enhanced.jpg

Kizevak Project

The Kizevak Project is located in the Raska District which is
prospective for porphyry copper-gold and polymetallic vein type
deposits. Historic past producing mines at Kizevak and Sastavci
produced lead, zinc and silver from open pits from the 1980s until the
early 2000s when they ceased operation due to conflict in the region.
Tethyan owns the Kremice exploration licence which surrounds third
party exploitation licences over the Kizevak and Sastavci open pit
mines. Tethyan's drill program targeted an area 1 km southeast along
strike of the Kizevak open pit mineralisation.

The drill target was identified by Tethyan from geological mapping
and soil sampling. Mineralisation is hosted in a steeply northeast
dipping volcanic sequence comprising an upper (150m thick, polymict,
coarse-grained, blocky volcanic breccia, which overlies an
approximately 100 m thick, coherent, massive, fine-grained porphyritic
andesite unit with minor interlayers of volcaniclastic rock. The
andesite overlies a lower volcanic breccia in which the drill holes
were terminated.

Mineralisation occurs as fault-hosted veins and vein breccias with
broad zones of sheeted and fracture fill mineralisation in the
footwall, hosted almost entirely within the andesite volcanic unit
which is moderately to strongly clay-pyrite altered. The mineralised
zone strikes southeast, dips steeply northeast, and is open in all
directions.

Mineralisation comprises 0.5 to 6 m thick, steeply northeast
dipping veins and vein breccias composed of coarse-grained, massive
galena-sphalerite-pyrite-arsenopyrite-pyrrhotite with variable quartz,
carbonate (calcite and rhodochrosite) and barite intergrowths. The
andesite footwall of the veins is moderately to strongly fractured with
carbonate-barite-galena-sphalerite-pyrite as fracture fill and sheeted
veins, which occur in zones between 8 and 38 m wide (estimated true
thickness). Individual veins within these zones are between 2 to 10 mm
wide with a vein density of 0.5 to 5 vol. % per metre.

Rudnica Copper-Gold Porphyry Prospect

Work continues at the Rudnica copper-gold porphyry prospect, with
a 1500 meters drill programme planned in Q4 2018. Drilling will be used
to explore untested copper-gold-molybdenum soil anomalies coincident
with moderate to high chargeability and high magnetic geophysical
anomalies, in an area of leached and silica altered andesite with weak
low temperature quartz veinlets which returned significant channel
sample results including 40 m @ 0.21 g/t gold, 30 m @ 0.24 g/t gold and
10 m @ 0.26 g/t gold (see news release dated March 2, 2018).

About Tethyan

Tethyan Resources plc is a precious and base metals mineral
exploration company incorporated in England & Wales and listed on the
Toronto Venture Exchange. Tethyan is focused on the Tethyan
Metallogenic Belt in Eastern Europe, mainly Serbia, where it is
acquiring and exploring a portfolio of quality precious and base metals
projects with known mineralisation and compelling drill targets.
Tethyan emphasises responsible engagement with local communities and
stakeholders, and is committed to proactively implementing Good
International Industry Practice (GIIP) and sustainable health, safety
and environmental management. More information can be found on our
website: www.tethyan-resources.com.

Sampling Methods and Data Verification

Drill core samples were collected from half cut PQ and HQ diameter
core, where the core was sawn along a pre-defined cutting line. Sample
intervals were selected by the geologists based on geological criteria
including presence of alteration and mineralisation, style of
mineralisation and lithological contacts. Minimum sample lengths of 0.5
metres and maximum sample lengths of 2 metres were employed. Each
sample weighed between 2 and 13 kg depending on the length of the
sample and diameter of drill core. Sampling was only conducted on
visually mineralised intervals, including 10 metres either side of the
visually mineralised interval. Data verification was conducted by the
Qualified Person including checking of detailed geological logs against
core observations, core photographs and analytical results. In
addition, digital data was verified using industry standard software to
validate the drill database prior to entering data into the master
database. No check assays have been conducted to date.

Quality Assurance and Quality Control

The drill core sampling program and sampling protocols were
supervised by Tethyan's Exploration Manager, Mr Andrew Tunningley
MAusIMM(CP), who is a Qualified Person as defined by National
Instrument 43-101. Quality Assurance is provided through provision of
standard operating procedures for the collection and submission of
samples as well as data handling and management. Quality Control is
monitored through the insertion of one certified reference material
sample and one blank sample per batch of 20 samples. One duplicate
sample is also inserted per batch. All samples are securely transported
from the project site to the ALS Global sample preparation laboratory
in Bor, Serbia by ALS couriers. Sample pulps are then sent to ALS Rosia
Montana, Romania by air freight for gold analysis by 30 gram fire assay
with AA finish (code FA-AA23). Multi-element analyses are conducted by
ALS Loughrea, Ireland using a highly oxidising digestion with ICP-MS
finish (code ME-ICPORE). ALS's laboratories are ISO 2005 accredited,
employ a Laboratory Information Management System for sample tracking,
quality control and reporting, and are independent of Tethyan.

Qualified Person

The technical information in this news release has been reviewed
and approved by Tethyan's Exploration Manager, Andrew Tunningley,
MAusIMM(CP), who is a Qualified Person as defined by National
Instrument 43-101.

Tethyan Resources Contact

Tethyan Resources plc +44 1534 881 885 Fabian Baker (CEO)
fabian@tethyan-resources.com

TSX Venture Exchange Disclaimer

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as such term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Forward Looking Statements

Certain information contained herein constitutes "forward-looking
information" under Canadian securities legislation. Forward-looking
information includes, but is not limited to, statements with respect to
the private placement, the use of proceeds. Generally, forward-looking
information can be identified by the use of forward-looking terminology
such as "intends", "will be" or variations of such words and phrases or
statements that certain actions, events or results "will" occur.
Forward-looking statements are based on the opinions and estimates of
management as of the date such statements are made and they are subject
to known and unknown risks, uncertainties and other factors that may
cause the actual results, level of activity, performance or
achievements of Tethyan to be materially different from those expressed
or implied by such forward-looking statements or forward-looking
information, including: the receipt of all necessary regulatory
approvals, capital expenditures and other costs, and financing and
additional capital requirements. Although management of Tethyan have
attempted to identify important factors that could cause actual results
to differ materially from those contained in forward-looking statements
or forward-looking information, there may be other factors that cause
results not to be as anticipated, estimated or intended. There can be
no assurance that such statements will prove to be accurate, as actual
results and future events could differ materially from those
anticipated in such statements. Accordingly, readers should not place
undue reliance on forward-looking statements and forward looking
information. Tethyan will not update any forward-looking statements or
forward-looking information that are incorporated by reference herein,
except as required by applicable securities laws.

TEL: +44-1534881885    TETHYAN RESOURCES PLC
E-mail: info@tpjunction.comWebsite: https://www.tethyan-resources.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1824600033TS11824601174-06474120180904