Source	CANADA NEWSWIRE
Date	09/05/2018
Time	06:02:22 AM

Company	 Transition Metals Corp.
Title	Transition Receives Positive Assay Results from New Exploration Projects
located in Northwestern Ontario





    CDNX Symbol: XTM











Press Release




" BC-TransitionMetalsAssay   09-05 0863
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Transition Receives Positive Assay Results from New Exploration Projects
located in Northwestern Ontario@

SUDBURY, ON, Sept. 5, 2018 /CNW/ - Transition Metals Corp (XTM - TSX.V)
("Transition", "the Company") is pleased to provide assays results from
preliminary prospecting completed on the company's Revell and Island Copper
Projects located in northwestern Ontario. Both the Revell and Island Copper
properties were acquired by XTM in April of 2018 as part of a much larger
staking program (see April 23, 2018 - Press Release) designed at acquiring
low-cost exploration assets consistent with the company's Project Generator
Business Model.
Revell Property
The Revell Property is located 50 km SE of the town of Dryden in Revell
and Hyndman townships along the TransCanada Highway. The Property covers a set
of underexplored Ni-Cu-PGM showings, called the Tache East and West showings
that were discovered in the 1960's. Historic drilling completed in 1967 on the
Tache West showing encountered two shallow zones of Ni-Cu mineralization
hosted within a marginal gabbroic unit that returned values of 10 ft (at) 0.64%
Ni, 0.77% Cu and 12 ft (at) 0.68% Ni, 0.90% Cu.
Three days were spent prospecting the Revell Property focusing on
locating and resampling the historic Tache West and East showings. A total of
24 samples were collected and submitted for analyses. Highlights from that
sampling are listed below.
Sample   Showing  Pt (ppm)      Pd (ppm)       Au (ppm)       Pt+Pd+Au 
(ppm)      Cu (wt.%)      Ni (wt.%)
------   -------   -------       -------        -------       
-------------        --------       --------

S899353 Tache West         0.269          0.371          0.361                
1.00           0.64           0.11
------- ----------         -----          -----          -----                
----           ----           ----

S899355 Tache West         0.264          0.393          0.259                
0.92           0.48           0.07
------- ----------         -----          -----          -----                
----           ----           ----

S899356 Tache West         0.102          0.150          0.081                
0.33           0.31           0.07
------- ----------         -----          -----          -----                
----           ----           ----

S899358 Tache West         0.179          0.274          0.117                
0.57           0.48           0.09
------- ----------         -----          -----          -----                
----           ----           ----

S899371 Tache East         0.092          0.294          0.057                
0.44           0.29           0.14
------- ----------         -----          -----          -----                
----           ----           ----

S899376 Tache East         0.068          0.193          0.051                
0.31           0.22           0.23
------- ----------         -----          -----          -----                
----           ----           ----

Island Copper Property
The Island Copper Property is located 15 km north of Sault Ste. Marie in
Aweres Township and covers an area that is interpreted to have high potential
for IOCG-style, Cu-Au-Ag mineralization. Mineralization on the property is
hosted in a highly altered granite breccia that is situated at the
intersection of major crustal faults thought to represent the terrain boundary
between Archean and Proterozoic rocks. Historic drilling completed on the
property by Kennco Exploration in 1965 reported 11.59 m (at) 3.4% Cu and 0.9g/t
Au at the Main Showing.
Prospecting the Island Copper Property focused on locating and resampling
the historic Main Showing. A total of nine samples were collected and
submitted for analyses. Assay results are listed below.
Sample    Showing   Cu (wt. %)   Ag (ppm)      S (wt. %)
------    -------   ---------      -------       --------

S899379 Main Showing         2.80      <1                 3.21
------- ------------         ----      ---                ----

S899380 Main Showing         9.00             7            9.41
------- ------------         ----           ---            ----

S899381 Main Showing         4.21             4            3.97
------- ------------         ----           ---            ----

S899382 Main Showing         4.67             1            5.37
------- ------------         ----           ---            ----

S899383 Main Showing         4.69             2            4.72
------- ------------         ----           ---            ----

S899384 Main Showing         1.61      <1                 1.63
------- ------------         ----      ---                ----

S899385 Main Showing         3.72      <1                 3.80
------- ------------         ----      ---                ----

S899386 Main Showing         3.14      <1                 3.19
------- ------------         ----      ---                ----

S899387 Main Showing         0.63             2            0.90
------- ------------         ----           ---            ----

Commenting on the news, Company CEO and President Scott McLean stated "We
are encouraged with the assay results from the initial prospecting at both the
Revell and Island Copper properties. We feel that the Revell Property has the
potential to host a new Ni-Cu-PGM environment that has seen only minimal
exploration over the past 50 years and the results from the Island Copper
Property demonstrate the high grade potential of this poorly understood
property. In the following months we look forward to further exploring and
evaluating both of these properties."
Qualified Person
The technical elements of this press release have been approved by Mr.
Grant Mourre, P.Geo. (APGO), a Qualified Person under National Instrument
43A-101. All analytical work performed on rock samples was conducted at AGAT
Laboratories with sample preparation completed in Thunder Bay and Sudbury,
Ontario and analyses completed in Mississauga, ON. The quality system used by
AGAT Laboratories complies with international standards ISO 9001:2015 and ISO
17025:2005.
Cautionary Note on Forward-Looking Information
Except for statements of historical fact contained herein, the
information in this news release constitutes "forward-looking information"
within the meaning of Canadian securities law. Such forward-looking
information may be identified by words such as "plans", "proposes",
"estimates", "intends", "expects", "believes", "may", "will" and include
without limitation, statements regarding estimated capital and operating
costs, expected production timeline, benefits of updated development plans,
foreign exchange assumptions and regulatory approvals. There can be no
assurance that such statements will prove to be accurate; actual results and
future events could differ materially from such statements. Factors that could
cause actual results to differ materially include, among others, metal prices,
competition, risks inherent in the mining industry, and regulatory risks. Most
of these factors are outside the control of the Company. Investors are
cautioned not to put undue reliance on forward-looking information. Except as
otherwise required by applicable securities statutes or regulation, the
Company expressly disclaims any intent or obligation to update publicly
forward-looking information, whether as a result of new information, future
events or otherwise.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Transition Metals Corp.



View original content:
http://www.newswire.ca/en/releases/archive/September2018/05/c8178.html

-0-                           09/05/2018
/For further information: Further information is available at
www.transitionmetalscorp.com or by contacting: Scott McLean, President and
CEO, Transition Metals Corp., Tel: (705) 669-1777/
(XTM.)

CO:  Transition Metals Corp.
ST:  Ontario
IN:  MNG
SU:

-30-