Source	MARKET NEWS
Date	09/06/2018
Time	06:57:27 AM

Company	 Integra Resources Corp.
Title	Commences Metallurgical Testwork Program At The





    CDNX Symbol: ITR











Press Release





Commences Metallurgical Testwork Program At The DeLamar Gold SilverProject 
--->@NEWS RELEASE
INTEGRA RESOURCES CORP ("ITR-V;IRRZF-0")
- Commences Metallurgical Testwork Program At The DeLamar Gold-Silver
- Project

Integra Resources Corp. (the "Company" or "Integra") is pleased to
announce that it has commenced a comprehensive metallurgical sampling
and testwork program on the DeLamar Gold and Silver Project ("DeLamar",
or the "Project"), located in the historic Owyhee County mining
district in southwestern Idaho. The metallurgical sampling and testwork
program will be conducted by McClelland Laboratories, Inc. in Reno,
Nevada, under the supervision of Jack McPartland, Metallurgist/Vice
President Operations at McClelland Laboratories, Inc.

"The DeLamar Gold-Silver Project has a long history of mining and
processing, producing high-grade and low-grade gold and silver during
various periods from the late 1800s and late 1900s. An abundance of
metallurgical records recovered on-site clearly demonstrate that the
metallurgy of DeLamar is not particularly complex, and that historical
gold-silver test recoveries using industry standard leaching techniques
were excellent," stated George Salamis, President and CEO of Integra
Resources. "Our mission with this initial round of testwork is to
follow-up on past conventional milling and heap leach testwork, and to
qualify the extent to which heap leaching can potentially be used as an
economically viable means of gold-silver extraction on the Project.
Given the large amount of heap leach testwork conducted on the Project
by previous operators, with recoveries of up to 84% gold and 64% silver
in laboratory column leach tests, we are confident that the results
should demonstrate that heap leaching is a potentially viable option
for the project."

"The Project hosts an extensive near surface resource that has the
potential for bulk mining. In addition, previous mine operators of the
DeLamar and Florida Mountain Deposits left behind significant oxidized,
transitional and unoxidized gold-silver resources at surface.
Metallurgical testwork on this resource will further de-risk the
project and provide processing options for the Company as it continues
to grow the existing resource and delineate new targets and deposits
around the DeLamar area," noted George Salamis, President and CEO.

HISTORY OF GOLD-SILVER MILLING AND METALLURGY AT THE DELAMAR
PROJECT1

Recent Historical Gold and Silver Operational Processing and
Recoveries

Records from recent historical gold ("Au") and silver ("Ag")
processing at DeLamar, as defined by the mineral processing that took
place on site from 1977 until 1998, hosts much of the most relevant
metallurgical data available to Integra at this time.  Processing was
performed by crushing, grinding, and tank leaching with cyanide,
followed by precipitation with zinc dust and in-house smelting of the
precipitate to produce silver-gold dore. Records show that from 1977
through 1992, the mill processed 11.686 million tonnes of mineralized
material with average head grades of 1.17 g Au/tonne and 87.1 g
Ag/tonne. During this 15-year period, the DeLamar mill recovered, on
average, 96.2% of the contained gold and 79.5% of the contained silver.
The historical mill feed during this period included oxidized, partly
oxidized, and unoxidized materials.

Historical Column Leach Test Work Designed to Evaluate Potential
Heap Leaching Options

In the 1980s, the NERCO Mineral Company ("NERCO") conducted
numerous column leach tests using mineralized material from the Florida
Mountain Deposit ("Florida Mountain"). The results of this testwork,
summarized below in Table 1, demonstrate the potential for heap leach
processing of mineralized material at Florida Mountain, and may
indicate the amenability of heap leaching on  mineralized material from
DeLamar as well, based on the similar host-rock types and styles of
mineralization for both Deposits. Clarification surrounding the
different metallurgical characteristics of Florida Mountain mineralized
material versus DeLamar mineralized material is one focus of the
current testwork.

Table 1. Compiled NERCO Florida Mountain Column Leach Test Results
(From Statter, 1989, and Hampton, 1988, compiled by Integra, 2017)

//st

Florida      Crush     Calculated Head       Duration   Metal Extraction
Mountain     Size      Grade
Area

Inches    Ag g/t        Au      Days       Ag %         Au %
g/t

Sullivan2    -1        8.50          0.58    60         41.9         82.3

Sullivan2    -1/2      7.78          0.62    60         53.8         82.0

Stone        -1        7.71          0.31    60         45.2         85.1
Cabin LG

Stone        -1/2      10.87         0.34    60         43.1         84.5
Cabin LG

Stone        -1        15.60         1.61    60         39.3         78.1
Cabin HG

Stone        -1/2      14.40         1.47    60         47.6         84.3
Cabin HG
Clark LG     -1        4.94          0.24    60         37.5         52.0

Clark LG     -1/2      4.35          0.24    60         53.6         83.7

Clark HG     -1        14.16         0.86    60         36.4         38.7

Clark HG     -1/2      15.29         0.79    60         48.9         59.3

Stone        1         60.38         3.70    60         39.7*        83.1*
Cabin Dump

Stone        -1        17.62         0.65    60         31.5*        92.2*
Cabin Dump

Stone        -1/2      15.98         0.62    60         42.9*        92.6*
Cabin Core

Stone        -1/2      18.17         12.00   60         36.2*        78.0*
Cabin Core

Tip Top      -2        17.35         1.03    56         41.6*        92.2*
Trench

Tip Top      -1        19.75         1.10    56         42.8*        91.5*
Trench

Tip Top      70%       21.81         1.03    56         45.0*        95.0*
Trench       -1/4

//et

*  *denotes an internal DeLamar mine assay factor was applied to
silver and gold analyses
*  Sullivan Core refers to drill core from the Sullivan claim in
the Florida Mountain Deposit, not the Sullivan Gulch area of the
DeLamar Deposit
*  Integra is unaware of the column diameter(s) or the oxidation
state(s) of the material tested

Statter (1989) reported a pilot column leach test was performed in
1988 using 14,850 pounds of Stone Cabin "run of dump" material. The
test was likely conducted at the DeLamar mine laboratory. Leaching was
conducted for 63 days resulting in 15.8% silver recovery and 72.2% gold
recovery.

In 1987, NERCO initiated construction of a small scale, trial
cyanide heap leach pad which was in operation for the last quarter of
1987 until the final quarter of 1990.  The trial leach pad used
low-grade run-of-mine material that was driven onto the pad by haul
truck then ripped by bulldozer to provide permeability. The material
size was reported to be approximately 70% at )20 centimeters ()8 inch).
The trial pad and stacked material became physically unstable and began
to slide downhill towards the tailings facility in 1990. In early 1991,
the entire heap was removed and placed into the tailings facility. The
trial leach pad was shut down due to physical instability, not due to
the lower leach results being obtained during the trial. The Company
has surmised that that the stacked material may not have reached the
optimum duration under leach, and therefore the overall calculated
recovery of only 41% gold and 8% silver may be understated by an
unknown quantity.

*  NI 43-101 Technical Report and Estimated Gold - Silver
Resources, DeLamar Project, Integra Resources Corp. Effective Date
March 8, 2018.

2018 Metallurgical Testwork Program on DeLamar and Florida
Mountain

The current metallurgical testwork program will address three main
objectives, in support of a planned 2019 PEA:

*  To establish the milling characteristics of mineralization from
the DeLamar and Florida Mountain Deposits;
*  To establish the amenability of different mineralization types
from both Deposits to potential heap leaching; and,
*  To provide the Company with information to establish future
"trade-off" parameters of using one or both of the above means of
gold-silver extraction on the project.

The program, to be conducted over the next several months at
McClelland Laboratories, Inc. in Reno, Nevada, under the super vision
of Jack McPartland, Metallurgist/Vice President of Operations at
McClelland Laboratories, Inc., will focus on the following:

*  Ore Variability (Bottle Roll) Composite Testing
*  Column Test Composite Testing
*  Load/Permeability Testing
*  Scoping Mill Testing, including Bond Ball Mill Work Index
tests, cyanidation tests, flotation tests and gravity concentration
tests

Sample media used in this metallurgical study has been collected
from diamond core drill holes completed over the course of the 2018
drill program at DeLamar and Florida Mountain. Results from the
metallurgical sampling program are expected in Q4 2018 and Q1 2019.

DeLamar Exploration Ongoing

Currently two drill rigs are in operation at the DeLamar Project,
with 60 drill holes completed over 18,500 m. Many drill assays remain
outstanding and are expected to be available for reporting upon in the
coming weeks and months.

Qualified Person

The scientific and technical information contained in this news
release has been reviewed and approved by E. Max Baker PhD. (FAusIMM),
Integra's Vice President Exploration, of Reno, Nevada, and is a
"qualified person"("QP") as defined in National Instrument 43- 101 -
Standards of Disclosure for Mineral Projects.

About Integra Resources

Integra Resources Corp. is a development-stage company engaged in
the acquisition, exploration and development of mineral properties in
the Americas. The primary focus of the Company is advancement of it's
DeLamar Project, consisting of the neighbouring DeLamar and Florida
Mountain Gold and Silver Deposits in the heart of the historic Owyhee
County mining district in south western Idaho. The first exploration
program in over 25 years is currently underway on the DeLamar Project
with more than 20,000 meters planned for 2018. The management team
comprises the former executive team from Integra Gold Corp.

ON BEHALF OF THE BOARD OF DIRECTORS George Salamis  President,
CEO, and Director

CONTACT INFORMATION

Corporate Inquiries: Chris Gordon, chris@integraresources.com
Company website: www.integraresources.com Office phone: 1 (604)
416-0576

This news release contains "forward-looking information" and
"forward-looking statements" (collectively, "forward-looking
statements") within the meaning of the applicable Canadian securities
legislation. All statements, other than statements of historical fact,
are forward-looking statements and are based on expectations, estimates
and projections as at the date of this news release. Any statement that
involves discussions with respect to predictions, expectations,
beliefs, plans, projections, objectives, assumptions, future events or
performance (often but not always using phrases such as "expects", or
"does not expect", "is expected", "anticipates" or "does not
anticipate", "plans", "budget", "scheduled", "forecasts", "estimates",
"believes" or "intends" or variations of such words and phrases or
stating that certain actions, events or results "may" or "could",
"would", "might" or "will" be taken to occur or be achieved) are not
statements of historical fact and may be forward-looking statements. In
this news release, forward-looking statements relate, among other
things, to: statements about the estimation of mineral resources;
magnitude or quality of mineral deposits; anticipated advancement of
mineral properties or programs; future operations; future exploration
prospects; the completion and timing of mineral resource estimates; the
length of the current market cycle and requirements for an issuer to
survive in the current market cycle; future growth potential of
Integra; and future development plans.

These forward-looking statements are based on reasonable
assumptions and estimates of management of Integra at the time such
statements were made. Actual future results may differ materially as
forward-looking statements involve known and unknown risks,
uncertainties and other factors which may cause the actual results,
performance or achievements of Integra to materially differ from any
future results, performance or achievements expressed or implied by
such forward-looking statements. Such factors, among other things,
include: possible variations in mineralization, grade or recovery
rates; actual results of current exploration activities; actual results
of reclamation activities; conclusions of future economic evaluations;
business integration risks; fluctuations in general macroeconomic
conditions; fluctuations in securities markets; fluctuations in spot
and forward prices of gold, silver, base metals or certain other
commodities; fluctuations in currency markets (such as the Canadian
dollar to United States dollar exchange rate); change in national and
local government, legislation, taxation, controls, regulations and
political or economic developments; risks and hazards associated with
the business of mineral exploration, development and mining (including
environmental hazards, industrial accidents, unusual or unexpected
formations pressures, cave-ins and flooding); inability to obtain
adequate insurance to cover risks and hazards; the presence of laws and
regulations that may impose restrictions on mining; employee relations;
relationships with and claims by local communities and indigenous
populations; availability of increasing costs associated with mining
inputs and labour; the speculative nature of mineral exploration and
development (including the risks of obtaining necessary licenses,
permits and approvals from government authorities); and title to
properties. Although the forward-looking statements contained in this
news release are based upon what management of Integra believes, or
believed at the time, to be reasonable assumptions, Integra cannot
assure its shareholders that actual results will be consistent with
such forward-looking statements, as there may be other factors that
cause results not to be as anticipated, estimated or intended.

Readers should not place undue reliance on the forward-looking
statements and information contained in this news release. Except as
required by law, Integra assumes no obligation to update the
forward-looking statements of beliefs, opinions, projections, or other
factors, should they change, except as required by law.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights 
reserved.Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1824800040TS11824801262-06550720180906