Source	CANADA NEWSWIRE
Date	08/19/2019
Time	06:40:39 AM

Company	 Mako Mining Corp.
Title	Drilling at Las Conchitas Extends Near Surface, High-Grade Gold
Mineralization, Including 19.55 g/t Gold and 40.6 g/t Silver Over 1.2
Meters





    CDNX Symbol: MKO











Press Release




" BC-MakoMining-LasConchit   08-19 1240
News release via Canada NewsWire, Toronto 416-863-9350 -!ME-

Attention co.371312:
^Drilling at Las Conchitas Extends Near Surface, High-Grade Gold
Mineralization, Including 19.55 g/t Gold and 40.6 g/t Silver Over 1.2
Meters@

TSX-V: MKO
VANCOUVER, Aug. 19, 2019 /CNW/ - Mako Mining Corp. (TSX-V: MKO) ("Mako"
or the "Company") is pleased to announce additional positive drill results
from the Las Conchitas area of its wholly-owned San Albino-Murra property
located in Nueva Segovia, Nicaragua.
The objective of the 2019 drilling campaign is to test high priority
exploration targets within the Las Conchitas area, identified by trenching,
geochemical soil surveys, extensive geological mapping and sampling of
historical workings.
The El Limon Zone was identified by a large 570 m by 280 m gold in soils
anomaly, oriented in a northeast-southwest direction. The El Limon soil
anomaly appears to be a continuation of the Mango gold geochemical anomaly
which has been tested and confirmed by drilling (see press release dated May
6, 2019).
The Company has completed 13 shallow drill holes totaling 1,060 m at the
El Limon Zone (see the attached map), with a goal to test the strike and dip
extension of the Mango Zone, where the Company intersected the highest gold
grade drilled to date of 376.49 g/t Au over 1 m in drill hole LC19-70 (see
press release dated May 6, 2019).
Drill hole LC19-101 intersected two mineralized zones, separated by a 2.5
m interval of low grade gold mineralization as follows: 4.62 g/t Au and 12.0
g/t Ag over 2.1 m and 19.55 g/t Au and 40.6 g/t Ag over 1.2 m (see table below
and attached cross section). This hole is located approximately 320 m
southwest, and along strike, of drill hole LC11-01, which intersected 69.96
g/t Au and 61.7 g/t Ag over 3.0 m (see Golden Reign Resources Ltd. press
release dated February 22, 2012).
2019 Diamond Drill Results in the El Limon Zone
Drill Hole      From       To       Width         Au          Ag     Interval 
Averages
(m)       (m)       (m)(x)         (g/t)       (g/t)

---

LC19-89           16.35     17.35         1.00        4.92          2.2   4.92 
g/t Au and 2.2 g/t
Ag over 1.0 m

---

LC19-91           84.70     85.80         1.10       18.59          7.9  18.59 
g/t Au and 7.9 g/t
Ag over 1.1 m

---

LC19-95           12.00     13.50         1.50        1.11          2.4   1.11 
g/t Au and 2.4 g/t
Ag over 1.5 m

---

LC19-96           16.00     16.50         0.50       36.46         27.0  36.46 
g/t Au and 27.0 g/t
Ag over 0.5 m

---

LC19-101           85.60     86.80         1.20        3.24          4.6  4.62 
g/t Au and 12.0 g/t
Ag over 2.1 m

---

LC19-101           86.80     87.70         0.90        6.46         21.9

---

LC19-101           90.20     91.40         1.20       19.55         40.6  19.55 
g/t Au and 40.6 g/t
Ag over 1.2 m

---

The mineralized intervals shown above utilize a 1.0 g/t gold cut-off
grade with not more than 1.0 meter of internal dilution. Lengths are reported
as core lengths. Drill holes LC19-93, LC19-94, LC19-99 and LC19-100
intercepted faults and were abandoned prior to reaching their target depth.
Drill holes LC19-90, LC19-92, LC19-97 and LC19-98 intercepted faults at the
projected depth of the mineralized zone and returned gold values below the
cut-off grade. (x)True widths vary depending on drill hole dip, the veins are
shallow dipping and typical true widths are 85-100% of the downhole width.
Sampling, Assaying, QA/QC and Data Verification
Drill core was continuously sampled from inception to termination of the
drill hole. Sample intervals were typically one meter. Drill core diameter was
HQ (6.35 centimeters). Geologic and geotechnical data was captured into a
digital database, core was photographed, then one-half split of the core was
collected for analysis and one-half was retained in the core library. Samples
were kept in a secured logging and storage facility until such time that they
were delivered to the Managua facilities of Bureau Veritas and pulps were sent
to the Bureau Veritas laboratory in Vancouver for analysis. Gold was analyzed
by standard fire assay fusion, 30 gram aliquot, AAS finish. Samples returning
over 10.0 g/t gold are analyzed utilizing standard Fire Assay-Gravimetric
method. Due to the presence of coarse gold, the Company has used 500-gram
metallic screened gold assays for analyzing samples that yielded a fire assay
result greater than 1 g/t, and samples immediately above and below drilled
veins. This method, which analyzes a larger sample, can be more precise in
high-grade vein systems containing coarse gold. All reported drill results in
this press release used the metallic screening method. The Company follows
industry standards in its QA&QC procedures. Control samples consisting of
duplicates, standards, and blanks were inserted into the sample stream at a
ratio of 1 control sample per every 10 samples. Analytical results of control
samples confirmed reliability of the assay data.
Qualified Person
John M. Kowalchuk, P.Geo, a geologist and qualified person (as defined
under NI 43-101) has read and approved the technical information contained in
this press release. Mr. Kowalchuk is a senior geologist and a consultant to
the Company.
On behalf of the Board,
"Akiba Leisman"CEO
About Mako
Mako Mining Corp. is a publicly listed gold mining, development and
exploration firm. The Company is developing its high-grade San Albino gold
project in Nueva Segovia, Nicaragua. Mako's primary objective is to bring San
Albino into production quickly and efficiently, while continuing exploration
of prospective targets in Nicaragua.
Forward-Looking Statements: Some of the statements contained herein may
be considered "forward-looking information" within the meaning of applicable
securities laws. Forward-looking information is based on certain expectations
and assumptions, including that the Company's exploration programs will be
successfully completed; that although the Company's production decision at its
San Albino project is not based on a technical study supporting mineral
reserves, and therefore not based on demonstrated economic viability,
management currently believes the project is on track to achieve its first
gold pour by the late summer of 2020; that the Company will be successful in
its proposed financing plans necessary for the construction at the San Albino
project. Such forward-looking information is subject to a variety of risks and
uncertainties which could cause actual events or results to differ materially
from those reflected in the forward-looking information, including, without
limitation, the risks that additional satisfactory exploration results at the
Mango zone will not be obtained; that the PEA is preliminary in nature and
there is no certainty that the PEA will be realized; the risk of economic
and/or technical failure at the San Albino project associated with basing a
production decision on the PEA without demonstrated economic and technical
viability; that exploration results will not translate into the discovery of
an economically viable deposit; risks and uncertainties relating to political
risks involving the Company's exploration and development of mineral
properties interests; the inherent uncertainty of cost estimates and the
potential for unexpected costs and expense; commodity price fluctuations, the
inability or failure to obtain adequate financing on a timely basis and other
risks and uncertainties. Such information contained herein represents
management's best judgment as of the date hereof, based on information
currently available and is included for the purposes of providing investors
with the Company's plans and expectations at its San Albino project and the
Las Conchitas area, and may not be appropriate for other purposes. Mako does
not undertake to update any forward-looking information, except in accordance
with applicable securities laws.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Mako Mining Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/August2019/19/c9723.html

-0-                           08/19/2019
/For further information: Mako Mining Corp., Akiba Leisman, Chief
Executive Officer, Telephone: 203-862-7059, E-mail:
aleisman(at)makominingcorp.com or visit our website at www.makominingcorp.com 
and
SEDAR www.sedar.com./
/Web Site: https://makominingcorp.com/ /
(MKO.)

CO:  Mako Mining Corp.
ST:  British Columbia
IN:  MNG MIN
SU:

-30-