Source	CANADA NEWSWIRE
Date	07/07/2020
Time	09:08:43 AM

Company	 Southern Empire Resources Corp.
Title	Southern Empire Reports Gold Results from Oro Cruz Historical Heap Leach
Pads





    CDNX Symbol: SMP











Press Release




" BC-SouthernEmpireResults   07-07 1546
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.559480:
^Southern Empire Reports Gold Results from Oro Cruz Historical Heap Leach
Pads@

VANCOUVER, BC, July 7, 2020 /CNW/ - Southern Empire Resources Corp.
("Southern Empire"; TSX-V: SMP) (Frankfurt: 5RE) is pleased to report gold
assay results for selective grab samples collected from the surface of two
historical heap leach pads located on its 2,160 hectare (5,338 acre) Oro Cruz
Gold Project in Imperial County, California.
Assessment of Historical Leach Pads - Background, Objectives and
Highlights
Historical mining of the American Girl, Padre y Madre, Queen and Oro Cruz
oxide gold deposits by the American Girl Mining Joint Venture ("AGMJV"; MK
Gold Company and Hecla Mining Company) occurred between 1987 and 1996. At that
time, processing was either by heap leaching of lower-grade, or milling of
higher-grade, gold-mineralized materials. Operations ceased in late 1996, due
to declining gold prices, leaving both the American Girl and Padre y Madre
historical leach pads, covering approximately 61 and 22 acres respectively.
Southern Empire believes that the gold-bearing material in the two
historical leach pads may contain significant residual gold and, as a first
phase of assessment, twenty-six (26) samples were collected; 12 from the
historical Padre y Madre and 14 from the American Girl leach pads. Gold assay
results are presented in Table 1 and sample locations are presented in Figures
1 and 2.
David Tupper, P.Geo. and Southern Empire's VP of Exploration stated: "We
are pleased to report that our preliminary surface sampling has confirmed gold
is present in historical heap leach pads that remain from the former American
Girl Mining Joint Venture operations."
Southern Empire's President and CEO, Dale Wallster stated: "Having now
unequivocally demonstrated that gold still exists in the historical leach
pads, we will use sonic drilling to quickly target the establishment of a
resource and provide us with samples for extractive metallurgical test work.
The potential for Southern Empire to ultimately reprocess this already mined
material represents additional upside to any high-grade, underground results
we get at Oro Cruz."
Steps Forward on the Historical Heap Leach Pads at the Oro Cruz Gold
Project
To establish a NI 43-101 resource for the historical heap leach pads,
Southern Empire has:
<<

--  Initiated permitting for sonic drilling of both the Padre y Madre and
American Girl heap leach pads with both the U.S. Bureau of Land
Management ("BLM") and Imperial County,

--  Initiated a review of historical AGMJV metallurgy in order to determine
the best methods for gold extraction from the existing heap leach pad
material, and

--  Engaged Mr. Garth Kirkham, the principal of Kirkham Geosystems Ltd., of
Vancouver, Canada, to oversee the resource establishment procedures at
Oro Cruz. Kirkham Geosystems is a full-service provider of geoscience
consulting services to the mining, environmental, oil & gas and
geotechnical industries focusing on offering 3D computer modeling
expertise using a variety of leading volumetric modeling systems. Mr.
Kirkham is the Past-President of the Canadian Institute of Mining,
Metallurgy and Petroleum (CIM) and is the co-Chair of the CIM Mineral
Resources and Mineral Reserves Committee and the Chair of the
Geoscientists Canada, Securities Committee. He is also currently a
representative for Canada on CRIRSCO - Committee for Mineral Reserves
International Reporting Standards.
<>>
Data Verification, Sampling Procedures and Quality Assurance/Quality
Control (QA/QC)
Surface grab samples of rock chips from larger boulders combined with
gravel and fines, all considered representative of the materials of the
historical American Girl and Padre y Madre heap leach pads at Oro Cruz were
collected from 20 centimetre deep, hand-dug pits. Samples were described and
photographed, and their location surveyed with handheld GPS, accurate to
within 3 metres.
Each sample was then in control of the geologist until it was shipped
from Yuma, AZ and Brawley, CA to either Bureau Veritas Mineral Laboratories
USA ("BVM") in Sparks, NV (samples OCR-11 to OCR-27) or ALS USA Inc. ("ALS")
in Reno, NV (samples OCR-27 to OCR-49), respectively. The samples were
collected in two events, as noted in Table 1. The averages of analytical
results from the two sampling events are comparable.
Samples were crushed, split and pulverized (250 grams to 75 microns
("µ"); 200 mesh) using BVM process PRP70-250 or ALS processes CRU012 and
PUL31, then a 30 gram homogenized sample was analyzed using fire assay
techniques with an atomic absorption spectroscopy (AAS) finish (procedures
FA430 at BVM and Au-AA23 at ALS). Four acid digestion of each sample was
followed by multielement Inductively Coupled Plasma ("ICP") mass spectrometry
analysis using MA3000 procedure at BVM and ME-ICP61 procedure at ALS. The
results were reported in grams gold/tonne ("g Au/t"; also parts per million,
or "ppm") and then converted to ounces gold per ton ("oz Au/ton"; also "opt")
using a ratio of 34.28.
One pulp field standard and one trip blank were inserted with samples
OCR-11 to OCR-27 that were analyzed at BVM. One pulp field standard and one
trip blank was submitted with samples OCR-27 to OCR-49. which were analyzed at
ALS. All lab standard and blank assay results reported in the BVM and ALS
analytical certificates and all field standards and blank samples assayed
within accepted QA/QC value ranges.
Standards and blanks submitted to BVM included the gold standard
MEG-Au-09.03 and blank MEG-BLANK.10.14 purchased from Shea Clark Smith/MEG,
Inc. (http://www.sheaclarksmith.com/). The submitted standards returned
accepted values of 2.091 Au ppm and <0.005 ppm Au respectively.
Standards and blanks including WCM Mineral Standard CU160 and WCM Mineral
Standard CU172 were submitted to ALS Geochemistry with samples OCR-27 to
OCR-49. These QA/QC standard material were purchased from WCM Minerals, a
division of WCM Sales Ltd., located in Burnaby, BC, Canada
(http://www.wcmminerals.ca/). The values returned for the submitted standards
were 2.93 Au ppm and 0.266 Au ppm respectively, which are within accepted
QA/QC ranges.
Qualified Person (QP)
The scientific and technical information contained in this news release
has been prepared, reviewed, verified and approved by David Tupper, P.Geo.
(British Columbia), Southern Empire's VP - Exploration and a Qualified Person
(QP) within the context of Canadian Securities Administrators' National
Instrument 43-101; Standards of Disclosure for Mineral Projects.
Work Programs During the COVID-19 Pandemic
As the health and safety of our employees, contractors and associated
communities is a top priority, Southern Empire will continue to monitor
COVID-19 regulatory recommendations and restrictions and, together with our
consultants and subcontractors, will follow governmental health and safety
regulations and protocol regarding personnel management, lodging, travel,
etc., in our current and future work related to both the Eastgate and Oro Cruz
Gold Projects.
The timing of Southern Empire's on-going exploration and development
programs will be contingent on governmental regulations regarding the COVID-19
pandemic.
About Southern Empire Resources Corp.
Southern Empire is focused on the acquisition, exploration and
development of gold deposits in North America, currently having two projects
in the American southwest.
In the Cargo Muchacho mountains of Imperial County, southeast California,
Southern Empire holds options to acquire a 100% interest in the 2,160 hectare
(5,338 acre) Oro Cruz Property located approximately 22.5 kilometres (14
miles) southeast of the Mesquite gold mine of Equinox Gold Corp.
With a history that includes extensive drilling and large-scale open pit
and underground mining that was suspended during the gold market downturn in
1996, the Oro Cruz Gold Project hosts numerous exploration targets in addition
to a high-grade oxide gold zone that, based on the historical mine records, is
amenable to conventional heap leach extractive methods.
Southern Empire also owns an 85% interest in the 817 hectare (2,020 acre)
Eastgate Gold Project, located 81 kilometres (50 miles) southeast of the city
of Fallon in Churchill County, Nevada. Southern Empire has just completed six
HQ-size core drill holes at Eastgate, in a first-pass drill program targeting
high-grade gold/silver epithermal vein systems. Selective core samples have
been submitted to ALS USA Inc.'s laboratories in Reno, Nevada and assay
results will be released after they become available. Permitting for the next
phase of drilling has been initiated.
On behalf of the Board of Directors,
Dale Wallster, CEO and DirectorSouthern Empire Resources Corp.
Cautionary Notice on Forward-Looking Information
Information set forth in this news release may contain forward-looking
statements that are based on assumptions as of the date of this news release.
All statements, other than statements of historical fact, that address
activities, events or developments that Southern Empire expects or anticipates
will or may occur in the future are forward-looking statements that reflect
management's current estimates, beliefs, intentions and expectations. They are
not guarantees of future performance. Southern Empire cautions that all
forward-looking statements are inherently uncertain and that actual
performance may be affected by a number of material factors, many of which are
beyond Southern Empire's control. Such factors include, among other things:
risks and uncertainties relating to Southern Empire's limited operating
history and the need to comply with environmental and governmental
regulations. Accordingly, actual and future events, conditions and results may
differ materially from the estimates, beliefs, intentions and expectations
expressed or implied in the forward-looking information. Except as required
under applicable securities legislation, Southern Empire undertakes no
obligation to publicly update or revise forward-looking statements or
information.
Neither TSX Venture Exchange nor its regulation services provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Southern Empire Resources Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/July2020/07/c2161.html

-0-                           07/07/2020
/For further information: please visit www.smp.gold and review our SEDAR
filings or contact: Lubica Keighery at (778) 889-5476, lubica(at)smp.gold/
(SMP. 5RE)

CO:  Southern Empire Resources Corp.
ST:  British Columbia
IN:  MIN MNG
SU:

-30-