Source	Business Wire
Date	07/07/2020
Time	02:04:04 AM

Company	 ARIZONA METALS CORP.
Title	[EXTERNAL] Arizona Metals Corp Announces Start of Drilling at Its 
Sugarloaf Pe...





    CDNX Symbol: AMC











Press Release




July 7, 2020 09:03 UTC

Arizona Metals Corp Announces Start of Drilling at Its Sugarloaf Peak Project 
Heap-Leach Gold-Oxide Target in La Paz County, Arizona; Two Drills Continue 
Turning at the Kay Mine Gold-Copper VMS Phase 1 Program in Yavapai County, 
Arizona 

NEWS RELEASE SUBMITTED BY BUSINESS WIRE 

FOR: Arizona Metals Corp 

TSX VENTURE SYMBOL: AMC 

TORONTO--(BUSINESS WIRE)-- Arizona Metals Corp. (TSX.V:AMC) (the “Company” or 
“Arizona Metals”) is pleased to announce that it has commenced a 1,300m drill 
program at its Sugarloaf Peak Project in La Paz County, Arizona. Drill core 
from two 150m holes will be sent to Kappes Cassiday and Associates of Reno, 
Nevada, to undergo bottle-roll and column testing of gold recoveries by 
leaching of oxide material. Samples will also be sent to ALS Minerals in Reno, 
Nevada for gold assay, multi-element testing, and spectral analysis to 
determine trace-element levels and hydrothermal alteration variations. 

Another two cored drill holes will be extended to depths of 450 m and 550 m to 
intersect a large, untested geophysical target (Figure 1) that the Company 
believes has the potential to host a higher grade “feeder” zone, that could be 
the source of the disseminated oxide mineralization identified at surface in 
the historic estimate. The locations, dips, and azimuths of the four planned 
holes are detailed in Table 1 below. 

The geophysical target is based on induced polarization (IP) data showing 
coincident high chargeability and high resistivity. Chargeability high 
anomalies often indicate the presence of sulfide minerals such as pyrite, and 
resistivity highs may indicate alteration minerals such as quartz. The 
mineralization identified to date at Sugarloaf contains both pyrite and quartz. 

  

																
																
Table 1. Sugarloaf planned drill hole locations and orientations
																
Hole ID		Pad		East (NAD83)		North 
(NAD83)		Elevation		Depth (ft)		Depth 
(m)		Az		Dip
SP-20-01		C		
				747630 
						
						3725020 
								
								387 
										
										
500 
												
												
152 
														
														
180 
																
																
-45 
																
SP-20-02		B		
				747680 
						
						3725022 
								
								388 
										
										
500 
												
												
152 
														
														
0 
																
																
-70 
																
SP-20-03		V		
				747880 
						
						3725300 
								
								375 
										
										
1500 
												
		
										
457 
														
														
0 
																
																
-90 
																
SP-20-04		E		
				747600 
						
						3724920 
								
								388 
										
										
1800 
												
												
549 
														
											
			54 
																
																
-57 
																
Total										
										
4,300 
												
												
1,311 
																

Marc Pais, CEO of Arizona Metals Corp., commented, “While our primary focus 
remains on the high-grade Kay Mine VMS project, where we have two drills 
turning, we believe there is significant unrecognized value in the Sugarloaf 
Project. We will first follow up on promising initial metallurgical testing 
completed by Kinross in 2009 and Agnico in 2013, to demonstrate that Sugarloaf 
has the characteristics required of a viable heap-leach mining operation. We 
will also be testing a large IP geophysical target located about 300m below the 
historic estimate, that we believe has the potential to host higher grade 
“feeder” zones. The IP targets were identified in 2012, but never drill tested.”

Sugarloaf Peak Highlights 

Project is 100% owned by Arizona Metals Corp. with no future payments
Located on 4,400 acres of BLM claims in mining-friendly La Paz County, Arizona
Historic estimate of “100 million tons containing 1.5 million ounces gold”* at 
a grade of 0.5 g/t (Dausinger, 1983, Westworld Resources). 
Heap-leach, open-pit target that starts at surface and is tabular with no dip
Open for expansion at depth and on strike
Metallurgical testing (bottle roll) by Kinross (2009) and Agnico (2013) 
achieved gold recoveries of up to 73% (inline with heap-leach mines currently 
in operation)

About Arizona Metals Corp 

Arizona Metals Corp owns 100% of the Kay Mine Property in Yavapai County, which 
is located on a combination of patented and BLM claims totaling 1,300 acres 
that are not subject to any royalties. An historic estimate by Exxon Minerals 
in 1982 reported a “proven and probable reserve of 6.4 million short tons at a 
grade of 2.2% copper, 2.8 g/t gold, 3.03% zinc, and 55 g/t silver.” The 
historic estimate at the Kay Mine was reported by Exxon Minerals in 1982. The 
historic estimate has not been verified as a current mineral resource. None of 
the key assumptions, parameters, and methods used to prepare the historic 
estimate were reported, and no resource categories were used. Significant data 
compilation, re-drilling and data verification may be required by a Qualified 
Person before the historic estimate can be verified and upgraded to be a 
current mineral resource. A Qualified Person has not done sufficient work to 
classify it as a current mineral resource, and Arizona Metals is not treating 
the historic estimate as a current mineral resource. 

The Kay Mine is a steeply dipping VMS deposit that has been defined from a 
depth of 60 m to at least 900 m. It is open for expansion on strike and at 
depth. 

The Company also owns 100% of the Sugarloaf Peak Property, in La Paz County, 
which is located on 4,400 acres of BLM claims. Sugarloaf is a heap-leach, 
open-pit target and has a historic estimate of “100 million tons containing 1.5 
million ounces gold” at a grade of 0.5 g/t (Dausinger, 1983, Westworld 
Resources). 

*The historic estimate at the Sugarloaf Peak Property was reported by Westworld 
Resources in 1983. The historic estimate has not been verified as a current 
mineral resource. None of the key assumptions, parameters, and methods used to 
prepare the historic estimate were reported, and no resource categories were 
used. Significant data compilation, re-drilling and data verification may be 
required by a Qualified Person before the historic estimate can be verified and 
upgraded to a current mineral resource. A Qualified Person has not done 
sufficient work to classify it as a current mineral resource, and Arizona 
Metals is not treating the historic estimate as a current mineral resource. 

The Qualified Person who reviewed and approved the technical disclosure in this 
release is David Smith, CPG. 

Quality Assurance/Quality Control 

All of Arizona Metals’ drill sample assay results have been independently 
monitored through a quality assurance/quality control (“QA/QC”) protocol which 
includes the insertion of blind standard reference materials and blanks at 
regular intervals. Logging and sampling were completed at Arizona Metals’ core 
handling facilities located in Anthem and Black Canyon City, Arizona. Drill 
core was diamond sawn on site and half drill-core samples were securely 
transported to ALS Laboratories’ (“ALS”) sample preparation facility in Tucson, 
Arizona. Sample pulps were sent to ALS’s labs in Vancouver, Canada, for 
analysis. 

Gold content was determined by fire assay of a 30-gram charge with ICP finish 
(ALS method Au-AA23). Silver and 32 other elements were analyzed by ICP methods 
with four-acid digestion (ALS method ME-ICP61a). Over-limit samples for Ag, Cu, 
and Zn were determined by ore-grade analyses Ag-OG62, Cu-OG62, and Zn-OG62, 
respectively. 

ALS Laboratories is independent of Arizona Metals Corp. and its Vancouver 
facility is ISO 17025 accredited. ALS also performed its own internal QA/QC 
procedures to assure the accuracy and integrity of results. Parameters for ALS’ 
internal and Arizona Metals’ external blind quality control samples were 
acceptable for the samples analyzed. Arizona Metals is not aware of any 
drilling, sampling, recovery, or other factors that could materially affect the 
accuracy or reliability of the data referred to herein. 

This press release contains statements that constitute “forward-looking 
information” (collectively, “forward-looking statements”) within the meaning of 
the applicable Canadian securities legislation, All statements, other than 
statements of historical fact, are forward-looking statements and are based on 
expectations, estimates and projections as at the date of this news release. 
Any statement that discusses predictions, expectations, beliefs, plans, 
projections, objectives, assumptions, future events or performance (often but 
not always using phrases such as “expects”, or “does not expect”, “is 
expected”, “anticipates” or “does not anticipate”, “plans”, “budget”, 
“scheduled”, “forecasts”, “estimates”, “believes” or “intends” or variations of 
such words and phrases or stating that certain actions, events or results “may” 
or “could”, “would”, “might” or “will” be taken to occur or be achieved) are 
not statements of historical fact and may be forward-looking statements. 
Forward-looking statements contained in this press release include, without 
limitation, statements regarding the resumption of drilling and the effects of 
the COVID-19 pandemic on the business and operations of the Company. In making 
the forward- looking statements contained in this press release, the Company 
has made certain assumptions. Although the Company believes that the 
expectations reflected in forward-looking statements are reasonable, it can 
give no assurance that the expectations of any forward-looking statements will 
prove to be correct. Known and unknown risks, uncertainties, and other factors 
which may cause the actual results and future events to differ materially from 
those expressed or implied by such forward-looking statements. Such factors 
include, but are not limited to: availability of financing; delay or failure to 
receive required permits or regulatory approvals; and general business, 
economic, competitive, political and social uncertainties. Accordingly, readers 
should not place undue reliance on the forward-looking statements and 
information contained in this press release. Except as required by law, the 
Company disclaims any intention and assumes no obligation to update or revise 
any forward-looking statements to reflect actual results, whether as a result 
of new information, future events, changes in assumptions, changes in factors 
affecting such forward- looking statements or otherwise. 

NEITHER THE TSX VENTURE EXCHANGE (NOR ITS REGULATORY SERVICE PROVIDER) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE 

Not for distribution to US newswire services or for release, publication, 
distribution or dissemination directly, or indirectly, in whole or in part, in 
or into the United States 

[IMAGE]

View source version on businesswire.com: 
https://www.businesswire.com/news/home/20200707005222/en/

Contacts

Marc Pais President and CEO Arizona Metals Corp. (416) 565-7689 
mpais@arizonametalscorp.com  www.arizonametalscorp.com  
https://twitter.com/ArizonaCorp 

Source: Arizona Metals Corp