Source	CANADA NEWSWIRE
Date	07/07/2020
Time	04:32:49 AM

Company	 GR Silver Mining Ltd.
Title	GR Silver Mining Reports High-Grade Drill Results and Extends the San
Juan Ag-Au Mineralized System at the Plomosas Project to 1 km with a 600
m Step-Out





    CDNX Symbol: GRSL











Press Release




" BC-GR-Silver-Mining-Drll   07-07 2478
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.338617:
^GR Silver Mining Reports High-Grade Drill Results and Extends the San
Juan Ag-Au Mineralized System at the Plomosas Project to 1 km with a 600
m Step-Out@

<<

--  1,723 gpt AgEq(x)1 over 2.7 m (15.1 gpt Au, 45 gpt Ag, 3.1% Pb and 0.9%
Zn) including 5,055 gpt AgEq over 0.9 m (46.9 gpt Au, 76 gpt Ag, 3.3% Pb
and 2.2% Zn)
--  25.7 m at 1.0 gpt Au, 2% Pb and 1% Zn
>>
VANCOUVER, BC, July 7, 2020 /CNW/ - GR Silver Mining Ltd. (TSXV: GRSL)
(FRANKFURT: GPE) (OTCQB: GRSLF) ("GR Silver Mining" or the "Company") - is
pleased to announce drill results at its 100%-owned Plomosas Silver Project
("Plomosas Project") in Sinaloa, Mexico. These results are located in the San
Juan-La Colorada Area, one of six priority areas with recent (2018) drill data
being released by the Company.
These drill hole results identify silver and gold mineralized zones in a
600 m step out from the previously released drill hole results at San Juan
(Figures 1 and 2) (see News Release dated May 4, 2020). They confirm
continuity of the Au-Ag mineralized system for at least 1 km, supporting a
geological model where both areas, La Colorada and San Juan, are part of a
single significant epithermal system with occurrence of not only Ag-Pb-Zn
mineralization hosted in polymetallic hydrothermal breccias, but also Au-Ag
enriched veins in high angle fault zones.
The drilling intercepts confirm prospective, near-surface, multiple vein
systems peripheral to other drilled areas. This creates the potential to
delineate a much larger epithermal system for future drilling and resource
estimation. To date, the Company has identified six veins in the San Juan-La
Colorada Area as a result of previous drill results and surface and
underground mapping/sampling. The Company believes that the Au-Ag bearing
structures are part of regional scale fault systems, hosting attractive low
sulphidation epithermal mineralization and thus providing the opportunity to
move forward confidently with further shallow drilling.
GR Silver Mining President and CEO, Marcio Fonseca, commented, "We are
very pleased with the progress of our exploration program at Plomosas. We see
significant strike length, down dip extensions and the presence of multiple
veins, exhibiting the potential to define a large low sulphidation epithermal
system covering most of the areas previously drilled. To date, we have been
able to collect key geological and geometrical components for the silver-gold
mineralized system at the San Juan-La Colorada Area, providing support for our
upcoming drilling program. Results to date are indicating that both
mineralization styles, Au-Ag epithermal veins and Ag-Pb-Zn hydrothermal
breccias, are present, defining a large system with multi-kilometre strike
potential".

_____________________________



1             AgEq is based on long term gold, silver, zinc and lead prices of
US$1600 per ounce gold, US$16.50 per ounce silver, US$0.85 per pound
zinc and US$0.95 per pound lead. The metallurgical recoveries are
assumed as 90% Ag, 95% Au, 78% Pb and 70% Zn.
Figure 1: San Juan-La Colorada Area Geology - Drill Hole Location Map
Figure 2: Drone Image of the San Juan-La Colorada Area (looking to the
NW)
Table 1 summarizes the most significant drill assay results for this
group of holes released for the San Juan-La Colorada Area.
Table 1: Summary Drill Hole Results - News Release July 7, 2020 (San
Juan-La Colorada Area)
Est.    Ag g/t     Au g/t      Pb %     Zn %
true
Drilled   width                                                  AgEq g/t
width            (m)
Hole No.      From       To   (m)
(m)       (m)

---

LCS18-01                 203.3     203.6             0.4           0.4         
14         0.1      3.3      5.2

---

LCS18-02                 179.2     198.3            19.1          17.2          
2         0.3      0.2      0.8

---

includes                 190.5     192.2             1.7           1.5          
8         2.1      0.8      4.1

---

LCS18-02                 239.8     265.5            25.7          21.8          
7         1.0      1.5      1.0

---

LCS18-03        206.7     209.3             2.7           2.4         45        
15.1      3.1      0.9          1,723

---

includes                 206.7     207.5             0.9           0.8         
76        46.9      3.3      2.2          5,055

---

LCS18-04        250.9     288.6            37.8          34.0          
5         0.3      0.8      1.0

---

includes                 276.0     287.6            11.6          10.4          
7         0.7      1.6      2.3

---

368.9     370.0             1.2           1.0        182         0.3      
0.1      0.2            224



LCS18-05        242.9     270.7            27.8          25.0         
26         0.3      0.6      0.8

---

includes                 247.0     251.5             4.5           4.0        
126         1.6      1.3      1.7            380

---
(x)AgEq is based on long term
gold, silver, zinc and lead
prices of US$1600 per ounce
gold, US$16.50 per ounce
silver, US$0.85 per pound zinc
and US$0.95 per pound lead. The
metallurgical recoveries are
assumed as 90% Ag, 95% Au, 78%
Pb and 70% Zn. "na" (equal sign) no
relevant assays. All numbers
are rounded. Results are uncut
and undiluted.
The drill holes in this news release were generated by a drill campaign
completed by First Majestic Silver Corp. ("First Majestic") in 2018 and not
previously released. They are part of an extensive surface and underground
diamond core drilling database, which GR Silver Mining is consolidating and
validating.
Table 2 lists the drill hole intervals previously not sampled ("NS") for
this group of released holes. The Company is investigating these holes for
evidence of mineralization in the core that warrants additional sampling and
assaying.
Table 3 provides collar coordinates for the drill holes presented in this
news release.
Table 2: San Juan-La Colorada Area - Drill Hole Intervals Not Sampled
(Intervals greater than 20m)
From-To (m)                                           From-To (m)

Hole
No.                             Sampling         Hole 
No.                             Sampling

---

LCS18-01
0-132.95
NS
LCS18-03
152.2-166.9
NS

---

LCS18-01         141.75-195.45
NS
LCS18-03           172.1-184.55
NS

---

LCS18-01
242-270.05
NS
LCS18-03
209.3-214
NS

---

LCS18-02
0-177.7
NS
LCS18-04
0-156.1
NS

---

LCS18-02         298.35-307.3
NS
LCS18-04           389.85-453.1
NS

---

LCS18-02         410.75-450.5
NS
LCS18-05
0-165.9
NS

---

LCS18-03
0-89.75
NS
LCS18-05
182.6-184
NS

---

LCS18-03
112-147
NS
LCS18-05
207.7-242.5
NS

---
All numbers are rounded.
NS -Core not assayed
by First Majestic
Table 3: Drill Hole Locations - San Juan-La Colorada Area (News Release
7/7/2020)
Hole No. East (m) North (m)  RL (m)   Az.    Dip     Depth (m)

---

LCS18-01         447872    2551275      939    232     -47           270

---

LCS18-02         447922    2551141      922    250     -75           458

---

LCS18-03         447922    2551141      922    250     -50           214

---

LCS18-04         447961    2551067      899    250     -75           453

---

LCS18-05         447961    2551067      899    250     -54           280

---
All numbers are rounded.
The San Juan-La Colorada Area drill results continue to demonstrate the
continuity of higher-grade mineralization along strike, expanding the
footprint of the low sulphidation epithermal system for approximately 1km. The
high grades encountered indicate both Au-Ag and Ag-Pb-Zn styles of
mineralization in an area with multiple deep-rooted fault systems, creating a
prospective setting for future discoveries (Photo 1).
Photo 1- High-grade Au Core Sample - Hydrothermal Breccia Drill Hole
LCS18-03.
The low sulphidation epithermal Au-Ag system is hosted predominantly in
high-angle faults, whereas the Ag-Pb-Zn mineralization is preferentially in
shallow angle faults and polymetallic hydrothermal breccias (click here to
view cross sections). Both mineralization styles have developed due to a
combination of multiple deep-rooted fault structures in a multi-event system,
where precious metals appear to be the younger mineralized phase. The
deep-rooted regional structures transect and served as a fluid conduit for a
large underlying hydrothermal system, cross cutting a volcanic sequence made
of andesites, tuffs and rhyolites, where brittle fracturing in host rocks has
created voids or traps for deposition of both styles of mineralization. The
combination of these structures, together with favorable host rocks
(permeability and porosity), have generated numerous alteration halos
(argillic, propylitic, oxidation and silicification) (Figures 1 and 2). These
altered areas are exploration guides for future drilling and expansion of the
mineralization footprint.
The Company is implementing detailed core relogging and multi-element
analysis by portable hand-held XRF (pXRF), particularly in non-sampled areas,
prior to being submitted to the laboratory for detailed chemical analysis.
Using pathfinder elements, the pXRF results enable data-driven determination
of the mineralized and un-mineralized alteration mineral assemblages. The
Company has successfully implemented a pXRF program at its nearby projects,
where it has proven to be a cost- and time-effective first pass analytical
method.
Previous owners completed aero- and ground geophysical surveys
(magnetometry and IP) covering most of the deep-rooted regional faults. In
general, for an IP survey, resistivity anomalies delineate the fault system
and chargeability differentiates oxide vs. sulphide mineralization potential
at depth. High resolution airborne magnetometry was undertaken by First
Majestic in 2016, covering the Plomosas Project. This form of geophysical
investigation is important in defining regional and local scale lithological
variations, as well as potentially buried intrusive bodies that can be
important heat and fluid sources in the genesis of epithermal mineralization
in volcanic environments such as at Plomosas. Fluid flow derived from
epithermal systems can result in the local destruction of magnetism,
particularly along structural pathways, which can also be used as a targeting
tool.
This geophysical 'fingerprint' of the mineralized system, together with
the abundance of faults, has resulted in promising new prospective zones for
oxide and sulphide mineralization types. GR Silver Mining continues to update
the 3D geological model of exploration together with results from drill holes,
bedrock mapping and soil and rock geochemistry and geophysics, generating
data-driven, drill-ready targets supported by all four data sets.
Qualified Person
The scientific and technical data contained in this News Release related
to the Plomosas Project was reviewed and/or prepared under the supervision of
Marcio Fonseca, P.Geo. He has approved the disclosure herein.
Quality Assurance Program and Quality Control Procedures ("QA/QC")
The recent drill holes completed by First Majestic from 2016 to 2018,
followed QA/QC protocols reviewed and validated by GR Silver Mining, including
insertion of blank and standard samples in all sample lots sent to First
Majestic's Laboratorio Central facilities in La Parilla, Durango, for sample
preparation and assaying. Additional validation and check assays were
performed by an independent laboratory at SGS de México, S.A. de C.V.
facilities in Durango, Mexico. The analytical methods applied for these recent
holes for Ag and Au assays comprised of Fire Assay with Atomic Absorption
finish for samples above Au >10ppm and Ag >300ppm and Gravimetric Finish. Pb
and Zn were analyzed using Inductively Coupled Plasma Optical Emission
Spectrometry.
The Company has also negotiated debt settlement with arm's length and
non-arm's length creditors. Pursuant to the debt settlement agreements, and
subject to acceptance by the TSX-V, the Company has settled aggregate debt of
$207,728 outstanding as at June 30, 2020, in consideration for which it will
issue an aggregate of 437,322 common shares at a deemed price of $0.475 per
share. Certain insiders of the Company participated in the debt settlements
(Marcio Fonseca, the Company's President, CEO and director, agreed to settle
$7,500 debt for 15,790 shares; Blaine Bailey, the Company's CFO, agreed to
settle $7,500 debt for 15,790 shares; and Trevor Woolfe, the Company's VP
Corporate Development & Exploration, agreed to settle $15,000 debt for 31,579
shares). Participation by Insiders in the debt settlements is also considered
a "related party transaction" pursuant to MI 61-101. The Company is exempt
from the requirements to obtain a formal valuation and minority shareholder
approval in connection with the Insiders' participation in the debt
settlements in reliance of sections 5.5(a) and 5.7(a) of MI 61-101,
respectively, on the basis that participation in the debt settlements by the
Insiders did not exceed 25% of the fair market value of the Company's 
marketcapitalization. All shares issued in relation to these debt settlements 
are
subject to a hold period expiring four months + one day after the date the
shares are issued, in accordance with applicable securities laws and the
policies of the TSX-V.
About GR Silver Mining Ltd.
GR Silver Mining Ltd. is a Mexico-focused company engaged in
cost-effective silver-gold resource expansion on its key assets which lie on
the eastern edge of the Rosario Mining District, Sinaloa, Mexico.
PLOMOSAS SILVER PROJECT
GR Silver Mining owns 100% of the Plomosas Silver Project located near
the historic mining village of La Rastra, within the Rosario Mining District.
The Project is a past-producing asset where only one mine, the Plomosas
silver-gold-lead-zinc underground mine, operated from 1986 to 2001. The
Project has an 8,515-hectare property position and is strategically located
within 5 km of the San Marcial Silver Project in the southeast of Sinaloa
State, Mexico. The Plomosas Project comprises six areas with an average of 100
surface and underground drill holes in each area, geophysical and geochemical
data covering most of the concession, and the delineation of 16
exploration/drilling targets.
The 100%-owned assets include all facilities and infrastructure
including: access roads, surface rights agreement, water use permit, 8,000 m
of underground workings, water access, 60 km - 33 KV power line, offices,
shops, 120-person camp, infirmary, warehouses and assay lab representing
approximately US$30m of previous capital investments. The previous owners
invested approximately US$18 million in exploration.
The silver and gold mineralization on this Project display the
alteration, textures, mineralogy and deposit geometry characteristics of a low
sulphidation epithermal silver-gold-base metal vein/breccia mineralized
system. Previous exploration was focused on Pb-Zn-Ag-Au polymetallic shallow
mineralization, hosted in NW-SE structures in the vicinity of the Plomosas
mine. The E-W portion of the mineralization and extensions for the main N-S
Plomosas fault remains under-explored. The Plomosas Silver Project has more
than 500 recent and historical drill holes in six areas - Plomosas Mine, San
Juan, La Colorada, Yecora, San Francisco and El Saltito. These drill holes
represent an extensive database allowing the Company to advance towards
resource estimation and potential project development in the near future.
SAN MARCIAL PROJECT
San Marcial is a near-surfac

" BC-GR-Silver-Mining-Drll   07-07 2478
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.338617:
^GR Silver Mining Reports High-Grade Drill Results and Extends the San
Juan Ag-Au Mineralized System at the Plomosas Project to 1 km with a 600
m Step-Out@

<<

--  1,723 gpt AgEq(x)1 over 2.7 m (15.1 gpt Au, 45 gpt Ag, 3.1% Pb and 0.9%
Zn) including 5,055 gpt AgEq over 0.9 m (46.9 gpt Au, 76 gpt Ag, 3.3% Pb
and 2.2% Zn)
--  25.7 m at 1.0 gpt Au, 2% Pb and 1% Zn
>>
VANCOUVER, BC, July 7, 2020 /CNW/ - GR Silver Mining Ltd. (TSXV: GRSL)
(FRANKFURT: GPE) (OTCQB: GRSLF) ("GR Silver Mining" or the "Company") - is
pleased to announce drill results at its 100%-owned Plomosas Silver Project
("Plomosas Project") in Sinaloa, Mexico. These results are located in the San
Juan-La Colorada Area, one of six priority areas with recent (2018) drill data
being released by the Company.
These drill hole results identify silver and gold mineralized zones in a
600 m step out from the previously released drill hole results at San Juan
(Figures 1 and 2) (see News Release dated May 4, 2020). They confirm
continuity of the Au-Ag mineralized system for at least 1 km, supporting a
geological model where both areas, La Colorada and San Juan, are part of a
single significant epithermal system with occurrence of not only Ag-Pb-Zn
mineralization hosted in polymetallic hydrothermal breccias, but also Au-Ag
enriched veins in high angle fault zones.
The drilling intercepts confirm prospective, near-surface, multiple vein
systems peripheral to other drilled areas. This creates the potential to
delineate a much larger epithermal system for future drilling and resource
estimation. To date, the Company has identified six veins in the San Juan-La
Colorada Area as a result of previous drill results and surface and
underground mapping/sampling. The Company believes that the Au-Ag bearing
structures are part of regional scale fault systems, hosting attractive low
sulphidation epithermal mineralization and thus providing the opportunity to
move forward confidently with further shallow drilling.
GR Silver Mining President and CEO, Marcio Fonseca, commented, "We are
very pleased with the progress of our exploration program at Plomosas. We see
significant strike length, down dip extensions and the presence of multiple
veins, exhibiting the potential to define a large low sulphidation epithermal
system covering most of the areas previously drilled. To date, we have been
able to collect key geological and geometrical components for the silver-gold
mineralized system at the San Juan-La Colorada Area, providing support for our
upcoming drilling program. Results to date are indicating that both
mineralization styles, Au-Ag epithermal veins and Ag-Pb-Zn hydrothermal
breccias, are present, defining a large system with multi-kilometre strike
potential".

_____________________________



1             AgEq is based on long term gold, silver, zinc and lead prices of
US$1600 per ounce gold, US$16.50 per ounce silver, US$0.85 per pound
zinc and US$0.95 per pound lead. The metallurgical recoveries are
assumed as 90% Ag, 95% Au, 78% Pb and 70% Zn.
Figure 1: San Juan-La Colorada Area Geology - Drill Hole Location Map
Figure 2: Drone Image of the San Juan-La Colorada Area (looking to the
NW)
Table 1 summarizes the most significant drill assay results for this
group of holes released for the San Juan-La Colorada Area.
Table 1: Summary Drill Hole Results - News Release July 7, 2020 (San
Juan-La Colorada Area)
Est.    Ag g/t     Au g/t      Pb %     Zn %
true
Drilled   width                                                  AgEq g/t
width            (m)
Hole No.      From       To   (m)
(m)       (m)

---

LCS18-01                 203.3     203.6             0.4           0.4         
14         0.1      3.3      5.2

---

LCS18-02                 179.2     198.3            19.1          17.2          
2         0.3      0.2      0.8

---

includes                 190.5     192.2             1.7           1.5          
8         2.1      0.8      4.1

---

LCS18-02                 239.8     265.5            25.7          21.8          
7         1.0      1.5      1.0

---

LCS18-03        206.7     209.3             2.7           2.4         45        
15.1      3.1      0.9          1,723

---

includes                 206.7     207.5             0.9           0.8         
76        46.9      3.3      2.2          5,055

---

LCS18-04        250.9     288.6            37.8          34.0          
5         0.3      0.8      1.0

---

includes                 276.0     287.6            11.6          10.4          
7         0.7      1.6      2.3

---

368.9     370.0             1.2           1.0        182         0.3      
0.1      0.2            224



LCS18-05        242.9     270.7            27.8          25.0         
26         0.3      0.6      0.8

---

includes                 247.0     251.5             4.5           4.0        
126         1.6      1.3      1.7            380

---
(x)AgEq is based on long term
gold, silver, zinc and lead
prices of US$1600 per ounce
gold, US$16.50 per ounce
silver, US$0.85 per pound zinc
and US$0.95 per pound lead. The
metallurgical recoveries are
assumed as 90% Ag, 95% Au, 78%
Pb and 70% Zn. "na" (equal sign) no
relevant assays. All numbers
are rounded. Results are uncut
and undiluted.
The drill holes in this news release were generated by a drill campaign
completed by First Majestic Silver Corp. ("First Majestic") in 2018 and not
previously released. They are part of an extensive surface and underground
diamond core drilling database, which GR Silver Mining is consolidating and
validating.
Table 2 lists the drill hole intervals previously not sampled ("NS") for
this group of released holes. The Company is investigating these holes for
evidence of mineralization in the core that warrants additional sampling and
assaying.
Table 3 provides collar coordinates for the drill holes presented in this
news release.
Table 2: San Juan-La Colorada Area - Drill Hole Intervals Not Sampled
(Intervals greater than 20m)
From-To (m)                                           From-To (m)

Hole
No.                             Sampling         Hole 
No.                             Sampling

---

LCS18-01
0-132.95
NS
LCS18-03
152.2-166.9
NS

---

LCS18-01         141.75-195.45
NS
LCS18-03           172.1-184.55
NS

---

LCS18-01
242-270.05
NS
LCS18-03
209.3-214
NS

---

LCS18-02
0-177.7
NS
LCS18-04
0-156.1
NS

---

LCS18-02         298.35-307.3
NS
LCS18-04           389.85-453.1
NS

---

LCS18-02         410.75-450.5
NS
LCS18-05
0-165.9
NS

---

LCS18-03
0-89.75
NS
LCS18-05
182.6-184
NS

---

LCS18-03
112-147
NS
LCS18-05
207.7-242.5
NS

---
All numbers are rounded.
NS -Core not assayed
by First Majestic
Table 3: Drill Hole Locations - San Juan-La Colorada Area (News Release
7/7/2020)
Hole No. East (m) North (m)  RL (m)   Az.    Dip     Depth (m)

---

LCS18-01         447872    2551275      939    232     -47           270

---

LCS18-02         447922    2551141      922    250     -75           458

---

LCS18-03         447922    2551141      922    250     -50           214

---

LCS18-04         447961    2551067      899    250     -75           453

---

LCS18-05         447961    2551067      899    250     -54           280

---
All numbers are rounded.
The San Juan-La Colorada Area drill results continue to demonstrate the
continuity of higher-grade mineralization along strike, expanding the
footprint of the low sulphidation epithermal system for approximately 1km. The
high grades encountered indicate both Au-Ag and Ag-Pb-Zn styles of
mineralization in an area with multiple deep-rooted fault systems, creating a
prospective setting for future discoveries (Photo 1).
Photo 1- High-grade Au Core Sample - Hydrothermal Breccia Drill Hole
LCS18-03.
The low sulphidation epithermal Au-Ag system is hosted predominantly in
high-angle faults, whereas the Ag-Pb-Zn mineralization is preferentially in
shallow angle faults and polymetallic hydrothermal breccias (click here to
view cross sections). Both mineralization styles have developed due to a
combination of multiple deep-rooted fault structures in a multi-event system,
where precious metals appear to be the younger mineralized phase. The
deep-rooted regional structures transect and served as a fluid conduit for a
large underlying hydrothermal system, cross cutting a volcanic sequence made
of andesites, tuffs and rhyolites, where brittle fracturing in host rocks has
created voids or traps for deposition of both styles of mineralization. The
combination of these structures, together with favorable host rocks
(permeability and porosity), have generated numerous alteration halos
(argillic, propylitic, oxidation and silicification) (Figures 1 and 2). These
altered areas are exploration guides for future drilling and expansion of the
mineralization footprint.
The Company is implementing detailed core relogging and multi-element
analysis by portable hand-held XRF (pXRF), particularly in non-sampled areas,
prior to being submitted to the laboratory for detailed chemical analysis.
Using pathfinder elements, the pXRF results enable data-driven determination
of the mineralized and un-mineralized alteration mineral assemblages. The
Company has successfully implemented a pXRF program at its nearby projects,
where it has proven to be a cost- and time-effective first pass analytical
method.
Previous owners completed aero- and ground geophysical surveys
(magnetometry and IP) covering most of the deep-rooted regional faults. In
general, for an IP survey, resistivity anomalies delineate the fault system
and chargeability differentiates oxide vs. sulphide mineralization potential
at depth. High resolution airborne magnetometry was undertaken by First
Majestic in 2016, covering the Plomosas Project. This form of geophysical
investigation is important in defining regional and local scale lithological
variations, as well as potentially buried intrusive bodies that can be
important heat and fluid sources in the genesis of epithermal mineralization
in volcanic environments such as at Plomosas. Fluid flow derived from
epithermal systems can result in the local destruction of magnetism,
particularly along structural pathways, which can also be used as a targeting
tool.
This geophysical 'fingerprint' of the mineralized system, together with
the abundance of faults, has resulted in promising new prospective zones for
oxide and sulphide mineralization types. GR Silver Mining continues to update
the 3D geological model of exploration together with results from drill holes,
bedrock mapping and soil and rock geochemistry and geophysics, generating
data-driven, drill-ready targets supported by all four data sets.
Qualified Person
The scientific and technical data contained in this News Release related
to the Plomosas Project was reviewed and/or prepared under the supervision of
Marcio Fonseca, P.Geo. He has approved the disclosure herein.
Quality Assurance Program and Quality Control Procedures ("QA/QC")
The recent drill holes completed by First Majestic from 2016 to 2018,
followed QA/QC protocols reviewed and validated by GR Silver Mining, including
insertion of blank and standard samples in all sample lots sent to First
Majestic's Laboratorio Central facilities in La Parilla, Durango, for sample
preparation and assaying. Additional validation and check assays were
performed by an independent laboratory at SGS de México, S.A. de C.V.
facilities in Durango, Mexico. The analytical methods applied for these recent
holes for Ag and Au assays comprised of Fire Assay with Atomic Absorption
finish for samples above Au >10ppm and Ag >300ppm and Gravimetric Finish. Pb
and Zn were analyzed using Inductively Coupled Plasma Optical Emission
Spectrometry.
The Company has also negotiated debt settlement with arm's length and
non-arm's length creditors. Pursuant to the debt settlement agreements, and
subject to acceptance by the TSX-V, the Company has settled aggregate debt of
$207,728 outstanding as at June 30, 2020, in consideration for which it will
issue an aggregate of 437,322 common shares at a deemed price of $0.475 per
share. Certain insiders of the Company participated in the debt settlements
(Marcio Fonseca, the Company's President, CEO and director, agreed to settle
$7,500 debt for 15,790 shares; Blaine Bailey, the Company's CFO, agreed to
settle $7,500 debt for 15,790 shares; and Trevor Woolfe, the Company's VP
Corporate Development & Exploration, agreed to settle $15,000 debt for 31,579
shares). Participation by Insiders in the debt settlements is also considered
a "related party transaction" pursuant to MI 61-101. The Company is exempt
from the requirements to obtain a formal valuation and minority shareholder
approval in connection with the Insiders' participation in the debt
settlements in reliance of sections 5.5(a) and 5.7(a) of MI 61-101,
respectively, on the basis that participation in the debt settlements by the
Insiders did not exceed 25% of the fair market value of the Company's 
marketcapitalization. All shares issued in relation to these debt settlements 
are
subject to a hold period expiring four months + one day after the date the
shares are issued, in accordance with applicable securities laws and the
policies of the TSX-V.
About GR Silver Mining Ltd.
GR Silver Mining Ltd. is a Mexico-focused company engaged in
cost-effective silver-gold resource expansion on its key assets which lie on
the eastern edge of the Rosario Mining District, Sinaloa, Mexico.
PLOMOSAS SILVER PROJECT
GR Silver Mining owns 100% of the Plomosas Silver Project located near
the historic mining village of La Rastra, within the Rosario Mining District.
The Project is a past-producing asset where only one mine, the Plomosas
silver-gold-lead-zinc underground mine, operated from 1986 to 2001. The
Project has an 8,515-hectare property position and is strategically located
within 5 km of the San Marcial Silver Project in the southeast of Sinaloa
State, Mexico. The Plomosas Project comprises six areas with an average of 100
surface and underground drill holes in each area, geophysical and geochemical
data covering most of the concession, and the delineation of 16
exploration/drilling targets.
The 100%-owned assets include all facilities and infrastructure
including: access roads, surface rights agreement, water use permit, 8,000 m
of underground workings, water access, 60 km - 33 KV power line, offices,
shops, 120-person camp, infirmary, warehouses and assay lab representing
approximately US$30m of previous capital investments. The previous owners
invested approximately US$18 million in exploration.
The silver and gold mineralization on this Project display the
alteration, textures, mineralogy and deposit geometry characteristics of a low
sulphidation epithermal silver-gold-base metal vein/breccia mineralized
system. Previous exploration was focused on Pb-Zn-Ag-Au polymetallic shallow
mineralization, hosted in NW-SE structures in the vicinity of the Plomosas
mine. The E-W portion of the mineralization and extensions for the main N-S
Plomosas fault remains under-explored. The Plomosas Silver Project has more
than 500 recent and historical drill holes in six areas - Plomosas Mine, San
Juan, La Colorada, Yecora, San Francisco and El Saltito. These drill holes
represent an extensive database allowing the Company to advance towards
resource estimation and potential project development in the near future.
SAN MARCIAL PROJECT
San Marcial is a near-surface, high-grade silver-lead-zinc open
pit-amenable project. GR Silver Mining is currently drilling at the San
Marcial Project, which contains 36 Moz AgEq (Indicated) and 11 Moz AgEq
(Inferred), exploring recently defined new high-grade gold and silver targets
along the project's 6 km mineralized trend. GR Silver Mining is the first
company to conduct exploration at San Marcial in over 10 years. The NI 43-101
resource estimate (San Marcial Project - Resource Estimation and Technical
Report) was completed by WSP Canada Inc. on March 18, 2019 and amended on June
10, 2020.
Plomosas and San Marcial collectively represent a geological setting
resembling the multimillion-ounce San Dimas Mining District which has
historically produced more than 600 Moz silver and 11 Moz gold over a period
of more than 100 years.
OTHER PROJECTS
GR Silver Mining's other projects are situated in areas attractive for
future discoveries and development in the same vicinity of Plomosas and San
Marcial in the Rosario Mining District.
Mr. Marcio Fonseca
P. Geo, President & CEO GR Silver Mining Ltd.
Facebook LinkedIn Twitter
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accept
responsibility for the adequacy or accuracy of this press release.
Disclaimer for Forward-Looking Information
This press release contains forward-looking statements and information
that are based on the beliefs of management and reflect the Company's current
expectations. When used in this press release, the words "estimate",
"project", "belief", "anticipate", "intend", "expect", "plan", "predict",
"may" or "should" and the negative of these words or such variations thereon
or comparable terminology are intended to identify forward-looking statements
and information. Such statements and information reflect the current view of
the Company. Risks and uncertainties may cause actual results to differ
materially from those contemplated in those forward-looking statements and
information. By their nature, forward-looking statements involve known and
unknown risks, uncertainties and other factors which may cause our actual
results, performance or achievements, or other future events, to be materially
different from any future results, performance or achievements expressed or
implied by such forward-looking statements.
SOURCE GR Silver Mining Ltd.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/July2020/07/c2205.html

-0-                           07/07/2020
/For further information: +1 (604) 202 3155, Email:
info(at)grsilvermining.com/
/Web Site: http://www.grsilvermining.com/ /
(GLYXF GRSLF GRSL.)

CO:  GR Silver Mining Ltd.
ST:  British Columbia
IN:  MIN MNG OTC
SU:

-30-