Source	MARKET NEWS
Date	06/26/2014
Time	04:40:57 AM

Company	 Midnight Sun Mining Corp.
Title	Drills 
14.2 Metres Grading 5.71% Copper At Solwe





    CDNX Symbol: MMA











Press Release	





MIDNIGHT SUN MINING CORP ("MMA-V")
- Drills 14.2 Metres Grading 5.71% Copper At Solwezi

Midnight Sun Mining Corp. (the "Company" or "Midnight Sun")
announces the results for the recently completed core drilling program
on the Solwezi copper property in northwest Zambia. The drill program
was undertaken in April and May 2014 and consisted of 739 metres HQ
core drilled in 12 holes.

Highlights of significant, near surface copper mineralization
include the following:

//st

5.71% copper over 14.2 metres, including 9.58% copper over 7.2 metres in
drill hole SLZ-DD-14-010;

5.08% copper over 8.0 metres in drill hole SLZ-DD-14-005; and

6.27% copper over 4.5 metres in drill hole SLZ-DD-14-001.

//et

Note: The above reported lengths are intercept lengths & not
estimated true widths

The recent drill program targeted an area of the Solwezi property
located approximately 10km southwest of the Kansanshi mine, the largest
copper mine in Africa, which is operated by First Quantum Minerals
(FQM-T). This program was designed to expand the area of high grade
copper mineralization and locate primary copper mineralization.

"These results continue to confirm the presence of high grade,
near surface, oxide copper mineralization in this location," commented
Bob Sibthorpe, President and CEO. "The Company is actively reviewing
the information provided by these latest results to further delineate
the geological model and design a follow up exploration program to
expand the known mineralized areas and identify the source of this high
grade copper."

Copper mineralization is mainly in the form of malachite, a
mineral comprised of 57.48% copper and often associated with acid
leaching operations. An image highlighting the area targeted by this
core drill program, tables listing full information on all drilling to
date, including reverse circulation ("RC") drilling, and location maps
are available on the Company's website at www.midnightsunmining.com.

The following table summarizes the assay results of the recently
completed 12 drill holes:

//st
Hole #        From (m) To (m) Interval (m) True width* (m) Copper %
SLZ-DD-14-001    13.50  18.00         4.50            3.60     6.27
SLZ-DD-14-002     0.00  13.00        13.00           10.40     0.06
SLZ-DD-14-003    10.00  19.95         9.95            7.96     0.50
&                29.40  37.00         7.60            6.08     0.46
SLZ-DD-14-004    17.35  17.75         0.40            0.32     1.40
&                43.00  43.90         0.90            0.72     0.51
SLZ-DD-14-005    21.70  29.70         8.00            6.40     5.08
SLZ-DD-14-006     14.0   24.0         10.0             8.0     0.08
SLZ-DD-14-007     8.00  13.90         5.90            4.70     1.15
&                17.50  48.00        30.50           24.40     0.55
including        33.50  37.50         4.00            3.20     3.17
SLZ-DD14--008     6.00  12.50         6.50            5.20     0.49
SLZ-DD-14-009    12.00  23.60        11.60            9.28     0.34
SLZ-DD-14-010    12.00  26.20        14.20           11.36     5.71
including        12.00  19.20         7.20            5.76     9.58
SLZ-DD-14-011    24.00  26.60         2.60            2.08     0.26
SLZ-DD-14-012    10.00  26.00        16.00           12.80     0.29
//et

* True widths are estimated to be between 75-85% of reported
intervals for all core holes & were estimated by cross sectional
analysis.

All drilling was carried out by Layne Drilling Zambia and assaying
was performed by Genalysis Laboratory Services, an accredited lab
located in Australia. Minor silver values were associated with the
higher grade copper samples.

The Company's technical report, dated July 27, 2013 on the Solwezi
property entitled "Technical Report on the Geology and Exploration
Summary of the Solwezi Group of Prospecting Licences," prepared in
accordance with National Instrument 43-101, is available on the
company's website, as well as on SEDAR at www.sedar.com.

Qualified Control/Quality Assurance: Samples obtained during core
drilling were transported directly to Genalysis Laboratories in
Chingola, Zambia by Midnight Sun personnel for sample preparation.
Samples were sorted, dried, crushed, and pulped before being sent to
Perth, Australia for final chemical analysis using ICP-MS methods. All
samples returning )20,000 ppm Cu were automatically re-checked by
Genalysis. Genalysis is a fully accredited Laboratory and sample
duplicates, standards and blanks were inserted by Genalysis and
verified by the qualified person. All assays received from the 2013
reverse circulation drill program in excess of 2% copper were tested
for acid solubility and these generally exceeded 95% acid soluble
copper.

Qualified Person: Warren Robb, P.Geo, a Qualified Person under NI
43-101, has reviewed and approved the technical data and contents of
this release.

About Midnight Sun: Midnight Sun is a mineral exploration company
with an African focus. The Company has entered into a definitive
agreement to option a 60% interest in the Solwezi Licences in Zambia.
This option agreement is a part of an ongoing strategic alliance with
Kam Chuen Resource Holdings Ltd. Kam Chuen holds an exclusive
prospecting license portfolio of over 150 exploration permits covering
over 100,000 km2 in five African countries. Kam Chuen has agreed to
provide Midnight Sun full access to its property portfolio, as well as
first right of refusal regarding the optioning of any of Kam Chuen's
exploration licenses, and in exchange, Midnight Sun has agreed to offer
Kam Chuen technical expertise in the management and selection of
properties.

ON BEHALF OF THE BOARD

Robert Sibthorpe B.Sc.(Geology), M.B.A.
President & CEO

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
NEWS RELEASE.

This news release includes certain statements that may be deemed
"forward-looking statements." All statements in this release, other
than statements of historical facts, are forward-looking statements.
Although the Company believes the expectations expressed in such
forward-looking statements are based on reasonable assumptions, such
statements are not guarantees of future performance and actual results
or developments may differ materially from those in the forward-looking
statements. Factors that could cause actual results to differ
materially from those in forward-looking statements include, changes in
market conditions, unsuccessful exploration results, changes in the
price of gold, unanticipated changes in key management personnel and
general economic conditions. Mining exploration and development is an
inherently risky business. Accordingly, the actual events may differ
materially from those projected in the forward-looking statements. This
list is not exhaustive of the factors that may affect any of the
Company's forward-looking statements. These and other factors should be
considered carefully and readers should not place undue reliance on the
Company's forward-looking statements. The Company does not undertake to
update any forward-looking statement that may be made from time to time
by the Company or on its behalf, except in accordance with applicable
securities laws.

TSX Venture closing price for MMA-V
Date: 2014/06/24
Closing Price: 0.15

TEL: 604-351-8850  Al Fabbro, Director
Midnight Sun Mining Corp.
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1417600002TS11417600298-04391620140626