Source	Marketwire
Date	06/24/2014
Time	06:00:27 AM

Company	 STRIKEPOINT GOLD INC.
Title	StrikePoint Identifies Strong Gold Geophysical Anomalies at Lobstick





    CDNX Symbol: SKP











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: StrikePoint Gold Inc.

TSX VENTURE SYMBOL: SKP

June 24, 2014

StrikePoint Identifies Strong Gold Geophysical Anomalies at Lobstick


VANCOUVER, BRITISH COLUMBIA--(Marketwired - June 24, 2014) - StrikePoint Gold 
Inc. (the "Company" or "StrikePoint") (TSX VENTURE:SKP) is pleased to announce 
it has received results from the direct-current, geophysical survey at the 
Company's 100% owned Lobstick Gold Project in the Wabigoon Subprovince, 
Ontario, Canada. The survey was performed by Insight Geophysics located in 
Oakville, Ontario.

The survey was accomplished on 3 parallel lines spaced 200 meters apart, for a 
strike length of 400 meters. Each line was over 2,000 meters in length to 
provide the depth penetration needed to evaluate the near surface gold zones 
and how they developed with depth. The geophysics survey was performed to 
identify the geometry of the system to target future drilling.

The survey was able to identify both chargeability and resistivity anomalies to 
a depth of 350 to 400 meters. These anomalies corroborate the known locations 
of the gold bearing shear zones and suggested that the historic drilling of 
these zones was not in the best locations for mineralization; but indicate 
better mineralization below these historic intercepts. This implies that the 
highly anomalous gold mineralization, with a previous reported gold grade of 
38.9 meters of 0.63 g/t Au, could improve with depth.

The survey identified several points of interest:

/T/

--  Disseminated auriferous pyrite showed strong correlation to
chargeability anomalies.
--  Chargeability anomalies improve significantly with depth on all
sections, and interconnect to form broad anomalies at these depths.
--  Mineralization at depth also showed strong resistivity anomalies,
inferring more intense alteration in host rock or change of rock type
associated with the mineralization.
--  Mineralization is continuous and open along strike and down dip.

/T/

These mineralized shear zones represent unique untested opportunities in the 
developing Wabigoon Subprovince since the Main Shear Zone has never been tested 
below a 25 meter vertical depth.

The rock types in the area are similar to the Cameron Lake and Goliath gold 
deposits in the region. Sedimentary rocks proximal to the shear zone suggest 
similar geometry to Treasury Metal's Goliath Gold Deposit and Barrick's Hemlo 
Gold Mines; acting as both cap rocks and focusing mineralizing fluids.

With these results, StrikePoint Gold Inc. will commence planning an initial 
stage of exploratory drilling, targeting these geophysical anomalies that were 
delineated. The company's website displays several figures related to the 
geophysical survey for observation.

John Florek, Technical Advisor of the Company and Qualified Person for purposes 
of National Instrument 43-101 has reviewed the technical information in this 
news release.

Additional information can be viewed at the Company's website 
www.strikepointgold.com.

On Behalf of the Board of Directors of Strike Point Gold Inc.

Shawn Khunkhun, President, CEO

- 30 -

CONTACT INFO:

StrikePoint Gold Inc.
Shawn Khunkhun
President, CEO
604-602-1440 or Toll Free: 1-800-321-8564
www.strikepointgold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=487879968