Source	Marketwire
Date	06/17/2014
Time	05:00:29 AM

Company	 SAVANT EXPLORATIONS LTD.
Title	Savant Explorations Ltd.: IP Defines High-Priority Drill Targets on the 
Buckhorn Copper Property, Arizona





    CDNX Symbol: SVT











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Savant Explorations Ltd.

TSX VENTURE SYMBOL: SVT

June 17, 2014

Savant Explorations Ltd.: IP Defines High-Priority Drill Targets on the 
Buckhorn Copper Property, Arizona


VANCOUVER, BRITISH COLUMBIA--(Marketwired - June 17, 2014) - Savant 
Explorations Ltd. (TSX VENTURE:SVT) ("Savant") is pleased to announce that a 
recently completed Induced Polarization ("IP") survey on the Buckhorn copper 
porphyry property in Arizona returned two strong chargeability anomalies that 
warrant drill testing. One of the anomalies, referred to below as Anomaly 1, 
coincides directly with an exploration target that was established by the 
presence of key surface indicators of porphyry copper mineralization which 
suggests that the IP anomaly may be related to a buried copper porphyry body.

IP Survey Results - Buckhorn Property

The IP survey was conducted along two lines; a main east north-east line of 4.2 
kilometres in length and a northwest cross line of 2 kilometres in length. The 
array used should detect chargeable material to a depth of about 450 metres. 
The main survey line was designed to test for porphyry copper mineralization 
beneath younger post mineralization volcanic rocks east of basement rocks that 
host distal porphyry copper-type alteration and where a basal conglomerate at 
the contact of the younger volcanic and basement rocks contains both fragments 
of leached porphyry rocks and exotic copper oxide.

A graphic presentation of the IP survey results is presented on a plan map and 
a fence diagram of the IP chargeability section with superimposed geology. The 
maps can be found on Savant's website at www.savantexplorations.com and should 
be referred to when reading this release.

The two anomalies, referred to as Anomaly 1 and 2, are defined by chargeability 
levels that are at least three times background, which, in this favourable 
geological setting, may suggest a metallic sulphide source.

The Buckhorn property is one of three properties recently acquired under option 
from Eurasian Minerals Inc. (TSX VENTURE:EMX)(NYSE MKT:EMXX) through its wholly 
owned subsidiary Bronco Exploration Inc. (see the Company's news release dated 
October 30, 2013).

Anomaly 1

Anomaly 1 is a 600 metre long feature that begins east of the contact of the 
covering volcanic rocks. The eastern end of this anomaly may mark the end of 
chargeable minerals or could be caused by the easterly thickening wedge of 
volcanic rocks exceeding the depth limit of the IP survey array. The 
north-westerly cross line indicates that the anomaly is at least 600 metres 
wide. To the southeast on this cross line, the anomaly may be offset by a fault 
that down-drops the zone beneath the detection depth of the survey.

John McClintock, President & CEO of Savant commented, "The location of Anomaly 
1 east of the basement alteration is exactly where we would expect to find a 
porphyry copper deposit buried at a shallow depth beneath the younger volcanic 
rocks. The target is large, potentially open at depth and to the southeast and 
northeast, and represents a priority target for drill testing."

Anomaly 2

Anomaly 2 is approximately 800 metres long and occurs in an area of covering 
river gravels and on a slope where the bed rock is covered by talus from 
younger volcanic rocks. The feature is interpreted to be flat lying, extending 
from surface to a depth of 250 metres. There is no obvious explanation for the 
anomaly, but its position and associated geology make it a compelling target 
for a shallow drill test.

IP Survey Specifications

Savant contracted Zonge International of Tucson Arizona to carry out 6.4 line 
kilometres of induced polarization surveying on the Buckhorn Property in May, 
2014. The survey was a frequency domain, dipole - dipole complex resistivity IP 
survey using a dipole spacing of 200 metres and readings from N 1 to 8. Zonge 
used a 30 Kw generator and a 6 channel Zonge GDP - 3224 instrument. Data was 
decoupled and a 2D smooth-model inversion of the data produced using Zonge's 
TSDIP program. Based on the 2% sensitivity level of the inversion model, the 
survey is conservatively looking to depths between 400 and 450 metres. IP 
chargeability effect can be caused by metallic sulphides as well as other 
minerals such as graphite, clays and magnetite.

Drill testing

Planning and permitting for a program of reverse circulation drilling to test 
both Anomaly 1 and Anomaly 2 has commenced.

About Savant

Savant is an exploration and discovery stage company focused on generating and 
exploring high quality precious and base metal properties in stable 
jurisdictions. Savant has recently initiated a new exploration and discovery 
strategy in Southwest United States with the acquisition of the Buckhorn, 
Jasper Canyon, and Frazier Creek properties. Savant also owns three other 
high-quality properties, Yuby-Gabriela, Blue Moon and Yava that management is 
seeking to monetize for maximum value to Savant and its shareholders. These 
other properties and assets are 100% owned with combined annual holding costs 
of approximately $30,000.

John McClintock, P. Eng., CEO of Savant is the Qualified Person, as defined by 
National Instrument 43-101, responsible for the technical data in this news 
release.

More information on the Company's activities is available at the Company's 
website at www.savantexplorations.com.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

This news release contains forward-looking statements. These statements are 
based on assumptions and judgments of management regarding future events or 
results that may prove to be inaccurate as a result of failure to obtain 
necessary regulatory approvals, the failure to reach agreement on final 
documentation, exploration results and other risk factors that are beyond 
Savant's control. There can be no assurance that such forward-looking 
statements will prove to be accurate as actual results and future events could 
differ materially from those anticipated in such statements. Accordingly, 
readers should not place undue reliance on forward-looking statements contained 
in this news release.

- 30 -

CONTACT INFO:

Savant Explorations Ltd.
John McClintock
President and CEO
(604) 568-5817
info@SavantExplorations.com
www.SavantExplorations.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=486719254